## Slide 1: Active Closed-Loop Control of DMRJ Engines NASA/AFRL Workshop on High-Speed Test Techniques Nov 30 - Dec 1, 2022
Robin L. Hunt
Hypersonic Airbreathing Propulsion Branch (D306)

## Slide 2: Benefits of Active Closed-Loop Control
Axial location
Pressure
Forebody shocks
Freestream Mach 3-7
Nozzle
Isolator
Combustor
Inlet
Increase thrust & acceleration
DMRJ propulsive performance improves with increased net static-pressure gain, which is related to the shock train position
The shock train leading edge (STLE) moves in response to variations in the inlet and/or combustor states, e.g., trajectory or engine operation change
  STLE too far forward → inlet unstart
  STLE too far aft → combustor interactions, flame out can occur
Active closed-loop control: manage isolator shock train position in real time
  Maximize thrust and acceleration
  Improve engine reliability by accommodating trajectory and attitude transients
Shock train
STLE

## Slide 3: Basic Control Loop & Control Challenges
Feedback sensors provide info used to determine current isolator condition (e.g., STLE position, OPR)
A change in fuel flow rate impacts the isolator backpressure
The controller outputs a command based on the current engine conditions and desired operational state
Sense
Decide
Actuate
Control algorithm development requires a lot of ground testing, modelling, and simulation
Feedback sensors must be robust (e.g., high temperatures)
Limited or no optical access
Packaging constraints (limited number of sensors, restricted placement of sensors)
Control algorithms and actuation must be fast to accommodate short timescales
  Planned trajectory or engine operational changes over 10-100s ms
  Unstart may be an order of magnitude faster
Inflow disturbances
Vehicle attitude changes
Combustor perturbations

## Slide 4: Adaptive Pressure Profile (APP) Method to Sense the STLE Location
Isolator pressure profile
Wall static pressure
Streamwise location
Isolator
Combustor
Hunt, G. J. and Hunt, R. L., “Locating the isolator shock train leading edge with limited pressure information,” Journal of Propulsion and Power, Vol. 37, No. 6, 2021, pp. 876-892. https://doi.org/10.2514/1.B38334
Time
APP uses a small number of pressure transducers and combines the measurements from multiple timepoints to build and continuously update a pressure profile. The learned profile is fit to new measurements to locate the STLE accurately.
Real-time learning approach means APP is adaptable and can adjust to changing conditions, but it must learn the profile shape more rapidly than it deforms
  Does not heavily rely on pre-flight calibration
  Reduces cost & the need for extensive ground testing
Robust, high-temperature pressure transducers can be used
Works in sparse transducer situations – typical of flight vehicles
Computationally inexpensive

## Slide 5: Evaluation of the APP Method
Tested in 3 different direct-connect isolator models with a range of Mach and Reynolds numbers, isolator geometries, etc.:
University of Michigan
Air Force Institute of Technology (AFIT)
NASA LaRC Isolator Dynamics Research Lab (IDRL)
General APP findings:
  Good accuracy for 3 – 6 pressure transducers
  Works with different sensor placements
  Only a few previous timepoints are needed to build the adaptive profile
  STLE location estimate accurate to within 1 duct height
  Maintains good accuracy when the STLE is upstream of the transducers or between transducers with large spacing
Time
Streamwise location
3
3
Flow
Streamwise location
Flow
Flow
2
1
2
1
Time
3 sensors
Truth
APP
Base

## Slide 6: Advancement of Controls Concepts
Sense
Decide
Actuate
Upcoming APP work:
Integrate APP with an algorithm to detect of sensor failure
Extend testing to isolators with distorted inflow
APP testing in large-scale ground test models
Some other recent control concepts:
  TDLAS as a possible flight-ready diagnostic for controls feedback (HIFiRE 1, 2)
  HIFiRE 2-C flight test (this work is CUI, Distro C, …)
  Purdue, UVA, Hampton U – NASA ULI, “Emission & Absorption Spectroscopy Sensors for Hypersonic Flight Control”