## Slide 1: Silicon Photonic Transceiver for Spacecraft Navigational Lidar
Nathan Dostart
NASA Langley Research Center
SPIE Photonex, Dec. 7, 2022

## Slide 2: NASA Moon to Mars
NASA is planning for sustained human presence on the Moon and Mars
Operational lunar and Martian bases need periodic resupply, multiple landers
New/improved sensors need to land payloads in close proximity (<1 km) and with high precision (< 100 m)

## Slide 3: Navigation Doppler Lidar Enables Moon to Mars
Navigation Doppler Lidar (NDL)
  Frequency-modulated continuous wave (FMCW) lidar system
  1550 nm, fiber-optic system
NDL measures spacecraft attitude, velocity, and altitude during descent
  <1 cm/s velocity resolution, ~10 cm range resolution
  >5 km operational range
Precise measurements enable reduced landing uncertainty
Small size allows for redundancy, supports small landers
2 NDL units flying to the moon in 2023

## Slide 4: NDL In Action

## Slide 5: NDL Operational Schematic
FMCW for range/velocity measurements
3 channels allow for vectorial position/velocity
NDL Flight Units
LO – Local Oscillator
BS – Beam Splitter
PD – Photodiode
PBS – Polarizing Beam Splitter
Transmit Path
LO Path
Return Path
Seed
Amp.
PBS
BS
LO Tap
PD
PD
Tele.
1:3
1:3
3x
Freq. Mod.
Up Ramp
Down Ramp
Dwell
t
fRF
fOpt
Transmit
Return
Het. Freq.
Delay
Doppler

## Slide 6: NDL Next Generation
Incorporate many components into silicon photonic PIC including
  Modulator
  LO tap
  Balanced receiver
Use liquid crystal multi-angle beam steering to reduce channel count
Reduced system size, more robust to environment, low assembly complexity, improved performance (hopefully!)
LCBS
LO – local oscillator
LCBS – liquid crystal beam steering
BS – beam splitter
PD - photodiode
Transmit Signal
LO
Return Signal
Seed
Amp.
Circ.
BS
LO Tap
PD
PD
Tele.
Freq. Mod.
SiP PIC
Gen 1 PIC

## Slide 7: Gen. 1 PIC and Packaging – Open Top

## Slide 8: Gen 1 PIC Overview
Mach-Zehnder Modulator
Y-split
Y-split
Y-split
PD
PD
BS
PD
PD
BS
PD
PD
BS
PD
PD
BS
PIC
RX1
RX2
RX3
RX4
MZM
RX4
RX1-3
90:10 Tap
Alignment Loop
MZM for evaluation
4x balanced receivers
Single LO input

## Slide 9: PIC Receiver Demo with NDL
Breadboard receiver with PIC
  PIC PDs with off-chip bias tees, RF amps, filter
Use NDL test unit for lidar measurement
  Beam on belt sander provides ~6 MHz Doppler frequency

## Slide 10: Receiver Measurements – The Bad News
~10 dB SNR drop
Partially explained by 5-6 dB estimate of total coupling loss
  Targeted/expected 3 dB, unknown cause for excess loss
More testing planned, current receiver non-optimal

## Slide 11: Receiver Measurements – The Good News
~25 dB additional common mode noise suppression
Existing spurs on NDL system require digital filtering, can cause measurement issues
  Imperfect synth modulation imprints 50 MHz spurs on LO
Improved common mode rejection improves NDL performance

## Slide 12: Future Work
Signal power drop higher than expected
  Further characterization required to identify source of loss
  Improved coupling efficiency
Modulator characterization and revised design for single sideband operation
Hermetic package with in-package receiver electronics
Space-qualification/environmental test campaign -> TRL 6

## Slide 13: Summary
Developed open-top silicon photonic PIC for space-based lidar system
Initial version showed reduced SNR but improved common mode rejection
Demonstration with existing lidar system
Further development focusing on
  Incorporating more functionality on the PIC
  Hermetic packaging and environmental testing for space qualification

## Slide 14: Thanks to the NDL Team
Keep an eye out for us on the Moon in 2023!