## Slide 1
GH35A-0659: Cropland and Land-clearing Emission Factors from FIREX-AQ
Katherine R. Travis, NASA LaRC (katherine.travis@nasa.gov)
J. H. Crawford, R. Moore, A. J. Soja, E. B. Wiggins, E. Gargulinski, A. Fried, J. E. Dibb, C. Warneke, J. P. DiGangi, J. B. Nowak, D. R. Blake, G. M. Wolfe, A. W. Rollins, J. A. Neuman, G. S. Diskin, A. Wisthaler, P. Campuzano Jost, D. Pagonis, H. Guo, A. E. Perring, J. M. Katich, P. R. Veres, J. L McCarty, C. Womack
Prescribed fires are a frequent tool for land management, used for both land-clearing and agricultural activities. Determining emissions and subsequent air quality impacts from these fires requires emission factors appropriate for the type of biomass being burned. The NOAA/NASA Fire Influence on Regional to Global Environments and Air Quality (FIREX-AQ) campaign that took place from July to September 2019 provided comprehensive sampling of prescribed fires in the Eastern United States. We calculate emission factors for agricultural and land-clearing activities from FIREX-AQ and the dependence of these emission factors on fuel type/burning characteristics (i.e., modified combustion efficiency).
Agricultural/prescribed fire plumes sampled during FIREX-AQ, colored by fuel type. a) Map of plume locations. b) Histogram of modified combustion efficiency (MCE) for sampled plumes.
Introduction
Identified 4 agricultural fuels (corn, rice, soybean, winter wheat) and 5 types of land-clearing (slash, piled slash, grassland, shrubland, Blackwater forest (understory) across 76 fires.
Half of all sampled fires (38 vs. 76) were burning corn agricultural residue.
Corn residue burned at a higher MCE (0.94) than rice or soybean residue (0.91), or prescribed fuels (0.90-0.91) likely due to drying of the fuel.
Land-clearing and agricultural fuels have distinct MCE
Conclusions: Variability in emission factors may be a strong function of MCE and/or fuel type. FIREX-AQ reveals new significant relationships with MCE/fuel due to the large increase in sample size over previous compilations.
Example photographs for fuel types sampled during the Eastern U.S. component of FIREX-AQ, from the DC-8 visible camera (corn, rice, soybean, winter wheat, shrubland), DC-8 infrared camera (piled slash, slash), and a ground-based camera (grass).
Approximately 30% of measured VOCs are long-lived (lifetime > 12 h) and may have larger impacts on air quality downwind of agricultural and prescribed fires.
Largest are formaldehyde (14%), acetaldehyde (11%), methylglyoxal, 2,3-butanedione (diacetyl), 5-methylfurfural, and acrolein (~6% each).
2,3-butanedione: only VOC with shorter lifetime against photolysis (~1 hour) than OH oxidation (~3 days).
Impact of this species is missed when viewing biomass burning emissions in terms of OH reactivity.
Corn methane EF is 2.7 g kg-1
Only 30% of Andreae (2019) or Akagi et al., 2011 EF (~6 g kg-1)
Liu et al. (2016) found insignificant positive correlations for NO, NO2, and SO2 for 15 agricultural fires in the Southeast U.S..
We obtain positive significant correlations for NO, NO2, SO2, ammonium and chloride.
Land-clearing and agricultural fuels have distinct emissions
After correcting for any significant dependence on MCE, the following species have significant differences (>50%) between agricultural and land-clearing fuels.
Akagi et al., 2011
Andreae et al., 2011
Determine 97 VOC emission factors, some never/rarely reported before for agricultural/land-clearing fires
Long-lived species are ~30% of total measured VOCs
VOC emission factors show possible evidence of different combustion processes
Evidence of significant positive relationships with MCE