## Slide 1: Operational Techniques in Microgravity for Cryogenic Fluid Management
December 7, 2022
B. D. Hoffman – JSEG, Fluid Dynamics Branch (MSFC-ER42)
J. M. Brodnick – NASA, Fluid Dynamics Branch (MSFC-ER42)

## Slide 2: Background
  The Fluid Dynamics Branch within the Propulsion Systems Department at the Marshall Space Flight Center is currently supporting multiple programs in need of in-space cryogenic fluid management (CFM) analysis.
    Space Launch System (SLS) upper stages
    Commercial Lunar Payload Services (CLPS)
    Human Landing System (HLS)
    Nuclear Thermal Propulsion (NTP) systems
SLS Upper Stage Concept
(NASA)
CLPS Concept
(Intuitive Machines)
HLS Concept
(SpaceX)
NTP Concept
(NASA)

## Slide 3: Background (continued)
  Design techniques to control propellant locations within tanks is commonly requested.
  Organizations are often interested in solutions for standard tank designs.
    Excludes various CFM technologies (many need flight experience to reduce risk of use)
    Excludes propellant management devices (can be heavy for large tanks)
  Typical propellant management needs include:
    Vapor only venting
    Unsubmerged ullage gas diffuser for pressurization
    Propellant only extraction for engine start or propellant transfer
    Propellant settled to mitigate ullage collapse and boiloff
  Performing in-space vehicle maneuvers is one way to manage propellants with standard tank designs.
  A variety of settling and unsettling events were simulated with computational fluid dynamics (CFD) to address some typical propellant management needs for a generic tank; results are presented herein.

## Slide 4: Simulation Methodology
  Used Loci/STREAM-VoF for every simulation
    Pressure based Navier-Stokes solver
    Volume of fluid (VoF) method of distinct phase representation
  Used a generic 2 m diameter tank with hemispherical domes
    2 m tall barrel section
    ~4 million unstructured hexahedral volume cells
  Used a non-inertial reference frame to specify vehicle dynamics
    Inputs varied by simulation
  Simulated LOX and GOX at different conditions
    Saturated:
      1 bar ullage pressure
    Unsaturated:
      4 bar ullage pressure
      90 K minimum liquid temperature
      250 K maximum ullage temperature
      Initially stratified around the gas-liquid interface
  Used an implicit Hertz-Knudsen model for phase change
    Evaporation and condensation at gas-liquid interfaces
    Accommodation coefficient of 0.001 for every simulation
Computational Domain
(20% Fill Level Shown)

## Slide 5: Settling Thrust Optimization

## Slide 6: Propellant Dynamics
Propellant Dynamics Animation
(100% Duty Cycle)
Liquid Center of Gravity (CG) Transients
  Settling was performed at 5 average acceleration levels corresponding to different duty cycles.
  Bulk slosh dynamics were comparable for every settling maneuver when nondimensionalizing by slosh frequency.
  Duration to reach a particular slosh state was the only real difference.
  Sim. Conditions:
  Bare tank
  Initial lateral offset
  Saturated fluids

## Slide 7: Settling Maneuver Design Tool
  A settling maneuver design tool like that shown can be created from the analysis results (markers).
    Selecting a duty cycle tells you the maneuver duration and thruster on time for the maneuver.
  A model (lines) can be used to extrapolate from a single data point in lieu of modeling the entire parametric space.
  1st Lateral Slosh Mode Frequency Scaling:
    Enabled by consistent bulk slosh dynamics for every considered average settling acceleration
    Reliant upon a calibration point for every tank configuration and initial fluid condition considered

## Slide 8: Lateral Slosh Reduction through Vehicle Roll

## Slide 9: Propellant Dynamics
Propellant Dynamics Animations
(Lateral Offset)
(Partially Offset)
(Circumferentially Distributed)
  Sim. Conditions:
  Bare tank
  0.1 m/s2 Avg. Acceleration
  Saturated fluids
  Settling was performed for 3 initial propellant distributions.
  Slosh dynamics varied by initial condition.
    Lateral Offset – lateral slosh
    Partially Offset – lateral slosh
    Circumferentially Distributed – symmetric slosh

## Slide 10: Effects of Roll on Settling Efficiency
  Liquid CG transients shown below demonstrate the time to reach nearly periodic slosh motion.
    Settling efficiency drops sharply beyond this point due to low slosh damping.
  Rolling a vehicle prior to settling can distribute liquid circumferentially and reduce lateral slosh motion.
  Long duration rolling to achieve a uniform distribution of liquid circumferentially results in symmetric slosh motion which persists longer.
    This effect is not well illustrated in the plotted metrics.
Liquid Center of Gravity (CG) Transients
X
Y

## Slide 11: CFM Impact of Anti-Slosh Baffles

## Slide 12: Propellant Dynamics
  Settling was performed for 2 tank configurations.
  The anti-slosh baffle aided propellant breakup during initial large amplitude lateral sloshing.
    This behavior will enhance ullage collapse.
  However, slosh damping was greatly increased by the baffle greatly reducing settling durations and enabling more settled final states.
Propellant Dynamics Animations
(No Baffle)
(Baffle)
  Sim. Conditions:
  Initial lateral offset
  0.1 m/s2 Avg. Acceleration
  Saturated fluids

## Slide 13: Effects of Baffles on Settling Efficiency
  Liquid CG transients shown below demonstrate the time to reach nearly periodic slosh motion.
  High damping was maintained across the wave amplitude space in the baffled tank enabling more rapid and complete settling than in the bare tank.
    Halting settling during slosh motion will allow the propellant to unsettle again due to residual liquid momentum.
    Having some structure like a baffle above the liquid once settling is halted gives the liquid a place to pin to via surface tension.
    High liquid momentum can overpower surface tension though so the final settled state must be chosen carefully.
Liquid Center of Gravity (CG) Transients

## Slide 14: Ullage Collapse Mitigation

## Slide 15: Propellant Dynamics during Slewing
  Slewing was performed for 2 slew profiles, notional illustrations of which are shown.
  Propellant naturally unsettles relative to the tank along left side in the animations shown.
  Translating the vehicle in the direction of unsettling during the slew minimizes propellant movement relative to the tank.
Liquid Position
Temperature Contour
Liquid Position
Temperature Contour
Propellant Dynamics Animations
(Slew Without Translation)
(Slew With Translation)
Vehicle Maneuver Illustration
Vehicle Maneuver Illustration
  Sim. Conditions:
  Bare Tank
  Initial settled propellant
  Unsaturated fluids

## Slide 16: Ullage Collapse during Slewing
  Various transient metrics quantifying ullage collapse are shown in the plots.
  Significant mixing occurred when purely rotating.
    Ullage temperature and pressure drop
    Initial condensation as the bulk liquid warmed from subcooled to saturated
    Trailing evaporation as ullage pressure approaches complete collapse and liquid becomes saturated
  Little mixing and thus ullage collapse occurred when including translation.

## Slide 17: Propellant Dynamics after Engine Cutoff
  Settling following engine cutoff was performed for 3 settling start times.
  Low amplitude pitching oscillation was performed prior to engine cutoff to induce low amplitude slosh motion.
  Engine cutoff occurred over 1.5 seconds.
Vehicle Pitch Rates and Axial Accelerations around Engine Cutoff
  Sim. Conditions:
  Baffled Tank
  Initial settled propellant
  Unsaturated fluids

## Slide 18: Propellant Dynamics after Engine Cutoff
  Slosh motion prior to engine cutoff facilitated unsettling as liquid momentum is unbounded without vehicle acceleration.
  Delaying settling allowed propellant to mix with the hot ullage gas through initial unsettling and the following high amplitude sloshing.
  Settling before propellant moves away from its initial state prevents most mixing.
Propellant Dynamics Animations
(No Settling)
(Settling Delayed 20 s)
(Immediate Settling)

## Slide 19: Ullage Collapse after Engine Cutoff
  Various transient metrics quantifying ullage collapse are shown in the plots.
  Without settling after engine cutoff, complete ullage collapse was approached.
  Delayed settling mirrored the initial ullage collapse observed without settling but retained excess ullage pressure once mixing was suppressed as expected.
  Ullage collapse was significantly mitigated when settling was started promptly following engine cutoff.

## Slide 20: Conclusion
  Propellant dynamics during in-space vehicle maneuvers were investigated with CFD analysis.
    Objective was to identify strategies for addressing CFM using vehicle maneuvers.
  Bulk propellant dynamics were found to be insensitive to settling acceleration magnitude.
    Dependent upon tank configuration and initial propellant distribution
  Settling costs reduce as average acceleration reduces, but maneuver duration increases.
  Rolling a vehicle prior to settling can distribute liquid circumferentially and reduce settling maneuver duration.
  Anti-slosh baffles can significantly reduce settling requirements but inherently aid ullage collapse when unsettling.
  Slew maneuvers can be designed to translate the vehicle during rotation to avoid unsettling.
  Settling should be done as soon as possible following engine cutoff to avoid unsettling.