## Slide 1: Crossflow Attenuated Natural Laminar Flow (CATNLF) Technology Development: From Concept to Flight
Michelle Banchy (Lynde), Richard Campbell, and Brett Hiller
AIAA HRS Young Professionals Technical Excellence Lecture
December 12, 2022

## Slide 2: Outline
Background and Motivation
CATNLF Concept Development
  Computational Study
  Wind Tunnel Test
  Flight Test
Current and Future Work
Summary
AIAA HRS YP Technical Excellence Lecture

## Slide 3: Why Laminar Flow?
“Laminar” and “turbulent” describes the state of the boundary layer (fluid very near the surface)
Laminar flow significantly improves vehicle performance by reducing skin friction and profile drag
For 777-class aircraft with laminar flow on 60% of the wings upper surface, the potential fuel burn savings per aircraft per year is 5-10%
  390,000 gallons of fuel savings
  $1.8 million in fuel cost savings
  8.2 million pounds of CO2 emissions reduced
Fully-Turbulent Airfoil
Airfoil with Laminar Flow
Less skin friction
Smaller wake
Transition from laminar to turbulent
AIAA HRS YP Technical Excellence Lecture

## Slide 4: Potential for Laminar Flow on Commercial Transports
Fuselage
Wings
(Upper Surface)
Nacelles
Vertical/Horizontal Tails
AIAA HRS YP Technical Excellence Lecture

## Slide 5: Challenge with Laminar Flow on Transport Wings
Transport aircraft require swept wings to reach desired cruise speeds, which leads to 4 primary mechanisms of transition
AIAA HRS YP Technical Excellence Lecture

## Slide 6: Challenge with Laminar Flow on Transport Wings
Transport aircraft require swept wings to reach desired cruise speeds, which leads to 4 primary mechanisms of transition
Attachment Line Transition
Cause: Turbulent fuselage boundary layer
Effect: Total loss of laminar flow
AIAA HRS YP Technical Excellence Lecture

## Slide 7: Challenge with Laminar Flow on Transport Wings
Transport aircraft require swept wings to reach desired cruise speeds, which leads to 4 primary mechanisms of transition
Attachment Line Transition
Cause: Turbulent fuselage boundary layer
Effect: Total loss of laminar flow
Crossflow Transition
Cause: Increasing sweep and Reynolds number
Effect: Leading edge transition
AIAA HRS YP Technical Excellence Lecture

## Slide 8: Challenge with Laminar Flow on Transport Wings
Transport aircraft require swept wings to reach desired cruise speeds, which leads to 4 primary mechanisms of transition
Attachment Line Transition
Cause: Turbulent fuselage boundary layer
Effect: Total loss of laminar flow
Crossflow Transition
Cause: Increasing sweep and Reynolds number
Effect: Leading edge transition
Tollmien-Schlichting Transition
Cause: Adverse pressure gradients
Effect: Midchord transition
AIAA HRS YP Technical Excellence Lecture

## Slide 9: Challenge with Laminar Flow on Transport Wings
Attachment Line Transition
Cause: Turbulent fuselage boundary layer
Effect: Total loss of laminar flow
Crossflow Transition
Cause: Increasing sweep and Reynolds number
Effect: Leading edge transition
Tollmien-Schlichting Transition
Cause: Adverse pressure gradients
Effect: Midchord transition
Bypass Transition
Cause: Surface imperfections
Effect: Turbulent wedges
Transport aircraft require swept wings to reach desired cruise speeds, which leads to 4 primary mechanisms of transition
AIAA HRS YP Technical Excellence Lecture

## Slide 10: Historic NLF Boundary
Wing Sweep, deg.
Laminar Flow Extent, ReT
x106
Historic NLF experiments
AIAA HRS YP Technical Excellence Lecture

## Slide 11: Historic NLF Boundary
Wing Sweep, deg.
Laminar Flow Extent, ReT
x106
Typical 777-Class Aircraft
Speed ≈ Mach 0.85
Wing Sweep ≈ 34 – 38 deg.
NLF Wing on Honda Jet
Speed = Mach 0.72
Wing Sweep = 10 deg.
Historic NLF experiments
AIAA HRS YP Technical Excellence Lecture

## Slide 12: Historic NLF Boundary
Wing Sweep, deg.
Estimated historic boundary for NLF
Laminar Flow Extent, ReT
x106
Additional flow control needed (i.e., suction)
Historic NLF experiments
AIAA HRS YP Technical Excellence Lecture

## Slide 13: Crossflow Transition on Transport Wings
Historic options to address crossflow transition on wings:
  Reduce wing sweep
    Penalty: Requires aircraft to fly slower
  Introduce a flow control system, such as suction
    Penalty: Increases weight, complexity, and cost
Neither option has “bought its way onto” commercial transports
Research Goal
Obtain significant extents of laminar flow on typical transport wings without historic crossflow penalties
AIAA HRS YP Technical Excellence Lecture

## Slide 14: CATNLF Concept Development
Goal: To develop technology
Reference: AIAA 2016-4326
Goal: To confirm computations
References: AIAA 2017-3058, AIAA 2019-3292
Goal: To advance technology
Reference: AIAA 2021-0173
Computational Study
Wind Tunnel Test
Flight Test
Test article
NASA Laminar Flow Design Method
Crossflow Attenuated NLF (CATNLF) design method changes the shape of the wing airfoils to obtain pressure distributions that delay transition by damping crossflow instabilities
2014 – 2017
2017– 2019
2019 – Present
AIAA HRS YP Technical Excellence Lecture

## Slide 15: CATNLF Concept Development
Goal: To develop technology
Reference: AIAA 2016-4326
Goal: To confirm computations
References: AIAA 2017-3058, AIAA 2019-3292
Goal: To advance technology
Reference: AIAA 2021-0173
Computational Study
Wind Tunnel Test
Flight Test
Test article
2014 – 2017
2017– 2019
2019 – Present
AIAA HRS YP Technical Excellence Lecture

## Slide 16: Computational Tools
Design Module: CDISC
Applies knowledge-based design rules to change geometry to match target pressure distributions
Flow Solver: USM3D
  Solves Navier-Stokes equations on unstructured tetrahedral grid
Boundary Layer Profile Solver: BLSTA3D
  Calculates boundary layer velocity and temperature profiles based on chordwise pressure distribution assuming conical flow
Boundary Layer Stability Analysis: LASTRAC
  Stability analysis and transition prediction using eN Linear Stability Theory method with compressibility effects
AIAA HRS YP Technical Excellence Lecture

## Slide 17: Example Turbulent Airfoil Design
Wing Station
NASA STARC-ABL Configuration
17
AIAA HRS YP Technical Excellence Lecture

## Slide 18: Example CATNLF Pressures
Notable differences:
Leading-edge acceleration
  Laminar uses rapid acceleration for crossflow (CF) control
Rooftop pressure gradient
  Laminar uses mild favorable gradient for Tollmien-Schlichting (TS) control
  Turbulent uses mild adverse gradient for shock strength reduction
Shock strength
  Turbulent has weaker shock
Acceleration
CP gradient
Shock strength
AIAA HRS YP Technical Excellence Lecture

## Slide 19: Pressure Changes Needed for CATNLF Concept
Design Conditions: Mach = 0.85, CL = 0.50, ReMAC = 30 x106, ΛLE = 35 deg.
Inboard
Outboard
Turbulent Wing
CATNLF Wing
Inboard
Outboard
AIAA HRS YP Technical Excellence Lecture

## Slide 20: Crossflow Growth Resulting from CATNLF Concept
CF N-factor Growth
CF N-factor Growth
Critical N-factor
Inboard
Outboard
Design Conditions: Mach = 0.85, CL = 0.50, ReMAC = 30 x106, ΛLE = 35 deg.
Turbulent Wing
CATNLF Wing
Inboard
Outboard
AIAA HRS YP Technical Excellence Lecture

## Slide 21: Tollmien-Schlichting Growth Resulting from CATNLF Concept
Critical N-factor
Inboard
Outboard
TS N-factor Growth
TS N-factor Growth
Design Conditions: Mach = 0.85, CL = 0.50, ReMAC = 30 x106, ΛLE = 35 deg.
Turbulent Wing
CATNLF Wing
Inboard
Outboard
AIAA HRS YP Technical Excellence Lecture

## Slide 22: Airfoil Changes Needed for CATNLF Concept
Inboard
Outboard
Design Conditions: Mach = 0.85, CL = 0.50, ReMAC = 30 x106, ΛLE = 35 deg.
Turbulent Wing
CATNLF Wing
Inboard
Outboard
AIAA HRS YP Technical Excellence Lecture

## Slide 23: Laminar Flow Extent for CATNLF Wing
CATNLF method enables laminar flow on 56% of the wing upper surface at the design condition, which provides a 7% drag reduction compared to a turbulent wing
Laminar
Turbulent
Flow
Configuration | CL | CD | ΔCD (from Baseline)
Turbulent Baseline | 0.500 | 0.0236 | 
NLF Design | 0.500 | 0.0220 | -16 counts (7% savings)
NLF Design (Fully Turbulent) | 0.500 | 0.0246 | +10 counts (4% penalty)
AIAA HRS YP Technical Excellence Lecture
Design Conditions: Mach = 0.85, CL = 0.50, ReMAC = 30 x106, ΛLE = 35 deg.

## Slide 24: Computational Results Relative to Past NLF Experiments
Computational predictions of a wing designed with CATNLF method significantly expand the historic boundary for NLF technology
Wing Sweep, deg.
Laminar Flow Extent, ReT
x106
Computational results of CATNLF wing in flight environment
Estimated historic boundary for NLF
Historic NLF experiments
AIAA HRS YP Technical Excellence Lecture

## Slide 25: CATNLF Concept Development
Goal: To develop technology
Reference: AIAA 2016-4326
Goal: To advance technology
Reference: AIAA 2021-0173
Computational Study
Flight Test
Test article
2014 – 2017
2019 – Present
AIAA HRS YP Technical Excellence Lecture
Goal: To confirm computations
References: AIAA 2017-3058, AIAA 2019-3292
Wind Tunnel Test
2017– 2019

## Slide 26: Facility Description
Test completed in October 2018 in the National Transonic Facility (NTF)
NTF is a pressurized cryogenic closed-circuit, continuous-flow, fan-driven wind tunnel
Motivation for testing in the NTF:
  Flight Reynolds numbers for relevant laminar flow data
  Semispan testing capability for reducing unit Reynolds numbers
  Acceptably low turbulence levels for laminar flow testing
Aerial view of the NTF complex
AIAA HRS YP Technical Excellence Lecture

## Slide 27: Instrumentation and Measurements
Model designed using CATNLF method called Common Research Model with Natural Laminar Flow (CRM-NLF)
5.2% scale semispan model
  Semispan length = 60.2 inches
  Reference chord = 14.3 inches
Data acquired:
  Surface pressure
  Transition visualization
  Force and moment
  Model deformation
Mach | α (deg.) | TT (F) | ReMAC (million)
0.86 | 1.5 to 3.0 | +40 | 10.0 to 15.0
 |  | -50 | 12.5 to 20.0
 |  | -150 | 20.0 to 30.0
Primary Test Conditions
CRM-NLF semispan model installed in the NTF
AIAA HRS YP Technical Excellence Lecture

## Slide 28: Wind Tunnel Pressure Measurements
Pressure measurements from the wind tunnel test showed CATNLF pressure distributions are obtained on the model
Inboard
Outboard
Computations
Wind Tunnel
Inboard
Outboard
AIAA HRS YP Technical Excellence Lecture

## Slide 29: Wind Tunnel Results Relative to Computational Predictions
Good agreement between pretest predictions and experimental extents of laminar flow suggest CATNLF assumptions, tools, and design method are valid
AIAA HRS YP Technical Excellence Lecture

## Slide 30: Wind Tunnel Results Relative to Past NLF Experiments
CRM-NLF in the NTF showed extents of laminar flow that nearly double the historic maximum seen at comparable wing sweep
CRM-NLF in the NTF
Wing Sweep, deg.
Laminar Flow Extent, ReT
x106
Estimated historic boundary for NLF
Historic NLF experiments
AIAA HRS YP Technical Excellence Lecture

## Slide 31: Wind Tunnel Results Relative to Past NLF Experiments
Difficulties acquiring high Reynolds number laminar flow data in a wind tunnel environment motivate flight test to expand historic NLF boundary further
CRM-NLF in the NTF
Wing Sweep, deg.
Laminar Flow Extent, ReT
x106
Computational results of CRM-NLF in flight
Estimated historic boundary for NLF
Historic NLF experiments
Smaller extents of laminar flow in tunnel due to different environment and limited model size
AIAA HRS YP Technical Excellence Lecture

## Slide 32: CATNLF Concept Development
Goal: To confirm computations
References: AIAA 2017-3058, AIAA 2019-3292
Wind Tunnel Test
2017– 2019
AIAA HRS YP Technical Excellence Lecture
Goal: To advance technology
Reference: AIAA 2021-0173
Flight Test
Test article
2019 – Present
Goal: To develop technology
Reference: AIAA 2016-4326
Computational Study
2014 – 2017

## Slide 33: CATNLF Flight Test Series
Series of 3 flight tests underneath the F-15 in collaboration with Armstrong Flight Research Center
  Resistive heating (ReHEAT) experiment to improve laminar flow detection (2019)
  Flow rake experiment to quantify the flow environment under the F-15 (2023)
  CATNLF “stub wing” test article to advance technology (2023)
CATNLF Experiment
AIAA HRS YP Technical Excellence Lecture
Flow Rake Experiment
ReHEAT Experiment
AFRC F-15 CLIP Flight Test Bed
Changeable test article

## Slide 34: Test Article Dimensions and Design Conditions
CLIP
Test Article
CLIP
Test Article
Front View
Side View
Geometry Parameters | 
Mean Aerodynamic Chord (MAC) | 5.9 ft
Span | 3.3 ft
Reference Area | 19.7 ft2
Leading-Edge Sweep | 35 deg
Max Thickness | 10% chord
Design Conditions | 
Mach | 0.85
Altitude | 5,000 ft
ReMAC | 31 million
Sectional Lift Coefficient | 0.50
Critical N-Factor | 10
Laminar Flow Target | Suction side only
AIAA HRS YP Technical Excellence Lecture

## Slide 35: Test Article Design
Laminar
Turbulent
AIAA HRS YP Technical Excellence Lecture
Designed test article is predicted to support laminar flow on approximately 53% of the suction side surface area in a flight environment
Design was conducted to enable flight test goals
  Primary Goal: To confirm the effectiveness of the CATNLF method in attenuating crossflow growth at conditions representative of a modern transonic transport wing
  Secondary Goal: To investigate the surface requirements for laminar flow applications on transonic transport wings

## Slide 36: Flight Test Strategy
Flight conditions are selected to acquire data for flight test goals
  Mach = 0.85
  Altitude = 5,000 – 49,500 ft
  ReMAC = 6 – 31 million
  Unit Re = 1.0 – 5.3 million/ft
Data and instrumentation:
  Transition images using IR with heating layer
  123 static pressure sensors
  12 dynamic pressure sensors
  54 subsurface thermocouples
  4 accelerometers
  F-15 conditions and nose boom probe
AIAA HRS YP Technical Excellence Lecture
Pressure side of test article showing instrumentation cavity

## Slide 37: CATNLF Compared to Historic NLF Boundary
Computational predictions of the CATNLF test article
significantly expand the historic boundary for NLF technology
Laminar Flow Extent, ReT
x106
Estimated historic boundary for NLF
Historic NLF experiments
Larger extents of laminar flow due to flight environment
CATNLF in flight* *Computational predictions
CRM-NLF in the NTF
Wing Sweep, deg.
AIAA HRS YP Technical Excellence Lecture

## Slide 38: Current and Future Work
Current status of CATNLF flight test:
  Test article manufactured and delivered to Langley September 2022
  Pre-flight instrumentation and safety analysis work underway
  First flight scheduled for June 2023
Future work for CATNLF:
  Plans to release flight test data to community to advance computational tools
  Potential follow-on wind tunnel test of flight test article to compare laminar flow in two environments
AIAA HRS YP Technical Excellence Lecture
Painted test article at Langley

## Slide 39: Summary
Laminar flow on transport wings has the potential to reduce fuel burn by 5-10%, but has been limited in practical application due to the challenge of crossflow growth on swept wings
A new NASA laminar flow design method, CATNLF, has been developed to provide the known NLF performance benefit without historic penalties
CATNLF design method has been developed in three phases:
  Computational study to develop technology
  Wind tunnel test to confirm computations
  Flight test to advance technology
CATNLF flight test effort is underway with first flight scheduled June 2023
Plans to release the flight test data to community and potential wind tunnel test of flight test article
AIAA HRS YP Technical Excellence Lecture

## Slide 40
Contact: Michelle Banchy (Lynde) <michelle.n.lynde@nasa.gov>