## Slide 1: Solving Forward and Inverse Problems for Hyperspectral Satellite Remote Sensors using Principal Component Analysis
Xu Liu
NASA Langley Research Center, Hampton, VA, USA
Wan Wu1, Qiguang Yang2, Xiaozhen Xiong1, Ming Zhao2, Daniel K Zhou1, Allen M Larar1, Robert J D Spurr3, Ping Yang4, Liqiao Lei2, Hyun-Sung Jang5, Yolanda Shea1, Snorre Stamnes1, David R. Thompson6, Xiong Liu7, Lihang Zhou8, Qing Yue6, Feng Xu9, and Larrabee Strow10
(1) NASA Langley Research Center, Hampton, VA, (2) SSAI Inc, Hampton, VA, (3) Rt Solutions Inc., Cambridge, MA, (4)Texas A&M Univ, College Station, TX, (5) NIA, Hampton, VA, (6) JPL/CalTech, Pasadena, CA, (7) Center for Astrophysics | Harvard & Smithsonian, Cambridge, MA, (8) NOAA, (9) University of Oklahoma, Norman, OK, (10) UMBC, College Park, MD
Acknowledgement
NASA Sounder SIPS, NOAA NUCAPS Team, NASA NAS and NCCS, NASA DACC, NASA Science of Terra, Aqua, and Suomi NPP, NAST-I, CPF, TEMPO, and SBG programs

## Slide 2: Introduction
Modern hyperspectral satellite remote sensors provide wealth of information on
  Atmospheric properties such as temperature, water vapor and trace gas vertical profiles
  Cloud and aerosol properties
  Surface properties (temperature, emissivity, reflectivity …)
Fast and accurate forward models are needed to invert hyperspectral data
  Hundreds to thousands of spectral channels with millions of observations each day
  Line-by-line (LBL) radiative transfer model (RTM) is too slow (needs millions of LBL RT calculations to account for atmospheric gas spectral contributions)
  Traditional channel-based forward models are also too slow (at least one RT calculations needed for each channel
Principal Component Analysis (PCA) converts hyperspectral data into super-channels
  Principal Components (PCs) capture the spectral correlations (remove redundant info)
  Super channels capture the information content of the original channel spectrum
  Super-channel number << than the original channel numbers

## Slide 3: Principal Component Based Radiative Transfer Model (PCRTM)
PCRTM was first developed in 2004 specifically for hyperspectral remote sensors
  Number of RT calculations are << number of spectral channels
    Orders of magnitude faster than LBL RTMs
  RT calculations done monochromatically
    Physical-based RTM and accurate relative to LBL RTMs
  Provides analytical Jacobian needed for satellite data inversions
PCRTM is different from other PCA-based RTMs
  PC scores (super-channels) which contain all spectral information
  Reduced inversion dimension for satellite data analysis
  Instrument Line Shape (ILS) functions included in the PCs (eigenvectors)
    No need to calculate high resolution spectra and then convolve with ILS
Multiple scattering clouds and aerosols included
Wide range of spectral coverage
  Thermal: 50-3000 cm-1
  Solar: 200 nm – 2500 nm
  Suitable for AIRS, CrIS, IASI, PREFIRE, IRS, IASI-NG, NAST-I, S-HIS, CLARREO, CPF, SBG, TEMPO, OMI, SCIAMACHY …
Fast:
  Milliseconds to fraction of seconds in IR
  3-4 orders of magnitude faster than LBL in solar
Accurate relative to LBL:
  Thermal: Bias error < 0.002 K RMS error < 0.03 K
  Solar: bias error < 0.001%, RMS error ~0.05%

## Slide 4: PCRTM Calculated Radiance Spectra Agree Well With Satellite Observations
SCIAMACHY
MODIS L2 + CPF simulator @646nm
PCRTM Simulated Reflectance @646 nm using MODIS L2 data
MODIS L1 Observed
Reflectance @646 nm
IASI
CrIS
AIRS

## Slide 5: PCA-based Inversion Algorithms
Iterative Optimal Estimation Inversion:
PCRTM compresses R, Se, and K into smaller dimensions
Applying PCA to X will further reduce the dimension of X, K and Sa
Advantages of using PCA
  reduces the ill-condition of the inversion process
  Speed up the inversion
  Easy to store the retrieved parameters with associated error covariance matrix
Geophysical Parameters | Original Dimension | PC-compressed Dimension
Temperature | 101 | 20
H2O | 101 | 15
CO2 | 101 | 1
O3 | 101 | 10
CO | 101 | 4
CH4 | 101 | 2
N2O | 101 | 2
IR Surface Emissivity | Hundreds -thousands | 8
MW Surface Emissivity | 15-22 | 5
Satellite Sensors | Original Dim | PC-compressed Dim
CrIS | 2211 | 124
AIRS | 2378 | 120
IASI | 8461 | 190
Example of PCs representing H2O vertical profiles
Notes: Flow diagram shown as applied to NAST-I, but has analogous applicability to all sensors.
Bottom QC is for spot checking in spectral domain, if desired; entire loop stays in PC domain (fast).
Super channels = PCs

## Slide 6: Two PCRTM-based Inversion Algorithms
L2 products: Single Field-of-view Sounder Atmospheric Product (SiFSAP)
  3-times higher spatial resolution
  Uses all spectral channel
  All sky algorithm-retrieves cloud explicitly
  Retrieve temperature, clouds, trace gases, and surface properties simultaneously
L3 Products: Climate Fingerprinting Sounder Products (ClimFiSP)
  Works on spatiotemporally averaged radiance spectra
  High quality climate product from multiple satellite data fusion
    Use consistent radiative kernels
    Ensure radiometric closures
Both products will be available at NASA GES DISC for public access
The PCRTM based algorithm can be easily extended to solar spectral region
Example of SiFSAP H2O product
Example of ClimFiSP derived global surface temperature trend

## Slide 7: Summary and Conclusions
PCA can be used to compress both the satellite observed data and the state vector in an inversion process
  Stabilize inversion solution by reduce random noise
  Speed up inversion process by reducing the matrix and vector dimensions
PCRTM is a fast and accurate forward model for analyzing satellite data
  Enable all sky retrievals due to accurate cloud calculations
  Uses all spectral channels instead limited selected channels
  Can be used for pre-launch sensor design and post-launch data analysis
PCRTM-based inversion algorithms provide radiometrically consistent products
  High-spatial resolution L2 products for weather, air quality, and atmospheric dynamic studies
  Consistent long-term climate data records (T, Q, cloud …) from multiple satellite IR hyperspectral sounders