## Slide 1: Validation of Cryogenic Propellant Tank Self-Pressurization
December 08, 2022
C. S. Patel – JSEG, Fluid Dynamics Branch (NASA MSFC-ER42)
H. Q. Yang – JSEG, Fluid Dynamics Branch (NASA MSFC-ER42)
B. R. Williams – Fluid Dynamics Branch (NASA MSFC-ER42)
Notes: This topic will be an overview of validation of propellant tank self-pressurization via CFD simulation and reduced order modeling.
The work was performed by my colleague Dr. Yang on behalf of the Fluid Dynamics Branch at the NASA Marshall Space Flight Center.

## Slide 2: Background
  NASA’s current and near-future missions and important of advancements in cryogenic fluid management (CFM), including safe and reliable long-term propellant storage
  NASA Space Technology Mission Directorate (STMD) has established CFM portfolio to improve CFM technologies for upcoming missions
    Fluid Dynamics Branch (ER42) within the Propulsion Systems Department at the Marshall Space Flight Center is tasked with testing and improving our computation tools for design and analysis of CFM systems
  ER42 supports multiple programs in need of in-space CFM analysis
    Space Launch System (SLS) upper stages
    Commercial Lunar Payload Services (CLPS)
    Human Landing System (HLS)
    Nuclear Thermal Propulsion (NTP) systems
  Self-pressurization of propellant tank over long time due to heat leakage in one of the challenging CFM problem

## Slide 3: Problem and Solution
  Nodal tool find it extremely difficult to accurately model self-pressurization because they lack essential dynamics of the problem
  Necessary to employ 3-D Computational Fluid Dynamics (CFD)
  CFD tool requirements: efficient, computationally scalable, modular with ability to incorporate various physics models, and robust enough to not accumulate conservation errors over several hours of simulated time
    Loci-Stream CFD tool along with the VOF module is a great candidate
  Validate Loci-Stream for predicting self-pressurization of a flight scale propellant tank so it can serve as a reliable design and analysis tool for NASA’s CFM application needs
    Liquid hydrogen tank pressurization tests carried out at the K-site testing facility provides a reliable data-set for this purpose
  Demonstrate accurate predictive capabilities of Loci-Stream-VOF and lumped gas liquid CFD model
Notes: Until recently, these long term (order of hours or days) CFD simulations have been too impractical to conduct due to prohibitive wall time and computational resource requirements.

## Slide 4: Experimental Setup
  Multiple tank self-pressurization tests were performed at the NASA Glenn Research Center K-site facility
  An insulated ellipsoidal tank was filled with liquid hydrogen (LH2) and allowed to pressurize through controlled heating
  Liquid fill level and heat flux sensitivities were studied
  Ullage pressure and axially varying temperatures in both fluid phases were the primary metrics used to quantify the self-pressurization process
Tank Configuration Schematic
(Temperature Sensor Locations Shown)
Reference:
Hasan M, Lin C, Dresar NV. Self-pressurization of a flightweight liquid hydrogen storage tank subjected to low heat flux. NASA TM 103804; 1991.

## Slide 5: Computational Model
  Loci-Stream
    Loci framework – flexible and scalable
    Pressure based solver for all speed flows for generalized meshes
    Laminar, RANS turbulence and DDES turbulence model equation options are available
  VOF Module
    Implements Volume of Fluid (VOF) method by solving additional VOF transport equation for two-phase flows
    Interface reconstruction to avoid smoothing of the sharp interface using PLIC (Piecewise Linear Interface Construction) method
  Loci-Stream-VOF
    Solves a single set of governing equations for two phases
    Boussinesq hypothesis for liquid
    Variable time step size is determined for each time step, by user defined maximum CFL condition
  Phase Change Mass Transfer Model
    Kinetic model by Hertz-Knudsen-Schrage (HKS)
    Antoine equation for saturation pressure
  Material Properties from NIST database
VOF Transport Equation
Conservation Equations
HKS Model
Antoine Equation
  Φ is Heat dissipation through shear stress
Notes: The Loci system uses a rule-based approach to automatically assemble the numerical simulation components into a working solver. This technique enhances the flexibility of simulation tools, reducing the complexity of CFD software induced by various boundary conditions, complex geometries, and different physical models. Loci plays a central role in building flexible goal-adaptive algorithms that can quickly match numerical techniques with various physical modeling requirements.
the geometrical reconstruction and backward projection of the VOF formulation are purely based on the assumption of conservation of liquid volume. In order to conserve total liquid mass, one must assume the liquid density to be constant. Thus, a physics-accurate internal energy formulation cannot be easily implemented alongside the VOF formulation. This problem is solved by representing the total energy conservation in a different thermodynamic state variable, enthalpy.
Boussinesq hypothesis - liquid is incompressible except for the buoyancy term in the momentum equation where density is a linear function of temperature

## Slide 6: Lumped Gas Liquid CFD Model
Solve self-pressurization problem more efficiently by observing
  Ullage is always near equilibrium due to low heat fluxes, and closed system
  Gas-liquid interface is always quiescent
  Interfacial thermal stratification in liquid dominates the problem dynamics
Advantages:
  Preclude any movement of the gas-liquid interface observed in the VOF method and alleviate restrictive time step requirements of VOF module
  Greater numerical stability at higher time-steps
  Increase spatial resolution with minimal impact to simulation wall time
Implementation:
  CFD-ACE+ solver for proof of concept
  A more general sharp interface model is implemented and being tested in Loci-Stream
Methodology
  Gas phase CFD is decoupled and simulated separately to obtain lumped gas reduced order model (ROM)
  Ullage dynamics are then coupled with time-accurate liquid CFD via gas-liquid interface boundary condition via the gas ROM
Illustration of Lumped Gas Liquid CFD Model
qin
(from reduced order model)
Liquid Phase
(initial temperature from test measurements)
Gas Phase
Notes:   This work was used to demonstrate the critical physics for tank self-pressurization and numerical methodologies that may be used to best resolve those physics.
  The findings informed development and operation of production level CFD tools used in the Fluid Dynamics Branch at NASA Marshall Space Flight Center.
    Development of a sharp interface model in the branch’s production level CFD tools where both fluid phases are distinctly and explicitly represented in CFD is underway.
the robustness and speed of the approach can enable rapid assessment of inline production work.

## Slide 7: Lumped Gas ROM – Methodology
  Derive boundary heat flux boundary condition for the liquid CFD
  Energy balance at the gas-liquid interface
  Gas phase internal energy conservation
  Obtain boundary condition for the heat flux into the liquid phase by combining the above equations
  Phase change mass transfer rate
  Invoke gas ROM assumptions
  Decompose gas temperature into sum of interface temperature and difference between interface and gas temperature. The latter, is then described as only a function of time and not ullage spatial coordinates

## Slide 8: Results – Gas ROM CFD
  Temperature fields for the 49% fill level simulations are shown
  Formation of natural convection cells and thermal stratification on the liquid side of the gas-liquid interface are important dynamics of the problem
    A successful model must capture both accurately in order to predict pressurization
Vapor Phase Analysis
(Final State Shown)
Liquid Phase Analysis
(Transients Shown)
Heat Flux : 3.5 W/m2
Heat Flux: 2.0 W/m2

## Slide 9: Results – Pressurization
  Four K-site LH2 self-pressurization experiments
  Simulated using both VOF and lumped gas ROM CFD
  Both VOF and gas ROM method capture pressurization well demonstrating successful validation
  Initial transients were also captured well by both methods although there is a slight overshoot in VOF method due to small interfacial instabilities encountered in VOF method
    Lumped gas method decouples gas and liquid CFD and is therefore more robust and captures the initial transience better

## Slide 10: Results – Temperature Probes
  Temperature trend and profile are shown for 49% fill case with 3.5 W/m2 heat load
  Again, both VOF and gas ROM method capture both temporal and spatial trends very well
  The agreement with experimental data for both VOF and lumped gas models emphasizes how well (i) the flow field is resolved, and (ii) energy conservation is maintained.
    Both must be simultaneously achieved for an accurate solution.
  The turbulent flow model fails at capturing the temperature trends in the ullage, which is discussed later.

## Slide 11: Results – Sensitivity to Mesh Resolution
  Initial (coarse) mesh resolution: equivalent to 4 million cells for the full 3-D model, a typical size used for propellant slosh applications
  Mesh independence was ensured by simulating three mesh resolutions
  The coarsest mesh produces acceptable qualitative predictions, but the pressurization rate is under-predicted
  The baseline mesh improves the prediction by better capturing the thermal stratification in the liquid phase, which is one of the two most important dynamics of this problem
  The finest mesh produces the best match with the experiment by further improving the accuracy of the interfacial liquid thermal layer resolution
  Note, further refinement may marginally improve pressurization with VOF model but is prohibitively costly in terms of wall time requirements
    Refinement with the gas ROM model was possible due to stability at higher time steps and slightly improves the predction
Coarse Mesh
Baseline Mesh
Refined Mesh
Notes: the prohibitively high cost of such CFD simulations is not justified by small improvements in predictive capability.

## Slide 12: Results – Effect of Flow Regime
  Laminar model performs well
  The 𝑘 − 𝜔 SST RANS model under-pressurizes
    Reason: high turbulent viscosity in the interfacial region
    The resulting high momentum and thermal diffusivity smears out the liquid side thermal stratification
  The liquid side interfacial temperatures plays a very important role in the dynamics of the problem
    Decides saturation pressure and the mass transfer rate in the phase change model  dictates the pressurization rate
  The root cause of the 𝑘 − 𝜔 SST model’s failure
    Developed for single phase applications
    Employing the same model simultaneously for liquid and gas phases with a continuous turbulent kinetic energy and turbulent dissipation field is not accurate description of the underlying physics encountered at a gas-liquid interface
  A more sophisticated RANS turbulence model is necessary for two phase VOF class of applications and is being investigated
  The 𝑘 − 𝜔 DDES (hybrid RANS-LES) model is less diffusive than the RANS model but still inferior to the laminar model in predictive capacity
Notes:   Models for both laminar and turbulent flow regimes were tested and compared
  The observation of high momentum and thermal diffusivity produced by the RANS model is further reinforce by examining the effect of mesh resolution on the turbulent flow simulations
  Coarse meshes are numerically diffusive and artificially increases the viscosity, but mesh refinement reduces this effect.
    No change in pressurization rate with the refined mesh - in contrast with the laminar flow regime behavior - demonstrating the high diffusivity generated by the turbulence model.
  The root cause of the 𝑘 − 𝜔 SST model’s failure to capture the thermal stratification in the gas-liquid interface region lie in the origin of the turbulence modeling

## Slide 13: Results – Sensitivity to Accommodation Factor
  HKS model for phase change mass transfer has an accommodation factor (AF or Cm) that drives the evaporation/condensation rates
    But does not have an empirically-derived value
    In fact, did not find a definitive AF value for LH2 at the given operating condition
    Necessary to demonstrate the impact of AF on the validation
  HKS equation suggests that higher AF causes higher mass transfer rate, but it does not linearly impact the observed phase change rate in a closed system which is near equilibrium, because higher ullage mass increases the ullage pressure, which suppresses the mass transfer rate
    The pressurization rate is expected to be insensitive to AF in a reasonably large range and converge logarithmically as the value approaches unity
  From experience, AF = 1e-5 produced insufficient pressurization
  Assessed the model sensitivity in range [1e-4, 1e-2]
    Difficult to simulate1e-2 due to extremely low time-step required for numerical stability
    Found the difference between AF of 1e-3 and 1e-4 to be reasonably insignificant
  Conclusion: AF above a minimum threshold of 1e-4 does not yield any significant change in self-pressurization rates for a closed quiescent system
  Note that lumped gas ROM CFD does not require AF
HKS Equation
Antoine Equation

## Slide 14: Contributions
  Quantification of self-pressurization of propellant tanks has direct application to long-term safe storage of cryogenic propellants, a need for many current and future programs
  Validated Loci-Stream-VOF and the lumped gas ROM CFD model against the K-site LH2 tank self-pressurization experiments
  Demonstrated that for all four K-site experiments, both methods have accurate predictive ability for ullage pressure and liquid as well as gas phase temperature probes.
  Showed that while both methods are accurate, lumped gas method has some advantages
    Precluding any movement of the gas-liquid interface alleviates small interface stabilities seen in VOF method
    Consequently, an order of magnitude (or more) speed up without degradation of the solution for an equivalent mesh, and simulations with more refined meshes are economical
  Developing a more general segregated gas/liquid domain approach to augment Loci-Stream-VOF capabilities
  In the current state, Loci-Stream with VOF module, and the lumped gas model are both well equipped to simulate fluid and thermal dynamics of cryogenic tank self-pressurization to support NASA’s future missions, and validation under in-space (microgravity) conditions is underway