## Slide 1
A Modeling and Simulation Study for the GeoXO Atmospheric Composition Instrument (ACX):
System Level SO2 and O3 Retrieval Performance as a Function of SNR
Monica Cook1, Francis Padula1, Aaron Pearlman1, Boryana Efremova1, Joel McCorkel2, Joanna Joiner2
1GeoThinkTank LLC
2NASA Goddard Space Flight Center
AMS 103rd Annual Meeting
8 – 12 January 2023
Denver, Colorado

## Slide 2
NOAAs Geostationary and Extended Observations (GeoXO) ACX Introduction
ACX: observations of air pollutants to improve air quality monitoring and mitigate health impacts from severe pollution and smoke events
Planned ACX Instrument | 
Spectral Resolution | 0.6 nm
Spectral Sampling | 0.2 nm
Spectral Range | 300 – 500 nm; 540 – 740 nm
Temporal Revisit | 60 min
Spatial Resolution | 25 km2 at nadir
https://www.nesdis.noaa.gov/next-generation/geostationary-extended-observations-geoxo
Atmospheric Composition Spectral Regions of Interest
Enhance NOAA’s current capabilities to monitor hourly variation in pollutants
Enhance NOAA’s air quality forecasting capabilities (pollution alerts, regulatory guidance, reduced health impacts)

## Slide 3
Urban
Vegetation
Water
Surface Reflectance
2 km
10 km
ACX Performance Assessment
Stratospheric +
Composition
Tropospheric
Composition
Boundary Layer
Composition
NO2
O3
SO2
[reference]
Objective:
Assess instrument performance considerations through end-to-end physics based imaging system & scene modeling & simulation to inform decision making.
Investigate the impacts of simulated ACX SNR specification on trace gas retrieval performance
Previously studied NO2 (420 – 450 nm) [EUMETSAT 2021]
This study investigates SO2 and O3 retrievals (approx. 300 – 350 nm)
100 km
ACX
High Concentration
Low Concentration
Translate instrument specifications to science performance metrics

## Slide 4: Utility of the Instrument Performance Assessment Simulations
End-To-End Image Chain
ACX Quantitative Analysis to Inform Decision Makers
Scene Phenomenology
Instrument Model
Simulated At Sensor Radiance
Simulated L2 Products
Technical Trade
Objective:
Assess instrument performance considerations through end-to-end physics based imaging system & scene modeling & simulation
Framework designed to rapidly facilitate various quantitative instrument performance assessment trade studies against engineering and science applications

## Slide 5: Modeling & Simulation Framework
RTM
Instrument Model
Retrieval Algorithm
Analysis
At Sensor Radiance
Known Column Amounts
Distribution of
At Sensor
Radiance + Noise
Error
(Retrieval – Truth)
Retrieved
Slant Column Amount
O3 SO2
Results
Inputs/Outputs
Plots illustrating simulated instrument retrieval performance as a function of SNR
MODTRAN 6
Atmospheric Scene of Interest

## Slide 6: Modeling & Simulation Framework
RTM
Instrument Model
Retrieval Algorithm
Analysis
At Sensor Radiance
Known Column Amounts
Distribution of
At Sensor
Radiance + Noise
Error
(Retrieval – Truth)
Retrieved
Slant Column Amount
O3 SO2
Results
Inputs/Outputs
Plots illustrating simulated instrument retrieval performance as a function of SNR
MODTRAN 6
Atmospheric Scene of Interest

## Slide 7
ACX SNR Performance Assessment – Scene Scenarios
Accounts for the variability of concentration amount for a given standard atmosphere under typical surface and aerosol conditions with varying view geometry and solar conditions from GEO-central orbital location (105°W)
MODTRAN default aerosol
MODTRAN standard atmosphere
constituent height in profile
typical surface reflectance
trace gas constituent
location
time of year
column amount
rural: spring/summer
Norman, OK
(near nadir)
Seattle, WA
(off nadir)
June 20 @ 1pm
March 20 @ 5pm
6%
4%
8%
boundary layer
tropospheric
low
high
medium
US Standard
72 scene simulations were generated for each trace gas to span the bounding cases of observation conditions
O3
SO2
March 20 @ 1pm
March 20 @ 4pm
7
RTM
Atmospheric Scene of Interest

## Slide 8: Modeling & Simulation Framework
RTM
Instrument Model
Retrieval Algorithm
Analysis
At Sensor Radiance
Known Column Amounts
Distribution of
At Sensor
Radiance + Noise
Error
(Retrieval – Truth)
Retrieved
Slant Column Amount
O3 SO2
Results
Inputs/Outputs
Plots illustrating simulated instrument retrieval performance as a function of SNR
MODTRAN 6
Atmospheric Scene of Interest

## Slide 9
The ACX instrument model consists of the following steps:
The MODTRAN output spectra are convolved with a gaussian simulating the instrument spectral response function, resulting in a 0.6 nm spectral resolution
The degraded resolution spectrum is resampled to the expected instrument sampling of 0.2 nm/pix
Noise is added to achieve varying SNR as described below
ACX Noise Simulation
Input Spectrum
0.6 nm resolution
Resampled to 0.2 nm
Noise Added
Average of 100 noise
added samples
Instrument Model

## Slide 10
Realistic baseline instrument parameters are used for setting up the tool
  Follows current GeoXO ACX Performance Operational Requirement Document (PORD) specifications
  Special thanks to Xiong Lu and Kelly Chance for assistance in this process
Can be updated as the ACX instrument evolves
ACX Instrument Response Model
Instrument Parameters | 
 | spectral radiance at instrument resolution
 | detector area
≈𝜋/(2f#)2 | solid angle of acceptance of instrument
 | integration time
 | wavelength
 | spectral interval per pixel
 | optical system transmittance, combined with grating efficiency
 | detector quantum efficiency
 | Bit depth
 | Read-out noise
 | Dark current
Instrument Parameters | 
 | spectral radiance at instrument resolution
 | detector area
 | solid angle of acceptance of instrument
 | integration time
 | wavelength
 | spectral interval per pixel
 | optical system transmittance, combined with grating efficiency
 | detector quantum efficiency
 | Bit depth
 | Read-out noise
 | Dark current
Instrument Model

## Slide 11
ACX SNR Simulations – 10 Levels Assessed
For each spectrum, 1000 implementations for 10 different SNR levels are generated
  Each increasing SNR level decreases the noise by factors of 1 through 10, corresponding to averaging 1 - 100 samples
  1000 random normally distributed noise implementations are generated for each SNR level
Note that the SNR values are calculated using nominal radiance defined in PORD
ACX Wavelength Range
SO2 Retrieval Range
O3 Retrieval Range
305 – 330 nm
331.1 – 336.1 nm
300 – 740 nm
Instrument Model

## Slide 12: Modeling & Simulation Framework
RTM
Instrument Model
Retrieval Algorithm
Analysis
At Sensor Radiance
Known Column Amounts
Distribution of
At Sensor
Radiance + Noise
Error
(Retrieval – Truth)
Retrieved
Slant Column Amount
O3 SO2
Results
Inputs/Outputs
Plots illustrating simulated instrument retrieval performance as a function of SNR
MODTRAN 6
Atmospheric Scene of Interest

## Slide 13
Simulated ACX Retrieval Algorithms and Analysis
Physical retrieval of concentration amount derived via comparison to a “Truth” LUT
Predicted at sensor radiance distribution as a function of SNR of known atmospheric concentrations
Concentration Amount: Low, Medium, High
Constrained Atmospheric Cases at a given SNR level
Fixed at a single view geometry
Truth LUT
Concentration Amount: none through extreme amount in finite step sizes
NO Noise Included
Fixed at a single view geometry
Compute retrieval concentration amount error (retrieval – truth):
Computation: determine error as the standard deviation of (retrieval – truth) for each SNR
Output: Illustrates the simulated instrument retrieval performance as a function of SNR and physical parameters of the scene simulated
Searched for Best Match
Retrieval Algorithm
Analysis

## Slide 14
Step 1 – Build Look Up Table (LUT)
Result: Observed reflectance for a realistic range of known constituent amounts
RTM
Solar Model
Reflectance Spectra
…
Scene Inputs
Aerosol
Surface Type
Time of Day
Location
Atm. Profiles
(Known Total Column Amount, )
Radiance
NO2, No Noise
Reflectance
NO2, No Noise
Step 2 – Calculate mean and inverse covariance matrix of spectra from noise model
Result: m and S-1
1000 implementations
10 SNR Levels
Radiance
HIGH NO2, SNR 01
Radiance
HIGH NO2, SNR 01
Radiance
HIGH NO2, SNR 1270
Radiance
HIGH NO2, SNR 01
Radiance
HIGH NO2, SNR 01
Radiance
HIGH NO2, SNR 3820
Radiance
HIGH NO2, SNR 01
Radiance
HIGH NO2, SNR 01
Radiance
HIGH NO2, SNR 1530
LOW
MED
HIGH
Retrieval Algorithm: Constrained Energy Minimization
Solar Model
Retrieval Algorithm

## Slide 15
t
10 SNR Levels
Radiance
HIGH NO2, SNR 01
Radiance
HIGH NO2, SNR 01
Radiance
HIGH NO2, SNR 1100
Radiance
HIGH NO2, SNR 01
Radiance
HIGH NO2, SNR 01
Radiance
HIGH NO2, SNR 4500
Radiance
HIGH NO2, SNR 01
Radiance
HIGH NO2, SNR 01
Radiance
HIGH NO2, SNR 1400
CEM(x)
Calculate CEM value for every spectra, t, in LUT
Reflectance
HIGH NO2, SNR 1800
x = observed spectra
For each spectra…
0.24
…
--0.5
…
0.74
…
…
1.001
…
0.664
CEM Values
Search LUT for CEM Value closest to 1
0.000360
from that LUT entry is retrieved value
Step 4 – For each SNR level, calculate bias and standard deviation (predicted error) from 1000 implementations
Result: Expected error for this SNR
Bias and standard deviation of 1000 implementations gives retrieval error
Repeat for each SNR level to plot as a function of SNR
Repeat with a new scene to plot as a function of constituent amount
Retrieval Algorithm: Constrained Energy Minimization
Step 3 – For each spectra, x … use constrained energy minimization (CEM) to determine slant column amount
Result: Retrieved amount for each observed spectra
Solar Model
Reflectance = Radiance
END RESULT
Retrieval Algorithm
Analysis

## Slide 16: Baseline Retrieval and Analysis Framework For This Effort
RTM
Instrument Noise Model
Retrieval Algorithm
Analysis
Solar Model
Scene Inputs
Aerosol
Surface Type
Time of Day
Location
Atm. Profiles
(Known Total Column Amount)
Radiance
HIGH NO2, No Noise
Instrument Inputs
Detector Specs
Optical System Transmittance
Detector Quantum Efficiency
Bit-Depth
Read-out Noise
Dark Current
1000 implementations
10 SNR Levels
Radiance
HIGH NO2, SNR 01
Radiance
HIGH NO2, SNR 01
Radiance
HIGH NO2, SNR 1270
Radiance
HIGH NO2, SNR 01
Radiance
HIGH NO2, SNR 01
Radiance
HIGH NO2, SNR 3820
Radiance
HIGH NO2, SNR 01
Radiance
HIGH NO2, SNR 01
Radiance
HIGH NO2, SNR 1530
Predicted Slant Column Amount for each spectra output from instrument noise model
10 SNR levels
1000 implementations per SNR level
Constrained Energy Minimization (CEM) compares each observed spectra to a LUT with known constituent amounts
Calculate bias and standard deviation of 1000 implementations to determine retrieval error
Repeat for each SNR level
Repeat for each constituent amount
CEM(x)
Note: Analysis based on a DOAS-like approach; results may vary with other operational approaches

## Slide 17: Modeling & Simulation Framework
RTM
Instrument Model
Retrieval Algorithm
Analysis
At Sensor Radiance
Known Column Amounts
Distribution of
At Sensor
Radiance + Noise
Error
(Retrieval – Truth)
Retrieved
Slant Column Amount
O3 SO2
Results
Inputs/Outputs
Plots illustrating simulated instrument retrieval performance as a function of SNR
MODTRAN 6
Atmospheric Scene of Interest

## Slide 18
Surface
5 km
10 km
100 km
Surface
10 km
100 km
ACX SO2 Modeling Scenarios
 |  | Norman, OK (near-nadir) | Seattle, WA (oblique)
 | SO2 Injected* | Slant Column Amount (SCA) | 
Low | 0.2 DU | 0.27 DU | 0.37 DU
Medium | 0.5 DU | 0.68 DU | 0.94 DU
High | 2.0 DU | 2.68 DU | 3.70 DU
Boundary Layer Case
Two modeling scenarios:
  Boundary layer case: SO2 injected into the atmosphere from 0 – 3 km (anthropogenic pollution)
    Three amounts of SO2 (Low, Medium and High)
  5 km tropospheric plume: SO2 injected into 1 km of the atmosphere at 5 km altitude (outgassing volcano)
    Three amounts of SO2 (Low, Medium and High)
Different viewing geometries result in different slant column amounts for the same amount of SO2 injected
* SO2 was injected to US standard atmospheric profile
Oblique viewing results in larger SCAs than near-nadir viewing
5 km
5km Tropospheric Plume

## Slide 19
ACX Simulated Boundary Layer Case vs Tropospheric Plume
approximate PORD value
approximate PORD value
approximate PORD value
Each data point and error bars: (mean ± 1 σ) of 1000 simulations
Norman, OK: June 20, 2021 @ 1 pm (closer to nadir viewing)
Retrieval results improve for greater amounts of SO2 in profile
Retrieval performance with a tropospheric plume outperforms retrieval performance for the boundary layer case
SCA = 0.27 DU
SCA = 0.68 DU
SCA = 2.68 DU

## Slide 20
ACX Simulated Boundary Layer Case vs Tropospheric Plume
Each data point and error bars: (mean ± 1 σ) of 1000 simulations
Norman, OK: June 20, 2021 @ 1 pm (closer to nadir viewing)
Retrieval results improve for greater amounts of SO2 in profile
Retrieval performance with a tropospheric plume outperforms retrieval performance for the boundary layer case
Results as a percentage of slant column amount show that boundary layer cases have extremely high error
note difference in axes
Similar results were found for the Seattle, WA: March 20, 2021 @ 1pm (backup slides)
SCA = 0.27 DU
SCA = 0.68 DU
SCA = 2.68 DU
approximate PORD value
approximate PORD value
approximate PORD value

## Slide 21
ACX Simulated View Geometries and Solar Zenith Angle
Each data point and error bars: (mean ± 1 σ) of 1000 simulations
All location, date and time combinations with SO2 added to the boundary layer
Retrieval results improve for greater amounts of SO2 in profile
Retrievals errors decrease as solar zenith angle decreases in most cases
approximate PORD value
approximate PORD value
approximate PORD value
note difference in axes
Boundary Layer Case
Location | Date | Local Time | SZA
Norman, OK | June 20 | 1 pm | 13.63°
Norman, OK | March 20 | 5 pm | 58.72°
Seattle, WA | March 20 | 1 pm | 47.55°
Seattle, WA | March 20 | 4 pm | 59.12°

## Slide 22
ACX Simulated View Geometries and Solar Zenith Angle
Each data point and error bars: (mean ± 1 σ) of 1000 simulations
All location, date and time combinations with SO2 added @ 5km altitude
Retrieval results improve for greater amounts of SO2 in profile
Retrievals errors decrease as solar zenith angle decreases in most cases
5 km Tropospheric Plume
note difference in axes
Location | Date | Local Time | SZA
Norman, OK | June 20 | 1 pm | 13.63°
Norman, OK | March 20 | 5 pm | 58.72°
Seattle, WA | March 20 | 1 pm | 47.55°
Seattle, WA | March 20 | 4 pm | 59.12°
approximate PORD value
approximate PORD value
approximate PORD value

## Slide 23
ACX Simulated View Geometries and Solar Zenith Angle
Each data point and error bars: (mean ± 1 σ) of 1000 simulations
See variation in retrieval performance with changes in solar zenith angle
Same location and SCA but different date and time – different results
Different locations and SCA with similar SZA – similar results
This illustrates the SZA impact on simulated retrieval performance
approximate PORD value
13.63° vs 58.72° SZA
58.72° vs 59.12 ° SZA
approximate PORD value
Location | Date | Local Time | SZA
Norman, OK | June 20 | 1 pm | 13.63°
Norman, OK | March 20 | 5 pm | 58.72°
Seattle, WA | March 20 | 1 pm | 47.55°
Seattle, WA | March 20 | 4 pm | 59.12°

## Slide 24
Surface
5 km
10 km
100 km
Surface
10 km
100 km
ACX O3 Modeling Scenarios
 |  | Norman, OK (near-nadir) | Seattle, WA (oblique)
 | O3 Injected* | Slant Column Amount (SCA) | 
Low | 50 DU | 476 DU | 653 DU
Medium | 60 DU | 489 DU | 671 DU
High | 70 DU | 503 DU | 690 DU
Boundary Layer Case
Two modeling scenarios:
  Boundary layer case: O3 injected into the atmosphere from 0 – 3 km (smog)
    Three amounts of O3 (Low, Medium and High)
  5 km tropospheric plume: O3 injected into 2 km of the atmosphere at 5 km altitude (photochemical reactions)
    Three amounts of O3 (Low, Medium and High)
Different viewing geometries result in different slant column amounts for the same amount of O3 injected
* O3 was injected to US standard atmospheric profile
Oblique viewing results in larger SCAs than near-nadir viewing
5 km
5km Tropospheric Plume
Note: There are multiple O3 operational retrieval algorithms; this study utilizes a DOAS-like approach

## Slide 25
approximate PORD value
approximate PORD value
approximate PORD value
ACX Simulated Boundary Layer Case vs Tropospheric Plume
Each data point and error bars: (mean ± 1 σ) of 1000 simulations
At near-nadir viewing and small SZA, retrieval performance is comparable for O3 injected into the boundary layer and at 5 km in the troposphere
Norman, OK: June 20, 2021 @ 1pm (near-nadir viewing, SZA = 13.63°)
SCA = 476 DU
SCA = 489 DU
SCA = 503 DU

## Slide 26
ACX Simulated Boundary Layer Case vs Tropospheric Plume
Each data point and error bars: (mean ± 1 σ) of 1000 simulations
At near-nadir viewing and small SZA, retrieval performance is comparable for O3 injected into the boundary layer and at 5 km in the troposphere
Norman, OK: June 20, 2021 @ 1pm (near-nadir viewing, SZA = 13.63°)
Note that retrieval bias as a percentage is small because O3 slant column amounts are large due to an increased amount of O3 in the stratosphere
approximate PORD value
approximate PORD value
approximate PORD value
SCA = 476 DU
SCA = 489 DU
SCA = 503 DU

## Slide 27
ACX Simulated Boundary Layer Case vs Tropospheric Plume
Each data point and error bars: (mean ± 1 σ) of 1000 simulations
At near-nadir viewing and small SZA, retrieval performance is comparable for O3 injected into the boundary layer and at 5 km in the troposphere
At oblique viewing and larger SZA, retrieval performance is better for O3 injected at 5 km in the troposphere compared to O3 injected in the boundary layer
Seattle, WA: March 20, 2021 @ 1pm (oblique viewing, SZA = 47.55°)
Note that retrieval bias as a percentage is small because O3 slant column amounts are large due to an increased amount of O3 in the stratosphere
approximate PORD value
approximate PORD value
approximate PORD value
SCA = 653 DU
SCA = 670 DU
SCA = 690 DU

## Slide 28
ACX Simulated View Geometries and Solar Zenith Angle
Each data point and error bars: (mean ± 1 σ) of 1000 simulations
All location, date and time combinations with O3 added to the boundary layer
Retrieval performance is comparable for all view geometries and solar zenith angles simulated when O3 is injected into the boundary layer, with the exception of near-nadir viewing on the summer solstice near solar noon (improved retrieval performance)
Boundary Layer Case
approximate PORD value
approximate PORD value
approximate PORD value
Location | Date | Local Time | SZA
Norman, OK | June 20 | 1 pm | 13.63°
Norman, OK | March 20 | 5 pm | 58.72°
Seattle, WA | March 20 | 1 pm | 47.55°
Seattle, WA | March 20 | 4 pm | 59.12°

## Slide 29
ACX Simulated View Geometries and Solar Zenith Angle
Each data point and error bars: (mean ± 1 σ) of 1000 simulations
All location, date and time combinations with O3 added @ 5 km altitude
Retrieval performance is comparable for all view geometries and solar zenith angles simulated with O3 injected at 5 km in the troposphere
5 km Tropospheric Plume
approximate PORD value
approximate PORD value
approximate PORD value
Location | Date | Local Time | SZA
Norman, OK | June 20 | 1 pm | 13.63°
Norman, OK | March 20 | 5 pm | 58.72°
Seattle, WA | March 20 | 1 pm | 47.55°
Seattle, WA | March 20 | 4 pm | 59.12°

## Slide 30
Summary and Conclusions
An end-to-end physics based imaging system and scene modeling & simulation capability has been further developed in support of the GeoXO program to conduct quantitative instrument performance assessments and trade studies of the ACX system
This work investigated the impacts of simulated ACX SNR specifications on trace gas retrieval performance:
Previously studied NO2 (420 – 450 nm) [EUMETSAT 2021]
This study investigated SO2 and O3 retrievals (approx. 300 – 350 nm)
Simulated ACX SO2 Retrievals Summary
Retrieval uncertainty decreased as the slant column amount of SO2 increased
Retrieval performance for a tropospheric plume outperforms retrieval performance for the boundary layer case
Retrievals errors decrease as solar zenith angle decreases in most cases
Simulated ACX O3 Retrievals Summary
Retrieval performance is better for O3 injected at 5 km in the troposphere compared to O3 injected in the boundary layer
  Exception is near-nadir viewing on the summer solstice near solar noon
Retrieval performance is comparable for most view geometries and solar zenith angles simulated
  Exception is boundary layer O3 injection with near-nadir viewing on the summer solstice near solar noon (improved retrieval performance)
Conclusions:
Retrieval of SO2 and low amounts of O3 in the boundary layer were found to be challenging regardless of SNR
Retrieval errors did not vary greatly with changes in SNR (up to 50%) for O3 and large amounts of SO2 at higher altitudes in the troposphere; performance for these scenarios was acceptable within this range of SNR values
Retrieval performance for O3 and larger amounts of SO2 at higher altitudes in the troposphere were shown to be sufficient with most SNRs modelled
Path Forward
Investigating variability in retrieval performance for different times throughout the day

## Slide 31
Backup

## Slide 32
Boundary Layer Case vs Tropospheric Plume
Each data point and error bars: (mean ± 1 σ) of 1000 simulations
Seattle, WA: March 20, 2021 @ 1 pm (off-nadir viewing)
Retrieval results improve for greater amounts of SO2 in profile
Retrieval performance with a tropospheric plume outperforms retrieval performance for the boundary layer case
approximate PORD value
approximate PORD value
approximate PORD value
SCA = 0.37 DU
SCA = 0.94 DU
SCA = 3.70 DU

## Slide 33
Boundary Layer Case vs Tropospheric Plume
Each data point and error bars: (mean ± 1 σ) of 1000 simulations
Seattle, WA: March 20, 2021 @ 1 pm (off-nadir viewing)
Retrieval results improve for greater amounts of SO2 in profile
Retrieval performance with a tropospheric plume outperforms retrieval performance for the boundary layer case
Results as a percentage of slant column amount show that boundary layer cases have extremely high error
approximate PORD value
approximate PORD value
approximate PORD value
SCA = 0.37 DU
SCA = 0.94 DU
SCA = 3.70 DU
note difference in axes

## Slide 34
approximate PORD value
approximate PORD value
approximate PORD value
Boundary Layer Case vs Tropospheric Plume
Each data point and error bars: (mean ± 1 σ) of 1000 simulations
At near nadir viewing and small SZA, retrieval performance is comparable for O3 injected into the boundary layer and at 5 km in the troposphere
Norman, OK: June 20, 2021 @ 1pm (closer to nadir viewing, SZA = 13.63°)
SCA = 476 DU
SCA = 489 DU
SCA = 503 DU

## Slide 35
Boundary Layer Case vs Tropospheric Plume
Each data point and error bars: (mean ± 1 σ) of 1000 simulations
At near nadir viewing and small SZA, retrieval performance is comparable for O3 injected into the boundary layer and at 5 km in the troposphere
At off-nadir viewing and larger SZA, retrieval performance is better for O3 injected at 5 km in the troposphere compared to O3 injected in the boundary layer
Seattle, WA: March 20, 2021 @ 1pm (off-nadir viewing, SZA = 47.55°)
approximate PORD value
approximate PORD value
approximate PORD value
SCA = 653 DU
SCA = 670 DU
SCA = 690 DU