## Slide 1
POC: Paul.Wercinski@nasa.gov. 650-776-9984
Adaptable, Deployable, Entry and Placement Technology (ADEPT) Enabling Future Science Missions
January 2023
Paul Wercinski and the ADEPT Team
NASA Ames Research Center

## Slide 2: Adaptable, Deployable Entry and Placement Technology (ADEPT)
ADEPT’s Major Benefits:
Overcomes entry vehicle packaging and volume constraints in LV shroud or as secondary payload
Deployed configuration achieves low ballistic coefficient (M/CdA), reducing peak heating and dynamic pressure loads;
Woven carbon fabric, tested up to 250 W/cm2, is suitable for extreme heating conditions including Venus science missions
3D Woven Carbon Fabric
Aft Surface
Front Surface
Struts
Ribs
Rigid Nose
Main Body
 | SmallSat Class (1-3m Diameter) (Tech Demo or Secondary Payload) | Robotic Class (4-12m Diameter) (Discovery, New Frontier, Flagship) |  | Exploration Class (Human Mars)
Ballistic and Lifting Entry Vehicle Concepts |  |  |  | 
SR-1
(2018 Flight Test)
ADEPT VITaL
(Venus Lander)
ADEPT Designs
Project Pterodactyl
Ice Giant DMA Concept
Human Exploration 20mt Concept
1-3m Diameter 6m Dia. 12m Dia. 18m Dia.
“Umbrella-like” mechanical deployment
POC: Paul.Wercinski@nasa.gov. 650-776-9984
ADEPT stowed in ESPA as secondary payload

## Slide 3
TRL
ADEPT Technology Maturation FY12-FY19
Component
Subsystems
Integrated Systems
2012 | … | 2019...
Fabric-level arc jet test to 250 W/cm2 |  | 
2012 | 2013
Fabric-level arc jet test to 250 W/cm2 | Aeroshell deployment demonstration
2012 | 2013 | 2014 | 2015
Fabric-level arc jet test to 250 W/cm2 | Aeroshell deployment demonstration | Distributed pressure loads (wind tunnel) & SPRITE-C system level aerothermal tests | 
2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019...
Fabric-level arc jet test to 250 W/cm2 | Aeroshell deployment demonstration | Distributed pressure loads (wind tunnel) & SPRITE-C system level aerothermal tests |  | Develop 0.7m flight system SR-1 Flight Experiment |  |  | Mission concept development Applications
POC: Paul.Wercinski@nasa.gov. 650-776-9984
BLAM arc jet tests
Wind tunnel test
Video: 2m Ground Test Article
deployment
Video: 35cm diameter sub-scale arcjet test
In-space deploy of Sounding Rocket 1 Test

## Slide 4: SmallSat Drag Modulation Aerocapture (DMA) for SMD Planetary Orbiter Missions
By modulating the time that a drag skirt is jettisoned from the spacecraft, the system can receive more or less delta-V and target a specific orbit
To overcome navigation and atmospheric uncertainties, a form of flight control is needed during the aerocapture pass through the atmosphere
NASA Ames partnered with JPL (Alex Austin PI) on developing mission concepts and technology development plans (eg. ADEPT Technology Readiness Assessment)
DMA science mission concepts and potential Earth Technology Demonstration mission recently presented to STMD TDM leadership and SMD sponsored ADRAT

## Slide 5: Aerocapture Tech Development Progress
ARC successfully flew a 70 cm diameter ADEPT skirt on a suborbital sounding rocket
ARC performed arcjet testing of flexible carbon fabric TPS at Mars relevant conditions.
Cart3D CFD simulations at Venus flight conditions
DSENDS 6-DOF simulation toolset provides capability to model the aerocapture maneuver
ADEPT vacuum bag and subsonic wind tunnel tests to assess shape change and possibility of flutter
JPL and ARC performed 8 sub-scale ballistic range shots at, giving valuable test data to inform DSENDS modeling
Investigated post-aerocapture PRM delta-v and operations requirements
Many years of development progress make drag modulated aerocapture ready for TDM
ARC performed arcjet testing of flexible carbon fabric at Mars relevant conditions
Extensive trade studies have yielded an integrated flight system design

## Slide 6
ADEPT Bibliography
Venkatapathy, E., et al, “Adaptive Deployable Entry and Placement Technology (ADEPT): A Feasibility Study for Human Missions to Mars” AIAA Aerodynamic Decelerator Systems Technology Conference, May 23-26, 2011, Dublin, Ireland. AIAA 2011-2608
Arnold, J., et al., “Thermal and Structural Performance of Woven Carbon Cloth for Adaptive Deployable Entry and Placement Technology,” AIAA Aerodynamic Decelerator Systems Technology Conference, March 25-28, 2013, Daytona Beach, FL.
Arnold, J., et al. “Arcjet Testing of Woven Carbon Cloth for Use on Adaptive Deployable Entry Placement Technology.” IEEE Aerospace Conference, March, 2013, Big Sky, MT.
Yount, Bryan, C., et al. “Structures and Mechanisms Design Concepts for Adaptive Deployable Entry Placement Technology” AIAA Aerodynamic Decelerator Systems Technology Conference, March 25-28, 2013, Daytona Beach, FL.
Kazemba, C., et al, “A Versatile 3D-Woven Carbon Fabric for Broad Mission Application of ADEPT” International Planetary Probe Workshop, June 16-20, 2014, Pasadena, CA.
Smith, B., et al, “ADEPT for Secondary Payloads” International Planetary Probe Workshop, June 16-20, 2014, Pasadena, CA.
Yount, Bryan, C., Kruger, Carl, E., Cassell, Alan, M., Kazemba, Cole, D. “Deployment Testing of the ADEPT Ground Test Article. International Planetary Probe Workshop, June 16-20, 2014, Pasadena, CA.
Smith, B. P., Cassell, A. M., Kruger, C. E., Venkatapathy, E., Kazemba, C. D., Simonis, K. R., “Nano-ADEPT: An Entry System for Secondary Payloads,” IEEE Aerospace Conference, Big Sky, MT, March 2015.
Smith, B., et al “Nano-ADEPT Aeroloads Wind Tunnel Test” IEEE Aerospace Conference, 2016.
Cassell, Alan, M., et al. “System Level Aerothermal Ground Testing for the Adaptive Deployable Entry and Placement Technology.” International Planetary Probe Workshop, June 13-17, 2016, Laurel, MD.
Cassell, A. M., et al “Human Mars Mission Design Study Utilizing the Adaptive Deployable Entry and Placement Technology” IEEE Aerospace Conference, Big Sky, MT, March 2017.
Wercinski, P. F. et al., “ADEPT Sounding Rocket One (SR-1) Flight Experiment Overview,” IEEE Aerospace Conference, Big Sky, MT, March 2017.
Cassell, A. M., et al “ADEPT, a Mechanically Deployabe Re-Entry Vehicle System, Enabling Interplanetary CubeSat and Small Satellite Missions” SmallSat 2018, Logan, UT, August 2018.
Cassell, A., et al “ADEPT for Interplanetary Small Satellite Missions” Interplanetary Small Satellite Conference, 29-30 April, 2019, San Luis Obispo, CA.
Cassell, A. M., et al “ADEPT Sounding Rocket One Test Overview” AIAA Aviation Conference, Dallas, TX, 17-21 June 2019.
Korzun, A. M., Dutta, S., McDaniel, R. D., Karlgaard, C., Tynis, J. A., “Aerodynamics for the ADEPT SR-1 Flight Experiment,” AIAA Aviation Conference, Dallas, TX, 17-21 June 2019.
Cruz, J. R., Green, J. S., “Subsonic Dynamic Testing of a Subscale ADEPT Entry Vehicle,” AIAA Aviation Conference, Dallas, TX, 17-21 June 2019.
Tynis, J. A., Karlgaard, C., “Reconstruction of the Adaptable Deployable Entry and Placement Technology Sounding Rocket One Flight Test,” AIAA Aviation Conference, Dallas, TX, 17-21 June 2019.
Dutta, S., Green, J. S., “Flight Mechanics Modeling and Post Flight Analysis of ADEPT SR-1,” AIAA Aviation Conference, Dallas, TX, 17-21 June 2019.
D’Souza, S. D., Johnson, B. J., Okolo, W. A., Nikaido, B. E., Smith, B. P., “Pterodactyl: Developing a Design, Build and Test Capability for Non-propulsive Control Systems for Lifting Nano-ADEPT,” AIAA Aviation Conference, Dallas, TX, 17-21 June 2019.
6