## Slide 1
Examination of Mars2020 shock-layer conditions via infrared emission spectroscopy of CO2
Augustin Tibère-Inglesse1
Thomas K. West IV2
Christopher C. Jelloian, Nicolas Q. Minesi, R. Mitchell Spearrin3
Justin Clarke, Luca di Mare, Matthew McGilvray4
Brett A. Cruden5
1 NASA Postdoctoral Program Fellow at NASA Ames Research Center
2NASA Langley Research Center, Hampton
3University of California, Los Angeles (UCLA)
4University of Oxford, England
5AMA Inc at NASA Ames Research Center, Mountain View
AIAA Scitech Forum, 23-27 January 2023, National Harbor, MD

## Slide 2: Outline
1) Introduction: MEDLI2
  2) OES results
  3) Comparison with LAS measurements
  4) Conclusion

## Slide 3: Mars2020 Entry Descent and Landing Instrumentation 2 (MEDLI2)
Total and radiative heat fluxes were measured during the Mars2020 atmospheric entry
Comparison with ground testing measurements
Forebody
Afterbody

## Slide 4
10% Lower Bound
90% Lower Bound
MTB08/09
MTB07
Shock Tube Informed Bias (STIB) methodology
Similarity between oblique and normal
shocks in particle time
The contribution of every flowfield point to the wall radiative heat flux is evaluated
Mapping of the contribution in terms of velocities and particle time
Evaluated at 9 time points and the two sensor locations
(MTB07/08) to obtain the test series matrix

## Slide 5: Focus of current EAST test series
Chart: Time (s)
Cruden (DPLR/NEQAIR) | 0.1881 | 0.25307 | 1.4078 | 2.1355 | 2.7565 | 3.4446 | 3.8459 | 4.4805 | 4.9017 | 4.2879 | 1.9816 | 0.79118 | 0.22579 | 0.068834 | 0.022408
Johnston (LAURA/HARA) | 0.15818 | 0.94027 | 2.4397 | 3.5502 | 4.1822 | 4.2585 | 4.1406 | 2.6199 | 1.2312 | 0.067115
Chart: Time (s)
Cruden (DPLR/NEQAIR) | 0.098256 | 0.11986 | 0.23815 | 0.63658 | 1.0379 | 1.3832 | 1.723 | 1.9636 | 2.3373 | 2.5618 | 2.6162 | 1.5132 | 0.59559 | 0.16402 | 0.044948 | 0.013362
Johnston (LAURA/HARA) | 0.063198 | 0.44082 | 1.2995 | 1.9683 | 2.2982 | 2.366 | 2.3868 | 1.9491 | 0.95004 | 0.031709
MTB08/09
MTB07
1.1 Torr (92s)
1.5 Torr (101s)
3.0-3.2 km/s
1-8 ms
2.5-2.6 km/s
3-12 ms
2.4-2.5 km/s
2-10 ms
2.7-3.0 km/s
1-7 ms
Total heat flux measurement compared to radiative flux predictions
Cruden model seems predicts faster increase, Johnston slower decay
Conditions near and after the peak of the heat pulse
Relevant velocities and particle times are extracted from STIB analysis

## Slide 6: Experimental setup of EAST
Driver
Driven
2 spectrometers
(Blue,IR)
Pressure sensors
Test conditions:
  Test gas is Mars atmosphere (95.4% CO2, 2.6% N2, 2.0% Ar)
  Conditions: 1.2 to 3.75 km/s at 1.1, 1.5 and 2 Torr
  Focus on IR radiation:
    From CO2 fundamental bands at 4.2 μm
    From CO2 overtone bands at 2.7 μm
Notes: Drop configurations

## Slide 7: Typical emission data
~ 10 cm of measurements → up to 0.4 ms in particle time
Spatial integrated radiance profiles (vertical) compared with simulations
CO2 fundamental
CO2 overtone

## Slide 8: Spectral radiance (1.1 Torr)
4.2 mm band
2.7 mm band
v > 3.2 km/s
v ≈ 2.6 km/s
v < 2.2 km/s
Underprediction of radiance in frozen cases (<2.7 km/s)
Measurements between the models at higher velocities
250-350 μs

## Slide 9: Summary at tpart = 300 μs (1.1 Torr)
Chemistry frozen below 2.7 km/s
The 2.7 μm band appears better predicted with Johnston/Park while the 4.2 μm generally closer to Cruden

## Slide 10: Extrapolating to larger test time (1.1 Torr)
~0.4 ms
MTB08: 3.0-3.2 km/s, 1-8 ms
MTB07: 2.7-3.0 km/s, 1-7 ms
3.0-3.2 km/s
1-8 ms
Measured radiance profiles are extrapolated using an exponential curve

## Slide 11: Extrapolating to larger test time (1.1 Torr)
~0.4 ms
MTB08: 3.0-3.2 km/s, 1-8 ms
MTB07: 2.7-3.0 km/s, 1-7 ms
Chart: Time (s)
Cruden (DPLR/NEQAIR) | 0.1881 | 0.25307 | 1.4078 | 2.1355 | 2.7565 | 3.4446 | 3.8459 | 4.4805 | 4.9017 | 4.2879 | 1.9816 | 0.79118 | 0.22579 | 0.068834 | 0.022408
Johnston (LAURA/HARA) | 0.15818 | 0.94027 | 2.4397 | 3.5502 | 4.1822 | 4.2585 | 4.1406 | 2.6199 | 1.2312 | 0.067115
Chart: Time (s)
Cruden (DPLR/NEQAIR) | 0.098256 | 0.11986 | 0.23815 | 0.63658 | 1.0379 | 1.3832 | 1.723 | 1.9636 | 2.3373 | 2.5618 | 2.6162 | 1.5132 | 0.59559 | 0.16402 | 0.044948 | 0.013362
Johnston (LAURA/HARA) | 0.063198 | 0.44082 | 1.2995 | 1.9683 | 2.2982 | 2.366 | 2.3868 | 1.9491 | 0.95004 | 0.031709
MTB08/09
MTB07

## Slide 12: Extrapolating to larger test time (1.1 Torr)
~0.4 ms
MTB08: 3.0-3.2 km/s, 1-8 ms
MTB07: 2.7-3.0 km/s, 1-7 ms
Chart: Time (s)
Cruden (DPLR/NEQAIR) | 0.1881 | 0.25307 | 1.4078 | 2.1355 | 2.7565 | 3.4446 | 3.8459 | 4.4805 | 4.9017 | 4.2879 | 1.9816 | 0.79118 | 0.22579 | 0.068834 | 0.022408
Johnston (LAURA/HARA) | 0.15818 | 0.94027 | 2.4397 | 3.5502 | 4.1822 | 4.2585 | 4.1406 | 2.6199 | 1.2312 | 0.067115
Chart: Time (s)
Cruden (DPLR/NEQAIR) | 0.098256 | 0.11986 | 0.23815 | 0.63658 | 1.0379 | 1.3832 | 1.723 | 1.9636 | 2.3373 | 2.5618 | 2.6162 | 1.5132 | 0.59559 | 0.16402 | 0.044948 | 0.013362
Johnston (LAURA/HARA) | 0.063198 | 0.44082 | 1.2995 | 1.9683 | 2.2982 | 2.366 | 2.3868 | 1.9491 | 0.95004 | 0.031709
Estimated total error:
  At MTB08 location: -3% (Johnston), +2 % (Cruden)
  At MTB07 location: -6.5% (Johnston), +2 % (Cruden)
Discrepancy between the models consistent with real flight simulation → validation of STIB method
Estimation at 1.5 Torr could not be made since the chemistry was frozen at the timescale of the experiment
MTB08/09
MTB07

## Slide 13: Spectral radiance (1.1 Torr)
Underprediction of radiance in frozen cases (<2.7 km/s)
Measurements between the models at higher velocities
4.2 mm band
2.7 mm band
v > 3.2 km/s
v ≈ 2.6 km/s
v < 2.2 km/s

## Slide 14: Shock trajectory affect on test gas properties
Shock timing stations (PCB)
Shock is decelerating as it traverses the tube
Test window

## Slide 15: Shock trajectory affect on test gas properties
Shock timing stations (PCB)
Test window
Shock is decelerating as it traverses the tube

## Slide 16: Shock trajectory affect on test gas properties
Shock timing stations (PCB)
Test window
Shock is decelerating as it traverses the tube
Test gas is accumulated from points upstream of the observation

## Slide 17: Shock trajectory affect on test gas properties
Shock timing stations (PCB)
Test window
Shock is decelerating as it traverses the tube
Test gas is accumulated from points upstream of the observation

## Slide 18: Shock trajectory affect on test gas properties
Shock timing stations (PCB)
Test window
Shock is decelerating as it traverses the tube
Test gas is accumulated from points upstream of the observation

## Slide 19: Shock trajectory affect on test gas properties
Shock timing stations (PCB)
Test window
Shock is decelerating as it traverses the tube
Test gas is accumulated from points upstream of the observation

## Slide 20: Shock trajectory affect on test gas properties
Shock timing stations (PCB)
Test window
Shock is decelerating as it traverses the tube
Test gas is accumulated from points upstream of the observation

## Slide 21: Shock trajectory affect on test gas properties
Shock timing stations (PCB)
Test window
Shock is decelerating as it traverses the tube
Test gas is accumulated from points upstream of the observation
Post shock condition modelled with Lagrangian code, LASTA
  For frozen shocks, Frozen solution is propagated
  For reacting shocks, 0D reaction calculated over the time of flight

## Slide 22: Effect of shock deceleration on measured radiance
DPLR simulations insensitive to kinetic model (frozen chemistry)
2.6 km/s, 1.1 Torr
2.57 km/s, 1.5 Torr
2.6 km/s, 1.5 Torr
Measured
DPLR/NEQAIR
Equilibrium
Frozen

## Slide 23: Effect of shock deceleration on measured radiance
DPLR simulations insensitive to kinetic model (frozen chemistry)
LASTA correctly predicts measured radiance in all cases and explains a discrepancy up to 15% with CEA (frozen)
Shock deceleration effects must be taken into account
2.6 km/s, 1.1 Torr
2.57 km/s, 1.5 Torr
2.6 km/s, 1.5 Torr
Measured
DPLR/NEQAIR
Equilibrium
Frozen
LASTA

## Slide 24: Comparison with Laser Absorption Spectroscopy measurements
T and n extracted from OES measurements by fitting spectra using NEQAIR
Reacting case:
  Emission closer to Cruden mechanism, Absorption to Johnston
  Discrepancies from Boundary Layer absorption on the LAS measurements, error under-estimated on Emission
Frozen cases:
  Absorption temperature in agreement with CEA/Frozen but below LASTA
  Emission temperature above frozen and close to LASTA prediction
Temperature measured using Laer Absorption are up to 10% lower than Emission measurements
CO2 number density profiles in good agreement (5%)
Temperature
CO2
Temperature
CO2
Circle: Laser Absorption
Line: Emission
Frozen
Cruden
Johnston
LASTA (cruden)
Frozen
Cruden
Johnston
LASTA
Reacting case : v = 2.96 km/s
Frozen case : v = 2.56 km/s

## Slide 25: Conclusions
Test series aimed at reproducing Mars2020 atmospheric entry was performed
Emission measurements were compared with DPLR/NEQAIR simulations using three kinetic models
  Below 2.7 km/s: Chemistry frozen on experimental timescale
  Above 2.7 km/s: Radiance lies between the kinetic models
Error for predicting flight based on STIB
  At 1.1 Torr (92s) : -3/+2% (Windside) or -6.5/+2% (Leeside) for Johnston/Cruden models
  At 1.5 and 2 Torr (>100 s): could not estimate due to frozen chemistry
Shock deceleration impacts post-shock radiation profiles
  Predicted by Lagrangian code LASTA
  Explains up to 15% increase in frozen radiance
Comparison with simultaneous laser absorption measurements:
  Temperature profiles within 10% agreement
  Number density profiles within error (<5% difference)
Chart: Time (s)
Cruden (DPLR/NEQAIR) | 0.1881 | 0.25307 | 1.4078 | 2.1355 | 2.7565 | 3.4446 | 3.8459 | 4.4805 | 4.9017 | 4.2879 | 1.9816 | 0.79118 | 0.22579 | 0.068834 | 0.022408
Johnston (LAURA/HARA) | 0.15818 | 0.94027 | 2.4397 | 3.5502 | 4.1822 | 4.2585 | 4.1406 | 2.6199 | 1.2312 | 0.067115

## Slide 26: Total error on backshell location (1.1 Torr)
MTB08/9
MTB07
Velocity range: 3-3.2km/s (MTB08) and 2.7-3 km/s (MTB08)
Particle time: 1-8 ms and 1-7 ms
Profiles fitted using exponential curve and extrapolated
to 8 and 7 ms
Estimated total error:
  At MTB08 location: -3% (Johnston), +2 % (Cruden)
  At MTB07 location: -6.5% (Johnston), +2 % (Cruden)
~0.4 ms

## Slide 27: Test 64A matrix
Densities were chosen corresponding to near peak heating, ½ of peak heating and at end of heat pulse
The velocity range is swept to cover most of the histogram
A follow up test in the low-density EAST tube (64B) will study earlier time points
Chart: Time (s)
 | 2 | 3.25
 | 1.75 | 3
 | 1 | 2
 | 3.195 | 3.2466 | 3.0293 | 2.603 | 1.5178 | 2.3486 | 2.1937 | 2.8832 | 3.4033 | 3.0746 | 2.5085 | 2.9683 | 2.4718 | 2.9052 | 2.9911 | 1.9886 | 2.1913 | 3.0141 | 2.8787 | 2.696 | 2.9569 | 2.7927 | 2.5702 | 2.1748 | 1.9705 | 2.276 | 2.9109 | 2.64 | 2.5335 | 2.1782 | 2.0591 | 2.6385 | 2.83 | 1.846 | 2.3538 | 1.9951 | 2.0629 | 2.0438 | 1.3902 | 1.3023 | 3.2949 | 1.7035 | 2.133 | 4.647 | #N/A | 1.9554 | 3.1247 | 2.8823 | 3.2789 | 2.0235 | 2.3 | 3.75 | 1.48 | 2.49 | 1.25 | 2.0919 | 1.9366 | 1.1657 | 2.6791
Chart: Velocity (km/s)
| 2 | 2.25 | 2.5 | 2.75 | 3 | 3.25 | 2 | 2.25 | 2.5 | 2.75 | 3 | 3.25 | 1.75 | 2 | 2.25 | 2.5 | 2.75 | 3 | 1.75 | 2 | 2.25 | 2.5 | 2.75 | 3 | 1 | 1.5 | 2 | 1 | 1.5 | 2
Planned Test Points | 0.0025415 | 0.0025415 | 0.0025415 | 0.0025415 | 0.0025415 | 0.0025415 | 0.0025415 | 0.0025415 | 0.0025415 | 0.0025415 | 0.0025415 | 0.0025415 | 0.0034656 | 0.0034656 | 0.0034656 | 0.0034656 | 0.0034656 | 0.0034656 | 0.0034656 | 0.0034656 | 0.0034656 | 0.0034656 | 0.0034656 | 0.0034656 | 0.0046208 | 0.0046208 | 0.0046208 | 0.0046208 | 0.0046208 | 0.0046208
4.3 um band | 0.0025213 | 0.0025221 | 0.0025196 | 0.0025194 | 0.002518 | 0.0025226 | 0.0025158 | 0.0034485 | 0.0034519 | 0.0034445 | 0.0034445 | 0.0034361 | 0.003432 | 0.0045937 | 0.0045848 | 0.0045697 | 0.0045975 | 0.004603 | 0.002512 | 0.0025118 | 0.020561 | 0.0025089 | 0.020353 | 0.0046204 | 0.020792
2.7 um band | 0.0025239 | 0.0025243 | 0.0025177 | 0.0025263 | 0.0025265 | 0.0025292 | 0.0025146 | 0.0025195 | 0.0025297 | 0.0025218 | 0.0025151 | 0.0025142 | 0.0034365 | 0.0034375 | 0.0034347 | 0.0034347 | 0.0034336 | 0.0034295 | 0.0034382 | 0.0034365 | 0.0034331 | 0.0046088 | 0.0045809 | 0.020353 | 0.0044333 | 0.0046204

## Slide 28: Extrapolating to larger test time (1.1 Torr)
Measured radiance profiles are extrapolated using an exponential curve
Relaxation time to equilibrium extracted from the extrapolation:
  4.2 μm: relatively good agreement with Cruden
  2.7 μm: lie in between the models, closer to Johnston
  Johnston model predicts a faster relaxation to equilibrium
~0.4 ms
MTB08: 3.0-3.2 km/s, 1-8 ms
MTB07: 2.7-3.0 km/s, 1-7 ms
Relaxation time
Cruden
Johnston
Solid: 4.2 μm
Dash: 2.7 μm
3.0-3.2 km/s
1-8 ms