## Slide 1: The Dragonfly Entry and Descent System
AIAA SciTech 2023
January 23, 2023
Michael Wright (Dragonfly EDL Phase Lead)
Karl Edquist (Dragonfly Deputy EDL Phase Lead)
Notes: APL led
EDL Partners include : NASA ARC&LaRC, Lockheed Martin, U. Central Florida, Airborne Systems, Vorticity LTD, Spirit/FMI

## Slide 2
2
: Largest of Saturn’s Moons
(4× density)
Notes: At Titan temperatures, water is a rock

## Slide 3
3
Launch: 2027
Arrival: 2034

## Slide 4: A Note on Scale
4
Key Dimensions:
Fuselage: 13.6x19.5x16.3 cm
Rotor Diameter: 1.2 m
Total Mass: 1.8 kg
Ingenuity
Key Dimensions:
Fuselage: ~3.85 m long
Rotor Diameter: ~1.35 m
Total Mass: ~900 kg
Dragonfly

## Slide 5
5
Selk Crater
Notes: Namib dunes provide a clear terrestrial analog
Interdune region tends to be flat and clear of hazards

## Slide 6: Flight System Elements
Rotorcraft Lander
Flight configuration with HGA stowed
Note: Images above are used to delineate elements and do not reflect current configuration
Cruise stage provides functions needed for travel between Earth and Titan
  Propulsion, guidance & control, (attitude control) and telecommunications
EDL Assembly provides functions needed for safe descent through Titan’s atmosphere
  Heatshield, backshell, parachute system, separation systems, and LGA
(Rotorcraft) Lander provides functions needed for surface exploration at Titan
  Octocopter for mobility (flight) at Titan
  Science instruments for studying Titan’s surface and atmosphere

## Slide 7
MDNav to EDL Handoff (7800 km); E–10 min
Cruise Stage Separation; E–10 min
Wake up; E-190 min
Cut thermal loop; E-16 min
Peak heating
254 km; E+227 s
Peak deceleration
232 km; E+241 s
Entry
* Times referenced to DAC1b CBE Mean
Turn to entry, spin up to 2 rpm; E-27 min
See talks by Brandis (Aerothermal) and Stern (TPS) in this session
Notes: Wake up from hibernation EI-3h
Entry beta = 106 kg/m2, FPA = - 47.8°
Very Mars-like to this point. Peak heating about 4m after EI, pushing 300 W/cm2 with a large contribution from shock layer radiation.
Peak deceleration 15s later, about 10.5g predicted, comfortably under 12g requirement

## Slide 8: Dragonfly Aeroshell
8
Backshell
Heatshield
Parachute Cone
Aeroshell
EDL
Assembly
4.5m Diameter
ELGA Radome (SLA-220)
PICA-D
SLA 561V
Notes: Not shown: Vent, Parachute lid/cover, access doors

## Slide 9
Drogue deployment
157 km; E+374 s
90 min Descent under drogue
Heatshield separation
4.5 km; E+94 min
Main parachute deployment 5km; E+92 min
Entry Interface (1270 km); E=0
Descent
* Times referenced to DAC1b CBE Mean
See talk by Winski (Flight Mechanics) in this session
Notes: This is where the time dilation begins; drogue is deployed at EI+6m, but then we are on it for 86 minutes
Drogue: 5.4m DGB, opening load < 14.7kN, deploy M=1.5, ~9s above 1.4, ~30s supersonic
Three functions: stability, deceleration, deploy the main
Main: 16.55m DGB, opening load < 8kN, low speed deploy @5km
Functions: stability, deceleration, facilitate heat shield and lander release

## Slide 10: Parachute Deceleration System (Airborne / Vorticity)
36.0 m
Drogue Parachute (5.4 m DGB)
  Mortar deploy via trigger at Mach 1.5
  Functions: stabilize capsule, decelerate through atmosphere, extract main chute
Main Parachute (16.55 m DGB)
  Low speed subsonic deploy
  Functions: stabilize capsule, facilitate heat shield and lander release
  Exploring alternate canopies (inflation & stability)
Huygens heritage swivels
  Prevent line twisting
37.5 m
45.0 m
Notes: MSL parachute design for peak load of 286 kN as opposed to 14.7 kN for the drogue and 6.1 kN for the main
Drogue:4.5m DGB (M2020 fabric, Kevlar lines, 10 diameter trailing distance); Main 16.55 m DGB (M2020 fabric, Kevlar lines, 8 diameter trailing distance)
Note that the parachute vendor is currently conducting a trade study for the main canopy (inflation and stability)
Swivel: Molybdenum disulphide dry film lubricant

## Slide 11
Lander Pose
2.2 km; E+109 min
Despin
2.1 km; E+110 min
Reconfigure EDL thermal loop;
2.3 km; E+107 min
Lander Separation
0.8 km; E+118 min; 2.9 m/s
Transition to Powered Flight
Release + 1 s
Lidar Ground Lock
2 km; E+111 min
Preparation for Powered Flight
* Times referenced to DAC1b CBE Mean
Notes: This is the “new” part. We have a whole series of activities who’se purpose is to release the lander in a state from which it can successfully transition to powered flight
EDL should probably be “EDR” for this mission; our responsibility ends once this goal is achieved and the lander will locate its first safe landing site and complete its first landing under the auspices of the onboard mobility system

## Slide 12
MDNav to EDL Handoff (7800 km); E–10 min
Cruise Stage Separation; E–10 min
Wake up; E-190 min
Cut thermal loop; E-16 min
Peak heating
254 km; E+227 s
Peak deceleration
232 km; E+241 s
Drogue deployment
157 km; E+374 s
90 min Descent under drogue
Heatshield separation
4.5 km; E+94 min
Main parachute deployment 5km; E+92 min
Lander Pose
2.2 km; E+109 min
Despin
2.1 km; E+110 min
Reconfigure EDL thermal loop;
2.3 km; E+107 min
Lander Separation
0.8 km; E+118 min; 2.9 m/s
Transition to Powered Flight
Release + 1 s
Lidar Ground Lock
2 km; E+111 min
Entry Interface (1270 km); E=0
Entry and Descent Con-Ops
* Times referenced to DAC1b CBE Mean
Turn to entry, spin up to 2 rpm; E-27 min
Notes: Wake up from hibernation EI-3h
Entry beta = 106 kg/m2, FPA = - 47.8°
Drogue: 5.4m DGB, opening load < 14.7kN, deploy M=1.5, ~9s above 1.4, ~30s supersonic
Main: 16.55m DGB, opening load < 8kN, low speed deploy @5km

## Slide 13: EDL Timeline Comparison
Max Deceleration
Drogue Deploy
Main Chute
This is MSL…
Altitude (km)
Time (s)
Lander Release
Notes: Seven minutes of terror became “2 hours of mild discomfort” for proposal purposes
As we learn more it is becoming more like “an interminable time of considerable angst”

## Slide 14: Key Entry Phase Challenges
Quantifying heating due to shock layer radiation
  dominated by CN-red and violet emission
  Less validated than air or CO2
  NASA/ESM has completed a test series in EAST focused on refining shock tube informed bias uncertainties.
TPS material qualification
  Non-oxidizing environment, radiation dominated heating
  Performance of RTV gap filler in such an environment
Singularities
  Radiative heating on main seal
  RF transparency of radome materials
  Heating on backshell singularities
EDL Phase thermal analysis
  Long descent time, cryogenic exterior, internal heat source
EAST Testing
Arc Jet / Lamp Testing
3D Material Response
M2020 Closeouts

## Slide 15: Key Descent Phase Challenges
Roll Coupling
  Initial roll rate of 2RPM, but over 100min for that to change
  Very difficult to assess potential sources of pitch-roll coupling
Transonic-subsonic aerodynamics
  Drogue chute is relatively smaller than that for Genesis
  Initial analysis shows that capsule dynamics dominates system dynamics
  Considerable time spent with an open backshell
Very long inflation time and possible high angle of attack at deploy for main chute
  Anti-inversion netting baselined
  Drop testing is planned
Thermal Analysis
  Once the heatshield is released, our “hot” problem immediately becomes a cold problem
  Exposed mechanisms require heaters
VST/TDT/12’ Testing
Free Flight CFD
Drop Test
Parachute FSI

## Slide 16: Key Preparation for Powered Flight Challenges
Open Backshell Dynamics
  Considerably amount of time spent on chute with no heatshield
  Two configurations: stowed and posed
Rotor-Backshell Aero Interactions
  Operating rotors at 1100RPM while attached to backshell
  Highly dynamically coupled problem
Altitude Knowledge
  We have no rangefinding until Lidar lock (potentially as low as 1km AGL
Releasing lander in a state from which it can transition to powered flight
  Requires specific range of yaw moment, strongly prefers pitch down rate at release
12’ Testing
TPF CFD
Posed Lander
Drop Testing
14x22 Testing

## Slide 18: Backup
18