## Slide 1: Multi-Star Wavefront Control: Update on Technology Development for Roman Space Telescope and Habitable Worlds Observatory
Dan Sirbu1, Ruslan Belikov1, Eduardo Bendek2, Olivier Guyon3, Julien Lozi3,
David Marx2,Chris Mendillo4, Eugene Pluzhnik1,
Camilo Mejia Prada2 , A J Eldorado Riggs2, Garreth Ruane2,
1NASA Ames, 2JPL/Caltech, 3Subaru Telescope / Subaru , 4UMass-Lowell,
241st AAS Meeting
January 9th, 2023
Image Credit: Hubble Picture of Alpha Centauri
Funded by NASA ISFM Program
HCIT is funded by NASA’s Exoplanet Exploration Program (ExEP) Office

## Slide 2: Astro2020 decadal survey recommendations for Habitable Worlds Observatory
illustration
https://www.nationalacademies.org/our-work/decadal-survey-on-astronomy-and-astrophysics-2020-astro2020
Astro2020 flagship recommendation requires a statistically robust
~25 exoearth yield estimate. Increased instrument efficiency improves margin!
Top two recommendations of
Astro2020 decadal survey:
Notes: Bruce Macintosh: ~6m is very approximate
Scott Gaudi: most trades should be re-opened

## Slide 3: Multi-Star Systems increase quantity & quality of direct imaging targets
illustration
Binaries extend the discovery space for
the Astro2020 flagship
Plotting hypothetical exo-Earth
contrast for all stars within 20 pc
~1/2 of all FGK stars are in
binary systems
41 of 67 stars in 10 pc
259 of 519 stars in 20 pc
Alpha Centauri A & B is a special
science case:
3x closer than any other star system
3x better spatial/spectral resolution
Based on Guyon 2019
Notes: Bruce Macintosh: ~6m is very approximate
Scott Gaudi: most trades should be re-opened

## Slide 4: Alpha Cen Opportunities with Roman
illustration
Due to unusual proximity, Alpha Cen breaks common-wisdom assumptions about what Roman can do:
1) NEAR candidate planet is within demonstrated lab contrast with SNWC
2) At gibbous phase, a large Earth-like planet around Alpha Cen B may be within CGI’s sensitivity limits (depending on final performance)
Roman CGI may be able to image Earth twins
Based on Bailey 2019
Roman MSWC
Simulations
Roman SNWC
Lab Demo
: 1.4RE in HZ of aCenB
(Gibbous phase)
: 7RE @1.1AU, aCenA
(quadrature)
Notes: Bruce Macintosh: ~6m is very approximate
Scott Gaudi: most trades should be re-opened

## Slide 5: MSWC For Mission Applications (Simulations)
illustration
10 λ/D
Alf Cen A
(blocked by coronagraph
10 λ/D
Castor A
(blocked by coronagraph
Castor B
Roman (with starshade)
Roman (with coronagraph)
Habex (with starshade)
Habex (with VVC)
LUVOIR-B/HWO (with VVC)
PICTURE-D (with VVC)
Sirbu et al.,
SPIE 2019
Notes: Bruce Macintosh: ~6m is very approximate
Scott Gaudi: most trades should be re-opened

## Slide 6: Previous Lab Demonstrations
illustration
Coronagraphic PSF
1% Bandwidth:
1.9e-9 contrast
10% Bandwidth:
8.6e-9 contrast
Note: images have a D-shaped field stop in place.
MSWC solution with “software binary”
Conventional (single-star)
Wavefront control
Multi-Star
Wavefront control
Primary star
Secondary star
(1) MSWC-0 demo at Ames (in-air testbed)
Belikov et al, SPIE 2016
(2) MSWC-0 demo at SCEXAO (internal source)
Pluzhnik et al, SPIE 2021
(3) SNWC and MSWC-s software binary demo at DST HCIT
Riggs et al., SPIE 2021
Multi-star laboratory image
(sub-Nyquist, no coronagraph)
(1)
(2)
(3)
10% Bandwidth:
9.6e-8 contrast
Notes: Bruce Macintosh: ~6m is very approximate
Scott Gaudi: most trades should be re-opened

## Slide 7: Occulting Mask Coronagraph (OMC) Testbed for Roman
John Hagopian
Seo et al, SPIE 2018
Planned insertion of binary source assembly
MSWC Shaped Pupil
Microsocope imaging of detail
Same design as Roman MSWC
mask (EXEP-contributed)
Manufactured with carbon nanotubes (by John Hagopian)
Notes: Bruce Macintosh: ~6m is very approximate
Scott Gaudi: most trades should be re-opened

## Slide 8: SNWC OMC Testbed Results
diffraction
Using only 1 DM and applying mild strokes (19.4 nm RMS)
Best total contrast at 2nd diffraction order is 5.1e-8 (~150x suppression of initial speckle field level of 7.6e-6)
Best total contrast at 3rd diffraction order is 8.7e-9 (~200x suppression of initial speckle field level of 1.7e-6)
Central star (behind field stop)
Sirbu et al, SPIE 2022
2nd diffraction order
3rd diffraction order
SNWC contrast history
Notes: Bruce Macintosh: ~6m is very approximate
Scott Gaudi: most trades should be re-opened

## Slide 9: Conclusions
  Binary
Binary star targets are important for direct imaging:
Improve science yield and quality of targets
Enable unique binary star science
Alpha Centauri is an unusually favorable outlier
(could potentially enable a large terrestrial planet with Roman coronagraph)
MSWC enables exoplanet imaging around binary stars
- Primarily an algorithm, but benefits from a mild grating in the system
- Selected as a contributed mode on Roman & Compatible with Habitable Worlds Observatory
TRL ~4 lab demonstrations at ACE, SCExAO, and HCIT
Best previous SNWC contrasts achieved in vacuum were around the 1st diffraction order (in single-star super-Nyquist mode): 1.9e-9 in monochromatic light, 8.6e-9 in 10% band
OMC demonstrations validated Roman MSWC mask design in vacuum and achieved 5.1e-8 SNWC contrast (2nd diffraction order), and 9.6e-9 (3rd diffraction order) in monochromatic
Recently installed binary star source will enable full MSWC demonstrations for Roman
Tech demonstrations on-sky with PICTURE-D and Roman will mature and reduce risk for Habitable Worlds Observatory
Binary Star Source (Nov. 2022)
Off-axis
star
On-axis
star
Eduardo Bendek
Notes: Bruce Macintosh: ~6m is very approximate
Scott Gaudi: most trades should be re-opened