## Slide 1: NASA GSFC SmallSats – A NOS3 Case Study
Mark Suder
Systems Engineer
TMC Technologies
NASA’s IV&V Program

## Slide 2: NASA IV&V JSTAR/ITC – Who we Are
NASA – National Aeronautics and Space Adm.
  NASA’s Software IV&V Program
      Software Independent Verification and Validation +
      Primarily NASA, also a few closely related organizations/missions
      Ensuring primarily NASA Class A Mission Success since 1993
      Full Development Lifecycle – Software (and related System) Requirements, Design, Code, Test, Assembly/Integration&Test, etc.
    JSTAR/ITC
      JSTAR (see logo); ITC = Independent Test Capability, the personnel team for the lab (sometimes used interchangeably)
      Experts in software only simulation of hardware and hardware emulation
        Especially, but not limited to, CPU instruction set simulation so flight binary executables can execute on commodity hardware
        Also, emulation of flight peripherals, buses, etc.
        And more…

## Slide 3: NOS3 Architecture
Combination of multiple pieces of open-source software
  A virtual spacecraft!
Flight Software
  Core Flight System (cFS) based
Ground Stations
  Ball Aerospace COSMOS
Dynamics Engine
  42
  Provides visualization
NOS Engine
  Communication protocols
  Hardware abstraction layer
Component simulators
NOS3 = NASA Operational Simulator for Small Satellites

## Slide 4: NOS3 Virtual Machine

## Slide 5: GSFC SmallSats In Development

## Slide 6: GSFC SmallSat HW Platforms
LEO Bus
  Low Earth Orbit Bus is based on the Spacecube Mini Z processor
    Xilinx Zynq 7020 Dual Core ARM A9 running the Linux OS
GEO Bus
  Geosynchronous Equatorial Orbit Bus is based on a GSFC In-House developed C&DH (MARES)
    RTG4 FPGA w/ LEON3-FT softcore running the RTEMS RTOS
Desktop Linux NOS3 Target
  Along with platform support for our two flight architectures, all flight software is built for the Linux NOS3 target for development and testing
NOS3 builds FSW for all of these environments

## Slide 7: GSFC SmallSat Common Components
Attitude Determination & Control System (ADCS)
  Reaction Wheels
  Inertial Measurement Unit
  GPS
  Star Tracker
  Magnetometer
  Fine Sun Sensor
Command and Data Handling
  LEO Bus: Spacecube Mini-Z
  GEO Bus: MARES Leon3
Communications
  Wireless S-Band Radio
Power
  EPS and Batteries

## Slide 8: GSFC SmallSats – Reuse Approach
SmallSat Software Baseline
cFE Core
(6.7)
GSFC cFS
Reuse Apps
GSFC
SmallSat Apps
Instrument cFS Apps
Device cFS Apps
NOS3 Sim
COSMOS Ground System
42 Dynamic Sim
Reuse Artifacts
(Develop once)
Mission Specific Artifacts
(Develop for each Mission)
For Mission Specific
Instruments
For New and
Mission
Specific
Devices
Device NOS3 Sims
COSMOS
Database
Mission Specific
Software
Completed Missions
Mission FSW Pipeline

## Slide 9: Component SW Development
Receive component spec sheet (and maybe component)
Develop standalone checkout application (NOS3 for development environment)
Test checkout application with component (flatsat)
Develop cFS application reusing code from checkout application (NOS3 for dev env)
Develop NOS3 hardware simulator (NOS3 for dev env)
Test cFS application (flatsat/real sat and NOS3 env)
Integrated FSW testing (flatsat/real sat and NOS3 env)

## Slide 10: NOS3 Uses
Development environment
  Toolchains, etc. – build for target and NOS3 environment
Test component apps
  Including commands/telemetry
  Interaction with hardware using NOS3 sims and real hardware
Test integrated apps / flight software
  E.g. Verify closed loop ADCS algorithm control using simulated sensors/actuators/42 dynamics
Develop operator tools and procedures

## Slide 11: NOS3 Benefits
Development
  Earlier flight software development
  Provides a workflow for iterative work
  Reduces “works for me” issues
  Develop and dry-run procedures safely
Testing
  Enables testing that is not physically possible
  Increases available testing resources
  Software integration testing
Operations
  Long duration testing
  Failure scenarios
  System / mission familiarization and training
Invaluable during COVID for enabling remote work

## Slide 12: NOS3 ADCS Benefit Example
Closed loop ADCS testing
  Not possible on Earth with real hardware
  NOS3 with 42 provided dynamics inputs/outputs
  E.g. Verified BurstCube sun safe mode slewed to and tracked sun
CSS
FSS
Slewing
+Y to Sun!
COSMOS Telemetry Grapher
42 Unit Sphere Viewer (shows truth)
Lighter =
42 Truth
Darker =
ADCS estimate
from sensors

## Slide 13: Open Source NOS3 – Path Forward
Lessons learned from GSFC SmallSats and NOS3 being fed into open source NOS3 (https://github.com/nasa/nos3)
  E.g. component (single repository) = FSW/GSW/Sim/Checkout app
Wanted to open source FSW/GSW/Sim/Checkout App for GSFC SmallSat common components (FSS, GPS, etc.)
  Not feasible
  So “generic” components being created in open source
Eventually (summer 2023?) have design reference mission including:
  A full suite of generic components
  ADCS algorithms

## Slide 14: Thank You!
Questions?
  Answers?
https://github.com/nasa/nos3
https://www.nasa.gov/centers/ivv/jstar/JSTAR.html
mark.suder@tmctechnologies.com