## Slide 1
Nathan Dostart
PolCube Calibration
2023/02/14
Notes: STILL

## Slide 2: Calibration Goals
Calibration on pixel-by-pixel basis
Each pixel assigned a wavelength band and polarization
  Measure spectral response and polarizer extinction to characterize in-band and out-of-band transmission
Measure absolute radiance, dark level (over temperature), and PSF
PSF will be deconvolved from raw images
All calibration will be performed on the 4x1 binned data

## Slide 3
Calibration Plan
Spectral & Radiometry calibration
Linearity calibration
Stray light calibration
Dark level calibration
Polarization calibration

## Slide 4: Calibration Goals
Calibration on pixel-by-pixel basis
Each pixel assigned a wavelength band and polarization
  Measure spectral response and polarizer extinction to characterize in-band and out-of-band transmission
Measure absolute radiance, dark level (over temperature), and PSF
PSF will be deconvolved from raw images
All calibration will be performed on the 4x1 binned data

## Slide 5: Spectral and Radiometric Calibration
Tunable laser source and integrating sphere
Yields absolute radiance measurement and spectral response function

## Slide 6: Linearity Calibration
White light source and integrating sphere
Varying light levels (dark to saturation) for each gain and integration time setting
Yields map of radiance to detector counts

## Slide 7: Stray Light Calibration
White light source and collimated beam
“In-field” stray light yields PSF measurement and relative angular location of each pixel
Out-of-field stray light yields additional noise term
Absolute angular location to be determined on orbit
Co-registration with known coastlines/islands

## Slide 8: Dark Level Calibration
Covered telescope, measure dark images during TVAC test
Yields temperature-dependent dark levels

## Slide 9: Polarization Calibration
White light source + integrating sphere + rotating linear polarizer
Yields exact polarizer alignment and extinction ratio

## Slide 10: Desired Information
Raw data from KASI calibration
PolCube models and analysis
Instrument operation details after integration onto BusanSat
Any known issues

## Slide 11: Thank you!