## Slide 1: Flight Software for the LOFTID Re-Entry Vehicle
Paul Brewster, Software Lead
March 21st, 2023

## Slide 2: Agenda
Project Introduction
Avionics Overview
PDSU Software
Camera Controller Software
Data Recorder Software
Conclusions

## Slide 3: Project Introduction
Hypersonic Inflatable Aerodynamics Decelerator (HIAD)
  Aeroshell designed to protect and decelerate a spacecraft entering from Low-Earth orbit
  Inflatable, allowing Aeroshell to be larger than the rocket’s shroud
  6-meter diameter
First Demonstration from Low-Earth orbit
  Launched in November from Vandenberg on ULA’s Atlas V
  Secondary payload to JPSS-2
  Orbited the Earth once, splashing down near Hawaii
  2.5 hours between launch and splash down, powered on for about an hour

## Slide 4: Agenda
Project Introduction
Avionics Overview
PDSU Software
Camera Controller Software
Data Recorder Software
Conclusions

## Slide 5: Avionics Overview
+
15
V
Power
Serial
/
Ethrnt
Discrete Cmds
/
Sig
LEGEND
Pwr
-
On Cmd
Pyro Btry Chrgr
28
V
Pyro
28
V
Ethrnt
Ethrnt
Ethrnt
Ethrnt
Ethrnt
GSE Ethrnt
GSE FSW Ethrnt
Ethrnt
(
X
6
)
Serial
28
V
Pyro
Pyro
Sensors
GPS
Iridium
Serial
Pyro
Pyro
Pyro
PAS Sep Loop
PAS Sep
LV Sep Loop
LV Sep
Subsystems
/
Components
Analog
DAS
ADAU
Inflation System
Ejection
System
DAS
Data Switch
Aeroshell
Parachute
Up
-
Look
Camera
5
V
,
28
V
5
V
12
V
DC
/
DC
PDSU
ISPS
PDSU
LNA
15
V Pwr
LV
5
V
+
15
V
-
15
V
Recovery Lights
Sys Btry Chrgr
LB Serial
LB Btry Chrgr
Pyro
28
V
Pyro
Battery
System
Battery
FOSS
IDR
RTB
IMU
Camera
Pod
(
X
6
)
PDSU
Modular Avionics Control Hardware
PDSU
Pyro
Relay
EDR
EDR Serial
EDR Btry Chrgr
GSE
28
V
PDSU
Interface Adapter
Board
LB
GSE

## Slide 6: Avionics Components with Flight Software
+
15
V
Power
Serial
/
Ethrnt
Discrete Cmds
/
Sig
LEGEND
Pwr
-
On Cmd
Pyro Btry Chrgr
28
V
Pyro
28
V
Ethrnt
Ethrnt
Ethrnt
Ethrnt
Ethrnt
GSE Ethrnt
GSE FSW Ethrnt
Ethrnt
(
X
6
)
Serial
28
V
Pyro
Pyro
Sensors
GPS
Iridium
Serial
Pyro
Pyro
Pyro
PAS Sep Loop
PAS Sep
LV Sep Loop
LV Sep
Subsystems
/
Components
Analog
DAS
ADAU
Inflation System
Ejection
System
DAS
Data Switch
Aeroshell
Parachute
Up
-
Look
Camera
5
V
,
28
V
5
V
12
V
DC
/
DC
PDSU
ISPS
PDSU
LNA
15
V Pwr
LV
5
V
+
15
V
-
15
V
Recovery Lights
Sys Btry Chrgr
LB Serial
LB Btry Chrgr
Pyro
28
V
Pyro
Battery
System
Battery
FOSS
IDR
RTB
IMU
Camera
Pod
(
X
6
)
PDSU
Modular Avionics Control Hardware
PDSU
Pyro
Relay
EDR
EDR Serial
EDR Btry Chrgr
GSE
28
V
PDSU
Interface Adapter
Board
LB
GSE

## Slide 7: Software Components
Class D Mission, Class C Software
PDSU Software
  Sequence Mission Timeline
  Data Acquisition
  Component Control
  Telemetry
Camera Controller Software
  6 Camera Controllers
  Each Controller Interfaces with 1 Visual and 2 IR Cameras
  Receives Camera stream, processes, records locally, sends to Data Recorders
Data Recorder Software
  Captures all network traffic and records the traffic to an SD card
  Identical software on the Internal and Ejectable Data Recorders
FOSS Software
  CPU/FPGA hybrid to sample laser return along multiple fiber optic strands measuring temperature
  FPGA used to perform 40K FFTs per second on the laser return signal

## Slide 8: Agenda
Project Introduction
Avionics Overview
PDSU Software
Camera Controller Software
Data Recorder Software
Conclusions

## Slide 9: PDSU Software
Target Hardware
  Modular Avionics Control Hardware (MACH) compute system
  Procured from Northrup Grumman
Target Processor
  Power PC 8280 Processor
Target OS
  LynxOS
    POSIX compliant
    Real-Time Operating System
Software Framework
  cFS 6.5

## Slide 10
PDSU Software
Architecture
Digital I/O Interface
Event
Services
Executive
Services
Time
Services
Command
Ingest
Telemetry
Output
Table
Services
Power Transfer
Control
Scheduler
House-keeping
Control
cFS Apps
cFE Apps
Power
Control
Ordnance
Control
Stored
Command
Nav
Filter
Calculation
IMU Interface
GPS Interface
Analog I/O
Interface
DAU Interface
Data Acquisition
Inflation System
Interface
Real-Time Beacon
Interface
Data Recorder Interface
Telemetry
Software Bus
Recovery
Light

## Slide 11: Major Changes for LynxOS
Based on posix OSAL and pc-linux PSP
OSAL
  Threaded Signal Handler behavior ambiguity
    POSIX does not define which thread receives a given signal
    Created dedicated Timer Thread to do signal handling
    Used msg queue for other threads to add and remove signals
  Pthread Mutexes were not recursive
    Added recursive functionality to OS_mutex
  Dynamic Object Loader API inconsistent
    Switched to using a module id for all shared object symbol lookups
PSP
  Shared Memory inconsistent
    Switched to POSIX real-time shared memory
  Reworked Timer Thread to reflect OSAL changes

## Slide 12: Minor Changes for LynxOS
OSAL
  Implemented os_vsnprintf since vsnprintf didn’t exist
  Changed setschedparams to setschedprio
  Added const to buffer variables being passed into a write function
  Replaced statvfs structure with statfs structure
  Removed gethostid
  Linked to netinet instead of pthreads and rt
PSP
  Switched away from long command line options
CFE
  Added _STDC_LIMIT_MACROS defines
  Modified network include files
  Fixed byte swapping in CCSDS header

## Slide 13: Agenda
Project Introduction
Avionics Overview
PDSU Software
Camera Controller Software
Data Recorder Software
Conclusions

## Slide 14: Camera Pod
Each Camera Pod consists of
  Camera Controller
    On-board data storage
    Network Connection to Data Recorders and GSE
  IMPERX Cheetah camera connected via HD-SDI
  Two FLIR BOSON Infrared Cameras connected via USB

## Slide 15: Camera Controller Software
Target Hardware
  AiTech A176 based on NVIDIA Jetson TX2 hardware
Target Processor
  ARM Cortex-A57 CPU
  Nvidia Pascal GPU
Target OS
  Jetson Linux
    Ubuntu based Linux
Framework
  Gstreamer media pipeline
Image courtesy of AiTech Systems

## Slide 16: Camera Controller Software Functionality
Receives
  Two IR Video streams (640x512 at 10Hz)
  One Visual Video stream (1920x1080 at 30 Hz)
Decodes/Encodes
  Uses the on-board GPU for real-time video encoding and decoding
Records
  Full resolution streams to on-board storage
Sends
  Visual Video to Data Recorders as H265 video at 12Mbs bitrate
  IR Video to Data Recorders as PNG compressed images at 1Hz

## Slide 17: Agenda
Project Introduction
Avionics Overview
PDSU Software
Camera Controller Software
Data Recorder Software
Conclusions

## Slide 18: Data Recorder
Two Data Recorders
  Internal Data Recorder
  Ejectable Data Recorder
Each Data Recorder contains
  A Single Board Computer
  A separate ejectable SD card
Data Sources
  PDSU
  6 Camera Pods
  Aeroshell Data Acquisition Unit (DAU)
  FOSS
Data Subscription
  All data is sent using multi-cast UDP
  Each source sends data just once to their respective multi-cast address
  The IDR, EDR, and GSE subscribe to the multicast addresses to receive the data
Data Storage
  Data is stored unprocessed on the SD card in PCAP format to maintain network information

## Slide 19: Data Recorder Software
Target Hardware
  AiTech A176 based on NVIDIA Jetson TX2 hardware
Target Processor
  ARM Cortex-A57 CPU
  Nvidia Pascal GPU
Target OS
  Jetson Linux
    Ubuntu based Linux
Framework
  libpcap
Image courtesy of AiTech Systems

## Slide 20: Data Integrity
Extensive Testing was done to ensure data integrity
  Specifically looking for dropped or corrupted packets
Issues were found in four places in the data pipeline
  Data not properly routed at the Data Switch
  Data not properly received by the Data Recorder
  Data not properly written to the SD card by the Data Recorder
  Data not properly verified during post-process integrity checks

## Slide 21: Data not properly routed at the Data Switch
Issue:
  In testing, significant chunks of data were dropped at the Data Switch once every few minutes
  The Data Switch drops packets due to high traffic load
  By analysis, average network bandwidth was well under data switch limits
    Overall network bandwidth was 20Mbps and the Data Switch was tested up to 60Mbps
Two Solutions
  Enable Internet Group Management Protocol (IGMP)
    Without IGMP, multicast packets are routed to all connected devices
    Each device is expected to drop the packet if it isn’t subscribed to that multicast packet
    Resulted in over x6 the bandwidth usage
  Camera Pod Controllers sending IR Video
    Each of the 6 Camera Controllers sends two IR images at 1Hz
    If the images are all sent at the same time, there is a sudden spike in traffic, even though average bandwidth is very small, causing dropped packets
    By staggering the image sends, there is never a sudden spike in traffic

## Slide 22: Data not properly received by the Data Recorder
Issue:
  The software does not receive the data from the network kernel buffer fast enough, resulting in data being lost in the buffer
Solution:
  A thread is created for each multicast address
  Each thread does a non-blocking poll to receive data from that address
  When no data is available, the thread sleeps to allow another thread to go
Other Attempts:
  Using a single thread to receive all of the multicast traffic. Design was simpler, but the libpcap filter was complex, which slowed overall execution time
  Using blocking polls to receive data. Reduced CPU usage but was overall slower.
  Using non-blocking polls with a timeout-based select function. Reduced CPU usage but was overall slower.

## Slide 23: Data not properly written to the SD card
Issue:
  Writing to the SD card is a slow process, although theoretical bandwidth is sufficient for the data
  Occasional multi-second delays in writes
Solution:
  A separate thread for writing data to the SD card
  Write data in 10MB chunks, optimizing the throughput
  Write each chunk as a separate file
  Use a ring buffer to handle the isolated delays

## Slide 24: Data Pipeline

## Slide 25: Data not properly verified during post-process integrity checks
Compare data from IDR, EDR, and GSE Data Recorder simulator to verify integrity
Issues
  Data Recorders are not started at the same time
  Data Recorders are not stopped at the same time
  The order of packets in the data file is not guaranteed
Process
  Merge the chunk files into one large data file for each Data Recorder
  Filter out non data from the network capture
  Separate each packet by their source
  Write the checksum for each packet into a checksum summary file corresponding to that source
  Compare the checksum summary files between two Data Recorders
  Search for differences in summary files, ignoring the cases where one has extra packets at the beginning or extra packets at the end

## Slide 26: Agenda
Project Introduction
Avionics Overview
PDSU Software
Camera Controller Software
Data Recorder Software
Conclusions

## Slide 27: Conclusions

## Slide 28: Credits
PDSU Software – Langley Research Center
  Matt Rodgers
  Jacob Cassidy
  Joel Amert (MSFC)
  David Keck
  Peter Huynh
Camera Controller Software – Marshall Space Flight Center
  Derek Moody
  Darrell Gaddy
  Brent Beabout
Data Recorder Software – Langley Research Center
  Matt Rodgers
FOSS Software – Armstrong Flight Research Center
  Allen Parker
Testing & QA
  Mark Wehman
  Shane Wolf