## Slide 1: Uncertainty Quantification (UQ) for Modeling and Simulation at NASA
Presenter: James Warner
Team: Patrick Leser, Paul Leser, Geoff Bomarito
Durability, Damage Tolerance, & Reliability Branch
NASA Langley Research Center
Statistical Engineering Interagency Agreement Meeting
March 24th, 2023

## Slide 2: UQ: Enabling Credible Modeling and Simulation (M&S) at NASA
Accelerating reliance on M&S
All models are wrong (but some are useful)*
*George Box, Journal of American Statistical Association, 1976.
Real world
Model
Model + UQ
Models vs. Reality
Scenario 1
Scenario 2
Response
Certification by Analysis
M&S-Enabled Paradigms at NASA
Integrate uncertainty quantification (UQ) into M&S for credibility
  UQ answers: how wrong might the model be? When is it useful?
Motivation and Challenge
Solution
Perform research and development of new state-of-the-art UQ methods
Transition advanced UQ methods from research to engineering practice
Approach
Digital Twin
Real Space
Virtual Space
Data
Information
Process
Physical Product
Virtual Model
Validation and Verification Models
Model-Based Engineering
Manufacturing Models
Sustainment/ Operational Models
System Models
Discipline Models
Design Models
Validation and Verification Models
Notes: *describe diagram in more detail (model is useful for scenario 1 but not 2)

## Slide 3: Multifidelity UQ Research and Development
Physics-based simulation
Data-driven model
Analytical model
…
UQ is computationally demanding
Multiple models often exist for predicting the same phenomena
Multifidelity UQ fuses predictions from:
  High-fidelity model for accuracy guarantees
  Low-fidelity models for speedup
Solution
Development of in-house and open-source software packages
Cutting-edge research with external partners from govt. and academia
Approach
Increasing Accuracy
Increasing Speed
Efficient, high-precision probabilistic prediction
Motivation and Challenge
Model Fusion
Available Computational Models
Multi-model Monte Carlo with Python; Open source via NASA Github

## Slide 4: Transitioning UQ Research to NASA Engineering
Trajectory Simulation for Entry, Descent, and Landing (EDL)
  Leveraged state-of-the-art multifidelity UQ to substantially improve upon traditional UQ approaches
Reliability Analysis for the Exploration Extravehicular Mobility Unit (xEMU) Spacesuit
  Introduced UQ where it traditionally is not used and demonstrated its benefits
Suit Component
Rock
Regolith
Impact

## Slide 5: Trajectory Simulation for EDL
Challenge: Traditional UQ methods used for EDL cannot achieve target landing precision required for future Moon and Mars missions
Predicted landing location
Individual high-fidelity predictions
Leveraging a high-fidelity model alone is too time consuming
Dispersion analyses simulate many trajectories to account for uncertain variables
Atmospheric Conditions
Current Vehicle State
Dispersion analyses simulate many trajectories to account for uncertain variables
Notes: *Hurricane analogy

## Slide 6: Trajectory Simulation for EDL
Challenge: Traditional UQ methods used for EDL cannot achieve target landing precision required for future Moon and Mars missions
Predicted landing location
Leveraging a low-fidelity model alone is too inaccurate
Individual low-fidelity predictions
Dispersion analyses simulate many trajectories to account for uncertain variables

## Slide 7: Trajectory Simulation for EDL
Challenge: Traditional UQ methods used for EDL cannot achieve target landing precision required for future Moon and Mars missions
Approach: high- and low-fidelity model fusion with multifidelity UQ
Predicted landing location
Multifidelity UQ improves efficiency and precision
Few high-fidelity sims
Many low-fidelity sims
Dispersion analyses simulate many trajectories to account for uncertain variables

## Slide 8: Trajectory Simulation for EDL
Challenge: Traditional UQ methods used for EDL cannot achieve target landing precision required for future Moon and Mars missions
Approach: high- and low-fidelity model fusion with multifidelity UQ
Results: Up to 100X performance improvement for trajectory simulation*
*J. E. Warner et al. Multi-Model Monte Carlo Estimators for Trajectory Simulation. AIAA SciTech 2021.
**Program to Optimize Simulated Trajectories II (POST2)
Performance Improvement for Predicting Trajectory Quantities
100X
10X
Multifidelity UQ
High Fidelity Only
Landing Latitude
Landing Longitude
Roll Rate
Max. Altitude
Mach1 Altitude
Flight Time
Terminal Velocity
Angle of Attack
High- Fidelity**
Simplified Physics
Simplified Dynamics
Data Driven
Trajectory Simulation Models
Low-fidelity
Computational Resource Allocation
102
100
Run Time %
High-Fidelity Only
Multifidelity UQ
Optimal Resource Allocation
Model Fusion
Notes: *Resource allocation & model fusion are automated in software
*Precision increases in terms of X instead of %

## Slide 9: Trajectory Simulation for EDL
Challenge: Traditional UQ methods used for EDL cannot achieve target landing precision required for future Moon and Mars missions
Approach: high- and low-fidelity model fusion with multifidelity UQ
Results: Up to 100X performance improvement for trajectory simulation
Impact:
  A breakthrough for making onboard, real-time guidance technology feasible
  A broadly applicable multifidelity UQ capability delivered for NASA problems
Notes: Note effort taken to get the funding & support

## Slide 10: Reliability Analysis for the xEMU Spacesuit
Challenge: Traditional certification approaches using factor of safety (FoS) cannot satisfy both weight and robustness requirements
Traditional Design Based on FoS
FoS Shortcomings
Difficulties specifying for new vehicles, materials, environments
Inconsistencies observed across programs, organizations
(Often) Overly conservative - may be sequentially applied by multiple teams
(Potentially) Under conservative – no direct connection to design reliability/risk
Factor of Safety
Knockdown factor
Load (L)
Resistance (R)
Margin
Calculated
Calculated
Certify design if Margin 0
Notes: Need to point out that it’s robustness to impact events / astronaut falls

## Slide 11: Reliability Analysis for the xEMU Spacesuit
Challenge: Traditional certification approaches using factor of safety (FoS) cannot satisfy both weight and robustness requirements
Probability Density
Load (L)
Resistance (R)
Failure Probability
Reliability-Based Design
Factor of Safety
Knockdown factor
Load (L)
Resistance (R)
Margin
Calculated
Calculated
Traditional Design Based on FoS
Certify design if Margin 0
xEMU Impact Dynamics Project Lead sought alternative reliability-based approach “to reduce conservatism where possible in order to avoid the pitfall of a heavy and overdesigned suit structure”
Certify design if Reliability Target Value
Reliability = Probability(R L)
Notes: Point out that you can still add in conservatism to probabilistic approach

## Slide 12: Reliability Analysis for the xEMU Spacesuit
Challenge: Traditional certification approaches using factor of safety (FoS) cannot satisfy both weight and robustness requirements
Approach: Introduced general UQ workflow for estimating reliability*
*J. E. Warner et al. Assessing Next-Gen Spacesuit Reliability: A Probabilistic Analysis Case Study. NASA/TM-20210019495.
2. Identify test specs that maximize parameter uncertainty reduction
4. Estimate reliability given calibrated parameter uncertainties
3. Estimate parameter uncertainty using test data
1. Identify model parameters with largest effect on reliability
Notes: OED also informs # tests to be performed

## Slide 13: Reliability Analysis for the xEMU Spacesuit
Challenge: Traditional certification approaches using factor of safety (FoS) cannot satisfy both weight and robustness requirements
Approach: Introduced general UQ workflow for estimating reliability
Results: applied UQ workflow to verify that the probability no impact failure (PnIF) in the xEMU brief is greater than the requirement
Probability
Stress
Impact Failure Probability
Strength
Brief/Rock/Regolith Impact Model
Impact
Computational Model
Reliability Prediction
Lunar Surface (Apollo 16 site)
xEMU Waist Brief Hip Assembly
xEMU Brief Material Properties
Regolith Properties
Model Parameter Uncertainty
PnIF ✅
Sensitivity Analysis + Model Calibration
Uncertainty Propagation
Notes: Point out that you can still add in conservatism to probabilistic approach

## Slide 14: Reliability Analysis for the xEMU Spacesuit
Challenge: Traditional certification approaches using factor of safety (FoS) cannot satisfy both weight and robustness requirements
Approach: Introduced general UQ workflow for estimating reliability
Results: applied UQ workflow to verify that the probability no impact failure (PnIF) in the xEMU brief is greater than the requirement
Impact:
  Viable path forward for certifying lightweight, next-generation xEMU spacesuit
  Reliability-based design paradigm for reduced conservatism/cost/risk at NASA
Notes: Note effort taken to get the funding & support

## Slide 15: Summary: UQ at NASA
UQ is required for the credible use of M&S for all NASA missions
  Make predictions with confidence, quantified uncertainty to inform critical decisions
  Enable paradigms like reliability-based design, Digital Twin, certification by analysis
Many hurdles to UQ adoption, workforce development is key
  Learning curve for successfully applying UQ for real world problems
  Rapidly evolving research field
  Overwhelming number of tools, methods
NASA UQ researchers continue to work to overcome these challenges
  Organized UQ Seminar Series in Spring 2023 with presentations and tutorials by external speakers (most recently, Prof. Bobby Gramacy from Va. Tech. on 3/20)
  Developing/releasing UQ software; providing tutorials on UQ approaches