## Slide 1
Hume Peabody
Staff Engineer
GSFC - Code 545
Hume.L.Peabody@nasa.gov
(301) 286-9141
  Thermal Design for Spaceflight
  Fall 2022
Note: Reference in this course to any specific commercial products, process, service, manufacturer, company, or trademark does not constitute its endorsement or recommendation by the U.S. Government

## Slide 2: Foreword
This package describes the Thermal Design process used at the NASA Goddard Space Flight Center
A Thermal Analysis package can be found at ntrs.nasa.gov under the title “Thermal Modeling and Analysis”
Any reference to a particular vendor’s hardware or software should not be considered as an endorsement of any particular tool by NASA or the United States Government
The illustrations of hardware and/or software capabilities are meant to be informational and other products may have similar or superior capabilities
2

## Slide 3: Thermal Design and Analysis Agenda
Architectures for Space Flight Design
Thermal Engineering
Thermal Design
  Challenges of Designing for Operation in Space
  Heat Transfer Basics Review
  Thermal Design Process
    Gathering Thermal Requirements
    Available Thermal Components
    Determining the Thermal Design Architecture
    Early Thermal Design Calculations
      Radiator and Heater Sizing
      Hand Calculation estimates
    Thermal Accommodation Requirements
3

## Slide 4
  Space Flight Designs

## Slide 5: Common Spacecraft Architectures
Many spacecraft utilize heritage designs to reduce the risk and cost associated with developing new technology
High level functions of all spacecraft include:
  Fitting into the launch vehicle, surviving the launch, and deploying into an operational configuration
  Self contained power generation capabilities
  Acquisition and storage of science data
  Communication with operators on the ground
  Maintaining Pointing and Location in orbit
The next slides go through the subsystems common to nearly all spacecraft

## Slide 6
Optics – reflect the incoming light where we want it
Typical Spacecraft Subsystems
6

## Slide 7
Detectors – convert incoming light into electrical signal
7
Typical Spacecraft Subsystems

## Slide 8
Mechanical – make sure everything fits into the rocket
8
Typical Spacecraft Subsystems

## Slide 9
Structural – make sure it survives the rocket ride
9
Typical Spacecraft Subsystems

## Slide 10
Mechanisms – moving parts (Solar Arrays, Antenna Dishes)
10
Typical Spacecraft Subsystems

## Slide 11
11
Typical Spacecraft Subsystems

## Slide 12
Propulsion – make sure we are in the right orbit
12
Typical Spacecraft Subsystems

## Slide 13
Guidance Navigation and Control – make sure we’re pointing where we want
(Also known at ACS: Attitude Control System)
13
Typical Spacecraft Subsystems

## Slide 14
Power – give us electrical power
14
Typical Spacecraft Subsystems

## Slide 15
Harness – all the wiring on the spacecraft
15
Typical Spacecraft Subsystems

## Slide 16
Thermal – make sure we don’t get too hot or too cold
16
Typical Spacecraft Subsystems

## Slide 17
010101101110
Electronics – make sure all the data is being processed and stored
17
Typical Spacecraft Subsystems

## Slide 18
Communications – allow us to “talk” to the spacecraft
010101101110
18
Typical Spacecraft Subsystems

## Slide 19
010101101110
010101101110
Flight Software – make sure everything can talk and respond to commands
010101101110
19
Typical Spacecraft Subsystems

## Slide 20
Hume Peabody
Staff Engineer
GSFC - Code 545
Hume.L.Peabody@nasa.gov
(301) 286-9141
  Thermal Engineering

## Slide 21: Thermal Engineering
Thermal Engineering is the management of energy to maintain components within optimum performance thermal limits to satisfy requirements. It encompasses the product life cycle from early concepts through operations:
  Design – the determination of what thermal hardware is necessary to meet requirements
  Modeling and Analysis – the simulation of operational conditions and prediction of the thermal performance of the design through computer models
  Implementation – the procurement, assembly, and integration of the necessary thermal hardware for the design
  Testing and Verification – exercising of the hardware under test environments similar to operational conditions to verify requirements are satisfied
  Operation – the checkout and usage of the thermal product under operating conditions

## Slide 22: What makes this even more difficult for Space?
With no atmosphere, convection/conduction cannot be used to reject heat. Only radiation can reject waste heat…(note radiation is proportional to surface area and Temp^4 in K or R)
  Fortunately for heat rejection purposes, space is very cold (~4K).
  But this cold environment may require heating for some components (which requires power and may affect Solar Array sizes)
  Radiators for very cold components are challenging, as the effectiveness of radiative heat rejection greatly diminishes with lower temperatures
Being on a moving spacecraft means that heat sources in space may be at different locations at different times relative to the spacecraft…makes for a frequently varying environment, especially considering orbital eclipses
Many space applications include very cold components (i.e. detectors) as well as warm components (e.g. electronics). Necessitates multiple thermal control zones…
Mass and volume are key drivers in space applications. This limits the implementation of some solutions that may be acceptable for terrestrial designs
Space is lacking in gravity, but Earth is not. This makes testing space applications difficult on the ground if they rely on zero gravity operation (e.g. heat pipes)
Space is generally not accessible for repairs – better get the design right and verified before launching into orbit!
  The necessity to thoroughly test drives cost, and money is a very finite resource…

## Slide 23
What do Thermal Engineers do for Space Designs?
Our accepted design philosophy is to ensure that the design meets requirements under stacked worst case conditions (Max/Min power, optical property variations, orbits, etc)
  Predictions are bounding case values, not instantaneous orbital predictions !!!
  High number of factors taken into account by thermal from other subsystems
The most basic function is to size radiators and heaters to maintain components within provided limits based on mechanical layout, power, and orbital inputs provided to thermal
  A variety of thermal devices are available to accomplish this goal…
The Thermal subsystem is strongly coupled with many subsystems on a typical spacecraft
  Either we really need inputs from them to do our design…
  Or we need resources from them…
  Or we need to constrain what they can do in flight or testing…
Multi Layer Insulation
Heater/Thermostats
Radiator
Heat Pipes and Loop Heat Pipes
In the simplest of terms, thermal engineers keep spacecraft, instruments, and components from getting too hot or too cold while on orbit

## Slide 24
Space-Based Thermal Engineering Process

## Slide 25: Space Flight Applications
Thermal Engineering for Space Flight Applications occurs at many levels of complexity throughout the project life cycle, from early concepts → design maturation → testing of final designs → operations
  Board Level
  Box Level
  Instrument Level
  Spacecraft Level
Aside from the obvious thermal requirements to meet temperature limits, a number of other implicit and explicit requirements exist:
  Minimize Mass, Power, and Volume
  Fit within Cost and Schedule constraints
  Consider accessibility (MLI blankets) and moving interfaces
  Consider Electrostatic Discharge, Shielding, and Contamination concerns
  Evaluate heat flows across interfaces and ensure they meet ICD requirements

## Slide 26
Hume Peabody
Staff Engineer
GSFC - Code 545
Hume.L.Peabody@nasa.gov
(301) 286-9141
  Thermal Design

## Slide 27: Thermal Design Agenda
Challenges of Designing for Operation in Space
Heat Transfer Basics Review
Thermal Design Process
  Gathering Thermal Requirements
  Available Thermal Components
  Determining the Thermal Design Architecture
  Early Thermal Design Calculations
    Radiator and Heater Sizing
    Hand Calculation estimates
  Thermal Accommodation Requirements

## Slide 28
  Challenges of Designing for Space

## Slide 29: Why is Space Thermal Design a Challenge?
Satellites experience harsh environments in orbit, ranging from ~393K (full sun near Earth) for part (or all) of an orbit to ~3K in shadow/eclipse. This can cause drastic temperature changes on a satellite, where most critical parts (electronics/ electrical) want to be around ambient temperature range (253K-313K), resulting in cycling from one extreme to another over the life of the mission.
Science instruments may have challenging temperature requirements ranging from cryogenic (<120K) to ambient, with stability and gradient requirements as well.
Design must work for all on-orbit conditions as well as for ground operations, launch, ascent, calibration activities, thruster burns, and possibly re-entry.
UV
IR
Albedo
Direct Solar
Planet IR
29

## Slide 30: Thermal Environment(s) of Space
Space mission must consider external heating sources when developing a thermal design.
Direct solar heating is the greatest source of heating for most spacecraft
The solar energy reflected by a planet (albedo) and the outgoing longwave radiation (or Planet infrared energy emitted by a planet/moon/asteroid based on its temperature) is also considered when close enough to the planet or body.
For heliocentric orbits (i.e., orbits about the sun) that are sufficiently far from a planet or moon, albedo/Planet IR may be negligible:
  Geosynchronous orbit (unless cryogenic radiator)
  Interplanetary Cruise phase
Cold space itself (not to be neglected) is the cooling effect of deep space, with a background temperature around 4K
Free Molecular Heating (FMH):
  Typically encountered only during the launch phase, after fairing separation where sufficient atmosphere remains to cause heating due to high velocity impingement of the particles.
  While this is usually specified in the applicable launch vehicle user manual, included in an integrated analysis done by the launch vehicle provider, the thermal engineer must be aware of this type of heating to ensure the analysis accurately includes its effect.
Aeroheating: heating of a solid body produced by its high-speed passage through air (or by the passage of air past a static body), whereby its kinetic energy is converted to heat by adiabatic heating.
  Not typically done by GSFC (ARC, LaRC)
30

## Slide 31: Environment – Solar Irradiance
Solar irradiance is the primary heating source to be considered in thermal design for most satellites. The intensity varies with distance from the sun; inversely proportional to the square of the distance from the sun (energy from an expanding sphere).
  Min: 1316 W/m2
  Mean: 1367 W/m2
  Max: 1420 W/m2
Based on a series of measurements since 1969 that document the recognized mean (top of the atmosphere, or 30km above the Earth’s surface) solar irradiance value of 1367 W/m2. This value is then adjusted for the 1.67% eccentricity of the Earth’s orbit about the sun and for an accepted 0.4% measurement error, to arrive at a range of solar constant to be used as a reference for determining the solar constant for GSFC Earth missions.
31

## Slide 32: Environment – Albedo
Albedo is sunlight reflected off a planet or moon. This is usually expressed as the fraction of incident sunlight that is reflected back to space and is highly variable.
  A first approximation is that this reflection or “scattering” is Lambertian, or equal in all directions. The typical range of albedo values prescribed are:
  0.25 < ALB < 0.35 (orbit average)
Since this reflection actually is dependent on the solar zenith angle, it can vary significantly with latitude in the sunlit portion of the orbit and the view factor of the satellite surface to the reflecting planet surface.
  Reflectivity is greater over land as compared with oceans and generally increases with decreasing local solar-elevation angles and increasing cloud coverage.
  Because of greater snow and ice coverage, decreasing solar elevation angle, and increasing cloud coverage, albedo also tends to increase with latitude.
Another consideration is the thermal time constant of the various surfaces that receive albedo energy. A probabilistic assessment of these variations can be used if the thermal time constant of the system warrants it.
See: Spacecraft Thermal Control Handbook, David Gilmore, et al, Aerospace CorpVol 1, Chapter 2
June-July-August
December-January-February
32

## Slide 33: Environment – Planetary IR (aka OLR: Outgoing Longwave Radiation)
Sunlight incident on the Earth (that is not reflected as albedo) is absorbed and eventually re-emitted as IR energy or blackbody radiation.
  The typical range prescribed for near-Earth missions is:
  208 < OLR < 265 W/m2 [243K < TBB < 258K]
  But, Earth IR (EIR) should be calculated using the energy balance equation: EIR = (1 – ALB) x SOL/4.0A
  214 < EIR < 266 W/m2 [214K < TBB < 266K]
This IR heating is a combination of energy emitted from the planet/body surface being orbited, and any atmospheric gases/cloud cover that may be present.
  While local variations may be less severe than localized albedo variations, the IR spectral emission bands can be more complex. A probabilistic assessment of these variations can also be used if the thermal time constant of the system warrants it.
Noting that Diurnal variations for bodies like the Moon (85°K to 400°K) or Mars (138°K to 293°K) are much more significant. Values for other planets, moons, etc should be determined from available data and concurred with by the Thermal Branch.
33

## Slide 34: Orbit Mechanics - Sun (β) Angles and Spacecraft Orientation
GSFC missions have expanded tremendously from the initial Low Earth Orbits of the earth observation missions to geosynchronous, lunar, interplanetary, etc. Since the solar irradiance was just shown to likely be the singular most important external heating contribution for most satellite missions, knowing the orientation with respect to the sun is key.
  Beta (b) angle is defined as the minimum angle between the solar vector and the orbit plane, and is function of the nodal crossing, altitude and orbit inclination and can vary from -90° < b < +90°. Some missions are designed to be “sun-synchronous” with a more restricted beta angle range.
As important as b angle, is the spacecraft orientation
  Many non-LEO/GEO missions (such as Lagrange 1/Lagrange 2, Lunar, Mars, interplanetary, etc) may also include multiple mid-course corrections, which are typically longer thruster burns where the orientation of the spacecraft is driven by the thrust direction
  Furthermore, some more recent missions employ Solar Electric Propulsion, which often has long thrusting periods (with much smaller thrusts) where spacecraft pointing is dictated by thrusting needs and not thermal needs
An Excel spreadsheet-based beta angle calculator has been developed for use at GSFC by Dave Everett. The most recent version may be found on the ETD/545 WIKI. A similar capability is also included in the ThermalTextbook_v2.xls on the ETD/WIKI
Furthermore, a presentation on Orbital Mechanics for Thermal Engineers by Matt Garrison is also available on the ETD/545 Wiki (Thermal Engineering Mini Courses-Subsystem Courses)
Recommend that sun angles for interplanetary cruise be determined and provided by GNC (heliocentric trajectories).
34

## Slide 35: Beta Angle
 = 90°
0° <  < 90°
 = 0°
Summer Solstice
Winter Solstice
Autumn Equinox
Spring Equinox
35

## Slide 36: Eclipses
A = Orbit Altitude
Re = radius of the Earth
α
α
Re+A
Sunlight
36
During eclipses, both the solar loading and albedo drop to zero as the planet or body blocks the view to the sun. Therefore, during eclipse, Planet IR is the only environmental heat source

## Slide 37: Beta Angle & Eclipse Calculators
Created by Dave Everett, can be found on our wiki
Based on Inputs from Matt Garrison
37

## Slide 38: Geostationary Orbit
38
Many missions orbit in a Geostationary orbit, where the period is exactly equal to one Earth day and the orbit is in the equatorial plane.
These orbits have the advantage of observing the same ground location at all times as the satellite rotates with the Earth to remain fixed above the ground, relatively speaking
Due to the tilt of the Earth’s rotational axis relative to the normal to its orbit plane, the range of Beta Angles for Geostationary orbits is -23.4° to +23.4°
In general, the only consequential environmental source for Geostationary orbits is Solar. Albedo and Planet IR are usually negligible
Winter Solstice
Summer Solstice
Spring and Autumn Equinoxes
b=-23.4
b=+23.4
b=0
Solar Ecliptic
Earth Orbit

## Slide 39: Lagrange Points
39
Lagrange points are special locations in the solar system where the gravitational and body forces balance. These points are desirable for spacecraft since they require considerably less fuel to maintain their position
Note: image not to scale
Besides being optimum for fuel usage, the Lagrange points are also good thermal points as they present very stable and consistent environments
L1 is at about 0.99 AU. Note that spacecraft here will see full sun
L2 is at about 1.01 AU. Spacecraft here need to orbit outside of the shadow cone of Earth to allow for illumination of the Solar Arrays
Lagrange points also can generally neglect albedo and Earth IR environmental sources

## Slide 40
How are these Heating Sources Determined?
  Thermal software allows for the specification of orbital parameters (Beta Angle, Altitude, Spacecraft Orientation, Number of Orbit Positions, etc), that when combined with a Geometric Thermal Model can compute the absorbed heat loads from celestial sources
  Other sources that are sometimes included are:
  Free Molecular Heating: a near vacuum environment where stray molecules of gas may travel large distances before colliding and releasing kinetic energy
  Solar Wind: solar particle ejections that may release kinetic energy when colliding with surfaces
  Forced Convection (e.g. Fairing Air Conditioning): forced air flow by an air conditioning unit to cool a spacecraft while encapsulating in the fairing of the launch vehicle
  Natural Convection: circulation of air driven by buoyancy forces
  Some other terms used when representing orbits:
  Anomaly: the relative location of a vehicle in the orbit, expressed in °
  Nadir: in the direction of the body being orbited (usually a planet)
  Zenith: away from the direction of the body being orbited
  Eclipse: when the orbited object blocks the view of the
  orbiting object from the sun (Solar+Albedo=0)
  Terminators: points just before entering and exiting eclipse
  Orbit Noon or Subsolar Point: when the angle between
  zenith and the solar vector is at a minimum (usually 0° anom.)
  Orbit Midnight: when the angle between zenith and
  the solar vector is at a maximum (usually 180° anom.)

## Slide 41: Constraints and Verification of Space Designs
Space applications are challenging given constraints on mass, volume, and power that may not be considered in thermal designs for other fields…
  With a significant part of the cost of a mission driven by a launch vehicle, mass is a very important constraint in space design, as the satellite mass cannot exceed the launch capability of the rocket
  Also implied in the selection of a particular launch vehicle is volume, given finite sizes of the fairing atop a rocket which contains the spacecraft
  Power is also an important factor, as it directly drives the size and accommodation of a solar array for a spacecraft
Verification of space flight designs may also present challenges…
  The testing of a flight design needs to provide similar conditions as flight, including vacuum, cold space view simulators, and radiative environmental heating simulation
  The usage of devices whose performance relies on a micro-gravity environment can also be a driver in the thermal design of spacecraft, particularly for two-phase heat transport devices
  Lastly, the importance of testing to discover any workmanship or design flaws cannot be overstated. Options to fix a problem after launch are nearly non-existent…

## Slide 42
  Heat Transfer Basics Review

## Slide 43: Thermodynamics
Thermodynamics is the branch of physics that deals with temperature, heat, and work their relation to energy, entropy, and the physical properties of matter
Thermodynamics generally has four governing laws
  The zeroth law of thermodynamics defines thermal equilibrium and forms a basis for the definition of temperature: If two systems are each in thermal equilibrium with a third system, then they are in thermal equilibrium with each other.
  The first law of thermodynamics states that, when energy passes into or out of a system (as work, heat, or matter), the system's internal energy changes in accordance with the law of conservation of energy.
  The second law of thermodynamics states that in a natural thermodynamic process, the sum of the entropies of the interacting thermodynamic systems never decreases. A common corollary of the statement is that heat does not spontaneously pass from a colder body to a warmer body.
  The third law of thermodynamics states that a system's entropy approaches a constant value as the temperature approaches absolute zero. With the exception of non-crystalline solids (glasses), the entropy of a system at absolute zero is typically close to zero.
- From Wikipedia

## Slide 44: Heat Transfer
Heat transfer is a discipline of thermal engineering concerned with the generation, use, conversion, and exchange of thermal energy (heat) between physical systems.
The most common modes of heat transfer are:
  Conduction: the transfer of energy related to the vibration of molecules as a function of temperature
  Convection: the transfer of energy related to a moving fluid across a surface
  Radiation: the transfer of energy related to electromagnetic radiation generated by the thermal motion of particles in matter
One other matter to consider is the storage or release of energy as f(T)
All three of the common modes show up in the kitchen…
- From Wikipedia

## Slide 45: Conductive Heat Transfer
One-Dimensional Conductive heat transfer through a material is estimated as:
Q(T) = k(T) * Ax * DT / L
where:
Q(T) - heat flow (function of temperature)
k(T) - conductivity of material (function of temperature)
A - cross-sectional area
L - distance between two locations
DT – Temperature difference between two locations
Note: For many spacecraft applications the conductivity may be considered constant since it is essentially a room temperature system. Temperature dependence is necessary for low temperature modeling or when the temperature range varies drastically during the mission.
45

## Slide 46: Basics - Conduction Heat Transfer
All materials are conductive, but some have much better conductivity than others
  Metals vs. Non-metals
  Alloy differences can also affect thermal conductivity
The properties typically used for thermal analysis are: Density, ρ; Thermal Conductivity, k; Specific Heat, CP
Low conductivity materials used as isolators, while higher conductivity materials may be used as spreaders or heat straps
46

## Slide 47: Convective Heat Transfer
Convection heat transfer is described by the following equation:
  Q(T) = A * h(T) * (Ts - Tf)
  where:
  Q(T) - heat flow from position 1 to position 2
A - Surface area
    h(T) - convection coefficient or heat transfer coefficient
    Ts - temperature of surface
    Tf - temperature of fluid (aka Freestream Temperature)
    There are two main types of convection: free and forced
    For Free Convection, the motion is driven by buoyancy forces/gravity
    For Forced Convection, the motion is driven by an external fan or pump or the motion of the article in a fluid medium (e.g. aircraft)
    The value for h is generally a complex derivation that depends on geometry, fluid properties, velocity (forced) or buoyancy (free), flow type (laminar vs turbulent), etc
Note: For spacecraft applications, convection does not apply with some exceptions: re-entry/launch aeroheating, ground operations in ambient conditions, pumped fluid loops, lower altitude balloons (which are not quite the vacuum of space)
47

## Slide 48: Thermal Radiation
Thermal Radiation is perhaps the most complex mode of heat transfer, being electromagnetic radiation that is emitted solely based on temperature and requiring no intermediary medium.
It is governed by Planck’s Law, which computes the Spectral Irradiance as a function of Temperature and Wavelength
Where:
  B Spectral Irradiance (W/ m2 / str / um)
  l Wavelength in um
  h Planck’s Constant: 6.62607015E-34 J/Hz
  c Speed of Light in Vacuum: 3.0E8 m/s
  k Boltzman Constant: 1.380649E-23 J/K
  T Temperature in K
B(l,T) = 2hc2/ l5 / [exp(hc/lkT) – 1] * 1E6 um/m
(Multiply further by 4p steradian to get W/m2 um)
48

## Slide 49: Thermal Radiation - Blackbody
Planck’s Law can be further manipulated, integrating over all wavelengths, 0 to p/2 and 0 to 2p for a hemisphere and boils down to the Stefan-Boltzman Law, which states:
Where:
  P Total power emitted from a body per unit area
  s Stefan-Boltzmann constant: 5.67x10-8W/(m2K4)
  T temperature of blackbody surface (K)
Considering Q = P * A, the familiar Q=sAT4 falls out for the heat emitted by a blackbody as a function of temperature
A blackbody surface is an idealized concept where the surface is a perfect absorber and emitter of thermal energy.
Taking the Sun’s temperature as 5777 K, the Stefan-Boltzman law can be used to estimate the flux at Earth. Given the Sun’s radius of 696349 km and the distance of the Earth from the sun of 1.496E8 km, the flux at the solar surface can be estimated as 5.67E-8* (5777^4) * 4p(696349E3)2. However, by the time that flux through a given angular section reaches 1 AU, it has spread out over 4p(1.5E11)2
  So, taking 5.67E-8 * (5777^4) * 6963492/1.496E82 yields 1368 W/m2
P = sT4
49

## Slide 50: Radiation View Factors and Reciprocity
So far, the discussion around radiation has focused only on emitted energy, but not on energy exchanged (or transferred between two bodies). To address this, the concept of a View Factor is introduced which represents the percentage of the total field of view of Surface 1 occupied by Surface 2.
Q12 = s A1 F12 ( T14 - T24 )
Where:
    Q12 - heat flow from surface 1 to surface 2
    s - Stefan-Boltzman constant: 5.669E-12 W/cm2 K4 or 0.1714E-08 Btu/hr ft2 R4
    A1 - surface area associated with surface 1
    F12 - geometric view factor from surface 1 to surface 2
    T1 - temperature of surface 1 (in Absolute units K [C+273.15] or R [F+459.67] )
    T2 - temperature of surface 2 (in Absolute units K [C+273.15] or R [F+459.67] )
View Factors also follow a reciprocity rule where A1F12 = A2F21. This can be derived considering the heat absorbed by Surface 2 from Surface 1 as Q2 = s A2 F21 (T14). Likewise, the heat absorbed by Surface 1 from 2 is Q1 = s A1 F12 (T24). When the surfaces are at equal temperatures in equilibrium, the net energy exchange is zero (Heat from 1 to 2 [Q2] equals Heat from 2 to 1 [Q1]). Therefore A1F12 = A2F21
50

## Slide 51: Radiation – A bit More Complexity
Everything discussed up to now has been in terms of a black body. But no real surfaces are truly a black body…
Furthermore, if no surfaces are perfect emitters, then likewise no surfaces can be perfect absorbers
Energy emitted by Surface 1 and incident on Surface 2 will act in 1 of 3 ways:
  It will be absorbed (a)
  It will be transmitted (t)
  It will be reflected (r)
  This necessitates that a + t + r = 1.0
Energy reflected (or transmitted) may be done so either diffusely (scattered in all directions) or specularly (where the incidence angle = the reflective angle)
Specular Reflection
Diffuse Reflection
w
w
A diffuse surface is one that distributes an incident beam in all directions; A specular surface would reflect the beam such that the angle of incidence is equal to the angle of reflection.
51

## Slide 52: Real Bodies
52

## Slide 53: Multiple Real Bodies
53

## Slide 54: Radiation Heat Transfer – Gray Body
So, if a surface is not a perfect absorber or emitter, then a new term called emissivity (e) needs to be introduced. e represents the fraction of energy emitted by a surface based on its thermo-optical properties compared to a blackbody (where e = 1).
Q12 = s e1 A1 B12 ( T14 - T24 )
Where:
    Q12 - heat flow from surface 1 to surface 2
    s - Stefan-Boltzman constant: 5.669E-12 W/cm2 K4 or 0.1714E-08 Btu/hr ft2 R4
    A1 - surface area associated with surface 1
    e1 - emissivity of surface 1
    B12 - interchange factor from surface 1 to surface 2 (aka Script F)
    T1 - temperature of surface 1 (in Absolute units K [C+273.15] or R [F+459.67] )
    T2 - temperature of surface 2 (in Absolute units K [C+273.15] or R [F+459.67] )
The geometric view factor is now replaced with an interchange factor (also called a Script F), which accounts for the Gray body nature of the surfaces in the Field of View
ei Ai Bij often referred to as a Radk or GR
54

## Slide 55: Radiation Heat Transfer – Gray Body
Consider a perfect cube, with the bottom having an e of 0.9, the sides having an e of 0.1 and the top being open to deep space.
The view factor from any one side to any other in a cube has a closed form solution of 0.2.
Start with 0.9*0.2 to Node 2 from Node 1 = 0.18
Of the 0.18, 0.1 gets absorbed by node 2, 0.162 gets reflected from 2
Of the 0.162 that gets reflected:
0.162*0.2*1 goes to space
0.162*0.2*0.9 gets absorbed by 1, 0.162*0.2*0.1 is reflected by 1 …
0.162*0.2*0.1 gets absorbed by 3, 0.162*0.2*0.9 is reflected by 3 …
0.162*0.2*0.1 gets absorbed by 4, 0.162*0.2*0.9 is reflected by 4 …
0.162*0.2*0.1 gets absorbed by 5, 0.162*0.2*0.9 is reflected by 5 …
As can be seen, the book-keeping to handle reflected energy to generate the interchange factor quickly becomes unwieldy without computer aid…
55

## Slide 56: Determining the View/Interchange Factor
The radiation interchange between surfaces is determined by the geometry of the surfaces, their orientation with respect to each other, and their thermo-optical properties
  View factors between these surfaces must be determined (this is needed in both heat transfer and applied optics)
  Although some materials have directional or spectral properties of reflection, some approaches only handle diffuse surfaces
  A diffuse configuration factor is the fraction of uniform diffuse energy leaving a surface that reaches another surface
There are several methods for calculating view/interchange factors:
  Nusselt unit sphere
  Hemicube
  Direct integration
  Monte Carlo Ray Tracing (Discussed in the Thermal Analysis Section)
Hand calculations may be suitable for simple geometries, but more complex interactions often require computer algorithms
56

## Slide 57: Computing View Factors
For those that love doing integrals, the formulas for radiation view factors for some simple geometries can be derived.
Some of these calculations have been tabulated in several references on heat transfer (e.g. Holman, 1986) or the NACA handbook. They range from ~zero (e.g. two small bodies spaced very far apart) to 1 (e.g. one body is enclosed by the other)
These calculations are possible for simple geometries, but the typical satellite has many surfaces that interact “radiatively”
Thermal software platforms are used to generate radiation views to space and between the many satellite surfaces. A typical satellite geometry model has 5000-20000 surfaces with calculated radiation view factors numbering in the 100s of thousands into the millions
57

## Slide 58: Computing View Factors
58

## Slide 59: Spectral Dependence of ThermoOptical Properties
As discussed earlier, there are two main external sources of heating on a spacecraft: Solar (incl Albedo) and IR (Planet and Spacecraft Surface radiation)
Plotting the Spectral Irradiance for varying temperatures shows the differences in the radiation wavelengths for solar heating vs. IR heating
This is important considering that absorptivity is also wavelength dependent
Essentially, the properties can be banded into the IR a, t, r and the Solar a, t, r
For thermal equilibrium, e = a
UV: 0 – 0.38 um
Vis:0.38-0.7 um
IR: 0.7 to 1000 um
For Thermal properties:
Solar: 0.25 – 2.7 um
IR: 2.7-1000 um
SOLAR
IR
59
Left Axis
Right Axis

## Slide 60: Spectral Coating Example
Examine the spectral properties for NS43G white paint for emittance (60-300 K) and reflectance (0-2.4 um) from NASA/TP–2005–212792
Note that the integration for emittance as a function of wavelength has already been done to yield an emittance as a function of temperature
But the reflectance from 0.2 to 2.4 um (200 nm – 2400 nm) yields about 0.74 when integrating the area under the curve
This gives a gray body solar absorptivity of about 0.26
60
e
r

## Slide 61
Radiation Summary
Radiation is a very important mode of heat transfer for spacecraft
    Radiation – electromagnetic waves of energy emitted as a function of temperature and absorbed by other surfaces
    Thermal Radiation is emitted in all directions from all objects above 0 K
    Higher temperature objects (like the sun) emit far more radiation than colder objects
      Furthermore, the radiation is emitted over a range of wavelengths and the profile depends on the temperature of the emitting surface
    Emitted energy that reaches a surface is either reflected, transmitted, or absorbed
    The thermo-optical properties which govern these relations are also wavelength dependent
    Typically, thermal assumes grey-body behavior, meaning that the absorptance, reflectance, and transmittance are all wavelength independent over the expected wavelengths for a mission
      Thermal typically works in a for absorptance in the solar spectrum and e for absorptance in the IR spectrum
      a is the difference between a black shirt (high a) and a white shirt (low a) on a hot day
      e is also used for emission in the IR spectrum, where most spacecraft tend to operate (we are not as hot as the sun)
    The view factor (% of 360° hemispherical field of view) to the emitting source also plays a large role in the energy transfer
    Just because the sun is in our field of view does not mean it occupies the entire field of view
      Much of our field of view in orbit is to deep space, with a background temperature of around 4 K
      Hence, we can still reject heat to the overall effective cold temperature even when viewing the sun

## Slide 62: Special Heat Transfer Considerations
Interface Conduction:
The heat transfer across a joint or interface can be a mixture of
conduction, radiation, and convection. However, in most cases it is modeled as only a conductive process and the heat flow is described by:
Q = Ac hif DT
Where:
hif - interface conductance
Ac - contact area
DT – Temperature difference between two locations
Interface conductance is a function of materials, temperature, contact pressure, and surface finish. An interstitial or filler material (i.e. ChoTherm, Nusil, eGraf, Grafoil, indium foil, gold foil) can be used to enhance interface conduction. Typical ranges 0.1 to 2 W/in2 K (Bare Joint to Good thick filler)
62

## Slide 63: Special Heat Transfer Considerations
Radiation Through Blankets
Heat transfer through a blanket is modeled as radiation using
the following equation:
Q = s A e* ( Ti4 - To4 )
Where:
e* - effective emissivity of the blanket (typically 0.01 – 0.05)
  s - Stefan Boltzman Constant (5.67E-8 W/m2 K4)
  A - area of the blanket (m2)
  Ti - absolute temperature of the inner layer (K)
  To - absolute temperature of the outer layer (K)
Can’t narrow the e* range until testing
“Stack” parameters for analysis
63

## Slide 64: Special Heat Transfer Considerations
Backloading or Equivalent Sink Temperatures
Sometimes, the radiative environment around a component or instrument is specified for design purposes. This may be the case for an instrument or component, where the accommodation on a particular spacecraft is represented by a set of heatloads (Backloads) or temperatures in particular directions (Equivalent Sinks)
For example, a spacecraft vendor might specify the effective temperature scene for 6 sides of box that surrounds the component. These temperatures would then be used for design purposes to locate radiators or blankets based on the optimum directions for heat rejection
Similarly, later in the project life cycle when some models have been delivered, the spacecraft vendor may provide the incident IR radiation from all surrounding surfaces on the component as Backloads, to allow representation of the integrated environment in a stand-alone component model.
The equations for both are shown below, where the summation is for all j where j is not a part of the component and each i is a part of the component:
QBL = S (s Radkij Tj4) and Tsink = [S {(s Radkij Tj4) + Qenv} / S (Radkij) / s ]0.25
This technique is often applied when a spacecraft vendor does not wish to provide a complex, integrated model to component vendors
64

## Slide 65: Special Heat Transfer Considerations
Energy Storage/Release
As heat is added to an object, the rate of its temperature rise is governed by its mass and specific heat. This represents an energy storage when the temperature increases
Conversely, when an object cools, it releases some of the energy it had stored while at the higher temperature
Energy storage is governed by the equation:
Qstored = m * Cp * dT/dt
This energy storage plays an important role in transient analyses. For steady state analysis, the dT/dt term is zero (i.e. constant T) and no energy is stored or released
A special case of energy storage can also be found in phase change (Solid to Liquid, Liquid to Vapor). Recall from Thermodynamics that phase change is an isothermal process (i.e. constant temperature)
  In space thermal applications, phase change is used in two phase devices such as heat pipes, where the waste heat from avionics is used to vaporize a liquid at the evaporator end. The vapor is transported via small pressure differences to the condenser end, where it releases its energy as it condenses back to liquid. This end is connected to a radiator to reject the heat to space. A wick structure then uses capillary forces to transport the liquid back to the evaporator
  A second space-based phase change application is the use of paraffin wax to provide a short term heat sink or a longer term thermally stable interface using a solid-liquid phase change process in a hermetically sealed container
65

## Slide 66: Putting it all together
Combining the principles of Thermodynamics and Heat Transfer, the thermal performance of a spacecraft can be evaluated
Beginning with the 1st law and Conservation of Energy for a Control volume:
dU/dt = Q – W : Change in internal energy = Heat - Work
For a system with no work (typical for a spacecraft)
Qstored = Qin – Qout + Qgenerated
Recognizing that the Qin and Qout terms may be composed of heat transfer relations (such as conduction in and radiation out):
m CP dT/dt = kA/L*(Text - TCV) – sAe(TCV4 – Tspace4) + Qgenerated
Note that for thermal equilbrium (steady state), dT/dt = 0, therefore:
0 = kA/L*(Text - TCV) – sAe(TCV4 – Tspace4) + Qgenerated
The discretization of a thermal design into many control volumes, the generation of all the heat transfer paths between these control volumes (Radiative, Conductive, Convective) and accounting for the heat generation is the foundational basis of thermal analysis
66

## Slide 67: Three Forms of Heat Transfer on a Satellite
Note: For many thermal designs, radiation is negligible, with temperature differences are too small to make meaningful contributions to the overall heat flows. However, for spacecraft, with a surrounding effective background temperature of about 4 K, radiation is the only mode for the rejection of waste heat from the system since conduction and convection to a vacuum are not possible
67

## Slide 68: Energy Balance: Satellite
68

## Slide 69: Energy Balance: Satellite
69
Note: AP is Projected area normal to source vector assuming uniform flux

## Slide 70: Square Spacecraft Bus Example
Consider a square spacecraft bus, 1.5 m to a side and 0.75 m tall.
Assume the panels are painted white with a =0.21 and e=0.89
Assume a max temperature of 35°C for heat rejection and a radiator efficiency of 80%.
This SC is orbiting the Sun-Earth L2 Lagrange point and has a field of regard that allows for a ±45° rotation about an axis out of the page
Assuming a Solar Constant of 1419 at Earth, which orientation yields the best over all heat dissipation rejection capability? What is the distribution per bay for each configuration?
a
b
c
d
a
b
c
d
70

## Slide 71: Square Spacecraft Bus Example
Begin with a simple energy balance at steady state:
0 = Qsolar - QRadiated + QDissipated
Qsolar is based on the absorbed solar load. The absorbed solar flux is (q” * A * a) = 1419 * (1/1.01)2 * (1.5*0.75) * 0.21 = 328.63 W for a fully illuminated side (e.g. a, left). For the angled sides, the flux is reduced by the cosine of the angle 328.63 * cos(45) = 232.39 (e.g. a,b right).
Note that with the allowed ±45° rotation, the worst case for each bay is:
  Left: a full, b 45, c none, d 45
  Right: a full, b full, c none, d none
a
b
c
d
a
b
c
d
71

## Slide 72: Square Spacecraft Bus Example
The heat that is rejected is based on the simple radiation formula:
QRadiated = s * A * e * (TRad4 – Tspace4)
TRad is an adjusted temperature based on the efficiency where h = TRad4 / Tmax4 (remember to use K !). TRad = (h*(Tmax+273.15)4)0.25 -273.15 = 18.3°C
Solving for QRadiated = s * A * e * (TRad4 – Tspace4) = 5.67E-8 * (1.5*0.75) * 0.89 * ((18.3+273.15)4 – (4)4) = 409.56 W
Note that the heat rejected does not need to be adjusted for orientation since space is in all directions, unlike the solar flux which is directionally dependent
a
b
c
d
a
b
c
d
72

## Slide 73: Square Spacecraft Bus Example
The worst case for each bay will be considered independently, even though the maximum illumination of one bay does not occur simultaneously with the maximum illumination of another
This is needed since any components in a given bay need to remain within temperature limits over any and all orientations throughout the mission
QDissipated is what capacity remains for a given bay after rejecting the absorbed solar load. It should be noted that only the QRejected is dependent on temperature; QSolar is not. If the rejection temperature is too low, it may not be possible to reject the absorbed load; consequently, the temperature may need to be higher to be in equilibrium
a
b
c
d
a
b
c
d
73

## Slide 74: Square Spacecraft Bus Example
For the left design, the QDissipations are:
  a: 409.56 - 328.63 = 80.93 W
  b,d: 409.56 - 232.39 = 177.17 W
  c: 409.56 - 0 = 409.56 W
  Total: 844.83 W
For the right design, the QDissipations are:
  a,b: 409.56 - 328.63 = 80.93 W
  c,d: 409.56 - 0 = 409.56 W
  Total: 980.98 W
a
b
c
d
a
b
c
d
74

## Slide 75: Square Spacecraft Bus Example
So, the right design is the clear winner, correct?
  Not necessarily. Note that the heat rejection capabilities of right bay a,b are markedly less than c,d. If you had components whose dissipations exceed 81 W, they could not go in those bays
  However, this limitation only applies to bay a in the left design. So, the optimum design depends on more than just the ability to reject heat, it also depends on the ability to lay out the components in the design
  Another consideration is heater power for cold cases. It is likely that the right design would only need heaters for a,b (since c,d) never see sun, whereas the left design may need it for a, b, and d.
a
b
c
d
a
b
c
d
75

## Slide 76
  Thermal Design Process

## Slide 77
Thermal Design Process Flow

## Slide 78: Gathering Necessary Thermal Inputs
Thermal requires inputs from other subsystems that fall into one of 5 categories:
  Component Operating and Non-operating Temperature Limits
    These should not come from thermal predictions
    They should be based on optimum performance of the component
  Component Waste Heat Dissipations
    Thermal responsible for transferring waste heat to be radiatively rejected to deep space
  Physical Layout of Components
    CAD layout of the design
    Often constrained by available packaging volumes, optical design, or electronics proximity requirements
  Flight Orientation and Orbital constraints
    Low Earth Orbit? Interplanetary? Lagrange Point? Sun Pointing? Field of Regard?
    These mission high level requirements dictate where solar system heat sources are
    The consequence is a limitation of optimum locations for radiative waste heat rejection
  Stability or Gradient requirements
    May require more complex heater control or additional non-structural material
The thermal design may begin once these are known, but sometimes it is necessary to start with some placeholders and assumptions…

## Slide 79: Op and Non-Op Limits
Component Operating and Non-Operating Temperature Limits
  Temperature limits should be specified by the responsible hardware engineer. In essence they represent an agreement that if thermal maintains the hardware within limits, then the performance should meet specifications
  These limits will often be referred to as Allowable Flight Temperatures (AFTs)
  Recall that temperature limits are one of the five inputs thermal needs to do a design. Therefore, it is not realistic to base limits on design predicts
  However, there will likely be times where the initial thermal limits were specified to a wider range and the thermal design predicts them to be well within that range (e.g. considerable margin exists)
  For these cases, it is reasonable to question if the test campaign needs to go all the way to the original limits or if the temperature limits could be adjusted based on thermal predicts.
  It’s a fair question, as there is little benefit in over testing hardware beyond its expected flight range
  That said, if using limits from a previous mission without understanding this evolution, it is possible that subsequent missions may need a wider range than the previous mission
  Once a component has undergone testing, it may make sense to adjust the limits to the levels seen during the testing campaign. Typically, the widest temperature levels are seen at the lowest test level
Component Limits may not remain the same throughout a project’s lifecycle. Thermal may push back against limits if they become too difficult to accommodate or if hardware changes necessitate narrower limits. The later in the lifecycle this occurs, the more of an impact it may have. Systems must be involved!

## Slide 80: Op and Non-Op Limits (Common Hardware)
Courtesy of Kan Yang and the Instrument Design Lab (IDL), here are some typical values that can serve as a starting point before specification by the responsible engineer:
Component | Typical Temperature Ranges (°C) |  |  |  | Stability range (°C, if applicable)
 | Operational |  | Survival |  | 
 | Min | Max | Min | Max | 
Electronics Boxes (Including Cryocooler Control Electronics, Digital Signal Processors, and Laser Control Electronics) | -10 | 40 | -40 | 60 | 
Antennas | -100 | 100 | -120 | 120 | 
Batteries | 0 | 25 | -10 | 35 | 
Mechanisms | 10 | 40 | -40 | 60 | 
Optical or Laser Bench (Near-IR, Visible, UV; often require stringent thermal stability) | 5 | 35 | -20 | 40 | ± 2
Lasers (often require stringent thermal stability) | 20 | 40 | -20 | 60 | ± 1
RF Components (Analog) | -10 | 40 | -25 | 60 | ± 2
Cryocooler Thermo-Mechanical Units | 5 | 45 | -35 | 70 | 
X-Ray Sources | 0 | 30 | -20 | 50 | 

## Slide 81: Op and Non-Op Limits (Common Hardware)
Some additional estimated limits for common hardware provided by Eric Grob (Former 545 Chief Engineer):
Component/Subsystem Operating Temp (°C) Survival Temp (°C)
Digital Electronics 0 to 50 -20 to 70
Analog Electronics 0 to 40 -20 to 70
Batteries 10 to 20 0 to 35
Infrared Detectors -269 to –173 -269 to 35
Solid-State Particle Detectors -35 to 0 -35 to 35
Momentum Wheels, Motors 0 to 50 -20 to 70
Solar Panels -130 to 125 -130 to 125
Thruster Valves (non-firing) 0 to 40 -10 to 50
Propulsion Tank 0 to 40 -10 to 50

## Slide 82: Op and Non-Op Limits (Detectors)
Courtesy of Kan Yang and the IDL, here are some typical values for detectors that can serve as a starting point before specification by the responsible engineer:
Wavelength Range | Portion of Electromagnetic Spectrum | Example Detector Types | Typical Operational Temperatures (K) |  | Thermal Stability Requirements | 
 |  |  | Low | High | More Stringent | Less Stringent
> 1 mm | Microwave and RF | Microwave / RF Receivers | 260 | 310 | ± 0.1 | ± 2
25 um - 1 mm | Sub-mm wavelengths / Terahertz range | Heterodyne Receiver (SIS, HEB), TES bolometers | < 1 | 40 | ± 0.1 | ± 1
2.5 um - 25 um | Mid-Infrared to Far-Infrared | HgCdTe, TES, Ge:Ga Photoconductors | < 1 | 100 | ± 0.001 | ± 1
750 nm - 2.5 um | Near-Infrared | HgCdTe, InGaAs, InSb, STJ, TES, Si<1100nm | 50 | 170 | ± 0.001 | ± 1
400 nm - 750 nm | Visible | Si CCD, Si CMOS, photodiodes, STJ | 170 | 340 | ± 0.005 | ± 1
1 nm - 400 nm | Ultraviolet | GaN, MAMA, Microchannel | 270 | 340 | ± 0.005 | ± 1
 | Ultraviolet | EMCCD, CCD, CMOS | 170 | 200 | ± 0.001 | ± 1
1 pm - 1 nm | X-Ray | Gas-filled, Scintillation, Microchannel, CdZnTe | 270 | 330 | ± 0.1 | ± 5
 | X-Ray | CCD, CMOS | 170 | 200 | ± 0.001 | ± 1
 | X-Ray | TES | < 0.1 | 1 | ± 0.0005 | < ± 0.001
< 10-12 m | Gamma Ray | CMOS, Scintillator, CsI, SiPM, CCD, Strip Detectors | 80 | 300 | ± 0.1 | ± 1

## Slide 83: Waste Heat Dissipations
Component Waste Heat
  Uncertainty in heat dissipation is by far the largest contributor to temperature uncertainty
  Typical to get Current Best Estimate values (CBE) and use these for cold cases (minimum dissipation)
  If no Allocation or Maximum Expected Value (MEV) is available, an uncertainty of 30% is often applied and used for Hot Cases
  In the case of an active cooler (ThermoElectric, CryoCooler), the dissipation often depends on the heat removed and can be estimated from device performance curves based on the Cold Tip Temperature, Heat Lift, Reject Temperature, and Input Power
  Most components have a relatively constant dissipation, with some notable exceptions:
    Transponders have Receive and Transmit modes
    Batteries only dissipate waste heat when there is a load (i.e. during eclipse)
    Reaction Wheels dissipate less in an idle mode than when spun up to slew the spacecraft
  Some component types work together and may have co-location requirements
    Ka band Transmitter and Travelling Wave Tube Amplifiers (TWTA) and Electrical Power Conditioner (EPC)
    Star Trackers and Inertial Reference Units (often co-located on an optical bench with stability rqmts)
    Magnetic Torque Bars may be used along with a Three Axis Magnetometer

## Slide 84: Common Spacecraft Waste Heat Dissipations
Many spacecraft have common hardware architectures
However, the power dissipations tend to be very mission specific
  Transponder power depends on distance to receiving asset (Ground Station, TDRS, DSN) as well as data rates and volumes
  Reaction Wheels depend on the mass of the spacecraft to slew and the rates required
  Batteries and Power Control Units depend on the loads of the attached avionics units
  Command and Data Handling Units depend on the amount of processing needed
That said, below is a list of common spacecraft avionics to consider, even if the power dissipations cannot be estimated without further inputs
  Avionics: Command and Data Handling (CDH), Solid State Recorder (SSR), Deployment Safety Inhibits
  Mechanisms: Mechanism/Gimbal Control Electronics (MCE/GCE), Actuators
  ACS/GNC: Reaction Wheel Assemblies (RWA), Wheel Drive Electronics (WDE), Inertial Reference/ Measurement Unit (IRU/IMU), Star Tracker (may include separate Camera Head and Data Processing Unit), Three Axis Magnetometer* (TAM), Magnetic Torquer Bar (MTB)*, GPS Receiver*
  Communications: Transponder (Transmitter/Receiver) [Ka, K, S, X bands], Traveling Wave Tube Amplifiers (TWTA), Electrical Power Conditioner (EPC)
  Power: Battery, Power Switching Electronics (PSE), Power Distribution/Conditioning Unit (PDU/PCU)
  Propulsion: Pressure Transducers, Catbed Heaters, Latch Valves
  Instruments: Main/Instrument Electronics Box (MEB/IEB), Cryocooler Electronics (CCE)
* Earth Orbiting

## Slide 85: Physical Layout (CAD)
Physical Layout of Components
  The Mechanical Engineer is most often responsible for packaging all the components necessary for an instrument or spacecraft
  Thermal should provide inputs as to location preferences (e.g. high dissipation box near to radiator, isolated battery with its own dedicated thermal control system)
  However, Thermal Engineers should realize other constraints on packaging
    Launch orientation and Aligning center of mass with Launch vector
    Center of Gravity location for Attitude Control System
    Fairing volume constraints
    Harness routing space allocations
    Optical/RF layouts (often beyond the Mechanical Engineer’s purview to change)
    Proximity requirements between detectors and readout electronics
    Clear Field of View constraints or locations reserved for deployable components
Work closely with the Mechanical Engineer early
  Accommodations are much easier to incorporate early in the design before it coalesces
  Obtain CAD geometry early, even as the design is changing frequently, to update the thermal model, but realize it may be a struggle to keep the thermal model up to date with the current layout.

## Slide 86: Flight Orbital and Orientation Constraints
Flight Orbital Constraints considered over the entirety of the mission
Some terminology and customs to know:
  Ram (Velocity) is often in +X, Wake (Anti Velocity) is often –X
  +Z is often Nadir (Planet pointing), -Z is often Zenith (Anti Planet)
  These two orthogonal vectors define the Y axis
  Rotations about X: Roll, Y: Pitch, Z: Yaw
Best to first begin with orbital constraints for the majority of mission…
  Altitude
  Launch Date
  Orbit Inclination, Right Ascension of Ascending Node, Beta Angle Range
  Pointing constraints: Nadir pointing? Field of Regard?
  Is a 180° yaw flip maneuver utilized at b=0 crossings to provide a dedicated “Cold” side of the spacecraft?
Then consider off nominal cases…
  Launch Profiles (Possible BBQ rolls of Launch Vehicle)
  Calibration Maneuvers
  Safe Hold Modes
  Avoidance maneuvers (Sun, Moon, etc)
  Cruise mode (interplanetary, Lagrange orbits)

## Slide 87: Gradient and Stability Requirements
Gradient and Stability Requirements often require careful consideration by the Thermal Engineer
Gradient Requirements are often expressed as a maximum allowable temperature difference between two spatial points
  Gradient requirements often derived from structural analysis and driven by either misalignments (typically of optics) or thermal stresses during cooldowns
  Try to avoid accepting gradient requirements between ANY two points. This is too arbitrary and if someone wants to specify a gradient requirement, they should do the work to determine where the requirement should be levied
Stability Requirements are often expressed as a maximum allowable temperature variation over time.
  0.1 K stability is NOT a requirement!! 0.1 K over 10 minutes is…
  Be sure to understand if it is 0.1 or ±0.1…this sometimes gets lost in translation
  Stability requirements often levied for detectors or optics to reduce signal noise
  Generally requires a more precise heater control scheme than thermostats provide

## Slide 88: First Questions
Once all requirements are known, a few questions should form in your mind:
  How many thermal zones are needed? Can any components be co-located to simplify the thermal design?
  What range of b angles need to be considered? Is there a dedicated “cold” side of the observatory based on orbital mechanics?
  Where should the radiator(s) be located? How will the heat be transported to the radiators (e.g. Directly coupled to backside? Heat Strap? Heat Pipe? )
  What coatings are needed and where?
  What size do the radiators need to be to stay below the upper operating limit with some power contingency?
  Do any components need active cooling (e.g. TEC, CryoCooler)?
  What areas might require thermal isolation/insulation in the design?
  How many heater zones are needed to stay above lower operating limits?
  Are there any challenging stability or gradient requirements that will require complex control or additional thermal considerations (e.g. optical bench)?
  Where are sensors needed for thermal control or knowledge?
  Is the design concept ground testable?
But before beginning to formulate a design to answer these questions, it helps to know what thermal components could be used to meet requirements…

## Slide 89
  Available Thermal Components

## Slide 90
Thermal Design Components for Space Applications
Radiator
Thermal Coatings
Heater
Thermostat
Multi Layer Insulation
Radiative Isolation
Interface Materials
Constant Conductance Heatpipes
Variable Conductance Heat Pipes
Loop Heat Pipes
Heat Straps
Thermistor
Platinum Resistance Thermometer (PRT)
Thermocouple
Silicon Diode
Cryo Cooler
Thermo Electric Cooler
Doublers and Spreaders
Annealed Pyrolytic Graphite Parts
Heat Switch
Louvers
Phase Change Materials
Mechanically Pumped Loops
90

## Slide 91
  Radiator – a dedicated structure whose purpose is the rejection of waste heat to deep space
  Coated with high emissivity coating to maximize heat rejection potential
  May be coated with high or low solar absorptivity coating depending on view to solar sources
  If not existing structure, then supports are needed
Coatings – films, tapes, paints, etc. applied to surfaces to obtain the desired thermo-optical properties for thermal control
  Thermo-optical properties are intrinsic to the material itself (e.g. white paint, black paint, Kapton, etc) a – Solar Absorptivity – percentage of sun energy (Direct Solar, Albedo [e.g. reflected solar]) absorbed
  e – IR Emissivity – percentage of planet energy (Planetshine) absorbed
    Also a measure of emissive capability of a surface to reject heat via IR radiation
Radiator and Coatings
Radiator with White Paint Coating
91

## Slide 92
Heater – an electrically resistive device which dissipates heat when a current is passed through it
  Typically either a Kapton-enclosed circuit or Dale-Ohm, cartridge style
    Kapton heaters often contain two traces for independent circuits. Typically applied with adhesive and overtaping with Aluminum Tape to minimize possible local hot spots. Watt density drives overall size of heater based on adhesives used
    Dale-Ohm heaters typically applied with adhesive and bolted to structure. Two units required for redundancy
  GOLD rules requires thermal to demonstrate maximum of 70% of power usage in cold cases at minimum voltage as specified by project (or 5°C of margin to lower limits)
    At maximum voltage, current draw and watt density become limiting factors
  Heater is energized by relay (software controlled switch) or thermostat (mechanical switch)
Heater
Kapton Thin Film Heater
Dale-Ohm Heater
92

## Slide 93
  Thermostat – a device with two materials with dissimilar Coefficients of Thermal Expansion that opens or closes an electrical circuit based on temperature
  Mechanical part that can wear, but usually takes > 100,000 cycles before failure
  Typically have two thermostats wired in series to prevent a single failed closed thermostat from continuously energizing a circuit
    If failed open, redundant side of spacecraft or instrument takes over
    Could also have quad-redundant which is two parallel sets of two series thermostats (can tolerate one failed open or one failed closed without having to switch sides)
  Typically bonded to structure near the location of temperature interest
  Deadband between open and close point usually around 5-7°C (9-13°F)
  High current design (3-5 A) different than lower current design (<3 A)
  Long lead time for procurement, need to know setpoint range before buying
Thermostat
Thermostats Installed on Panel
Thermostats
93

## Slide 94
  MLI – Multi Layer Insulation – aka blankets – lightweight covering of structure that impedes heat flow
  Typically alternating layers of Dacron/Nylon mesh and Vapor Deposited Aluminum (VDA) mylar sheets with outermost layer typically Kapton/Black Kapton/Germanium Black Kapton/Stamet
  Edges either stitched or taped
  Grounding wires included in design; may help with EMI/EMC
  Sometimes, Kevlar is included in blanket layup for Micrometeoroid protection
  Mechanically supported by buttons, velcro, tie-downs, or double sided transfer adhesives (e.g. tapes)
  If it is not a radiator, aperture, or mechanism, thermal probably wants a blanket there…
Multi Layer Insulation (Blankets)
Multi Layer Insulation
Multi Layer Insulation Layup
94

## Slide 95
  Radiative Isolation – this is not so much a component, but an alternative to Multi Layer Insulation
  MLI is most often used for larger scale components
  For much smaller components (a few inches), a blanket may not be a practical solution since the seams at the edges are typically the poorest performing part of the blanket
  Furthermore, blankets around tight corners also do not perform nearly as well as large, flat spaces
  Therefore, for radiative isolation of smaller parts, typically SLI (Single Layer Insulation) with low emissivity coatings (such as Vapor Deposited Aluminum: VDA) is used instead
  Alternatively, a coating may also be applied to the part (such as Vapor Deposited Gold or Aluminum) rather than using a sheet of SLI
  In either case, the general idea is to have a low emissivity/high reflectivity surface that reduces the amount of heat absorbed from the surroundings
Radiative Isolation
95

## Slide 96
  I/F Materials – materials at interfaces (I/F) between components that improve heat flow; generally work better with increased pressure at contact area
  NuSil – paste like filler, a bit “messy” to install, very good thermally, poor electrically
  ChoSeal – sheet like filler, cut to shape, easy to install, good thermally, good electrically, retorque
  ChoTherm – sheet like filler, cut to shape, easy to install, good thermally, poor electrically, retorque
  eGraf – sheet like filler, cut to shape, easy to install, not-reusable, good thermally, OK electrically
  Stycast, Eccobond, Arathane – bonding adhesive for thermostats, heaters, and thermistors
Interface Materials
Nusil After Installation
Nusil Installation
Cho Therm
eGraf
96

## Slide 97
Constant Conductance Heat Pipe (CCHP)
CCHP – Constant Conductance Heat Pipe – a passive, sealed system with no moving parts which utilizes an evaporation / condensation cycle to transport heat
  Source heat evaporates working fluid (often ammonia) into vapor state
  Pressure differences push vapor to cold end
  Cold end typically tied to radiator where it condenses back to liquid and releases heat
  Capillary wick transports liquid back to evaporator end
    Since capillary forces are weaker than gravity, heat pipe must be level during ground testing to function
    Can operate in reflux mode, where gravity is the force that makes liquid return to evaporator, but this necessitates that the evaporator is below the condenser
    Non-planar (3D) CCHPs are difficult to ground test and their use is not recommended by the branch
Constant Conductance Heat Pipe (CCHP)
Flexible CCHP
Heat Pipe Extrusions
97

## Slide 98
Variable Conductance Heat Pipe (VCHP)
  VCHP – Variable Conductance Heat Pipe – a sealed system which utilizes an evaporation/ condensation cycle to transport heat; includes a cold biased reservoir of Non-Condensable Gas (NCG) and a heater to regulate effective length of condenser
  Same basic operating principles as CCHP
  Reservoir at condenser end is filled with NCG and includes a wick structure to transport condensed working fluid from reservoir back to pipe
  When sensed temperature at evaporator is below setpoint…
    Heater turned on at reservoir…reservoir temperature increases…pressure increases pushing NCG into pipe…NCG impedes condensation and reduces available length for heat rejection…evaporator temperature increases
  When sensed temperature at evaporator is above setpoint…
    Heater turned off at reservoir…cold biased…reservoir temperature decreases…pressure decrease allows NCG to recede back towards reservoir…increases available length for heat rejection… evaporator temperature decreases
Variable Conductance Heat Pipe
QOUT
QIN
Transition Tube
Variable Conductance Heat Pipe Schematic
98

## Slide 99
LHP – Loop Heat Pipe – a loop system which utilizes an evaporation/condensation cycle to transport much more heat than a CCHP and maintain control temperatures to ±1°C
  Wick structure in evaporator transports liquid through evaporator. Source heat evaporates working fluid (often ammonia) into vapor state
  Pressure differences in evaporator drive vapor through vapor line to condenser
  Condenser typically tied to radiator where vapor condenses back to liquid and releases heat
  Liquid return line transports liquid back to evaporator driven by capillary pressure difference from evap wick
  Compensation chamber is a pressure regulated reservoir that can add or remove working fluid from the flow loop in response to operating temperature/power changes
    Wick structure transports liquid between compensation chamber and evaporator
    Since only the evaporator contains the pumping wick structure, an LHP is more flexible to accommodate ground testing. Entire LHP does not need to be level, only the evaporator
  Expensive option, but very flexible and adjustable in flight to varying source and sink configurations
    Often requires dedicated controller circuit
    Requires heaters to induce start up of loop
    Could also require accommodation to prevent freezing of sub-cooled liquid returning from condenser
Loop Heat Pipe
Loop Heat Pipe (LHP) Schematic
Loop Heat Pipe and Radiator System
Loop Heat Pipe CAD Layout with Radiator
99

## Slide 100
  Heat Strap – flexible laminate of thin foils or braids of high conductivity material
  Typically Copper or high purity Aluminum
    Encapsulated Pyrolytic graphite now also becoming more common
  Limited heat transport capability
  Flexible to not carry structural load
    Often used to provide shortest thermal path with minimal mass
    Also used to connect detectors to coolers to minimize impact of cooler on detector package (e.g. multiple load paths, vibration isolation)
Heat Strap
Heat Strap
100

## Slide 101
Thermistor – a sensor whose electrical resistance changes in a predictable manner with temperature
  Different from other Resistive Thermal Devices (RTD) in that they are typically ceramic or polymers
  Calibration curves included with each thermistor; curves tend to be non-linear
  Each sensor read independently on its own channel – cannot electrically combine
  Requires a current to be passed through the thermistor to measure resistance
  Best used for nominal temperature ranges (-60°C/213 K to +60°C/333 K)
  PRT – Platinum Resistance Thermometer – a platinum Resistive Thermal Device whose electrical resistance changes in a predictable manner with temperature
  Similar to a thermistor, but tends to be a bit more accurate
    Temperature vs. Resistance tends to be fairly linear
  Good for colder temperature ranges (but not yet into the cryogenic range) (60 K to 333 K)
Thermistor and Platinum Resistance Thermometers
Thermistor
101

## Slide 102
  Si Diode – Silicon Diode – a device where current is only allowed to flow in one direction
  Since the forward voltage drop across the silicon diode is temperature dependent, the measured voltage can be used to infer the temperature
  Best used for cryogenic applications ( < 60 K)
  TC – ThermoCouple – a device where the junction of two dissimilar metals produces a predictable voltage based on the temperature due to the Seebeck effect
  Less accurate than Thermistors, PRTs, or Silicon Diodes
  Typically only used for ground testing
  Often removed before flight
    If not, they must be clipped and grounded to not act as antennae for EMI/EMC
  Cannot go as cold as PRTs/Silicon Diodes
Silicon Diodes and Thermocouples
Thermocouple
102

## Slide 103
Cryo Cooler – a mechanical device that uses a thermodynamic cycle (typically Stirling) to achieve cooling
  Can remove small amounts of heat from colder environment utilizing power to do so
  Compression/Expansion of gases during cycle
  Power consumption depends on heat load removed, cold side temperature, and hot side temperature
    May require control algorithm if trying to maintain thermal stability of cooled side
  Most often used to cool detectors which tend to like colder operating temperatures
    Thermal isolation of cold side is often a challenge
  Often induce vibration/jitter that must be compensated
  Expensive, but sometimes the only way to get cold enough for detector science
Often includes a TMU (Thermo Mechanical Unit) separate from Cold Head
Cryo Cooler
1 Stage Cryo-Cooler
2 Stage Cryo-Cooler
103

## Slide 104
  TEC – Thermo-Electric Cooler – aka Peltier Coolers – an electrical device which utilizes the Peltier effect to achieve cooling, but usually only around 6-10% efficient
  Can remove small amounts of heat from colder environment utilizing power to do so
  Peltier Effect – opposite of Seebeck – heat is evolved (heating) at one junction and absorbed (cooling) at the other
  Power consumption depends on heat load removed, cold side temperature, and hot side temperature
  May require control algorithm if trying to maintain thermal stability of cooled side
  Most often used to cool detectors which tend to like colder operating temperatures
  Multi-stage TECs (look like Aztec Pyramids) used to achieve greater cooling. Each subsequent layer towards the base must remove (heat removed by above layer) + (power needed to remove that heat), hence the growth of the footprint
  Tend to be fairly weak in shear, so mechanical support while still providing thermal isolation is challenging
  Not too expensive (compared to cryocoolers), but cannot currently get much below -130°C
Thermo Electric Cooler
1 Stage TEC
3 Stage TEC
6 Stage TEC
104

## Slide 105
Doublers and Spreaders - used to improve in plane conduction
  These are generally used to reduce the thermal resistance between a heat source and the radiator (or radiative sink)
  Doublers and Spreaders are typically thicker metal mounting plates, where the local thickness helps share heat between multiple components (e.g. Active Primary Avionics Box next to Redundant Avionics Box) or to increase the footprint of a thermal interface
  Spreaders may also be heatpipes attached to a radiator panel or embedded in a honeycomb radiator. The use of heatpipes (and the accompanying efficiency) is often a more costly, but more mass efficient way to improve radiator efficiency over simply making the radiator thicker
APG – Annealed Pyrolytic Graphite – a sealed aluminum component with embedded graphite sheets to improve the in-plane thermal conductivity for heat spreading
  APG is a newer technology where a machined aluminum part is sliced in half with the center material hogged out and replaced with sheets of pyrolytic graphite.
  The PG and the two aluminum parts are then sealed in a high temperature, high pressure process, which embedded the PG inside the part and anneals the aluminum
  While this makes for a softer aluminum (T0 instead of T6), the embedded PG significantly improves the overall in plane heat conduction (typically by a factor of about 4)
Doublers and Spreaders
105

## Slide 106
Heat Switch – a device which passively actuates based on temperature to improve or degrade a thermal path
  Typically uses Parafin wax which expands or contracts with temperature in combination with a spring mechanism to adjust thermal path
  High conductivity path difficult to achieve and tend to be high mass
  Typically used to save heater power by decoupling from radiator
  PCM – Phase Change Material – a device that relies on phase change to absorb/release heat
  Often used to provide excellent thermal stability
    Phase Change is an isothermal (constant temperature) process
  Tends to be high mass, so not often used unless really necessary
  Typically not a good conductor, so high conductivity vias introduced within PCM
  Louvers – mechanical device which adjusts view factor to sink
  Like Venetian Blinds or Pinwheels
  Similar to a thermostat, a bimetallic actuator responds to temperature
  and rotates the blade or fans. Not used much any more
  Mechanically Pumped Loops – a mechanical device which circulates a working fluid through a closed loop system for heat absorption/rejections
  Not subject to gravity effects like heat pipes
  Moving parts suffer from wear, jitter, vibration isolation, etc.
  Used on Mars/Jupiter missions by JPL
Less Common Thermal Components at our disposal
Louver
106

## Slide 107
  Determining the Thermal Architecture

## Slide 108
Thermal Design Process Flow

## Slide 109: Determining the Thermal Architecture
Now, back to those questions…
  How many thermal zones are needed? Can any components be co-located to simplify the thermal design?
  What range of b angles need to be considered? Is there a dedicated “cold” side of the observatory based on orbital mechanics?
  Where should the radiator(s) be located? How will the heat be transported to the radiators (e.g. Directly coupled to backside? Heat Strap? Heat Pipe? )
  What coatings are needed and where?
  What size do the radiators need to be to stay below the upper operating limit with some power contingency?
  Do any components need active cooling (e.g. TEC, CryoCooler)?
  What areas might require thermal isolation/insulation in the design?
  How many heater zones are needed to stay above lower operating limits?
  Are there any challenging stability or gradient requirements that will require complex control or additional thermal considerations (e.g. optical bench)?
  Where are sensors needed for thermal control or knowledge?
  Is the design concept ground testable?

## Slide 110: A Brief Discussion on Biasing Design Parameters
Any design input parameters include uncertainty. It is a prudent practice to use this in a manner that generates a robust design if the uncertainty is realized during flight operation. Some biasing parameters are based on uncertainty, others are based on expected variations over the mission life
Uncertainty
  Solar Flux, Albedo Factor, Planet IR
  Power Dissipation
  Blanket effectiveness
  Interface Conductances
  Optical Property Uncertainty
Expected Variations
  Beta Angle
  Optical Property Degradation
  Power Profiles (based on Operations)
  Solar cell energy conversion
  Voltage range
These are considered the “Known Unknowns”. To further protect against the “Unknown Unknowns”, the design should maintain margin to the limits (typically 5°C of temperature margin, or 30% of heater margin)
  It is much easier to blanket an oversized radiator late in the project life cycle than it is to add to an undersized radiator
Hot vs Cold Case
Env: High Values vs Low Values
Power: High Dissipations vs Low Dissipations
Blankets: Low e* vs High e* (usually, but may depend on direction of heat flow)
I/F Cond: Low vs. High
Opt Props: High a, Low e vs Low a, High e
Solar Cells: Not Converting vs Converting
Voltage: Max Voltage vs Min Voltage
Beta Angle: Highest flux vs Lowest flux

## Slide 111: Thermal Zones
Examine the temperature component limits
  Are any nearly the same? If so, consider if those components can be located on a radiator panel or a common interface to a radiator
  It is generally not desirable to group components together thermally if the temperature limits are different, since this would under utilize the capacity of a thermal control system.
  If Component A has an upper limit of 30°C and Component B has 40°C, sizing a radiator to handle both would limit the heat rejection to a lower temperature (i.e. larger radiator)
  Likewise, if Component A has a lower limit of 0°C and Component B has -20°C the overall heater power would need to be higher to maintain 0°C than for -20°C
  Fortunately, many components do tend to have the same limits of -10° to +40°C
  Grouping together multiple components into a single zone also reduces the risk that power growth will exceed capacity, whereas the risk is higher for a single component/single radiator system
  Batteries tend to have narrower temperature limits, while Comm Transponders tend to have wider temperature limits
  Sometimes, a thermal zone may also be dictated by co-location, co-alignment, stability or gradient requirements

## Slide 112: Thermal Transport and Radiator Determination
Once you have established the nominal Thermal Zones, the next step is to determine where a Radiator will be located and how to transport the heat from the Dissipation location to the Radiator
  Radiator locations are often driven by the coldest available location to effectively reject heat, usually related to orbital constraints to avoid solar illumination of the radiator
  Thermal should stake our claim to these locations very early on !
  It is difficult to shift an entire layout to accommodate a new radiator location and thermal should be able to quickly identify where the optimum locations are for radiators
  Once the Radiator location is known, the next step is to determine the transport method
  Ideally, the back side of a mounting panel is ideal for a radiator if the orientation can work. This minimizes the thermal resistance between the dissipating component and the radiator.
  If this will not work and the component is near to the radiator, a heat strap may be appropriate
  Lastly, if the distance between component and radiator is larger or the heat dissipation is large, then a two-phase device (CCHP, VCHP, LJP) may be the best option
  Lastly, knowing the radiator location and the thermal resistance between the dissipating component(s) and the radiator (as a function of the transport method), the size may be determined to reject the known heat dissipation, while maintaining the temperature below the upper limits with appropriate margin

## Slide 113: What Coatings are needed?
Coatings are an integral part of any space based thermal design
  They are generally used to improve heat rejection (high e), minimize solar absorption (low a), or minimize IR absorption (low e) for radiative isolation
  Coatings may have charge mitigation requirements (needing a conductivity requirement) and/or be impacted by space environment effects (atomic oxygen erosion, solar exposure, dust, handling, etc)
  Coating values vary by mission and should eventually be specified by the GSFC Coatings Committee for all coatings in use
  This typically includes both Beginning of Life (BOL) and End of Life (EOL), which may include degradation based on the mission duration and flight environment
  Generally, the EOL properties for a are higher than the BOL based on expected degradation; e is often unaffected but may include the measurement uncertainty when used in the analysis

## Slide 114: Active Cooling Needs
For components with particularly low temperature limits, passive cooling with a simple radiator may not be practical
  Since radiator area is proportional to Absolute Temperature to the 4th, the area to cool a detector to cryogenic temperatures may not be practical to accommodate. For this case, a CryoCooler or ThermoElectric Cooler may be necessary
  First, the heat lift should be determined (i.e. how much heat needs to be removed). This is usually a small number on the order of 10s to 100s of mW
  This is generally a combination of component dissipation, thermal isolation (both conductive and radiative), and wire parasitic heat loads
  If the temperature is around -120°C or higher, a ThermoElectric cooler might be sufficient, but will likely be a multi-stage cooler
  If the Temperature is below -120°C, a CryoCooler may be needed. At this point, reach out the the Cryo branch for assistance
  Any kind of active cooler will have an associated performance curve which relates the heat lift, cold tip temperature, heat reject temperature, and required input power. Thermal will need to factor this variability into any thermal analysis.
  These devices tend to be quite inefficient (~6-10%...10 W input power to remove 1 W), but may be a viable option to reduce overall radiator size with the T4 radiative relation

## Slide 115: Thermal Isolation Determination
For components with low temperature limits, the nominal design may not provide enough thermal isolation, leading to larger radiators or warmer temperatures without proper isolation
  Conductive Thermal isolation is achieved by minimizing Thermal Conductivity (k) and Cross Sectional Area (Ax), while maximizing Length (L)
  This is often in direct contradiction with Mechanical desires, which are Small L/Large Ax
  Material selection is often a key to thermal isolation, but material must be selected with strength in mind to meet structural requirements (Titanium, G10 good choices)
  Radiative Thermal Isolation can be accomplished using Coatings or Multi Layer Insulation (aka blankets)
  The absorption of heat can be minimized by selecting coatings (Paints, films, tapes) with a low emissivity (e)
  An alternative to low e coatings is the use of Multi-Layer Insulation which is composed of alternating layers of Dacron mesh and mylar sheets to inhibit heat flow
  The choice between coating and MLI should also consider stray light implications for optical systems. A low e coating is highly reflective
  In general, where there is not a radiator or an aperture, there is a blanket…

## Slide 116: Heater Zone Determination
With radiators located and sized for the maximum operating temperature and the dissipation with margin, attention is turned to the cold end of the operating range. With the minimum power and a radiator sized for a hot case, it is likely heater power is needed to remain above cold operating limits
  Heaters should be sized to ensure that no controlled components fall below the lower operating limit
  Furthermore, the average power in the worst cold case should not exceed 70% of the heater capacity
  The control of the heater should also be considered
  Are electronic switches needed (i.e. Flight Software control) or do mechanical thermostats suffice?
  FSW Pros: commandable in flight, allows finer control, Cons: finite resource, requires active FSW
  Thermostat Pros: only power feed is needed, Reliable when used in series, Cons: larger control band (usually 5-7 C between On and Off)
  For stability control heaters, the control authority should also be robust (i.e. the heater power needed in worst case hot cases should not be near zero)
  Heater circuits are generally inexpensive enough to implement redundancy (Primary and Redundant sides), even for higher risk posture missions
  Note that a portion of heater power usage is implicitly included in power budgets
  If the system includes power growth allowance, then the Solar Array already includes power representing the difference between Allocation and Current Best Estimate
  e.g. Component A expects to be 50 W, but the allocation held for Solar Array sizing is 65 W to allow for potential power growth. Therefore, if the component is off and does not need more than 65 W of heater power, no more demands are placed on the Power Budget

## Slide 117: Thermal Sensor Determination
With radiators and heaters determined, the design is nearing completion. However, knowledge of the thermal performance during ground testing and flight is crucial and sensor layout is an important step
  For most missions, thermistors are sufficiently accurate for flight telemetry
  However, sometimes Platinum Resistance Thermometers (PRTs) or Silicon Diodes are needed for accuracy at lower temperatures
  The need for Primary and Redundant sensors should also be considered. Like heaters, the implementation of redundancy is usually comparatively inexpensive
  Any sensors used for control (Heater, Cooler) should be identified and communicated with Flight Software as well as the desired control algorithm (Thermostatic, PID, etc)
  The total number of Flight Sensors should be communicated with Flight Software and the Command and Data Handling groups to ensure display and sufficient readout channels
  Thermocouples could be considered for additional ground testing, but are generally not considered reliable enough for flight telemetry
  These may be removed prior to launch or clipped and grounded to prevent EMI issues if accessibility prevents their removal
  With proper planning, the accommodation of test only TCs can be optimized

## Slide 118: Considerations for Thermal Ground Testing
Any thermal design must consider the ability to test on the ground. This usually falls into one of two types of considerations:
Ability of the Design to be tested
  Does a lack of possible deployed components (Sun Shield, Solar Array) present any problems?
  Are two phase devices able to function?
    Constant conductance and variable conductance heatpipes must be level or with the Evaporator end of the pipe higher in elevation than the Condenser end (Reflux mode)
    Are there any effects of gravity on flow through an LHP condenser?
Capabilities of the Test Facility
  How will the flight thermal environment be simulated?
  Is a chamber shroud enough to represent the environment?
  If not, are heater panels (cooled by radiative views to shroud), cryo panels (cooled by dedicated cooling lines), and thermal target plates (cooled by a cryo cooler) needed?
  How many thermal zones need to be simulated in the test? Is this within the capabilities of the facility?
  Is simulation of solar sources needed or will Infrared heater plates suffice?
  What additional targets, sources, or equipment is needed for the instruments?

## Slide 119
  Early Thermal Design Calculations

## Slide 120
To begin, the power dissipation and component limits must be known
Estimate TRad based on degrading factors such as: required margin (5 K), a Transport resistance (e.g. DT from a strap), and radiator inefficiency
  If a radiator is larger than the footprint of the heat source, then there is likely to be a gradient as heat conducts in plane away from the source and radiates to space to points on the radiator further away from the footprint of the source
  The efficiency may be estimated by the (Tavg / Tmax)4 where Tmax represents the temperature at the input to the radiator and Tavg represents the average radiator temperature. Ideally, this number sound be relatively high (80-90%) or it may be necessary to make the radiator thicker or add spreader heat pipes
  For example, assuming a 40°C limit, holding 5°C of margin, assuming a 3°C DT from the transport, and a radiator efficiency of 85% yields: TRad = 19.85°C – remember to convert to K for the (Tavg / Tmax)4
The Dissipation should also be increased, to account for potential power growth. Unless the value given is an allocation or Maximum Expected Value (MEV), 30% is reasonable
Assume a reasonable, but high emissivity based on white or black paint (0.87)
Begin with the basic radiative heat transfer equation and rearrange to solve for the radiator area (assuming deep space at 0 K for simplicity)
ARad = 1.3 * QDissipation / ( s e TRad4)
For a 100 W dissipation and a limit of 40°C, this suggest you need 0.3583m2 of radiator area for this design (allowing for 30% power growth)
Radiator Sizing to Deep Space

## Slide 121
The previous hand calc assumed a perfect view to deep space. But what if the radiator direction is not purely to deep space?
The equation is adjusted to:
ARad = QDissipation / { s e ( TRad4 - TSink4 ) }
The plot shows the impact of a varying Sink Temperature
Radiator Sizing to a Sink
Note that sinks below about 200 K have very little impact on the radiator size for this warm a TRad
It is not until the sink warms above 200 K (-73°C) that the required area increases appreciably
It should be noted this holds true for components near room temperature. If TRad was much lower (for say an IR detector), then this effect may not be seen
It also explains why much of our testing can be done with LN2 panels at 80 K for many room temperature avionics

## Slide 122
If a sink temperature in a given direction has been specified, then this value may be used. Some projects may have these environments already defined in various directions if they are expecting numerous competing instrument designs
If the sinks are not specified, then the thermal analyst may use a simple cube model in the characteristic orbit environment with appropriate optical properties to determine the sink
A massless surface with an adiabatic backside, no additional heat applied, and the appropriate optical properties will reach an equilibrium temperature based on rejecting the exact amount of heat absorbed from the environment.
This temperature is effectively the equivalent sink temperature
Note that this technique may also be used in larger models (using a very small square over the actual model) to determine the effective sink temperatures. These values may later be used to determine what panel temperatures should be during TV testing to emulate the flight environment.
Once sink temperatures are known, they may be used for radiator sizing
Once the estimated radiator size is determined, begin working with the mechanical engineer on placement and packaging
Determining the Sink Temperature

## Slide 123
Heater sizing cannot be done without first knowing the radiator size and the minimum component temperature
A “cold“ sink temperature may be used, but assuming a sink of zero will never produce an undersized heater…
Begin again with the basic radiation equation and rearrange to solve for QHTR
QHTR = s e ARad ( TLow4 )
Tlow is the minimum component temperature increased to account for any margin or transport losses. This also assumes that the component has no dissipation and would be applicable for a survival heater.
If instead the heater is an operational heater, then any dissipation may be removed from the calculated QHTR to determine the heater size
Lastly, the heater should be sized to use no more than 70% of the available capacity based on the average usage, so the actual size to model is QHTR / 0.7
For that 100 W box, assuming a lower non-operating limit of -20°C, no dissipation, the 3°C transport resistance, and the radiator size of 0.3583m2, QHTR would evaluate to 75.9 W and the heater would be specified to 108.44 W at minimum voltage
When reporting the heater power usage in the power budget, it is important to note that of the 108.44 W, 130 (100 W + 30%) should already be booked. So, while this does not place increased power generation demands on the solar array, it does require a power service capable of this power level
Note that the instantaneous power would be even higher for a higher voltage, but the average power would remain the same regardless of voltage
Heater Sizing

## Slide 124
Step 1: Get requirements
  Electronics box, dissipating 15 to 40 W and needing to stay between -10°C and 40°C
  Orbit beta angles go from 0° to 90°, nadir viewing
  Spacecraft has provided a cold side such that it will never have direct sun, but will always have glancing view of Earth
Step 2: Size the radiator
  Energy balance: QSRC + QIN + QHTR= QOUT
  40 + QIN + 0.0 = QOUT (Assume no heater power is needed in hot case)
  Environment: QIN = Bij * e * EarthFlux * Area (Bij to earth for surface normal to Planet is about 0.2)
  QIN = 0.2 * 0.85 * 243 * Area (Hot Case Earth flux is around 243 W/m2)
  Radiation: QOUT = s * e * Bij * Area * (THOT4 -TSPACE4) (e of 0.85 typical for radiator)
  QOUT = 5.67E-8 * 0.85 * 1.0 * Area * (3084 – 44) (308 K = 35°C = 40°C – 5°C margin)
  Area is about 0.1 m2
  Step 3: Size the heater
  Energy balance: QSRC + QIN + QHTR = QOUT
  15 + QIN + QHTR = QOUT
  Environment: QIN = Bij * e * EarthFlux * Area (Bij to earth for surface normal to Planet is about 0.2)
  QIN = 0.2 * 0.85 * 208 * 0.1 (Cold Case Earth flux is around 208 W/m2)
  Radiation: QOUT = s * e * Bij * Area * (TCOLD4 -TSPACE4) (e of 0.85 typical for radiator)
  QOUT = 5.67E-8 * 0.85 * 1.0 * 0.1 * (2684 – 44) (268 K = -5°C = -10°C + 5°C margin)
  QHTR is about 6.7 W; to have 6.7W with 70% duty cycle, 10 W heater needed
  Step 4: Verify the hand calcs with more detailed model
  Sometimes we don’t even have a good feel for the Bij to the sun or Earth
  In these cases, we typically model a cube in a representative orbit with a=1 and e=1 to get the loads
Hand calculations many Thermal Engineers do

## Slide 125
Establishing the Worst Case
To determine the worst case, it is typical to perform a sweep through a range of b angles or Field of Regard positions if the worst case hot or cold is not intuitively obvious
For b angles, usually about 7-15 points throughout the range is sufficient
For Field of Regard, usually evaluating the corners, center, and midsides is enough
Once the worst case is found, a sweep through all other cases usually does not need to be performed every time the analysis is run. While the design may change, the environments generally do not unless a major design change necessitates revisiting (e.g. new radiator or location)
It should be noted however, that what may be the worst case for one component, may not be for all components. So, once the sweeps are complete, a subset of worst cases should be identified, and the design checked against these cases

## Slide 126
Once the initial estimates are made for temperature zones, radiator sizes, and heater sizes, the mechanical engineer may begin to lay out the overall spacecraft or instrument architecture
Along with inputs from all other disciplines, the physical layout of the overall design begins to take shape
As this matures, the thermal engineer should begin a more detailed model to verify that the early estimations were reasonable
Discussions with other disciplines is also needed regarding the necessary accommodations to implement the thermal design, such as power services and harness
These early radiator and heater sizings lay the foundation for the numerous iterations and updates of the design throughout the project life cycle, but are by no means the end of the process
The next section details some of the accommodation considerations and interfacing with Systems Engineering and the Project
Next Steps

## Slide 127
  Accommodation of Requirements from Thermal

## Slide 128
Thermal Design Process Flow

## Slide 129
You have a design, but what do you need from others to implement it?
Thermal Designs are never detached from the rest of the system
  Radiators: may require mechanical support and may impose flight constraints
  Thermal Mass for Stability: may require stronger mechanical support
  Heatpipes: require mechanical support and may impose test levelness requirements
  Blankets: require grounding, venting, and may need further work for stray light concerns
  Heaters: will require harness, power services, and possibly flight software for control
  Thermostats: will require harness
  Sensors: will require harness, and flight software read out capability
  Coolers: will require harness, power services, and flight software control, may require jitter isolation

## Slide 130
Accommodating the Thermal Design
Harness
  Harness routing and wire definitions are needed for all sensors, heaters, and any other thermal components needing power/readout
Power Services
  A limited number of switches/relays are available
  Circuits can carry a limited number of amps
Flight Software
  A limited number of channels are available to be read by the avionics and be stored in the housekeeping telemetry stream
  Control algorithms for heaters/coolers may require additional lines of code
Mechanical Support
  Additional mass and design work may be needed to support radiators (brackets)
Flight Constraints
  Sun or other source avoidance may need to be accounted for by ACS/GNC
Test Constraints
  Testing orientation may be difficult to accommodate given other GSE needs (targets, stimulators, cryo and heater panels, chamber availability)
Documentation
  Drawings need to be done for hardware locations, electrical schematics, coating masking
  Work Order Authorizations need to be generated for the installation of thermal hardware

## Slide 131
Working with Systems Engineering

## Slide 132
Working with Systems Engineering
In the Thermal Design process, Systems Engineering wraps around all disciplines
  At times what is best for one subsystem is detrimental to another
  It is the Systems Engineering Teams job to determine the optimum
  Thermal interfaces closely with Systems, both on incoming/outgoing design parameters
Most often, Systems keeps a Master Equipment List (MEL) which captures all the hardware necessary for the design and includes mass, Technology Readiness Level (TRL), redundancy, Temperature Limits, etc. Thermal provides inputs to the MEL in terms of the mass of the thermal hardware to implement into the design
As a corollary, Systems also keeps a Power Equipment List (PEL), which serves as the bookkeeping for all power used by the system. For thermal, this is an excellent source for the dissipations for the various components, both Current Best Estimates (CBE) and Maximum Expected Value (MEV) or Allocations
As projects mature, updates to the MEL and PEL must be vetted and tracked to ensure that no changes have a significant impact on the design (e.g. power growth leading to a larger radiator)

## Slide 133
Resource Budgets
For a given project, there are finite resources that are tracked throughout the project life cycle, including:
  Mass
  Power
  Cost
  Time (expressed as Schedule)
The thermal engineer is responsible for keeping their contributions to these budgets up to date
  This includes regular updates to Mass and Power as the design evolves throughout the project life cycle (especially the heater power demands)
  It also includes the procurement of the necessary hardware to meet the cost budget constraints and the overall Integration and Test (I&T) flow for the project
  Many of the smaller thermal components, such as heaters, sensors, and thermostats are off the shelf products and have their own IEEE specifications
  Other, more complex thermal hardware (such as HeatPipes, CryoCoolers, Radiator Panels) will need to have their specifications generated and go out for competitive procurement

## Slide 134
Where does Thermal Analysis Fit In?
Once a design concept has been formulated, thermal analysis of the design is performed to ensure requirements are met
  The generally accepted practice is to stack all worst case hot and cold parameters and ensure the predictions are within limits with margin
The updates and data that feed into the budgets are typically derived from this detailed thermal analysis of the system
  A presentation on Thermal Analysis can be found at ntrs.nasa.gov under the title “Thermal Modeling and Analysis”
Some foundations should first be discussed that are not design/project specific…
  Design Margin Philosophy: GSFC typically maintains 5°C of margin to limits or for components under heater control utilizes no more than 70% of heater capacity. Greater margins may be needed for cryogenic applications. Other organizations may have different margin philosophies…
  Power Growth Allowance: if power dissipation Allocations (or Maximum Expected Values [MEV] or Not To Exceed [NTE] values) are not specified, it is advisable to include a factor for power growth allowance beyond a Current Best Estimate [CBE]. Until measured values are available (usually late in a program), 30% uncertainty is not unreasonable
  Material Properties: Thermophysical properties should have traceability to their source and not just be what was used on the last project
  Thermo-Optical Properties: Thermo-optical properties should consider the range of possible values for a mission based on measurement uncertainty as well as expected degradation due to the space environment

## Slide 135: Wrap Up
The thermal design process is well established
  It begins with gathering requirements
  The thermal engineer then specifies the thermal design including components to meet requirements as well as resources needed for implementation
  Analysis is performed to validate the design and once an accepted level of maturity is reached at critical project milestones, the proposed hardware is procured
  The hardware is then installed during the integration and test phase
  After the hardware installations are completed, the article is put through rigorous testing to ensure performance and that all requirements are met
  The thermal model is correlated to the test data to provide the most accurate predictions for flight
  The hardware is then delivered to the next higher level of assembly (e.g. instrument, spacecraft, launch vehicle)
Once in flight, the thermal telemetry is monitored during commissioning to ensure performance is within expected parameters
  Resources permitting, a correlation to flight data may also be performed
135

## Slide 136: Other Resources
GOLD Rules: GSFC-STD-1000G
GEVS: GSFC-STD-7000B
(GSFC Internal) ETD Wiki: https://spaces.gsfc.nasa.gov/display/CODE545/545+Home
(GSFC Internal) Orbit Calculator (Excel spreadsheet), David Everett, dtd 2/27/2017
Spacecraft Thermal Control Handbook , The Aerospace Corporation, David Gilmore Editor, 2002
  Vol 1: Fundamental Technologies
  Vol 2: Cryogenics
Satellite Thermal Control for Systems Engineers Robert Karam Progress in Astronautics and Aeronautics Series, V-181 Published by AIAA, © 1998
Radiant-Interchange Configuration Factors, National Advisory Committee for Aeronautics, December 1952.
Thermodynamics of Space Flight (Heat Transfer Phenomena in Space), NASA GSFC, M. Schach and R. Kidwell, Jr., March 1963.
136

## Slide 137: Other Resources - continued
Hardware:
S-311-P-079, “PROCUREMENT SPECIFICATION FOR THERMOFOIL HEATER”
S-311-P-18, “THERMISTOR, (THERMALLY SENSITIVE RESISTOR), INSULATED AND UNINSULATED, NEGATIVE TEMPERATURE COEFFICIENT, SPECIFICATION“
S-313-013, “ADHESIVE BONDING OF PLATINUM RESISTANCE TEMPERATURE SENSORS TO SUBSTRATE SURFACES”
S-311-641, “SWITCHES, THERMOSTATIC, GENERAL REQUIREMENTS FOR”
S-311-641/02, “SWITCH, THERMOSTATIC, BIMETALLIC, SPST, NARROW DIFFERENTIAL, HERMETIC, DETAIL SPECIFICATION FOR”
“MECHANICALLY PUMPED FLUID LOOPS FOR SPACECRAFT THERMAL CONTROL: PAST, PRESENT & FUTURE”, P. BHANDARI, TFAWS 2004
HEAT PIPE DESIGN HANDBOOK, VOLS 1 & 2, JUNE 1979 (B&K ENGINEERING FOR NASA GSFC
CHI S. W., HEAT PIPE THEORY AND PRACTICE: A SOURCEBOOK, 1976
REAY D. A., HEAT PIPES: THEORY, DESIGN AND APPLICATIONS, 2014
KARAM R. D., SATELLITE THERMAL CONTROL FOR SYSTEMS ENGINEERS, 1998
FAGHRI A. HEAT PIPE SCIENCE AND TECHNOLOGY, 2ND EDITION, 2016
ZOHURI B. HEAT PIPE DESIGN AND TECHNOLOGY: MODERN APPLICATIONS FOR PRACTICAL THERMAL MANAGEMENT, 2ND EDITION, 2016
Installation/Fabrication Processes:
S-313-022/541-SPEC-022 ADHESIVE BONDING KAPTON THERMOFOIL HEATERS TO SUBSTRATE SURFACES
S-313-014/541-SPEC-014, “ADHESIVE BONDING OF THERMISTOR SENSORS TO SUBSTRATE SURFACES”
545-WI-8072.1.8, “PROCEDURE FOR VERIFICATION OF THERMOSTAT OPERATION”
546-WI-8072.1.74 PROCEDURE FOR APPLICATION OF TRANSFER ADHESIVES FOR TAPE FABRICATION, THERMAL BLANKET PRODUCTION, AND HEATER ATTACHMENTS
541-WI-8072.1.26, “PROCESSES FOR THE ADHESIVE BONDING OF THERMAL CONTROL COMPONENTS ON FLIGHT HARDWARE”
Thermal Insulation:
NASA/CR-72747, “FINAL REPORT – THERMAL PERFORMANCE OF MULTI-LAYER INSULATIONS”, J. BARBER (LeRC), APRIL 20TH, 1971
NASA/CR-134477, “FINAL REPORT – THERMAL PERFORMANCE OF MULTI-LAYER INSULATIONS”, W. JOHNSON (MSFC), APRIL 5TH, 1974
NASA/TP-1999-209263, “MULTI-LAYER INSULATION MATERIAL GUIDELINES”, M. FINCKENOR (MSFC)
549-WI-8072.0.2, “DESIGN AND FABRICATION OF THERMAL BLANKETS”, NASA GSFC/549
137

## Slide 138: Other Resources – NESC Academy
Organized kinda like Netflix
  Subsystems: Passive Thermal
https://nescacademy.nasa.gov
Numerous videos on thermal design
138

## Slide 139: References
“Spacecraft Thermal Control Handbook”, David Gilmore, 2002
“Space Mission Analysis and Design”, Wiley & Larsen, 3rd edition, 5th printing 2003
“Thermal Radiation Heat Transfer”, Siegel & Howell
General Environmental Verification Specification (GEVS) for STS and ELV Payloads, Subsystems, and Components
  http://arioch.gsfc.nasa.gov/302/gevs-se/toc.htm
“Test Requirements for Launch, Upper-Stage, and Space Vehicles”, MIL-STD-1540
139

## Slide 140
Acronyms
  NASA: National Aeronautics and Space Administration
  GSFC: Goddard Space Flight Center
  PDR: Preliminary Design Review
  CDR: Critical Design Review
  PSR: Pre-Ship Review
  GNC: Guidance, Navigation, and Control
  FSW: Flight Software
  Comm: Communications
  QA: Quality Assurance
  CAD: Computer Aided Design
  EMI/EMC: Electro Magnetic Interference/Compatibility
  GEVS: General Environment Verification Specifications
  GMM: Geometric Math Model
  TMM: Thermal Math Model
  Qij: heat flow from i to j
  Ti: temperature for i
  Ax: cross sectional area
  L: length
  k: thermal conductivity
  mCp: Mass times Specific Heat
  s: Stefan Boltzman Constant
  Ai: surface area for i
  Radk: Radiation coupling
  Bij: Interchange Factor
  Fij: View Factor
  a: banded UV absorptivity
  e: banded IR absorptivity/emissivity
  TB: Thermal Balance
  TV: Thermal Vacuum
  GSE: Ground Support Equipment
  ICD: Interface Control Document
  EEE: Electrical, Electronic, and Electromechanical
  WOA: Work Order Authorization
  I&T: Integration and Test
  IR: Infrared
  UV: Ultraviolet
  BOL: Beginning of Life
  EOL: End of Life
  MLI: Multi Layer Insulation
  CCHP: Constant Conductance Heat Pipe
  VCHP: Variable Conductance Heat Pipe
  NCG: Non-Condensable Gas
  LHP: Loop Heat Pipe
  I/F: Interface
  MLI: Multi Layer Insulation
  OSR: Optical Surface Reflector
  RTD: Resistance Temperature Device
  PRT: Platinum Resistance Thermometer
  TC: Thermocouple
  TEC: Thermo Electric Cooler
  PCM: Phase Change Material
  APG: Annealed Pyrolytic Graphite
  PSA: Pressure Sensitive Adhesive
  VDA: Vapor Deposited Aluminum
  General Terms Analysis Terms Hardware Terms

## Slide 141
1D One Dimensional
2D Two Dimensional
3D Three Dimensional
a Solar Absorptance
Alt Altitude
ASSY Assembly
Bij Interchange Factor
BOL Beginning of Life
CAD Computer Aided Design
Cp Specific Heat
DT Temperature Difference
e Infrared Emissivity
e* Effective Emissivity
EOL End of Life
FD Finite Difference
FE Finite Elements
GOLD Goddard Open Learning Design
GSFC Goddard Space Flight Center
hcond/hevap Condenser / Evaporator Heat Transfer Coefficient
HP Heat Pipe
HR Heat Rate
ID Identifier
More Acronyms
IF Interface
Incl Inclination
IR Infra Red
k Thermal Conductivity
MCRT Monte Carlo Ray Trace
MLI Multi-Layer Insulation
NCG Non-Condensable Gas
PCM Phase Change Material
PID Proportional-Integral-Derivative
r Density
RAAN Right Ascension of Ascending Node
Radk Radiation coupling
RES Reservoir
SC Spacecraft
SINDA Systems Improved Numerical Difference Analyzer
STEP Standard for the Exchange of Product Model Data
STOP Structural-Thermal-Optical-Performance
TD Thermal Desktop
TEC Thermo Electric Cooler
UV Ultraviolet-Visible
VCHP Variable Conductance Heat Pipe
VP View Port