## Slide 1: From Natural Language Requirements to the Verification of Programmable Logic Controllers: Integrating FRET into PLCverif
CERN BE-ICS group
Zsófia Ádám (BUTE)
Borja Fernández Adiego
Ignacio David Lopez Miguel (TU Wien)
Jean-Charles Tournier
Marcin Bes
Enrique Blanco Viñuela
NASA AMES Robust Software Engineering & KBR
Anastasia Mavridou
Andreas Katis
Thomas Pressburger
Khanh V. Trinh

## Slide 2: Context – CERN (European Organization for Nuclear Research)
CERN has the biggest particle accelerator complex in the world and many critical and complex industrial installations
Cryogenics plants
Cooling and ventilation systems
Images from cds.cern.ch
Superconducting magnet test benches
LHC
(Large Hadron Collider)
Access and protection systems

## Slide 3: Context – PLCs at CERN
if (MMoSt and AuAuMoR) at any time before the end of the PLC cycle,
then AuMoSt should be true at the end of the same PLC cycle
At CERN, more than 1000 PLCs (Programmable Logic Controllers) are installed to control and/or protect the installations
Example case study 2
Ambiguous or incomplete specification
Need to guarantee “complex” properties
PLCverif
Enables formal verification to PLC programs

## Slide 4: Roadmap
PLCverif
FRET
Conclusions
FRET-PLCverif integration
PLCverif limitations
FRET new developments

## Slide 5: PLCverif
Property failed
Trace leading to the violation
If Out1 is FALSE
then Out2 is TRUE
PLC program
Property to verify
(verification case)


Intermediate Model (IM)
Control-Flow Automaton (CFA)
Model reduction and abstraction techniques
Property OK
Other methods
Model checking algorithms
(external tools)
1
2
3
4
5
PLCverif hides the complexity of using formal methods
Different PLC languages, property specification methods and model checking tools can be added (open architecture)
PLCverif references: https://gitlab.com/plcverif-oss and www.cern.ch/plcverif

## Slide 6
PLCverif
Currently 8 patterns based on
the experience of CERN PLC program developers

## Slide 7: PLCverif current limitations
2 main property specification limitations
  Validation of (complex) requirements
  (Very) limited expressive power
    basic assertions
    8 patterns
If ((not MTBF_WCC_PCLSW20_FSL) or (not MTBF1_WCC_LSW20_FSL and MTBF1_LSW20_POS) or (not MTBF2_WCC_LSW20_FSL and MTBF2_LSW20_POS) or (MTBF2_LSW20_POS and not MTBF2_WCC_LSW20_TSH) or (not MTBF_WCC_PCLSW20_TSH) or (not MTBF1_WCC_LSW20_TSH and MTBF1_LSW20_POS)) is true at the end of the PLC cycle,
then SIF01_DB.SIF01_PC20K should be always true at the end of the same cycle
Example case study 1
if (MMoSt and AuAuMoR) at any time before the end of the PLC cycle,
then AuMoSt should be true at the end of the same PLC cycle
Example case study 2
Need for a new specification method  FRET

## Slide 8
FRETish
captures + assists
stores + displays
explains
formalizes
analyzes + diagnoses
connects + exports

## Slide 9: Capturing PLCVerif Requirements with FRET
Structured natural language (FRETish)
  Scope condition component* shall* timing response*
Amenable to formal analysis and simulation
( G (((!( MMoSt and AuAuMoR )) and ( X ( MMoSt and AuAuMoR ))) -> ( X ( F ( AuMoSt and PLC_END ))))) and (( MMoSt and AuAuMoR ) ->
( F ( AuMoSt and PLC_END )))
When (MMoSt & AuAuMoR) the CPC_FB_OnOff shall eventually satisfy AuMoSt & PLC_END
New features
  New “External Mode” facilitates connection with third-party tools e.g. PLCVerif
  New phrase: “at the next/previous occurrence of p, q”
  New requirement templates to support PLC Scan cycles (read sensor values, execute PLC program, write actuator values)

## Slide 10
Case study and integration
if (MMoSt and AuAuMoR) at any time before the end of the PLC cycle,
then AuMoSt should be true at the end of the same PLC cycle
Case study 2
PLC program running in 100s of applications
(UNICOS framework)
PLC program
Variable glossary
1
LTL formula
2
Launch
FRET
1

## Slide 11: Conclusions
Creations of requirements in FRET fits well into the PLCverif verification workflow
Thanks to FRET, PLCverif provides
  validation capabilities for the verification requirements
  bigger expressiveness for complex requirements
It has been applied to 2 real case studies at CERN
To the best of our knowledge, this is the first attempt to specify formal requirements using a structured natural language for PLC program verification
Future work: support of verification of time properties in PLCverif and the support for different type widths in the FRET simulator (e.g. 16/32 bit integers)

## Slide 12
Variable glossary
LTL formula
1
2
Launch
FRET
1
Case study and integration
if (MMoSt and AuAuMoR) at any time before the end of the PLC cycle,
then AuMoSt should be true at the end of the same PLC cycle

## Slide 13
Variable glossary
LTL formula
1
2
Launch
FRET
1
FRET-PLCverif integration

## Slide 14: Case study
Several 100s of PLC-based control systems at CERN are developed with UNICOS
A failure in the UNICOS library would be propagated in all the UNICOS control systems
OnOff object designed to control digital actuators
Part of the (simplified) OnOff specification
FRET property specification
if (MMoSt and AuAuMoR) at any time before the end of the PLC cycle,
then AuMoSt should be true at the end of the same PLC cycle

## Slide 15: Case study
Property validation
thanks to FRET simulator
LTL formula from FRET
FRET
PLCverif

## Slide 16: Case study