## Slide 1: Regulatory Approach for Nuclear Thermal Propulsion
Alexander Pingel1, James Werner1, Alexander Foutch1, 2
1Analytical Mechanics Associates, Inc.
2Missouri University of Science and Technology
Powering the Next Era of Space Exploration

## Slide 2: Acknowledgements
This work was supported by NASA’s Space Technology Mission Directorate (STMD) through the Space Nuclear Propulsion (SNP) Project
Contract No. 80LARC17C0003
Task No. 10.020.000
Regulatory Approach for NTP

## Slide 3: Agenda
Introduction and Assumptions
Regulatory Roadmap
Challenges
Conclusions
Regulatory Approach for NTP

## Slide 4: Introduction and Assumptions
Nuclear Thermal Propulsion (NTP) testing required to mature technology and demonstrate system performance
This work summarizes scoping for NTP system ground testing
  Identifying deliverables for authorization
  Identifying focus areas for testing to support those deliverables
  Identifying challenges to be addressed early in project planning
Assumptions:
  A ground test is the preferred option for NTP testing
  Testing will occur at a Department of Energy (DOE) regulated site
NTP Regulatory Approach
Regulatory Approach for NTP
Notes: In 2022, AMA performed regulatory planning and analysis for the SNP project.
Identified
Note that while ground testing preferred, swim lane included for flight testing.

## Slide 5: Regulatory Roadmap
Diagram intended to show, at a high level, the deliverables and dependencies through the regulatory authorization and testing
  Notes the interdependence between development areas
    Fuel development and testing
    Reactor design
    Regulatory submittals
  Describes dependencies and likely development path
Full diagram included in Appendix to paper
NTP Regulatory Approach
Regulatory Approach for NTP

## Slide 6: Regulatory Roadmap
Overview Diagram
Regulatory Approach for NTP
Notes: Full roadmap – too small to really see, but the presentation will move through the “swim lanes” top to bottom

## Slide 7: Reactor Design Components
Fuels
  Development and characterization of fuels
  Confirm performance under expected conditions
Reactor
  Confirm design constraints will be satisfied
  Confirm mission parameters will be met
Transportation
  Ensure safe transportation of reactor to test site
Regulatory Approach for NTP

## Slide 8: Iterative Fuel Design Essential for Authorization
Novel fuel usage through extensive characterization
Regulatory Approach for NTP
Fuel Design requires iteration and interfaces throughout the system design process

## Slide 9: Reactor Design Options Narrow with Testing
Regulatory Approach for NTP
Reactor design is shaped by fuel requirements as well as mission parameters

## Slide 10: Cask Design Required for Transporting Entire Reactor
Development to begin after initial form factor is estimated, due to lengthy design cycle
Regulatory Approach for NTP
Lessons can be learned from SMR transport of complete reactors

## Slide 11: Facilities Development
Facilities required for technology maturation
Existing
  Fuel fabrication
  Critical testing
  Reactor fabrication
New
  SMART
  Integration
  Ground testing
Regulatory Approach for NTP

## Slide 12: Final Fuel Quantities Require Large Production Line
Regulatory Approach for NTP
Modification of existing licensed facility

## Slide 13: Critical Tests Confirm Neutronic Design
Regulatory Approach for NTP
Critical testing for neutronic design planned early to provide feedback to reactor design

## Slide 14: Reactor Fabrication for Specialized Components
Modification from existing fabrication facility or new facility
Regulatory Approach for NTP
Integration and assembly possible at test site or separate location

## Slide 15: SMART Facility Valuable, but Significant Effort
Advanced fuel testing facility can provide excellent data but adds risk and complexity
Regulatory Approach for NTP
Advanced development options offer technical assurance at increase to cost and schedule

## Slide 16: Design and Approach Dependent on Site, Testing
Affordable designs with less containment possible, if testing results can support fuel performance
Regulatory Approach for NTP
Ground demonstration facility a consideration early to set ground test requirements

## Slide 17: Flight Demonstration Option Considered
Relieves ground environment restrictions in exchange for launch requirements
Regulatory Approach for NTP
Flight demonstration has advantages/disadvantages in regulatory space

## Slide 18: Challenges
Model extrapolation
  Large uncertainties for prospective system analysis
Test authorization with open system
  Fission product release analysis requires fuel characterization
  High speed and temperature exhaust requires extensive containment
    Alternatively high system confidence if exhaust is not captured
Test results from ground test applying to space application
  Environment changes
  Auxiliary systems
    Supporting terrestrial regulations and requirements
Requiring advance planning and specific consideration
Regulatory Approach for NTP

## Slide 19: Conclusions
NTP Ground Testing poses challenges, as with any novel system
Foresight, planning, and cooperation can:
  Analyze proposed system
  Assure safe operation
  Obtain testing authorization
Demonstrating capabilities is the first step
  Flight testing
  Technology maturation
  Faster and more efficient space travel
Regulatory Approach for NTP

## Slide 20: Questions and Contact
Questions?
Happy to discuss further:
  At the AMA or NASA booths
  Email @ alexander.j.pingel@ama-inc.com
Thank you!
Regulatory Approach for NTP