## Slide 1: Effects of Varying the Heat Transfer Coefficient on Engine Performance
Powering the Next Era of Space Exploration
Daria Nikitaeva
Corey Smith (Presenter), Matthew Duchek
Analytical Mechanics Associates, Inc.

## Slide 2: Acknowledgements
This work was supported by NASA’s Space Technology Mission Directorate (STMD) through the Space Nuclear Propulsion (SNP) Project
Contract No. 80LARC17C0003
Task No. 10.020.000

## Slide 3: Agenda
Introduction to Nuclear Thermal Propulsion (NTP) Modeling
Applicable Correlations for Nusselt Number
System Integration and Iterative Solution
X-NTP Heat Transfer Coefficient (HTC) Analysis
Conclusions and Future Work

## Slide 4: Nuclear Thermal Propulsion (NTP) Modeling Overview
NTP engines provide thrust levels comparable to chemical engines while doubling the specific impulse with a hydrogen propellant
  The propellants used are limited by compatibility of engine materials
  Heat is produced via nuclear fission and the heat distribution along the flow channels must be considered
The non-nuclear engine may leverage components previously developed through chemical rocket engine development programs
  Both bleed and expander cycles are applicable in this work
This presentation will focus on the effects on the engine performance by varying the recommended Westinghouse Nusselt (Nu) number within its stated error margins and using hydrogen as the propellant
NTP is a monopropellant system that relies on convective heat transfer from a reactor to the propellant to enable high in-space thrust and specific impulse.

## Slide 5: Applicable Correlations for Nusselt Number [11]
Turbulent heat transfer correlation options for gaseous working fluids in cylindrical tubes.
Many correlation options for Nusselt number exist and each result in different predicted heat transfer behavior.
5
Correlation | Formula | Operability Regime
Dittus-Boelter |  | 
McCarthy & Wolf |  | 
 |  | Not Specified
Westinghouse |  | 
Nunner |  | 
Gnielinski |  | 
Taylor |  | 
Correlation | Formula | Operability Regime
Dittus-Boelter |  | 
McCarthy & Wolf |  | 
 |  | Not Specified
Westinghouse |  | 
Nunner |  | 
Gnielinski |  | 
Taylor |  | 

## Slide 6: System Integration
Each component is coded to have mass and energy conservation as well as a defined process (such as pump characteristics for pressurizing the fluid)
The components are assembled in the model and connected to each other by logic based on cycle specifications set by the user
Standalone components defined by a set of parameters with fluid states as inputs and outputs.
Based on the component parameters and fluid state inputs, the component provides its operating characteristics and fluid outputs INDEPENDENT of the model itself.

## Slide 7: Iterative Solution
The NTP system performance is solved by performing double iteration.
Guess
Non-core channels
Solve reactor and find: &
Guess
Desired Temperature: or
Desired Chamber Pressure:
Adjust
Adjust FSV
Solve the nozzle and get
Set pump inlet and
Does match ?
Does match ?
Is stable? Does match ?
YES
NO
NO
YES
YES
NO
Reactor converges on temperature separately from the engine which converges on and .
Pump
Turbine Circuit
Final Shutoff Valve
Legend
Work/Heat Flow
only Flow
Flow
Control Signals

## Slide 8: X-NTP HTC Analysis
Heat transfer coefficients for convection applications usually come with a error
There is interest in H-NTP engines with Isp as low as 700 seconds (lower risk demonstration as described in AMA/Industry Flight Demo Study)
The chamber temperature is swept to encompass this requirement and provide a general overview of the reference engine performance
If the fuel temperature is treated as the constraint/requirement instead of Isp, this model could show the Isp and other KPPs that result from limiting the fuel temperature with the best- and worst-case HTC values to a value set by material performance capability
Explores impact to internal components and provides upper and lower bounds on expected temperatures.

## Slide 9: H-NTP HTC Variation (Westinghouse Correlation)
Using Reference Reactor / Engine Parameters and a 2700 K Chamber Temperature.
An increase in the HTC leads to a lower magnitude of temperature change than a decrease.
Chamber Temperature: 2700 K | 
Max Cladding Temperature (K) | 
HTC ±0% | 2804.9
HTC +20% | 2764.1
HTC -20% | 2861.3
Max Moderator Surface Temperature (K) | 
HTC ±0% | 237.0
HTC +20% | 236.0
HTC -20% | 277.7
Max CD/Reflector Surface Temperature (K) | 
HTC ±0% | 602.4
HTC +20% | 573.9
HTC -20% | 632.0

## Slide 10: H-NTP HTC and Isp Variation
Keeping the thrust the same lowers the net enthalpy entering the turbine, resulting in inadequate work produced.
Throat diameter decreased to restrict mass flow rate due to high power demand on turbomachinery.
Variation in HTC does not contribute to large variances in engine performance
The reference engine is not designed to support lower Isp values, resulting in the turbine requiring more mass flow rate from decreased turbine inlet temperature
Due to an unoptimized system at lower specific impulse values, the turbine will require additional external power to support pump operation.

## Slide 11: H-NTP HTC and Isp Variation (Continued)
Prediction of the heat transfer coefficient and required chamber temperature impact the max clad temperature.
This result can be used to inform the maximum fuel temperature correlated to the specific impulse. However, an experiment could help narrow the temperature band with a more accurate approximation of the HTC than the recommended Westinghouse correlation.

## Slide 12: X-NTP HTC Conclusions
Varying the HTC ±20% results in predictable maximum temperature trends (lower HTC results in higher material temperatures)
A decrease in HTC will result in a larger magnitude in temperature change than in increase
To maintain the same thrust at lower chamber temperatures:
  Reactor power decreases
  Isp decreases
  Maximum fuel temperature decreases
  Mass flow rate increases
  Turbine inlet temperature decreases resulting in inadequate work produced to drive the engine

## Slide 13: References
[1] Robbins, W. H., and Finger, H. B. An Historical Perspective of the NERVA Nuclear Rocket Engine Technology Program. Publication NASA-CR-187154. Analytical Engineering Corporation, 1991.
[2] Gustafson, J., Kreicicki, M., Swanson, R., Zilka, B., and Witter, J. K. Space Nuclear Propulsion Fuel and Moderator Development Plan Conceptual Testing Reference Design. Virtual Event, 2021.
[3] Nikitaeva, D., Smith, C., D., and Palomares, K. Nuclear Thermal Propulsion Turbomachinery Modeling. Cleveland, OH, 2022.
[4] Emrich, W. Jr. Principles of Nuclear Rocket Propulsion. Butterworth-Heinemann, Kidlington, Oxford, United Kingdom, 2016.
[5] Thomas, G. R. An Interim Study of Single Phase Heat Transfer Correlations Using Hydrogen. Publication WANL-TNR--056, 4233809. 1962, p. WANL-TNR--056, 4233809.
[6] Bartz, D. R. “A Simple Equation for Rapid Estimation of Rocket Nozzle Convective Heat Transfer Coefficients.” Journal of Jet Propulsion, Vol. 27, No. 1, 1957, pp. 49–53. https://doi.org/10.2514/8.12572.
[7] Balje´, O. E. “A Study on Design Criteria and Matching of Turbomachines: Part A—Similarity Relations and Design Criteria of Turbines.” Journal of Engineering for Power, Vol. 84, No. 1, 1962, pp. 83–102. https://doi.org/10.1115/1.3673386.
[8] Balje´, O. E. “A Study on Design Criteria and Matching of Turbomachines: Part B—Compressor and Pump Performance and Matching of Turbocomponents.” Journal of Engineering for Power, Vol. 84, No. 1, 1962, pp. 103–114. https://doi.org/10.1115/1.3673350.
[9] Moran, Michael J., Shapiro, Howard N., Boettner, Daisie D., and Bailey, Margaret B. Fundamentals of Engineering Thermodynamics. John Wiley & Sons, Inc, 2014.
[10] Bell, I. H., Wronski, J., Quoilin, S., and Lemort, V. “Pure and Psuedo-Pure Fluid Thermophysical Property Evaluation and the Open-Source Thermophysical Property Library CoolProp.” Industrial & Engineering Chemistry Research, Vol. 53, 2014, pp. 2498–2508. https://doi.org/10.1021/ie4033999.
[11] Nikitaeva, D., Smith, C., D., and Palomares, K. Comparison of Convective Heat Transfer Correlations and Their Application to Nuclear Thermal Propulsion. Cleveland, OH, 2022.

## Slide 14: Questions?
Daria Nikitaeva (Lead Author)
daria.d.nikitaeva@ama-inc.com
Corey Smith (Presenter)
corey.d.smith@ama-inc.com | corey.d.smith@nasa.gov

## Slide 15
BACK-UP