## Slide 1: Evaluation of Acoustic Propagation in Layered Media using Wave Confinement
Subhashini Chitta, Wave CPC, Inc, Tullahoma, TN, USA
Mary L. Houston, Analytical Mechanics Associates, Inc., Hampton, VA, USA
James H. Stephenson, U.S. Army Combat Capabilities Development Command, Aviation & Missile Center, Hampton, VA, USA
John Steinhoff, Wave CPC, Inc, Tullahoma, TN
Distribution Statement A: Approved for Public Release
1

## Slide 2: Outline
Problem Description
Long Range Propagation
Application to Rotorcraft Noise
Flight Test Comparisons
Conclusions

## Slide 3: Problem Description
Homogeneous medium:
  Diverging straight line propagation
  Radius of curvature increases equally in all directions
  Amplitude loss is equal in all directions
cv

## Slide 4: Problem Description
Homogeneous medium:
  Diverging straight line propagation
  Radius of curvature increases equally in all directions
  Amplitude loss is equal in all directions
Nonhomogeneous medium:
  Curved paths: Diverging or Converging
  Do not propagate equally in all directions
  Radius of curvature increases or decreases
  Amplitude loss is not equal in all directions
cv

## Slide 5: Problem Description
Nonhomogeneous medium:
  Diverging (Example):
    Increasing speed of sound above and below source
    Higher amplitude loss at source height
  Converging (Example):
    Decreasing speed of sound above and below source
    Lower amplitude loss at source height
  Caustic regions:
    Converging regions that form an envelope
    Secondary sources that diffract
Speed of sound
z
s
Speed of sound
z
s

## Slide 6: Long Range Propagation
Wave Confinement (WC) Method
  Grid-based
  Solves linear wave equation,
    represents the wavefront
    All linear propagation effects are automatically accounted for, including diffraction and caustics
    Not feasible to fit short physical wave on a coarse grid
    We call it a “Computational Wave” (CW)
      Has the same linear propagation effects as physical wave of any frequency
Computational wave
Time evolution of a wavefront
S
Physical wave

## Slide 7: Long Range Propagation
Computational wave
Time evolution of a wavefront
S
Wave Confinement (WC) Method
  Numerical Solution
    Prevent numerical errors: Wave equation is modified by adding a confinement term,
    F: dissipation + anti-dissipation
    The solution converges to an eigenfunction: no numerical dissipation
    ~ 4-6 grid cells
    For background wind,
4-6 grid cells
Physical wave

## Slide 8: Long Range Propagation
Computational wave
Time evolution of a wavefront
S
Wave Confinement (WC) Method
  Numerical Solution
    Prevent numerical errors: Wave equation is modified by adding a confinement term,
    F: dissipation + anti-dissipation
    The solution converges to an eigenfunction: no numerical dissipation
    ~ 4-6 grid cells
    For background wind,
4-6 grid cells
centroid
Physical wave

## Slide 9: Long Range Propagation
Integral Calculations
  Ideal Case: Axisymmetric point source of amplitude, :
    Amplitude of CW
    Amplitude of physical wave
      can be specified as a function of frequency or time and independent of direction.
    SPL of physical wave
    Arrival time

## Slide 10: Long Range Propagation
Integral Calculations
  Ideal Case: Axisymmetric point source of amplitude, :
    Amplitude of CW
    Amplitude of physical wave
      can be specified as a function of frequency or time and independent of direction.
    SPL of physical wave
    Arrival time
  Reality: Angle dependent source of amplitude, :
    Need emission angles, , corresponding to far field points
    =
    Initialize multicomponent, , to carry emission coordinates
    SPL of physical wave
    Arrival time
Ground

## Slide 11: Long Range Propagation
Validation for point source
  Case 1: Wind blowing toward +x direction,
Minimal deviation in azimuth angle due to wind
Ray markers
WC
Homogeneous medium
Azimuth angle contours

## Slide 12: Long Range Propagation
Validation for point source
  Case 1: Wind blowing toward +x direction,
Expanding (upward bending)
Contracting (downward bending)
Ray markers
WC
Elevation angle contours

## Slide 13: Long Range Propagation
Elevation angle contours
Ray markers
WC
Homogeneous medium
Validation for point source
  Case 1: Wind blowing toward +x direction,

## Slide 14: Long Range Propagation
Elevation angle contours
Downward bending
Amplitude loss is lower
WC
Homogeneous medium
Validation for point source
  Case 1: Wind blowing toward +x direction,

## Slide 15: Long Range Propagation
Validation for point source
  Case 2:
Elevation angle contours
Ray markers
WC

## Slide 16: Long Range Propagation
Elevation angle contours
Validation for point source
  Case 2:
  Contract : propagation is in the same direction as wind
  Expand : propagation is opposite to wind
Ray markers
WC

## Slide 17: Application to Rotorcraft Noise
Source Spectra at R = 100 ft
  Linear microphone array deployed over bare, level ground
    Testing begins at dawn when winds are lowest
  Sound levels are recorded as the rotorcraft passes over the microphone array
    Each microphone is at a different emission angle
    Source noise data acquired between x = -2000 ft and x = 2000 ft
    Spectra taken every ½ second
OASPL [dB]

## Slide 18: Application to Rotorcraft Noise
Source Spectra at R = 100 ft
  Noise is back propagated to representative hemisphere of 100 ft radius surrounding the aircraft
    (Assuming straight ray propagation)
  Propagation effects are removed
    Spherical spreading
    Atmospheric absorption
    Pressure doubling due to ground reflection
OASPL [dB]

## Slide 19: Application to Rotorcraft Noise
Far Field Spectra
  Inverse distance weighting scheme is used to provide spectra at emission coordinates
Ground

## Slide 20: Flight Test Comparisons
Computational Set-up
  Source location
Run # xs [ft] ys [ft] zs [ft]
038403 -8451 -147 147
042420 -8331 -148 163
  Grid size:
    1750 × 724× 356
  Computational domain:
    14000 ft × 5792 ft × 2848 ft
    Grid cell size: 8 ft
    ~ 18 grid points
  Microphone locations:
    4 on advancing side
    4 on retreating side
Mic # | x [ft] | y [ft] | z [ft] | Adjusted z [ft]
8 | -1120 | 1133 | -3 | 0
12 | -1127 | -1139 | 8 | 0
17 | -554 | 981 | -3 | 0
18 | -565 | -981 | 6 | 0
42 | 576 | 992 | -5 | 0
43 | 575 | -974 | 5 | 0
59 | 1705 | 977 | -5 | 0
60 | 1705 | -983 | 3 | 0

## Slide 21: Flight Test Comparisons
Computational Set-up
  Atmospheric Conditions
    Variations are only in z direction
    Temperature is measured with 10 ft resolution over 500 ft
    Wind is measured at 12 altitudes over 1000 ft
    The data is fitted to a curve
  Ground Conditions
    Flat ground
    Perfectly reflecting

## Slide 22: Flight Test Comparisons
Limitations
  Source variation due to wind
    Hemisphere data are measured ~7000 ft further than the source location
    Crosswind conditions can significantly impact the tail rotor source amplitudes
  Lack of information above the hemisphere
  Cannot extract separate emission angles in caustic/intersecting regions
  Perfectly reflecting ground is assumed
  No atmospheric turbulence is currently solved
OASPL [dB]
Notes: Remove microphones used for comparison

## Slide 23: Flight Test Comparisons
Run 038403
Mic # |  | 
8 | 3.0 | 188.1
12 | 3.1 | 171.5
17 | 3.7 | 186.4
18 | 4.0 | 173.2
42 | 5.4 | 185.4
43 | 5.7 | 173.9
59 | 7.1 | 184.6
60 | 7.2 | 174.2
Mic # |  | 
8 | 3.0 | 188.1
12 | 3.1 | 171.5
17 | 3.7 | 186.4
18 | 4.0 | 173.2
42 | 5.4 | 185.4
43 | 5.7 | 173.9
59 | 7.1 | 184.6
60 | 7.2 | 174.2
OASPL [dB]
Notes: Adjust the microphone locations

## Slide 24: Flight Test Comparisons
Run 038403
Sound from a small region on the source hemisphere reaches the microphones
Emission coordinates for the microphones are outside the hemisphere
59
8
60
12
Mic # |  | 
8 | 3.0 | 188.1
12 | 3.1 | 171.5
17 | 3.7 | 186.4
18 | 4.0 | 173.2
42 | 5.4 | 185.4
43 | 5.7 | 173.9
59 | 7.1 | 184.6
60 | 7.2 | 174.2
Mic # |  | 
8 | 3.0 | 188.1
12 | 3.1 | 171.5
17 | 3.7 | 186.4
18 | 4.0 | 173.2
42 | 5.4 | 185.4
43 | 5.7 | 173.9
59 | 7.1 | 184.6
60 | 7.2 | 174.2
OASPL [dB]
Notes: Adjust the microphone locations

## Slide 25: Flight Test Comparisons
Run 038403
Sound from a small region on the source hemisphere reaches the microphones
Emission coordinates for the microphones are outside the hemisphere
Source SPL for relevant microphones
Mic 59
Mic 60
Mic # |  | 
8 | 3.0 | 188.1
12 | 3.1 | 171.5
17 | 3.7 | 186.4
18 | 4.0 | 173.2
42 | 5.4 | 185.4
43 | 5.7 | 173.9
59 | 7.1 | 184.6
60 | 7.2 | 174.2
Mic # |  | 
8 | 3.0 | 188.1
12 | 3.1 | 171.5
17 | 3.7 | 186.4
18 | 4.0 | 173.2
42 | 5.4 | 185.4
43 | 5.7 | 173.9
59 | 7.1 | 184.6
60 | 7.2 | 174.2
59
8
60
12
OASPL [dB]
Notes: Adjust the microphone locations

## Slide 26: Flight Test Comparisons
Run 038403
On y = 0 plane

## Slide 27: Flight Test Comparisons
Run 038403
Time snapshot of CW
On y = 0 plane
Stronger wave due to ducting

## Slide 28: Flight Test Comparisons
Run 038403
Microphone 8 Microphone 12
Microphone 17 Microphone 18
Microphone 42 Microphone 43
Microphone 59 Microphone 60
Good agreement overall

## Slide 29: Flight Test Comparisons
Run 038403
  Standard deviation of each measured harmonic for 1.5 s of data is used for comparison
  Variation in amplitude is significant
Notes: the variation in amplitude is significant over even 1.5 seconds of data"

## Slide 30: Flight Test Comparisons
Run 038403
Atmospheric ducting causes the signal to be 6 dB higher than straight ray
Good agreement overall
Measured main rotor harmonics stronger on retreating side: Source SPL same for both sides
Microphone 8 Microphone 12
Notes: 96, 192, 288, 384??

## Slide 31: Flight Test Comparisons
Run 038403
Atmospheric ducting causes the signal to be 6 dB higher than straight ray
Good agreement overall
Measured main rotor harmonics stronger on retreating side: Source SPL same for both sides
Microphone 17 Microphone 18
Notes: 96, 192, 288, 384??

## Slide 32: Flight Test Comparisons
Run 038403
Atmospheric ducting causes the signal to be 6 dB higher than straight ray
Good agreement overall
Measured main rotor harmonics stronger on retreating side: Source SPL same for both sides
Over prediction at higher tail rotor harmonics
  Source amplitudes of tail rotor harmonics are not corrected for wind
  Significant variation in TR harmonics present across 1.5 seconds of data
Microphone 42 Microphone 43
Notes: 96, 192, 288, 384??

## Slide 33: Flight Test Comparisons
Run 038403
Atmospheric ducting causes the signal to be 6 dB higher than straight ray
Good agreement overall
Measured main rotor harmonics stronger on retreating side: Source SPL same for both sides
Over prediction at higher tail rotor harmonics
  Source amplitudes of tail rotor harmonics are not corrected for wind
  Significant variation in TR harmonics present across 1.5 seconds of data
Microphone 59 Microphone 60
Notes: 96, 192, 288, 384??

## Slide 34: Flight Test Comparisons
Run 042420
Source SPL for all microphones
59
8
60
12
Mic # |  | 
8 | -2.8 | 190.5
12 | -3.1 | 174.7
17 | -2.9 | 189.1
18 | -3.1 | 176.4
42 | -3.0 | 187.1
43 | -3.0 | 177.0
59 | -3.1 | 185.0
60 | -3.0 | 177.1
Mic # |  | 
8 | -2.8 | 190.5
12 | -3.1 | 174.7
17 | -2.9 | 189.1
18 | -3.1 | 176.4
42 | -3.0 | 187.1
43 | -3.0 | 177.0
59 | -3.1 | 185.0
60 | -3.0 | 177.1
OASPL [dB]

## Slide 35: Flight Test Comparisons
Run 042420
On y = 0 plane
Time snapshot of CW
Upward bending: weaker wave
Caustic: Stronger wave

## Slide 36: Flight Test Comparisons
Run 042420
Good agreement overall
Upward bending causes the signal to be 3 dB lower than straight ray
Microphone 8 Microphone 12

## Slide 37: Flight Test Comparisons
Run 042420
Microphone 17 Microphone 18
Good agreement overall
Upward bending causes the signal to be 3 dB lower than straight ray

## Slide 38: Flight Test Comparisons
Run 042420
Microphone 42 Microphone 43
Good agreement overall
Upward bending causes the signal to be 3 dB lower than straight ray
Over prediction at higher tail rotor harmonics
  Source amplitudes of tail rotor harmonics are not corrected for wind
  Significant variation in TR harmonics present across 1.5 seconds of data

## Slide 39: Flight Test Comparisons
Run 042420
Microphone 59 Microphone 60
Good agreement overall
Upward bending causes the signal to be 3 dB lower than straight ray
Over prediction at higher tail rotor harmonics
  Source amplitudes of tail rotor harmonics are not corrected for wind
  Significant variation in TR harmonics present across 1.5 seconds of data

## Slide 40: Conclusions
Validations for propagation show that WC can accurately capture propagation effects due to wind and temperature
WC method also compares quite favorably to measured acoustic emissions of rotorcraft vehicles even under adverse weather conditions
Crosswind conditions can significantly impact the tail rotor source amplitudes, which will significantly affect long range predictions
Sound from above the hemisphere can also reach ground when the there are duct-like atmospheric regions

## Slide 41: Acknowledgments
Dr. Frank Caradonna
SBIR funding from Army Contracting Command under Contract # W911W6-19-C-0024

## Slide 42: Long Range Propagation
Computational Set-up
GROUND
SOURCE SPHERE
s
    Immersed boundary

## Slide 43: Long Range Propagation
Computational Set-up
GROUND
SOURCE SPHERE
ABL
ABL
ABL
s
    Immersed boundary
Solve advection equation along the normal direction

## Slide 44: Elevation Angles for both Conditions
Elevation Angle contours for 038403 using WC
Elevation Angle contours for 042420 using ray tracing

## Slide 45: Long Range Propagation
Integral Calculations
  Ideal Case: Axisymmetric point source of amplitude, :
    Amplitude of CW adjusted to point source, = . Also, called as attenuation factor, .
    Amplitude of physical wave, or
      can be specified as a function of frequency or time and independent of direction.
    SPL of physical wave,
    Arrival time, ds
  Reality: Angle dependent source of amplitude, :
    Need emission angles, corresponding to far field points.
    =,
    Initialize multicomponent, , to carry emission coordinates
Ground

## Slide 46: CW Propagating in Domain
46
CW on ground and x-z plane
  On x-z plane, there are direct and reflected wave fronts
  On ground plane, reflected and direct wavefronts are in phase

## Slide 47: Flight Test Comparisons
Run 038403
On y = 0 plane
Time snapshot of CW
Intersecting waves overlap
Amplitude will be sum of the waves
Emission angles will be average values
Since the region of interest is so small, Source SPL will be the same for each one separately