## Slide 1: 4pPA1 - Turbulence effects on shaped booms: Central composite design of modeled atmospheric turbulence parameters for sonic boom propagation
Will Doebler1, Peter Parker1, Robert Downs2, and Alexandra Loubeau1 184th Meeting of the Acoustical Society of America May 11, 2023 1NASA Langley Research Center, 2US DOT Volpe National Transportation Systems Center
www.nasa.gov

## Slide 2: Turbulence effects on shaped booms
4pPA1 Central composite design of modeled atmospheric turbulence parameters for sonic boom propagation William Doebler, Peter Parker, Robert Downs, Alexandra Loubeau
4pPA2 Propagation simulations using KZKFourier Robert Downs, Michael Barzach, Will Doebler, Peter Parker, Alexandra Loubeau, Joel Lonzaga
4pPA3 Finite impulse response filter development Robert Downs, Michael Barzach, Jacob Klos, Joel Lonzaga, William Doebler, Peter Parker, Alexandra Loubeau
2

## Slide 3: Outline
Background
  Turbulence and sonic boom modeling software (PCBoom, KZKFourier)
Collect data
  Turbulence parameters using atmospheric models
Design of Experiments approach
  Select turbulence parameters
Following presentations describe:
  KZKFourier propagation, improved FIR filter generation for PCBoom, and code validation
3

## Slide 4: Turbulence causes spiking and rounding of N-wave booms
Atmospheric Boundary Layer
Need to predict loudness and variability for community noise surveys
4
Image from NASA/CR-2022-220509
Measurements from 16 microphones
spaced ~100 ft (30.5 m) apart

## Slide 5: Stout and Sparrow’s KZKFourier turbulence model solves:
diffraction
thermoviscous absorption
nonlinearity
scalar turbulence
vector turbulence
relaxation
Input
plane
waveform
Output
turbulized
waveforms
KZKFourier
Turbulence Parameters
Ambient Parameters
5
Image from NASA/CR-2022-220509

## Slide 6: KZKFourier can take days to run. FIR filters provide fast, approximate results.
Input
plane
waveform
Output
turbulized
waveforms
KZKFourier
Input
plane
waveform
Output
turbulized
waveforms
FIR Filter Bank
Filter 1
Filter 2
Filter 3
Filter N
Slower,
Faster,
6
Ideally the same as KZKFourier results
Method 1
Method 2

## Slide 7: FIR Filters are implemented in PCBoom. Current filters are inaccurate for shaped signatures.
7
Predicted level for -1 standard deviation is greater than the mean

## Slide 8: Improve PCBoom filters by sampling atmospheric KZKFourier inputs.
KZKFourier Atmospheric Inputs:
Ambient parameters
  Pressure
  Temperature
  Relative humidity
Turbulence parameters
  Friction velocity
  Mixed-layer velocity scale
  Surface-layer temperature scale
  Atmospheric boundary layer height
Other Inputs:
Waveform information
Propagation resolution and other settings
What are typical daytime ranges across the US?
Use Design of Experiments principles to efficiently sample these 7 factors to run KZKFourier and update FIR filters
8

## Slide 9: Ambient and turbulence quantities were collected or derived from atmospheric model databases.
Two databases used for more robust statistical results
  Climate Forecast System Version 2 (CFSv2)
  European Centre for Medium-range Weather Forecast Reanalysis 5 (ERA5)
Parameter | CFSv2 | ERA5
Pressure | Yes | Yes
Temperature | Yes | Yes
Relative Humidity | Yes | Derived
Friction velocity | Yes | Yes
Mixed-layer velocity scale | Derived | Derived
Surface-layer temperature scale | Derived | Derived
Atmospheric boundary layer height | Yes | Yes
Parameter | CFSv2 | ERA5
Pressure | Yes | Yes
Temperature | Yes | Yes
Relative Humidity | Yes | Derived
 | Yes | Yes
 | Derived | Derived
 | Derived | Derived
 | Yes | Yes
Availability of KZKFourier Input Parameters
9

## Slide 10: Daytime ambient and turbulence parameters were grouped by season and 5th and 95th percentiles of each were computed.
Winter
Spring
Summer
Fall
CFSv2 median and 5th to 95th percentiles
Parameter | Min 5th Percentile | Max 95th Percentile
ABL (m) | 24.4 | 4034.7
(m/s) | 0.025 | 0.98
(m/s) | 0.102 | 3.83
(K) | -1.96 | 0.21
(atm) | 0.83020 | 1.01897
(K) | 255.68 | 326.68
(%) | 5.10 | 99.8
Parameter | Min 5th Percentile | Max 95th Percentile
ABL (m) | 24.4 | 4034.7
 | 0.025 | 0.98
 | 0.102 | 3.83
 | -1.96 | 0.21
 | 0.83020 | 1.01897
 | 255.68 | 326.68
 | 5.10 | 99.8
ERA5 and CFSv2 10-year, hourly, daytime, seasonally-pooled stats
10
Location
Location
Location
Location

## Slide 11: Daytime ambient and turbulence parameters were grouped by season and 5th and 95th percentiles of each were computed.
Winter
Spring
Summer
Fall
CFSv2 median and 5th to 95th percentiles
Parameter | Min 5th Percentile | Max 95th Percentile
ABL (m) | 24.4 | 4034.7
(m/s) | 0.025 | 0.98
(m/s) | 0.102 | 3.83
(K) | -1.96 | 0.21
(atm) | 0.83020 | 1.01897
(K) | 255.68 | 326.68
(%) | 5.10 | 99.8
Parameter | Min 5th Percentile | Max 95th Percentile
ABL (m) | 24.4 | 4034.7
 | 0.025 | 0.98
 | 0.102 | 3.83
 | -1.96 | 0.21
 | 0.83020 | 1.01897
 | 255.68 | 326.68
 | 5.10 | 99.8
ERA5 and CFSv2 10-year, hourly, daytime, seasonally-pooled stats
11
How to sample 7
factors efficiently?
Location
Location
Location
Location

## Slide 12: Use design of experiments principles to optimally sample KZKFourier inputs.
Full factorial
Fractional factorial
Response = 1 + A + B + C + AB + AC + BC + ABC
Response = [1 + ABC] + [A + BC] + [B + AC] + [C + AB]
3 factors, 2 levels -> 8 cases, 8 unknowns
4 cases, 4 “aliased” unknowns
Useful if interaction terms, e.g. AB, are negligible
Example:
12
Animated slide

## Slide 13: Use design of experiments principles to optimally sample KZKFourier inputs
Full factorial, 3 levels
Response = 1 + A + B + C + A2 + B2 + C2 + AB +AB + BC
3 factors, 3 levels -> 27 cases
15 cases
Useful if some curvature is expected and if extrema are lower priority
Example:
Central Composite
Animated slide
13

## Slide 14: Other designs considered
Fractional Factorial
Definitive Screening
Box-Behnken
Factorial
Central Composite
Animated slide
14

## Slide 15: Candidate designs to sample 7 KZKFourier inputs
 | Unique Cases | Factor Levels | Shape
Full Factorial | 37=2187 57=78125 | 3 or 5 | Cube
Definitive Screening Design | 21 | 3 | Reduced cube
Minimum-Run Resolution V (MR5) Fractional Factorial (FF) | 31 | 2+center point | Cube
Central Composite Design (CCD) with MR5 | 45 | 5 | Sphere
Box-Behnken | 57 | 3 | Sphere
CCD with Regular FF | 79 | 5 | Sphere
Chose CCD with MR5 because it avoids the unlikely extrema and requires only 45 cases to be run.
15
Notes: https://functionbay.com/documentation/onlinehelp/default.htm#!Documents/resolutionofexperimentaldesigns.htm
Resolution of Experimental Designs
An experimental design is of resolution 𝑅 if no 𝑝− factor effect is aliased with another effect containing less than 𝑅−𝑝 factors. When the fractional factorial design is developed, the defining relation (𝐼) is composed of roman letters. As an example, 2^(3−1) design is constructed with the defining relation 𝐼 = 𝐴𝐵𝐶 or 𝐼=−𝐴𝐵𝐶. In this case, the minimum number of letters in the defining relations represents the resolution of design. Hence, 2^(3−1) design is called a resolution III.
1. Resolution III designs. These are designs in which no main effects are aliased with any other main effect, but main effects aliased with two-factor interactions and two-factor interactions may be aliased with each other. A 2^(3−1) design with 𝐼=𝐴𝐵𝐶 is of resolution III (2_𝐼𝐼𝐼^(3−1)). These are main effects only designs.
2. Resolution IV designs. These are designs in which no main effect is aliased with any other main effect or with any two-factor interaction, but two-factor interactions are aliased with other. A 2^(4−1) design with 𝐼=𝐴𝐵𝐶𝐷 is of resolution IV (2_𝐼𝑉^(4−1)). These are main effects clear designs.
3. Resolution V designs. These are designs in which no main effect or two-factor interaction is aliased with any other main effect or two-factor interaction, but two-factor interactions are aliased with three-factor interactions. A 2^(5−1) design with 𝐼=𝐴𝐵𝐶𝐷𝐸 is of resolution V (2_𝑉^(5−1)). These are two-factor interactions clear designs.

## Slide 16: Central Composite Design
45 “cases,” which are combinations of the 7 ambient and turbulence input parameters to KZKFourier.
Extrema (1) of each factor is only sampled when other quantities are at their midpoint (0)
Many interior points
Case | Factor 1 | Factor 2 | Factor 3 | Factor 4 | Factor 5 | Factor 6 | Factor 7
1 | -0.61 | -0.61 | -0.61 | 0.61 | -0.61 | -0.61 | 0.61
2 | -0.61 | 0.61 | -0.61 | -0.61 | 0.61 | -0.61 | -0.61
3 | -0.61 | 0.61 | 0.61 | 0.61 | -0.61 | -0.61 | 0.61
4 | -0.61 | -0.61 | 0.61 | -0.61 | -0.61 | -0.61 | 0.61
5 | 0.61 | 0.61 | 0.61 | 0.61 | 0.61 | 0.61 | 0.61
6 | -0.61 | -0.61 | -0.61 | -0.61 | 0.61 | 0.61 | -0.61
7 | 0.61 | 0.61 | -0.61 | -0.61 | -0.61 | 0.61 | -0.61
8 | -0.61 | 0.61 | -0.61 | 0.61 | 0.61 | 0.61 | -0.61
9 | 0.61 | -0.61 | 0.61 | -0.61 | 0.61 | -0.61 | -0.61
10 | 0.61 | 0.61 | -0.61 | 0.61 | -0.61 | 0.61 | 0.61
11 | -0.61 | -0.61 | -0.61 | 0.61 | -0.61 | 0.61 | -0.61
12 | -0.61 | -0.61 | -0.61 | 0.61 | 0.61 | 0.61 | 0.61
13 | -0.61 | -0.61 | 0.61 | 0.61 | 0.61 | -0.61 | -0.61
14 | 0.61 | -0.61 | -0.61 | 0.61 | 0.61 | -0.61 | -0.61
15 | 0.61 | 0.61 | -0.61 | 0.61 | -0.61 | -0.61 | -0.61
16 | -0.61 | 0.61 | 0.61 | -0.61 | -0.61 | -0.61 | -0.61
17 | 0.61 | 0.61 | -0.61 | -0.61 | 0.61 | 0.61 | 0.61
18 | 0.61 | 0.61 | 0.61 | -0.61 | -0.61 | 0.61 | 0.61
19 | -0.61 | 0.61 | 0.61 | -0.61 | 0.61 | 0.61 | -0.61
20 | 0.61 | 0.61 | 0.61 | 0.61 | 0.61 | -0.61 | -0.61
21 | 0.61 | -0.61 | -0.61 | -0.61 | 0.61 | -0.61 | 0.61
22 | 0.61 | -0.61 | -0.61 | -0.61 | -0.61 | 0.61 | 0.61
23 | 0.61 | -0.61 | 0.61 | 0.61 | 0.61 | 0.61 | -0.61
24 | -0.61 | -0.61 | 0.61 | -0.61 | -0.61 | 0.61 | -0.61
25 | 0.61 | -0.61 | 0.61 | 0.61 | -0.61 | -0.61 | -0.61
26 | -0.61 | 0.61 | 0.61 | -0.61 | 0.61 | -0.61 | 0.61
27 | 0.61 | 0.61 | -0.61 | -0.61 | -0.61 | -0.61 | 0.61
28 | -0.61 | -0.61 | 0.61 | 0.61 | -0.61 | 0.61 | 0.61
29 | 0.61 | -0.61 | 0.61 | 0.61 | 0.61 | -0.61 | 0.61
30 | -0.61 | 0.61 | -0.61 | -0.61 | -0.61 | 0.61 | 0.61
31 | -1 | 0 | 0 | 0 | 0 | 0 | 0
32 | 1 | 0 | 0 | 0 | 0 | 0 | 0
33 | 0 | -1 | 0 | 0 | 0 | 0 | 0
34 | 0 | 1 | 0 | 0 | 0 | 0 | 0
35 | 0 | 0 | -1 | 0 | 0 | 0 | 0
36 | 0 | 0 | 1 | 0 | 0 | 0 | 0
37 | 0 | 0 | 0 | -1 | 0 | 0 | 0
38 | 0 | 0 | 0 | 1 | 0 | 0 | 0
39 | 0 | 0 | 0 | 0 | -1 | 0 | 0
40 | 0 | 0 | 0 | 0 | 1 | 0 | 0
41 | 0 | 0 | 0 | 0 | 0 | -1 | 0
42 | 0 | 0 | 0 | 0 | 0 | 1 | 0
43 | 0 | 0 | 0 | 0 | 0 | 0 | -1
44 | 0 | 0 | 0 | 0 | 0 | 0 | 1
45 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Central Composite
16
Irregular fraction
Axial points
Center point
Normalized Factor Selection Table
Animated slide

## Slide 17: Ambient and turbulence parameter densities and CCD sampling points (red)
17
ABL (m)
(m/s)
(m/s)
(K)
(%)
(atm)
(K)
ABL (m)
(m/s)
(m/s)
(K)
(%)
(atm)
(K)

## Slide 18: Next steps and summary
Collected turbulence parameters
Next steps
  Propagate the 45 cases using KZKFourier
  Compute turbulence approximation filters
  Validate filters with additional cases
  Implement in PCBoom
Summary
PCBoom module: FiltView
N-wave filters ineffective for shaped supersonic waveforms
has few user-selectable atmospheric inputs
Central Composite Design
18
Location
Animated slide

## Slide 19: Quesst
www.nasa.gov |
19
william.j.doebler@nasa.gov
19

## Slide 20: Derived parameters from CFSv2
Mixed-layer velocity scale
  Boundary layer height is provided
  Surface temperature is provided
  Sensible heat flux is provided
  Density is derived using Ideal Gas Law
      Surface pressure is provided
      J/kg K
  gravity = 9.81 m/s2
  specific heat at constant pressure kJ / kg K
Surface-layer temperature scale
20

## Slide 21: Derived parameters from ERA5
Relative humidity at 2 meters above ground
    Temperature in Kelvin at 2 m is provided
    Dewpoint temperature in Kelvin at 2 m is provided
Mixed-layer velocity scale
    Boundary layer height is provided
    Skin temperature is provided
    Instantaneous sensible heat flux is provided
    Density is derived using the Ideal Gas Law
      Surface pressure is provided
      J/kg K
    gravity = 9.81 m/s2
    specific heat at constant pressure kJ / kg K
Surface-layer temperature scale
21

## Slide 22: Note on heat flux sign convention
CFSv2 and ERA5 heat flux have opposite sign convention
  “The ECMWF convention for vertical fluxes is positive downwards”
Ostashev and Wilson (2016), “the sensible heat flux [is] from the surface to the overlying air”
Need to multiply ERA5 heat flux by -1 to match Ostashev and Wilson model used in KZKFourier
22
+
KZKFourier sign convention:
Heat flux from the surface to the air
CFSv2
ERA5