## Slide 1
NASA Projected HTPB Useage 2023-2029
Tim Lawrence/ Bobby Taylor
May 22, 2023
JANNAF HTPB Specification Workshop

## Slide 2: Background
Beginning in 2032, SLS Boosters will make the transition from PBAN to HTPB
This change could have a large impact on the HTPB polymer market both in price and specifications
First flight of BOLE is scheduled for 2032, however between 2023 and 2029 seven motor loadings are planned
NASA also utilizes HTPB motors for Booster Separation and Launch Abort for each SLS flight
Commercial Crew also uses HTPB boosters (AJ60 and GEM 63) and will transition to GEM63XL
HTPB usage across the large solid rocket motor industry is projected to significantly grow during this time period due to new programs – Vulcan(GEM63XL), Sentinel, GBI, BOLE

## Slide 3: Comparison of SLS and BOLE
Motor Performance:
3.6Mlbf Thrust, 1015 psi MEOP
5 Segment PBAN Propellant
PBI-NBR Insulation
Heritage D6AC Steel Cases
Aft Skirt & Nozzle:
ENKA Material for Nozzle
Natural Rubber Flex Bearing
Heritage Shuttle Hydraulic TVC
Hydrazine-driven APU
Forward Skirt & Avionics:
Heritage nose cone & skirt
SLS Avionics
Heritage BSM Placement
SLS Booster
BOLE Booster
(>+3mT to TLI)
Motor Performance:
4.2Mlbf Thrust, 1330 psi MEOP
5 Segment HTPB Propellant
AFEPDM + PBI-NBR Insulation
T1100 Composite Cases
Aft Skirt & Nozzle:
ENKA Material for Nozzle
Silicone Elastomer Flex Seal
Battery-driven EHA TVC
Thermal or Li-Ion Batteries
Forward Skirt & Avionics:
Integral nose cone & frustum
Modified SLS Avionics
More capable forward skirt
Optimized BSM Placement

## Slide 4: Propellant Development
BOLE Propellant is HTPB, 88% solids with R45M polymer binder
R45M will be procured per Northrop Grumman internal specification S273017
BOLE motor contains ~150klbs of R45M
Motor | Estimated Purchase Date | Quantity (klbs)
DM-1 | 2022 | 150
DM-2 | 2023 | 150
DM-3 | 2024 | 150
QM-1 | 2025 | 150
QM-2 | 2026 | 150
EM-9 | 2027 | 300

## Slide 5: HTPB Polymer Usage in NASA and Space Force Flights
BOLE igniter will use BSM HTPB propellant
  Quantities insignificant for both systems at two igniters (~50 lbs) and ten BSM’s (~150 lbs) per flight set
Launch Abort System for Orion utilized HTPB in the Jettison Motor and the Abort Motor
  Estimate 100 lbs of polymer per Jettison Motor
  Estimate 560 lbs of polymer per Abort Motor
Commercial Crew will be using GEM63
  Estimate up to 19,500 lbs of polymer per launch (based on two boosters)
Space Force will be using Vulcan (GEM63XL)
  Estimate up to 60,000 lbs of polymer per launch (based on six boosters)

## Slide 6: Summary
SLS Booster will purchase R45M per commercial specification at 150klbs per year beginning in 2022, increasing to 300 klbs per year in 2028
NG is carrying a risk for R45M lot variability
  Will be assessed as we move forward
Total SLS, Commercial Crew and Space Force motors using HTPB is significant and a driving case for production
  One Flight of SLS uses 300,643 lbs of HTPB
  One Flight of Commercial Crew uses 19,500 lbs of HTPB
  One Flight of Vulcan can use up to 60,000 pbs of HTPB