## Slide 1: A hybrid transfer function procedure for broadband auralization within small flight vehicle interiors
Albert R. Allen
Siddhartha Krishnamurthy
NASA Langley Research Center
Hampton, VA 23681, USA

## Slide 2: Background
Urban Air Mobility
  short, low altitude missions
  small-medium complement
  multiple electric propulsors
  VTOL, hover, and cruise capabilities
  https://www.nasa.gov/uam-overview/
37.5 nmi

## Slide 3: Motivation and Goals
UAM community (exterior) noise has received significant interest, but interior cabin noise is also expected to be an issue
  Numerous propulsor noise sources near fuselage
  Electric drive systems with rapidly varying RPM
Existing UAM cabin flight recordings are limited in availability
  Early design stage interior auralization is desired
Interior auralization by simulation
  Utilize existing, widely used vibroacoustic simulation techniques
  Ability to accept general excitations
  Broad frequency range for auralization

## Slide 4: Possible Applications
Flight simulators
Psychoacoustic testing
Design guidance
https://www.nasa.gov/offices/setmo/facilities/vertical_motion_simulator

## Slide 5: Scenario Considered
6-passenger UAM Lift+Cruise reference vehicle*
Simplifications & assumptions
  carbon laminate skin & frames
  acrylic windshields
  wing, tail, & interior trim removed
  frequency independent damping
  no fuselage scattering
*C. Silva et al., VTOL Urban Air Mobility concept vehicles for technology development. In Proceedings of the 2018 Aviation Technology, Integration, and Operations Conference, Atlanta, GA, June 2018.

## Slide 6: Modeling Procedure
(IFFT & sum contributions)
discretized excitation field
transfer function dataset
unit normal force

## Slide 7: Hybrid Modeling Procedure
point-by-point response
phase information retained
model building and execution difficult at high frequencies
subsystem average response
phase information is lost
smaller matrices, fast solve times
Finite Element Analysis
Statistical Energy Analysis
high frequencies
low frequencies

## Slide 8: Finite Element Component
Populating Hm,k=pk/fm at low frequencies using FE modal decomposition...
mode shapes
unit force
natural frequencies
Green's function for enclosed acoustic volume

## Slide 9: SEA Component I
1) Power input ( ) is now applied to a subsystem by specifying a spatially nonspecific MS normal force:
2) (Solve) Loss factor matrices are inverted resulting in subsystem energies
3) Average MS pressure within the interior determined:
Populating Hm,k=pk/fm at high frequencies using SEA...
*J. E. Manning, Formulation of SEA parameters using mobility functions. Phil. Trans. R. Soc. Lond. A, 346:477–488, 1994.
mechanical conductance

## Slide 10: SEA Component II
4) MS force and resulting MS interior pressures are "projected" onto FE resolution to populate
5) Phase is reintroduced assuming interior diffuse field (θ uniformly sampled from [-π, π])
*M. N. Ichchou, et al. Equivalent “rain on the roof” loads for random spatially correlated excitations in the mid-high frequency range. JSV, 322:926–940, 2009.
NOTE: An equivalent MS force is determined assuming diffuse field conditions on exterior (approx.) by using a correction factor*

## Slide 11: Transfer Function Dataset
500 Hz

## Slide 12: Noise Source
Fuselage exterior acoustic field due to propulsors during hover
1. Acoustic Predictions for each Rotor
NASA Auralization Framework
2. Sound Synthesis and Propagation
3. Auralized sound on fuselage exterior
Broadband Self Noise
Periodic Loading + Blade Thickness Noise

## Slide 13: Auralization
interior
exterior

## Slide 14
Conclusions
Hybrid auralization procedure demonstrated
  Deterministic, FE-based detail at low frequencies
  May be likened to an equalizer array with detail corresponding to the SEA subsystem partitioning scheme at high frequencies
  Congruous transfer function dataset amenable to various dynamic loads
  Adjustable simulation fidelity
Future Focus
Turbulent boundary layer excitation
Implementation within flight simulator systems

## Slide 15
Backup Slides

## Slide 16: Fuselage Properties

## Slide 17: Representative pressure spectrum from eight propulsors

## Slide 18: Fuselage/Interior Mode Count
1393 structural modes
502 acoustic modes
Modes included in analysis based on sliding envelope sized by a rudimentary convergence study

## Slide 19: Interior Sound Field Diffusivity

## Slide 20: Source Modeling

## Slide 21: Source Modeling