## Slide 1: An Overview of the Proprotor Performance Test in the 14- by 22-Foot Subsonic Tunnel
Nikolas Zawodny, Kyle Pascioni, and Christopher Thurman
Aeroacoustics Branch
NASA Langley Research Center
Vertical Flight Society 79th Annual Forum & Technology Display
16-18 May 2023
Funding provided by the NASA RVLT project

## Slide 2: Introduction and Objectives
Propellers historically designed as a means of thrust generation in axial forward flight
Rotors historically designed as a means of providing vertical lift during takeoff and landing and operate in edgewise forward flight
Urban Air Mobility (UAM) vehicle platforms that utilize articulating propulsors require elements of both
Such proprotors experience complex aerodynamics and acoustics during transition phases of flight
Objectives:
  Acquire data emulating transition flight conditions representative of AAM configurations
  Compare results with existing low- and mid-fidelity prediction techniques to identify shortcomings
Tiltwing Concept Vehicle
VTOL mode
Cruise mode

## Slide 3: Proprotor Designs
Two proprotor designs considered in this study
  2 ft. diameter
  NACA 0012 airfoil profiles
OPT5
  Conventional “optimum hovering rotor” design
  Model-scale representation of rotor designed for RVLT tiltwing concept*
COPR5**
  Computationally optimized for maximum cruise efficiency
  Constraints of target thrust and radiated tonal noise
*Whiteside et al., NASA TM 20210017971, NASA Langley Research Center, 2021.
**Zawodny et al., NASA TM 20220015637, NASA Langley Research Center, 2023.
OPT5
COPR5
Twist Distributions
Chord Distributions
Source: NASA
Source: NASA

## Slide 4: Experimental Setup: Wind Tunnel Facility
14- by 22-Foot Subsonic Tunnel
  Used extensively for both aerodynamic and acoustic studies
  Utilized the open-jet test section configuration
  Large test section size relative to proprotor diameters
Airfoil with “tear drop” base fairing and floor ramp structure
Inflow microphone and hotwire probes
  Initial insight for future acoustic testing
  Assessment of freestream turbulence
Propeller
Test Stand
Fairing
Floor Ramp
Inflow Microphone
Hotwire Probe
Proprotor
Downstream View
Sideline View
Source: NASA
Source: NASA

## Slide 5: Experimental Setup: Propeller Test Stand (PTS)
Designed to evaluate installed propeller/rotor noise and performance in NASA’s wind tunnel facilities
Wide range of operational capabilities
  Roll, pitch, and yaw articulations
  Operational speed range of 250 to 16k RPM
  Capable of 52 kW continuous operation
Onboard measurements
  Six-component multiaxis load cell (Mini85)
  Aft-mounted triaxial accelerometer
  Thermal probes
  Laser tachometer for rotation rate monitoring
Illustration of PTS Articulation
Source: NASA

## Slide 6: Experimental Setup: Propeller Test Stand (PTS)
Designed to evaluate installed propeller/rotor noise and performance in NASA’s wind tunnel facilities
Wide range of operational capabilities
  Roll, pitch, and yaw articulations
  Operational speed range of 250 to 16k RPM
  Capable of 52 kW continuous operation
Onboard measurements
  Six-component multiaxis load cell (Mini85)
  Aft-mounted triaxial accelerometer
  Thermal probes
  Laser tachometer for rotation rate monitoring
Cutaway View of PTS Motor Assembly

## Slide 7: Experimental Setup: Test Conditions
Considered hover (H), transition (T), and forward flight (FF) conditions
  Range of collective , propeller incidence angle , and advance ratio settings
  Propeller nomenclature used for T and FF conditions
Surface tripping methods investigated
  Low Reynolds numbers
  Primary focus on a LE serrated tape
Blade surface oil flow visualizations performed for select hover conditions
Proprotor | Condition | (o) |  |  | (o)
OPT5 | H | 0, +8 | 0.27 – 0.52 | 0 | -
 | T | +8, +16 | 0.12 – 0.52 | 0.1 – 1.7 | 5 – 52
 | FF | +8, +16, +24 | 0.12 – 0.52 | 0.35 – 1.7 | 0
COPR5 | H | -15 | 0.20 – 0.50 | 0 | -
 | T | -10, -7.5, -5 | 0.20 – 0.43 | 0.4 – 1.4 | 5 – 50
 | FF | 0 | 0.10 – 0.39 | 0.2 – 1.5 | 0
Proprotor | Condition |  |  |  | 
OPT5 | H | 0, +8 | 0.27 – 0.52 | 0 | -
 | T | +8, +16 | 0.12 – 0.52 | 0.1 – 1.7 | 5 – 52
 | FF | +8, +16, +24 | 0.12 – 0.52 | 0.35 – 1.7 | 0
COPR5 | H | -15 | 0.20 – 0.50 | 0 | -
 | T | -10, -7.5, -5 | 0.20 – 0.43 | 0.4 – 1.4 | 5 – 50
 | FF | 0 | 0.10 – 0.39 | 0.2 – 1.5 | 0
Schematic of Proprotor Forces and Moments
Tested Conditions

## Slide 8: Experimental Setup: Measurement Uncertainty
Load cell prone to DC thermal drift issues
  Thermal gradients
  Prominent constant cantilever load
  Required use of highest load calibration range for sensor
Thermal soaking processes implemented
Repeatability errors assessed
  Repeated operating conditions during run sequences
  Used to compute force/moment and coefficient uncertainties
Flight Condition | T, N, Y (N) | Q, n, m (Nm)
H | 4.448 | 0.113
FF, T | 2.224 | 0.057
Force and Moment Repeatability Errors
Measurement Uncertainties of Thrust and Power Coefficients
Measurement Uncertainties of Normal Force and Yaw Moment Coefficients

## Slide 9: Computational Tools
Analytical modeling
  Extensions of Von Mises* by Leng et al.** to account for proprotors at incidence
  Prediction of off-axis forces and moments build upon method of Ribner
  Current model capitalizes on terms derived by fitting previous experimental data spanning several propellers of varying geometry and blade count
CAMRAD-II modeling
  Mid-fidelity comprehensive rotorcraft analysis code
  Allows for use of different wake models and different blade dynamics
  The following were utilized in this study:
    Preexisting NACA 0012 C81 table data
    General free-wake geometry model
    Rigid blade assumption
*Von Mises, R., Theory of flight, Courier Corporation, 1959.
**Leng, Y., Moschetta, J.M., Jardin, T., and Bronz, M., “An Analytical Model for Propeller Aerodynamic Efforts at High Incidence,” 54th 3AF International Conference on Applied Aerodynamics, Paris, France, March 2019.
Ribner, H. S., “Propellers in Yaw,” NACA Report No.820, 1945.

## Slide 10: Results: Hover Performance
OPT5
  Clean blades found to exhibit very low FM values
  FM predicted to be around 0.76 using CAMRAD II*
  Application of trip tape seen to dramatically improve FM, yet still low compared to prediction
  Unable to achieve design target disk loading (20 psf)
COPR5
  Little to no change in performance with trip tape application
  Higher FM levels than those of OPT5
  Excellent comparison with measurements from previous study**
Figure of Merit vs. Tip Mach Number
*Thurman, C., Zawodny, N., and Pascioni, K., “Computational Study of Vortex-Induced Separation for a 5-Bladed Rotor,” VFS International 79th Annual Forum & Technology Display, West Palm Beach, FL, May 2023.
**Zawodny, N. S., Pettingill, N. A., Lopes, L. V., and Ingraham, D. J., “Experimental Validation of an Acoustically and Aerodynamically Optimized UAM Proprotor – Part 1: Test Setup and Results,” NASA TM 20220015637, NASA Langley Research Center, 2023.

## Slide 11: Results: Surface Oil Flow Visualizations
Severe flow separation on outer 12% of blade span
Tip vortex impingement from previous blade visible
Trip tape appears to delay separation
OPT5 (Mtip = 0.50)
Source: NASA

## Slide 12: Results: Surface Oil Flow Visualizations (contd.)
Attached flow across majority of blade span
No prominent indications of vortex impingement
Difficult to visually identify tip vortex formation
COPR5 (Mtip = 0.45)
Source: NASA

## Slide 13: Results: Forward Flight
COPR5
  Well-defined propulsive efficiency profile
  Good agreement with previous measurements in LSAWT facility
  Slight divergence at low advance ratios, potentially due to tripping configurations
OPT5
  Baseline collective setting performs poorly
  Found to be too aggressive, promotes stall on blades
  Reduced collective setting seen to perform much better, similar peak performance as COPR5
Large error bars indicative of low thrust and/or power settings
COPR5 selected for further interrogation of transition flight conditions
Propulsive Efficiency vs. Advance Ratio

## Slide 14: Results: Transition
Performance profiles for several different collective/pitch settings
Analytical and CAMRAD II predictions included
  Analytical predictions provide good approximations, simple linear trends
  CAMRAD II predictions better at predicting profile shapes, divergence in power predictions
CAMRAD II predictions unable to converge below
Analytical predictions pursued for further interrogation of off-axis forces and moments
Thrust Coeff. vs. Axial Advance Ratio
Power Coeff. vs. Axial Advance Ratio

## Slide 15: Results: Transition (contd.)
Analytical trends line up well with measured data
  Deviations at higher propeller incidence angles
  Yaw moment exhibits largest deviations
Previous experiments indicate that represents a sharp turning point in coefficient slopes
Analytical predictions expected to worsen at higher propeller incidence angles.
Normal Force Coeff. vs. Axial Advance Ratio
Yaw Moment Coeff. vs. Axial Advance Ratio

## Slide 16: Concluding Remarks
Investigated aerodynamic performance of two proprotors across range of advance ratios and incidence angles
  Conventional rotor design
  Design computationally optimized for forward flight condition
Unexpected flow physics encountered on conventional rotor design
  Considerable overprediction in thrust output capability
  Flow separation on outboard portion of blade
  Strong perpendicular blade-vortex interactions
Successful measurements of off-axis loads and moments
  Over a limited range of proprotor incidence angles
  Reasonable agreement with analytical predictions
Future Work
  Measurements of aerodynamic loads and moments across full edgewise range of incidence angles
  Acoustics across full range of transition flight conditions

## Slide 17: Acknowledgments
Assistance with testing
  Aeroacoustics Branch: Niki Pettingill, Stefan Letica
  Flow Physics and Control Branch: Mehti Koklu
Test development and operations
  LSAWT personnel: John Swartzbaugh, Stan Mason, Bryan Lamb, Jeff Collins, Tyrone Pilgrim
  14x22 personnel: Abby Cayton, Frank Quinto
  RVLT leadership: Benny Lunsford, Susan Gorton

## Slide 18: Thank you.
Aeroacoustics Branch
NASA Langley Research Center
Vertical Flight Society 79th Annual Forum & Technology Display
16-18 May 2023
Nikolas Zawodny | Kyle Pascioni | Christopher Thurman
nikolas.s.zawodny@nasa.gov | kyle.a.pascioni@nasa.gov | christopher.thurman@nasa.gov

## Slide 19: Backup Slides

## Slide 20: Results: Transition (concl.)
Side force and pitching moment also measured
  No analytical predictions currently available
  Previously regarded as being of secondary importance
  Situation will change with installation configurations (i.e., proprotor-wing)
Trends align well with normal force and yaw moment data
Side Force Coeff. vs. Axial Advance Ratio
Pitch Moment Coeff. vs. Axial Advance Ratio