## Slide 1: Artemis Navigation Architecture: Early Capabilities and Long Term Evolvability and Evolution
Evan Anzalone, NASA/Marshall Space Flight Center, Evan.J.Anzalone@nasa.gov
Cheryl Gramling, NASA/Goddard Space Flight Center, Cheryl.J.Gramling@nasa.gov
ESA GNC Conference, June 12, 2023

## Slide 2: ACD-SCaN PNT Trade Study Membership
Co-Leads: Evan Anzalone (ACD), Cheryl Gramling (SCaN)
ACD S&MA – Dan Londa
ACD Surface System Integration (SSI): Toni Ranos, Alex Osorio
EHP: Brian Lewis, Claude Wallace, Michael Khayat, John Lewis, Mike Cooke, Scott Bleisath, with additional support
ESDMD TIO/ADO Lunar Architecture Team: Ben Sellari, Kevin Larman
Flight Operations Directorate: John Sangree, Glenn Pogue, Paul Lane, Daren Welsh
Gateway: Chris Woodland, Scott Cryan
HLS: Juan Orphee, Dave Woffinden, Greg Dukeman, Todd Freestone
JSC Navigation Mode Team – Greg Holt
LunaSAR: Cody Kelly, Lisa Mazzuca
Mars Exploration Capabilities – Denise Varga
SCaN: Laurie Mann, Juan Crenshaw, Nick Speciale
Steering Committee:
Primary Customer: Mark Kirasich
Artemis: Erika Alvarez, Lawrence Jones, Ted Kenny
SCaN: Greg Heckler, Jason Mitchell, Jim Armitage, Jaime Esper, Jim Schier

## Slide 3: Artemis Exploration Goals Dependent on PNT
Explore Areas of Scientific Interest
Near Lander
Into PSR
Into Lava Tubes, etc.
Autonomous Rover (LTV/PR) Exploration
Demonstrate Autonomy and Operations in NRHO for Moon to Mars Objectives
Maintain Gateway in NRHO Orbit
RPOD in NRHO
21 Day Autonomous Operations
Demonstrate Capability and Deploy Assets to Build Out Artemis Base Camp
Demonstrate Precision Landing
Remove Approach Constraints and Improve Precision
Deploy and Protect Base Camp Area
Autonomous Rover (LTV/PR) Cargo Transfer
Artemis III
Artemis IV
Artemis V
Artemis V+
PNT is required across the architecture to ensure safe and successful Artemis Campaigns.
Increasingly Complex & Longer Traverse
2 km range with EVA
10 km range w/ EVA + LTV
20+ km range w/ EVA + LTV + PR
Telerobotic Rover Operation
Gateway
HLS, Cargo, ISRU, LTV, SH, PR, Logistics
EVA, PR, LTV
Science

## Slide 4: Lunar Navigation From An Apollo Crew Perspective
“Distances are deceiving”
“Maps are primarily only useful for large surface features”
“Craters were hidden behind other craters, ridges, and old worn-down mounds”
“Even when the crewmen climbed to a ridge, the landmark often was not clearly in sight.”
“It is, however, potentially dangerous to proceed on the assumption that no navigation aids are needed and to discover in the middle of a mission that ‘seat of the pants’ navigation is inadequate”
Apollo 14 Crew Came within 20 m of
Cone Crater objective without realizing It (LROC)
  “Navigation is more difficult with so much dark terrain and crude nav aids” – DRATS 2021 Summary

## Slide 5: Comparison of Artemis to other NASA Planetary Surface Missions
Artemis
Apollo
Mars Rovers
VIPER
Increasing Daily Traverse Distance
Artemis
Mars Rovers
Apollo (300m/6km)
VIPER
Increasing Speed
Mars Rovers
VIPER
Apollo
Artemis
Artemis
VIPER
Apollo
Mars Rovers
Decreasing Availability of Line of Sight to Earth
Decreasing Availability of Lighting During Operations
Increasing Navigation Accuracy & Timeliness Required
Artemis
VIPER
Mars Rovers
Apollo
Artemis at Lunar South Pole presents more stressing distance, lighting, earth availability, and navigation challenges than previous programs.

## Slide 6: Architecture Trade Study Flow and Process
Current Requirement Set:
Template + Justification
Requirement Set:
Template + Justification
PNT Sources, Technologies Perceived/Known:
Template
Map ConOps Requirements to Artemis Mission
ConOps:
Identify All
Currently Perceived/Known Use Cases
Requirements Gaps
Requirements
Products
PRODUCTS
Req: Art# Map
Architecture: Art# Map
Architecture: Use Case Map
Tech TRL
RFI Material Prep
Plans & Integration Roadmap
Briefing Material
Forward Work

## Slide 7
Focused on relative PNT solutions due to limited implementation schedule, scored on 1, 5, 9 scale
If programmatic concerns are primary driver  Dead Reckoning and Motion Sensors (IMU)
Combining multiple relative techniques may reduce operational constraints and improve accuracy
  Fiducials and Optical: Star Trackers / Camera / LIDAR could provide best benefit
Approaches could be augmented with initial deployments of orbital and surface infrastructure
  Requires funding and development of user terminal (needed for long-term infrastructure)
Recommendation: Perform subsequent ACD and EHP co-led detailed trade study (includes traverse, cost, and schedule impacts) for down-select and deployment on Artemis III and IV. Focus on EVA navigation with applicability to LTV.
Early Missions Assessment & Recommendation – Artemis III And IV

## Slide 8: Sustaining Missions PNT Assessment - Artemis V+
ESDMD requirement for localization of crew on surface
Considered additional solutions with longer lead time from relative-only options
Ranked technologies for absolute surface nav that could provide ~1’s to ~100’s of meters
Assessed qualitatively based on 1,5,9 (red, yellow, green) scale
Included scoring for ability to meet relevant Artemis use cases identified
  Multiple weighting scenarios assessed (equal shown below)
Orbital Relays and 3GPP Infrastructure provide robust approaches to meet Artemis PNT architecture absolute localization needs but have large programmatic impacts.
Notes: Field testing shows optimistic capability to orienteer to ~150 m on average
Results:
  Absolute Navigation: Orbital Relays and/or 3GPP
  Relative Navigation: Fiducials and/or Odometer/Pedometer w/ IMU and/or Dead Reckoning
    Fiducials provide high accuracy for near-field support and awareness of nearby assets
    Motion Sensing (IMU + Odometry) enables propagation over short distances
    Dead Reckoning allows astronaut to be grossly aware of their location (but could still get lost)
      Does not support tele-robotics or high speed vehicle motion

## Slide 9: As perspectives change, requirements and approaches change
Orbit
Landing
Traverse
Return to Hab (Contingency)
Surface & Rendezvous
Localization with 10 m
Global
Immediate Surroundings
Absolute
Relative
Local
Coverage Area:
Mission Phase:
Type of Knowledge:
Accuracy:
100 m
50 m
10 m
~1 m
~10 cm
Primary needs are for real-time operations; can improve via post-processing
Understood and well-captured in requirements
Forward work needed to define approaches and requirements

## Slide 10: Use Case/Requirements/Solution
Lunar Reference System (Frame, Time, and Products)
10
NRHO
Science/ Technology
Traverse
LL0  DOI
PDI
Landing
10km
0.1 m/s
100 m
0.1m/s
50/25m
50/ 25 m
TBD
10m
X km radius from HLS
Fiducials*
LIDAR
Retro-Reflector
Real Time
Post-Processed
<<=1 m
Earth DTE
Earth GNSS, Inverted PNT
Orbital Relays/LCRNS
Differential
Motion Sensors (IMU, Odom, etc.)*
3GPP/PL Infrastructure
Future Deployment
Baseline Recommendation
Optical Navigation (Camera)*
Foundation
RPOD Suite
Breadcrumbs*
Lighting*
*- Traverse options without relay

## Slide 11: Forward Work
Assessment of Orienteering Approach in Field Studies and Generated Imagery
Image/NASA/Bill Stafford
Development and Implementation of Navigation Aids
Cross-element Integration and Development of Test Objectives in Flight Campaign
Lunar Navigation System
Gateway

## Slide 12
Many Thanks To All Who Supported This Trade Study!

## Slide 13: Acronym List
Acronym | Description
3GPP | 3rd Generation Partnership Project (cell)
ACD | Artemis Campaign Development
DRATS | 
DTE | Direct to Earth
DTM | 
EHP | EVA Human Mobility Program
ESDMD | Exploration Systems Development Mission Directorate
EVA | Extra Vehicular Activity
GNSS | Global Navigation Satellite Systems
IMU | Inertial Measurement Unit
ISRU | In Situ Resource Utilization
HLS | Human Landing System
JSC | Johnson Space Center
LiDAR | Light Detection And Ranging
LLO | Low Lunar Orbit
Acronym | Description
LTV | Lunar Terrain Vehicle
NRHO | Near Rectilinear Halo Orbit
Odom | Odometer
OSLAP | Orbital and Surface Lunar Architecture for PNT
PDI | 
PNT | Position, Navigation, and Timing
PR | Pressurized Rover
PSR | Permanently Shadowed Region
RFI | Request for Information
RPOD | Rendezvous, Proximity Operations, and Docking
SAR | Search and Rescue
SCaN | Space Communications and Navigation
SH | Surface Habitat
S&MA | Safety and Mission Assurance
SSI | 
TRL | Technology Readiness Level