## Slide 1
NESC Avionics Packaging Assessment
Avionics Mechanical Packaging Processes and Best Practices
Carmel Conaty Assessment Lead
Beth Paquette, Milt Davis, Technical Leads

## Slide 2
Background
Scope:
Assess and perform a gap analysis of the packaging guidelines and standards that are utilized for space applications across the centers and with our industry partners
  Recent failures have identified packaging scenarios that warrant attention from the packaging community
The assessment includes a survey of the community of experts on best practices followed with the development guidelines and checklists
The assessment includes testing in areas where key gaps were identified
Products:
Technical memo that includes a checklist and guidelines targeting mission-critical, near-term challenges that have a greater impact on mission success for space flight electronic packaging. The following products would be included:
  Recommendations, lessons learned, and a set of guidelines/checklist for packaging and packaging-related reviews throughout the project life cycle.
  Best practices to ensure confidence in the structural integrity from the box to the board and component level
  Process or methodology for establishing confidence in margins (natural frequency, damping, rotational stiffness, structure environment, thermal environments, part de-rating)

## Slide 3
Background
Key Deliverables
Face to face June 2022, at GSFC
Design survey questions
Review materials gathered on packaging lessons learned and packaging failures
Gap analysis of packaging guidelines and standards across the centers and with our industry partners
Development guidelines and checklists
Vibration testing & results
Stakeholder briefing
Engineering colloquium presentation (taped for NESC academy) and Roadshow
Final report
Key Stakeholders
NASA Engineering Organizations (GSFC/JPL/MSFC/AMES/LaRC)
Center packaging community, center leadership and Avionics Technical Discipline Team (TDT)
Applied Physics Lab (APL)
Industry
Commercial Crew Program (CCP)
Assessment is currently on Pause until October 2023 (earliest)

## Slide 4
Work Completed To Date
Sub Teams
Assessment was broken down into different sections: Board design, manufacturing, and workmanship, Component Solder Fatigue, Box System design and implementation and Cost benefit analysis/verification by analysis vs test.
Avionics Packaging Assessment Face to Face
A hybrid full day meeting held on June 21, 2022 at GSFC to provide updates, status, and a forum for technical discussion on best practices to improve the current NASA approach for packaging design, analysis, and verification for unique packaging circumstances. The agenda included an overview of packaging culture/processes at each center and APL, overview of the Avionics COP, challenges and opportunities in the domestic advanced packaging environment, and in-depth sub-team and large group discussions on the priorities and next steps for the assessment.
Written Guidelines
Initial draft of the guidelines gathered to date has been developed and is being reviewed by the team.
Outlines completed and in a draft formal report format
Main takeaway has been communication early and often with all engineering disciplines and technicians, and mentorship is key.

## Slide 5
Work Completed To Date
Additional Testing to Complete the Assessment
Defined specific testing recommendations that would be needed to fill gaps identified in current design guidelines recommendations. Test plans are complete and parts procurements begun.
Detailed test plans (board vibration testing) including budget and schedule are completed.
Testing Details
Simplified Steinberg equation for Printed Circuit Board (PCB) deflection significantly overestimates time-to-failures for Ball grid arrays (BGAs) and Column Grid Arrays (CGAs)
Modification of the simplified Steinberg equation is required to be established by literature review and test for flight use
Improve analysis by Including fatigue of individual columns attached to package substrate and to the PCB board to establish mechanical cycles to failure for individual columns required for Steinberg or new life prediction equations for vibration use
Assemble CGA onto board and perform vibration under sequential levels to failures to establish failure mechanisms and time to failures for developing new parameters for Steinberg or new equations
Test Status:
  Boards are designed and ordered, and all components are received
  Board assemblies to be completed this summer

## Slide 6
Work Completed To Date
Qualitative Electronics Packaging Risk Assessment Tool In Development
Risk Tool Inputs
User inputs project initial conditions
Compares 4 different flight project risk classes A through D
Number of printed wiring assemblies, Heritage/Reuse, Hardware quantity/cost, Testing quantity/costs, and Labor Rates
Risk Tool Methodology
Compares cost of recovery based on project critical path burn rate and project reserves at time of failure
Compares probability of consequence based on electronics design and technology
Likelihood calculator
Risk Tool Outputs
Cost of Engineering Test Unit (ETU) risk mitigation testing
Compares cost of ETU testing vs the cost of failure recovery
Compares cost of additional packaging analysis vs cost of testing
Tool Insights
User will evaluate results based on engineering judgment and experience
User will use this tool to communicate risks and mitigation solutions to the project
Based on user inputs, the tool will highlight when the cost of an ETU test is less than the risk cost threat cost threat of not performing an ETU mechanical test

## Slide 7
Acronyms
Acronym | Definition
APL | Applied Physics Lab
BGA | Ball Grid Array
CCP | Commercial Crew Program
CGA | Column Grid Array
ETU | Engineering Test Unit
PCB | Printed Circuit Board
NESC | NASA Engineering Safety Center
TDT | Technical Discipline Team