## Slide 1
Wavelength-Agility for Multi-Parameter Measurements
Advancements in Burst-Mode Filtered Rayleigh Scattering
for High-Speed Gas-Phase Multi-Parameter Measurements
Amanda M. Braun1, Mikhail N. Slipchenko1,2, Jason Leicht2, Neil S. Rodrigues3, Paul M. Danehy3, Sukesh Roy2, and Terrence R. Meyer1
Improved Spectral Purity
The FRS laser source must have a spectral linewidth that is much narrower than the absorption line of the molecular filter to ensure that the background scattering will be fully absorbed.
Propane
Filtered w/o Etalon
Filtered w/ Etalon
Spectral purity of burst-mode laser was increased from ~0.9998 to ~0.999999 with the addition of an etalon inside the amplification stage [1].
Increased spectral purity gives additional attenuation of stray scattering.
To deconvolve the effects of pressure, temperature, and velocity, multiple incident laser frequencies can be used to quasi-spectrally resolve the signal [2-5].
Current modulation of the burst-mode laser seed wavelength [6-8] across an iodine absorption band allowed for a measurement bandwidth of up to 1 kHz.
Preliminary temperature, pressure, and radial velocity maps of an underexpanded jet with ambient temperature air as the working fluid
This work was funded by a NASA Space Technology Graduate Research Opportunity Fellowship
Acousto-optic modulators were used to create discrete, frequency-shifted pulses during the burst [9].
Challenges
Low signal levels
Strong background interferences
Multiple cameras and/or molecular filters to spectrally resolve the signal
Outside Absorption Band
Inside Absorption Band
FRS signal taken at 100 kHz for four frequencies (-600 MHz, -200 MHz, +200 MHz, +600 MHz) for two different central frequencies
1Purdue University, School of Mechanical Engineering, West Lafayette, Indiana 47907, USA
2Spectral Energies, LLC, 4065 Executive Dr, Beavercreek, Ohio 45430, USA
3Advanced Measurements and Data Systems Branch, NASA Langley Research Center, Hampton, Virginia 23681, USA
Laser intensity
Number density
Optics efficiency
Probe length
Solid collection angle
Mole fraction of species, j
Rayleigh cross-section of species, j
Rayleigh lineshape profile
Filter transmission profile
Doppler shift
Pressure
Velocity
Temperature
Angle between scattering and incident laser vectors
[1] A. M. Braun, M. N. Slipchenko, J. Leicht, T. R. Meyer, P. M. Danehy and S. Roy, “Methods to improve burst-mode laser spectral purity for high-speed gas-phase filtered Rayleigh scattering,” Accepted to Opt. Lett. (2023).
[2] J. N. Forkey, N. D. Finkelstein, W. R. Lempert, and R. B. Miles, “Demonstration and characterization of filtered Rayleigh scattering for planar velocity measurements,” AIAA J. 34(3), 442–448 (1996).
[3] M. Boguszko and G. S. Elliott, “Property measurement utilizing atomic/molecular filter-based diagnostics,” Prog. Aerosp. Sci. 41(2), 93–142 (2005).
[4] U. Doll, G. Stockhausen, and C. Willert, “Endoscopic filtered Rayleigh scattering for the analysis of ducted gas flows,” Exp. Fluids 55(3), 1690 (2014).
[5] U. Doll, G. Stockhausen, and C. Willert, “Pressure, temperature, and three-component velocity fields by filtered Rayleigh scattering velocimetry,” Opt. Lett. 42(19), 3773 (2017).
[6] T. W. Fahringer, R. A. Burns, P. M. Danehy, P. M. Bardet, and J. Felver, “Pulse-Burst Cross-Correlation Doppler Global Velocimetry,” AIAA J. 58(6), 2364–2369 (2020).
[7] N. S. Rodrigues, P. M. Danehy, N. Jiang, P. Hsu, J. Leicht, and S. Roy, “100 kHz High-Spectral-Resolution NO-PLIF Measurements for Compressible Flows,” in AIAA SCITECH 2023 Forum (2023)
[8] R. A. Burns, T. W. Fahringer, and P. M. Danehy, “Velocity measurements across an oblique shock using pulse-burst cross-correlation DGV,” in AIAA Scitech 2021 Forum (2021).
[9] A. J. Saltzman, K. T. Lowe, and W. F. Ng, “250 kHz three-component Doppler velocimetry at 32 simultaneous points: a new capability for high speed flows,” Meas. Sci. Technol. 31(9), 095302 (2020).
Basic design for two frequency-shifted pulses
Potential for N, Measurement
Potential for ~MHz V, pT Measurement
Potential for 100’s of kHz V, pT Measurement
Filtered Rayleigh scattering (FRS) overview
Burst-mode laser principles
FRS Signal Intensity