## Slide 1: Responsible AI Framework for Air Traffic Management
1
Parimal Kopardekar, PhD
Director, NASA Aeronautics Research Institute

## Slide 2: Outline
OUTLINE
Evolution Airspace Operations Future
Key Proposal
Responsible AI Framework
Use Cases
Collaboration and Harmonization

## Slide 3: Hypothesis: Role of Automation
Future system will require increased levels of automation to address increased diversity, density, environmental considerations resulting in higher complexity
Historical basis for this hypothesis

## Slide 4: Evolution of Airspace Operations and Safety
+Density
Safety
+ Efficiency and
proactive planning
+ Service oriented
architecture for
tailored mission
oriented services
+ Complexity, scalability,
and dynamic adaptation
Epoch 1
Epoch 2
Epoch 3
Epoch 4
(~2035)
Epoch 5
(~2045)
S-curves
Procedural
Estimate the current and planned a/c positions
Radar
Know the current and estimate planned a/c positions
Trajectory
Know & exchange
current and planned a/c positions
Introduces 3rd-party
service providers
Machine-to-machine
interactions and humans collaborate
Automated in-time safety
monitoring and alerting services
Automatically-assured adaptive
in-time safety threat management
Collaborative
Connected,
performance-based,
collaborative ATM
Highly-Automated
ML/AI – based dynamic, robust
performance and safety
Human-centered safety monitoring, assessment and mitigation
Digital Transformation of ATM
Human-centered safety monitoring, assessment and mitigation
Integrated predictive risk
mitigation across domains

## Slide 5
Current ATM
Transition to UTM-inspired Airspace Traffic Management
All services are provided by FAA
Human address off-nominal situations and contingencies to ensure safety
Very little interaction among users and third parties
Human at the epi-center of information integration
Every data for every vehicle moves through FAA systems
Management by clearances
Each change is focused on domain-specific FAA system
UTM-inspired-ATM
Services are provided FAA and third-parties
Automation addressed off-nominal situations and contingencies to ensure scalability while maintaining safety
Users collaborate/cooperate for efficiency, preferences for flights into constraints resources
Automation at the epi-center of information integration
New paradigm: Digital, connected ecosystems, outside applications
Movement towards management by exceptions
Each change is focused on trajectory optimization
Research Needed: Architecture, data exchanges, service allocation/roles/responsibilities, rules of engagement, performance requirements for aircraft and airspace system technologies, automation for contingency management and disruption handling, machine learning environment and algorithms for continuous improvement, safety assurance/certification/acceptance approaches, and technology transfers.

## Slide 6: Key Question
Will automation be able to manage off-nominal, non-normal, unexpected, contingency situations?

## Slide 7: Proposal
Type 1: Decisions that are reversible, strategic, or impact only efficiency, capacity, sustainability but do NOT impact safety of operation directly
Type 2: Decisions that are irreversible, tactical, and COULD impact safety of operation directly including other measures of performance

## Slide 8: Responsible AI Framework: Factors Particularly for Type 2 Decisions
Explainability
Transparency
Visibility in Learning – external validation before implementation
Security
Safety
Trustworthiness
Stay within the rules of behavior

## Slide 9: Behavior Rules
Every system or subsystem must have clear “system behavior” rules to ensure compatibility and harmonization with rest of the universe
Example, Asimov’s Rules
  First law is that a robot shall not harm a human, or by inaction allow a human to come to harm.
  Second law is that a robot shall obey any instruction given to it by a human, and
  Third law is that a robot shall avoid actions or situations that could cause it to come to harm itself.
Challenge with Asimov’s rules were not easily testable

## Slide 10: Example Behavior Rules
Flow management System
  Demand should not exceed capacity in any given time
Conflict management system
  No two aircraft should ever come closer than minimum separation
Surface management system
  Two aircraft should not occupy the same runway at the same time

## Slide 11: Responsible AI Framework: A Process
Identify a set of ATM Services (e.g., traffic synchronization)
Select and Focus on a Service at-a-time
Identify a set of behavior rules
Identify a set of test conditions and success criteria
Build a model for services
Identify nominal scenarios and corner cases – Train model
AI based concept, algorithms, and technology
Independent Safety Monitor (non-AI, e.g., In-time Aviation Safety Management System)
Real Situation
Test model against behaviors and success criteria
AI based concept, algorithms, and technology

## Slide 12: Safety Monitor - Proposal
Not human
Layer of deterministic automation
Not intended to duplicate same capabilities such as AI-based approaches for total system performance
Safety monitor – manages for safety! One function.
  Like humans do today – safe, expeditious, and orderly flow in that sequence
  We have precedence – Traffic Collision Avoidance System (TCAS)
Architecting a new system is key
System-level “digital twin” running in the background

## Slide 13: Use Cases

## Slide 14
ML based trajectory prediction
Goal: Improve ETA predictions by providing accurate ML derived aircraft performance model (APM) parameters
Approach:
Collected and processed data from thousands of historical flights
Used physics-based approach (ODE-fitting) to obtain best APM coefficients for each flight
Trained ML model to capture relationship between characteristics of flights and ‘best’ APM coefficients
Challenges: Highly coupled parameters, proprietary values, no ground truth (labels) available.
ML-based method shows significant improvement in trajectory prediction compared to traditional model parameters
Example result

## Slide 15
Runway Configuration Assistance (RCA)
Goal: Create an AI/ML tool to predict/recommend optimum time frame for runway configuration changes based on historical data and weather/traffic forecasts, without access to simulators
Approach:
Processed traffic and weather data from FAA’s ASPM, NASA’s Sherlock and NOAA’s LAMP
Developed supervised learning to mimic the controllers (ATCo)
Developed offline model-free reinforcement learning (CQL) to enhance decision-making of the ATCo
RCA tool and supervised learning show significant performance in CLT and especially in DEN, despite its complexity of runway configurations
Validation metrics:
Agreement with historical decisions
Violation of obvious configuration scenarios
Feb 5, 2019, at 6AM
Visualization dashboard:
Prediction of the configuration changes given the scheduled traffic and forecast of weather conditions.
Can be used by ATCo to identify optimum time-interval for configuration changes.

## Slide 16
ATCSCC Webinar Speech2Text
Digital Information
Outcomes
More efficient review
Computable analytics
Collect and preprocess
Provide downstream information extraction and text processing
Automatically create text-based transcriptions
Digital TMIs
ATCSCC Webinar transcription
Goal: Utilize recent trends in AI/ML to provide automated transcriptions of ATCSCC webinar audio and extract relevant information from the transcript to help specialists.
Challenges: Unstructured audio data, highly domain-specific. Creating manual transcriptions takes time.
ML Models:
Speaker Diarization: Split speaker segments from long audio
Speech2Text: Convert audio into text transcriptions.
Audio-Lexical Inverse Text Normalization: Add text formatting, punctuation, and capitalization to raw text.
Named Entity Recognition: Used to extract key words and phrases from text transcriptions.
Notes: There are neural network models associated with each one of these steps

## Slide 17: Collaboration and Harmonization
Factors for Responsible AI
Behavioral rules for ATM enterprise
Basic architecture – safety monitor construct
AI-based technology will be secret sauce but set of test conditions and success criteria does not have to be

## Slide 18
Embracing Innovation in Aviation while Respecting its Safety Tradition
Parimal.H.Kopardekar@nasa.gov