## Slide 1
NASA Environmental Control and Life Support Technology Development for Exploration: 2022-2023 Status
ICES-2023-312
Walter Schneider, NASA Marshall Space Flight Center
Arthur Brown, NASA Marshall Space Flight Center
Chris Allen, NASA Johnson Space Center
Daniel Barta, NASA Johnson Space Center
Daniel Gazda, NASA Johnson Space Center
Melissa McKinley, NASA Johnson Space Center
Alesha Ridley, NASA Johnson Space Center
Imelda Stambaugh, NASA Johnson Space Center
52nd International Conference on Environmental Systems

## Slide 2: Background of ICES Paper
Overview of Paper
Paper provides top-level summary of ECLS and Environmental Monitoring and includes references
Technology solutions to close capability gaps
Technology solutions that have advantages over currents ECLS systems
  Mass, Power, Volume
  Operations
Current and Potential Mission Application
International Space Station
Orion
Gateway
Lunar Surface
Mars Transit
Mars Surface

## Slide 3: Background of ICES Paper
ECLSS Environmental & Monitoring Technology Areas
Atmosphere Revitalization
  Carbon Dioxide Removal
  Trace Contaminant Control
  Particulate Filtration
  Condensing Heat Exchanger
  Oxygen Recovery from Carbon Dioxide
  Oxygen Generation
  High Pressure Oxygen
Water Recovery and Management
  Distillate/Condensate Processing to Potable Water
  Wastewater Processing, including Urine, Brine, and Hygiene
  Microbial Control and Dormancy
Waste Management
  Universal Waste Management System
  Fecal Can Alternate Design
Environmental Monitoring
  Atmosphere Monitoring
  Water Monitoring
  Microbial Monitoring
  Particulate Monitoring
  Spacecraft Acoutics

## Slide 4: Atmosphere Revitalization CO2 Removal
Gap 2896 – Highly reliable, closed-loop-forward carbon dioxide removal systems
Thermal Amine System
CO2 removal based on thermally regenerated solid amine with passive water save
Thermal Amine System on the ISS
Four Bed Carbon Dioxide Removal
Uses a zeolite-based sorbent to remove CO2
Four Bed CO2 Removal System
During Ground Testing Installed on the ISS

## Slide 5: Atmosphere Revitalization CO2 Removal
Gap 2896 – Highly reliable, closed-loop-forward carbon dioxide removal systems
CO2 Deposition
Creating a cold surface to capture CO2 and then recover the CO2
CDep Full Scale Test Stand
Liquid Amines
Liquid amines supported by capillary structures to remove CO2
Liquid Amine Test Stand
Capillary Sorbent Flight Experiment
Ionic Liquid/Honeywell Collaboration
Removal of Carbon Dioxide using ionic liquids
Photo Courtesy of Honeywell International, Inc.
Carbon Dioxide Removal by Ionic Liquid System (CDRILS) Four-Crew Prototype

## Slide 6: Atmosphere Revitalization CO2 Removal
Gap 2896 – Highly reliable, closed-loop-forward carbon dioxide removal systems
CO2 Removal by Rapid Cycle Temperature Swing Adsorption
Zeolite coated plates with active thermal control to improve CO2 removal resulting in faster heat transfer and lower pressure drop resulting in smaller bed sizes.
Beds Coated with Zeolite 13X
Four-inch Printed Lattice
Monolithic Sorbents for CO2 Removal
Mitigates dust generation issues common to packed beds, providing higher packing efficiency, improved pressure drop and capacity
Air Cooled Thermal Swing Adsorption Compression
Captures and stores CO2 in high surface area, high-capacity sorbents, compresses the CO2 gas until it reaches the right pressure and then delivers it down stream (ex. to a Sabatier)
CO2 Compression and Storage
Air Cooled Thermal Swing Adsorption Compression Ground Unit

## Slide 7: Air Revitalization Trace Contaminant Control
Gap 2898 - Adsorbents and catalyst media to address Trace Contaminant Control System Obsolescence
Third Generation Catalytic Oxidizer
Photo Courtesy of Precision Combustion, Inc.
High Temperature Catalytic Oxidizer Evolution
An exploration forward design consisting of a redesigned adsorption guard bed and a novel high-temperature catalytic oxidizer
Catalytic Oxidizer Assembly Life Test Stand
Sorbent Development Test Facility at Kennedy Space Center
New sorbents are under evaluation to replace obsolescent SOA materials. In addition, new and alternative sorbents have been evaluated, including sorbents for acid-gas removal

## Slide 8: Air Revitalization Particulate Filtration
Gap 2962 - Particle Filtration
Technologies to filter waste carbon from Methane Post Processor Assembly
Umpqua Regenerable Carbon Filter
Assembled Cold trap filter
Waste Carbon Filtration
Spacecraft Atmosphere Filtration
Scrolls filter element eliminates periodic cleaning or replacement by astronauts
Scroll Bacteria Filter Element

## Slide 9: Air Revitalization Condensing Heat Exchanger
Gap 2960 – Robust Condensing Heat Exchanger
ISS Condensing Heat Exchanger
Improved hydrophilic coating for better microbial control, siloxane resistance and overall lifetime. Lower mass, additively manufactured with titanium.
Condensing Heat Exchanger CAD Model
Uses a femtosecond laser ablation process to engineer micro/nano surfaces on a silver plated condensing surface to mitigate microbial growth as well as treat the condensate water collected
Laser Processed Condensing Heat Exchanger
LP-CHX 1/10th Scale Test Article

## Slide 10: Air Revitalization Oxygen Recovery
AYRSORB F25 and AYRSORB F100 MOFs
for Hydrogen Separation
Plasma Pyrolysis Testbed
Methane Post Processor Assembly
Gap 2897 - Recovering and Recycling Additional Oxygen from Metabolic Carbon Dioxide
Increasing the amount of CO2 processed by the Sabatier by recovering hydrogen from the Sabatier’s methane byproduct
Plasma Pyrolysis and H2 Separation
Increase Oxygen Recovery from ~ 50% to Greater than 75%
Solid Oxide Electrochemical Cell for Hydrogen Separation
Honeywell Carbon Vapor Deposition
Deposition of waste carbon within substrate. Produces a dense solid carbon product.
Methane Pyrolysis Brassboard
Photo Courtesy of Honeywell International, Inc.

## Slide 11: Air Revitalization Oxygen Recovery
Increase Oxygen Recovery from ~ 50% to Greater than 75%
Bosch Technologies
Theoretical 100% oxygen recovery.
Replaces the Sabatier and Methane Processing
Series Bosch Test Stand
Gap 2897 - Recovering and Recycling Additional Oxygen from Metabolic Carbon Dioxide
ISS Sabatier Upgrades
Replaceable getter, additional temperature sensors on the reactor, humidity sensors, and a focus on maintainability
Sabatier 2.0 in Test Stand

## Slide 12: Air Revitalization Oxygen Generation
Gap 2903 - Oxygen generation system improved reliability and decreased complexity
Advanced Oxygen Generation Assembly
Redesigned for maintainability, separate domes for cell stack and rotary separator accumulator, a new cell stack design, improved membrane support structure, and a recirculation loop purge and flush for dormancy
AOGA Oxygen Hydrogen Dome Assembly Mock-up
Static Vapor Feed Electrolysis
Electrolyzer technology to generate low pressure oxygen without a recirculation loop for water feed, no need for water-hydrogen phase separator
Giner SVFE Cell Stack
Giner Prototype System

## Slide 13: Air Revitalization High Pressure Oxygen
Gap 2956 - High pressure oxygen for EVA tank resupply
Electrochemical Oxygen Generation and Compression
Utilizes solid state process and materials to separate and compress oxygen
Ceramic O2 Generator (COG) Cell Stack
COG Cell Stack producing Oxygen at WSTF
High Pressure Oxygen Test Rig
High Pressure Electrolysis
Generate Oxygen at 3600 psi
Regulate pressure down for spacecraft O2 generation
High Pressure Electrolysis Cell Stack
Low Pressure Oxygen Compression
Cobham oxygen compressor for use in conjunction with the AOGA or SVFE to deliver high pressure oxygen
Cobham Oxygen Compressor

## Slide 14: Water Recovery and Management Wastewater Processing
eXploration Potable Water Dispenser
Eliminates dead legs and utilizes in-situ ultraviolet sterilization
Gap 2925 - Robust Advanced Water Recovery System
Gap 2918 - Potable water dispenser (PWD) design (sparing and dormancy)
eXploration Potable Water Dispenser
Water Processor Assembly Upgrades
Upgrades include improvement to the life of the Catalytic Reactor, multi-filtration bed with synthetic resin, new microbial check valve
Upgraded Catalytic Reactor on the ISS

## Slide 15: Water Recovery and Management Wastewater Processing
Gap 3612 - Water Recovery System for Surface Missions (lunar and Mars)
SAMBR: Urine and Grey Water Carbon Removal and Nitrogen Conversion
MABR: Urine and Grey Water Carbon Removal and Nitrogen Conversion
AnMBR: Organic Waste Solids and Carbon Removal
/MABR
or MABR
PMBR: Organic Waste Nitrogen Conversion
CDI: Sodium Removal
Wastewater Processing Using Bioreactors

## Slide 16: Water Recovery and Management Urine and Brine Processing
Brine Processor Assembly
Recovers water from the Urine Processor Assembly waste brine effluent
BPA Installed on ISS
Gap 2914 - Brine processing to recover water from urine brine.
Planetary Urine Processor
A simplified distillation technology to process urine that takes advantage of the gravity environment
Concept 1a on PUP Test Stand
Gap 3612 - Water Recovery System for Surface Missions (lunar and Mars)
Gap 2925 - Robust Advanced Water Recovery System
Urine Processor Assembly
Upgrades include a Pressure Pump Separator Assembly, Distillation Assembly Upgrades, and Single Channel Pump
PPSA Prior to Flight to the ISS
Upgraded DA on the ISS

## Slide 17: Water Recovery and Management Microbial Control and Dormancy
Gap 2933 - Disinfection Strategy That Complies with the Potable Water Microbial Specification during Nominal and Uncrewed Ops
Silver Dosing, Passive
Technology to dose water using silver impregnated foam that releases slowly over time
Full scale silver foam cartridge (22 cm x 4.1 cm dia, 290 mL volume, 27.8 g) and flow through test bed
Intelligent Optical Systems Silver Monitor
Silver Monitor
Technology monitor silver levels in potable water
Front-top view of DirectINJECT dosing system test bed
Silver Dosing, Active
Technology to continuously dose a silver biocide solution into the potable water stream
Silver Dosing, Active
Technology to dose water with silver using a silver electrolysis reactor
Silver Electrolysis Reactor
Materials Compatibility with Silver
Effort to determine materials and coatings that will prevent or minimize silver plating on surfaces to maintain levels of silver in solution
316L bellows ready for parylene-C deposition

## Slide 18: Water Recovery and Management Microbial Control and Dormancy
Gap 2933 - Disinfection Strategy That Complies with the Potable Water Microbial Specification during Nominal and Uncrewed Ops
Ultraviolet
Non-chemical alternative to microbial control in potable water and for biofilm prevention
Pipe loop experiment using UV-C side-emitting optical fiber
Hydrogen Peroxide
Alternative to the start-of-the-art urine pretreatment
Three sets of Hydrogen Peroxide Pretreatment Tests
Bromine
Halogen binding resins for dosing bromine for potable water disinfection
Bromine Microbial Check Valve
SilverXX
A passive coating that generates reactive oxygen species for disinfection and prevention of biofilm growth

## Slide 19: Water Recovery and Management Dormancy
Gap 2908 - Dormancy
Dormancy could last for up to one year depending on the specific mission, but could be up to three years due to contingencies
NASA is investigating methods for:
  Preventing biofilm growth
  Controlling biofilm growth
  Removing biofilm growth
Microbe and Microbial Simulated Microgravity Testing
Sanuwave Bellows Tank and Shockwave Applicators Test Set Up
Photo courtesy of Sanuwave

## Slide 20: Waste Management Waste Management
Universal Waste Management System
An exploration class toilet for use on long duration missions
Fecal Can Alternate Design
Lower mass and volume alternative to the hard sided fecal canister
Gap 2931 - Compact Low Logistics Commode for Exploration (Primary Toilet Systems)
Alternate Fecal Canister in full configuration, empty (stowed) configuration and Hard-sided Canister
Toilet on Artemis-2 vehicle

## Slide 21: Environmental Monitoring Atmosphere Monitoring
Gap 2899 - Major constituent and trace contaminant gas monitoring for cabin air
Technology Development Unit 1
Technology Development Unit 2
Spacecraft Atmosphere Monitor
Single Instrument that Measures both Major Constituents (N2, O2, CO2, and water vapor) and trace volatile organic concentrations (e.g. benzene, alcohols) using Gas Chromatograph and Mass Spectrometry Technology
Anomaly Gas Analyzer
Measures combustion gases in the spacecraft atmosphere
Anomaly Gas Analyzer During Testing

## Slide 22: Environmental Monitoring Atmosphere Monitoring
Gap 2899 - Major constituent and trace contaminant gas monitoring for cabin air
FLIR Griffin Trace Gas Monitor
A COTS portable gas chromatograph-mass spectrometer to monitor volatile organics in the habitable volume
FLIR in Benchtop Testing
Air Quality Monitor
For monitoring Trace Contaminants
AQMs deployed on the ISS

## Slide 23: Environmental Monitoring Atmosphere Monitoring
Gap 2899 - Major constituent and trace contaminant gas monitoring for cabin air
Laser Air Monitor
Tunable laser diode adsorption spectroscopy to measure CO2, O2, water vapor, and cabin pressure
Orion Flight Configuration
Major Constituents Analyzer
Measures CO2, O2, N2, CH4, H2, and water vapor
Major Constituents Analyzer on the ISS
Portable Tunable Laser Spectrometer
Measures CO2, O2, and water vapor. Multiple units can be placed in multiple locations for evaluate special difference in concentration
PTLS Sensor Feb 2023

## Slide 24: Environmental Monitoring Water Monitoring
Gap 2902 – In-Flight Water Quality Monitors for Quantification and Identification (TOC)
Gap 2902 – In-Flight Water Quality Monitors for Quantification and Identification (Organic and Inorganic Identification )
Mini-Total Organic Carbon Analyzer
Measures organic carbon in the potable water to determine if the water is safe for use
MiniTOCA Engineering Development Unit
Spacecraft Water Impurity Monitor
Measures organics and inorganics in potable water using mass spectrometry and gas chromatography. Full characterization in situ, without the need to return water samples to Earth
SWIM Conceptual Drawing

## Slide 25: Environmental Monitoring Microbial Monitoring
Swab Method for Surface Microbial Monitoring
Gap 2900 – On-board monitors that measure particles in the crew respiratory hazard range, survive dormancy, and work in low pressure
MinION 1.0 (on ISS)
MinION 2.0
BioMole/MinION
Biomolecule sequencer for in-flight microbial monitoring
Syringe Method for Water Microbial Monitoring
Syringe Method for Air Microbial Monitoring
Collect air sample

## Slide 26: Environmental Monitoring Particulate Monitoring
Gap 2900 – On-board monitors that measure particles in the crew respiratory hazard range, survive dormancy, and work in low pressure
APM in the ISS US Laboratory Module
Airborne Particulate Monitor
Measures a range of particle size and concentrations
Exploration Particulate Monitor Instrument Suite
A suite of instruments for aerosol monitoring on future space missions
Small size particle counter
Photo courtesy of Aerosol Dynamics
Aerosol sampler and sensor that distinguishes between cabin dust, lunar dust and smoke
Photo courtesy of telosair
Mass concentration gravimetric sensor
Photo courtesy of Access Sensor Technologies

## Slide 27: Acoustic Control Acoustic Control
Gap 2959 – Acoustic Monitoring and Control
Quiet Fans
Fans designed to meet noise requirements
Prototype quiet fan built for acoustic and aerodynamic testing to verify the design concept
Noise Abatement
Noise mitigation along the propagation path
Noise mitigation in the toilet compartment mock-up using a newly developed absorbent foam encased within a cleanable Kaption coating

## Slide 28: Conclusion and Acknowledgements
Conclusion
This paper summarizes NASA current technology development efforts in Atmosphere Revitalization, Water Recovery and Management, Waste Management, and Environmental Monitoring
Significant progress has been made in the development and evaluation of exploration forward ECLSS and Environmental Monitoring technologies.
Technology developments are reflected in the NASA roadmaps to support capability gap closure for future space missions
The paper includes 71 references for the reader to find more detail in the technology areas
Acknowledgements
  ECLSS Community
  NASA Civil Servants
  NASA Support Contractors
  Industry Partners
  Academic Partners
  Funding Programs
  Exploration Systems Development Mission Directorate
    Mars Campaign Office
    Gateway Program
    Orion Program
  Space Technology Mission Directorate
    Small Business Innovative Research Program
    Game Changing
  Space Operations Mission Directorate
    International Space Station