## Slide 1: REVISITING VOYAGER 2 PLASMA OBSERVATIONS DURING THE URANUS FLYBY AND PLASMA OBSERVATION REQUIREMENTS FOR FUTURE MISSION TO URANUS’ MAGNETOSPHERE E. C. Sittler Jr., R. G. Michell, and M. Samara NASA Goddard Space Flight Center, Geospace Physics Laboratory, 8800 Greenbelt Road, Greenbelt, MD, USA, email: edward.c.sittler@nasa.gov
ABSTRACT
We revisit the Voyager 2 (V2) plasma observations during its Uranus flyby in Jan 24, 1986. For this flyby it was found to be a highly dynamic magnetosphere with protons [1,2] and electrons [1,3] dominating the plasma environment with significant radiation belts [4,5] and large dipole tilt [6,7] relative to Uranus spin axis. The emphasis of this talk is the
measurement requirement for an Ion Mass Spectrometer (IMS) 1 V ≤ E/Q ≤ 50 kV and Electron Plasma Spectrometer (ELS) 1 eV ≤ E ≤ 30 keV; in both cases a wide field-of view 360 x 90. The main measurement goal is “What is the relative composition of the major and minor ion species within Uranus’ magnetospheres, including both the inner magnetosphere, ionospheres, radiation belts and the deep
magnetotail regions for both hot and cold ions?
References:
[1] Bridge, H. S., Belcher, J. W., Coppi, B., Lazarus, A. J., McNutt, Jr., R. L., Olbert, S., Richardson, J. D., Sands, M. R., Selesnick, R. S., Sullivan, J. D., Hartle, R. E., Ogilvie, K. W., Sittler Jr., E. C., Bagenal, F., Wolff, R. S., Vasyliunas, V. M., Siscoe, G. L., Goertz, C. K., Eviatar, A., (1986), Science, 233, 89-93, https://doi.org/10.1126/science.233.4759.89.
[2] Selesnick, R. and McNutt Jr., L. R., (1987), JGR. 92, 15,249 – 15,262.
[3] Sittler Jr. E. C., Ogilvie, K. W. and Selesnick, R. (1987) ,JGR, 92, 15,263 – 15,281.
[4] Stone, E. C., Cooper, J. F., Cummings, A. C., McDonald, F. B,, Trainor, J. H., Lai, N., R. McGuire, Chenette, D. L., (1986), Science, 233, 93-97,https://doi.org/10.1126/science.233.4759.93.
[5] Mauk, B. H., Krimigis, S. M., Keath, E . P., Cheng, A. F., Armstrong, T . P., Lanzerotti, L. J.,
Gloeckler, G., and Hamilton, D .C., (1987), JGR, 92, 15,283 – 15,308.
[6] Ness, N. F., Acuna, M. H., Behannon, K. W., Burlaga, L. F., Connerney, J. E. P., Lepping, R. P.,
Neubauer, F. M., (1986), Science, 233, 85-89, https://doi.org/10.1126/science.233.4759.85.
[7] Connerney, J. E. P., Acuna, M. H. and Ness, N. F., JGR, 92, 15,329-15,336.
[8] Cohen, I. J., Turner, D. L., Kollmann, P., Clark, G. B., Hill, M. E., Regoli, L. H., and Gershman, D. J., (2023), GRL, ESS Open Archive, https://doi.org/10.22541/essoar.167874177.75849866/v2
[9] Scarf, F. L., Gurnett, D. A., Kurth, W. S., Coroniti, F. V., Kennel, C. F., and Poynter, R. L., (1987), JGR, 92, 15,217 – 15,224.
TRAJECTORY PLOT DIFFERENT VIEWS
Figure 2. Energy Time Color Spectrogram of ion and electron intensities within Uranus’ Inner Magnetosphere .
Gradient Drift Time Scales versus Proton Charge Exchange Loss & Electron Ionization Loss Times Scales, respectively, due to Uranus’ H corona as a Function of Voyager 2 SCET. Similar calculations, not shown, were done for convection time scales for injection events from the magnetotail.
Conclusions
Sittler et al. (1987) were the first to propose injection event occurring within Uranus’ magnetosphere using Voyager 2 plasma data (PLS) and was not considered in the Cohen et al. (2023) paper who argued against injection events using only energetic particle data (LECP). The plasma data (10 V to 5950 V) as shown in Sittler et al (1987) is the most sensitive data set to detect injection events at Uranus. The observed energy-time dependence of the ion data and the large asymmetry in the electron data, especially for the keV electrons, make a very strong argument for injection events occurring at Uranus.
Sittler et al. (1987) show that the solar wind SSW ~ 1025 ions/s can be an important source of plasma to the magnetosphere and with 50 kV across the tail with injection from the tail can provide the hot plasma observed within Uranus’ inner magnetosphere.
  McNutt et al. (1987) argued against a solar wind source, since energetic 4He++ was not detected by LECP but is contrary to expectations, therefore, a future plasma instrument should have a charge state capability, at min to detect 4He++ ions < 10 kV energies.
  Another potential source of protons to the tail is ionospheric protons being pulled out by electrons within the auroral oval (McNutt et al. (1987).
McNutt et al (1987) showed that Uranus’ hydrogen corona can be a significant of source of the warm protons T ~ 10 eV within Uranus’ inner magnetosphere, but pickup energies ~ 1 eV/amu requires a mechanism to energize warm protons to ~ 10 eV. Proton charge exchange with H corona is an important sink for protons.
Inside the inner edge (plasmasphere) where convected electric field is short circuited by the polarization electric field due inward convected keV ions and electrons drifting in opposite directions and using warm proton densities by McNutt et al (1987) Sittler et al. (1987) estimated thermal electrons must have Tec < 2 eV.
Sittler et al. (1987) estimated convective time scales between 1-3 days with electrons providing the most important constraints. Here, they compared convection time scales with gradient drift time scales for electrons and protons and large day night asymmetry for keV electrons. H corona not important sink for electrons.
As shown in Figure 3 for the various tail plasma sheet crossings, the Electron density ne ~ 2 x10-3 /cm3 and Te ~ 1 keV. Bohannon et al (1987) showed the plasma proton P ~ 7.5 and electrons e ~ 2.5 for total  ~ 10. The pressure from energetic protons much smaller than plasma electron pressure ~ e / 10.
Since UKR was primarily on the nightside (Warwick et al., 1986) this would also support the asymmetry we see for electron energies < 6 keV.
Once we finish this FY23 our recovery of the plasma electron observations for both V! and V2 Jovian flybys we can then do Uranus.
Figure 1
Figure 3
Figure 6
Figure 7
Figure 8
Figure 9
Figure 10