## Slide 1
LaRC Structural and Thermal Systems Branch (D206)
Thermal Technology Highlight
Ruth Amundsen, Senior Thermal Engineer
23 August 2023
Notes: STILL

## Slide 2
The flexible thermal protection system (FTPS) was developed to enable large inflatable heatshields, which can land higher mass than existing heatshield technologies
FPTS consists of 3 layers: external woven ceramic fabric, middle layer of insulators, internal gas barrier
In Nov. 2022, the Low-Earth Orbit Flight Test (LOFTID) project demonstrated re-entry of 6-meter (~20 ft.) inflatable aeroshell from LEO
FTPS and trajectory design utilized a probabilistic margin process to reduce over-margining and ensure significantly severe thermal response for model correlation and material proofing
Flexible Thermal Protection System (FTPS)
Cross Section of Inflated LOFTID Payload and Heatshield
Inflatable Toroids
FTPS
LOFTID Centerbody
loftid_fact_sheet_layout_090922_508.pdf (nasa.gov)
Toroid
Gas Barrier
Insulation
Ceramic Fabric
Re-Entry Flow
Example Maximum Critical Temperature Probability Distribution
Probabilistic Risk Analysis and Margin Process for a Flexible Thermal Protection System - NASA Technical Reports Server (NTRS)

## Slide 3
Material layup underwent years of design and testing to reach current fidelity and readiness for flight
Flexible Thermal Protection System (FTPS)
Testing at Boeing LCAT Arc Jet Facility
LOFTID Inflation and Separation
Source: LOFTID project imagery.
Source: LOFTID Demonstration Images | NASA
Test Coupon
Heated FTPS Material