## Slide 1
GFSSP Training Course
André LeClair & Alok Majumdar
Propulsion Systems Department
NASA/Marshall Space Flight Center
alok.k.majumdar@nasa.gov
andre.c.leclair@nasa.gov
Thermal & Fluids Analysis Workshop
August 21-25, 2023
NASA/GSFC

## Slide 2
Course Outline
For more information about GFSSP:
https://www.nasa.gov/gfssp
Introduction
Hands-on Demonstration Problems
  Steady-state (Pipe System)
  Transient (Tank Blowdown)
Brief Overview of Mathematical Formulation and Resistance Options
Tutorials
  Waterhammer
  Pipe Chilldown

## Slide 3
Generalized Fluid System Simulation Program (GFSSP) Objective
    Provide a generalized and easy-to-use flow analysis tool
Started development in 1994
      General purpose computer program to compute flow network parameters
            Pressure
            Temperature
            Flow distribution in flow network
            With solid to fluid (conjugate) heat transfer
        Initially developed to analyze
          Turbopump Internal Flow
          Propulsion Systems Transient Flow
Background

## Slide 4
Navier Stokes or Network Flow Analysis
Computational Fluid Dynamics
(CFD)
Navier Stokes Analysis
(NSA)
Network Flow Analysis
(NFA)
Finite Difference
Finite Element
Finite Volume
Finite Volume
Finite Difference
GFSSP

## Slide 5
Navier Stokes Analysis
Suitable for detailed flow analysis within a component
Requires fine grid resolution to accurately model transport processes
Used after preliminary design
Network Flow Analysis
Suitable for flow analysis of a system consisting of several components
Uses empirical laws of transport processes
Used during preliminary design
Navier Stokes or Network Flow Analysis

## Slide 6
Network Definition
Flow Problem
GFSSP Model

## Slide 7
Units and Sign Conventions
Units
External Internal
(input/output) (inside GFSSP)
        Length inches feet
        Area inches2 feet2
        Pressure psia psf
        Temperature °F °R
        Mass Injection lbm/sec lbm/sec
        Heat Source Btu/s OR Btu/lbm Btu/s OR Btu/lbm
Sign Conventions
        Mass Input to Node: positive (+)
        Mass Output from Node: negative (-)
        Heat Input to Node: positive (+)
        Heat Output from Node: negative (-)

## Slide 8
Principal Variables
  Unknown Variables Available Equations to Solve
  1. Pressure 1. Mass Conservation Equation
  2. Flowrate 2. Momentum Conservation Equation
  3. Fluid Temperature 3. Energy Conservation Equation of Fluid
  4. Solid Temperature 4. Energy Conservation Equation of Solid
  5. Species Concentration 5. Conservation Equations for Mass Fraction of Species
  6. Mass 6. Thermodynamic Equation of State
Mathematical Formulation (1/2)

## Slide 9
Auxiliary Variables
              Thermodynamic Properties
              Flow Resistance Factor
              Heat Transfer Coefficient
  Unknown Variables Available Equations to Solve
  Density
  Specific Heats Equilibrium Thermodynamic Relations
  Viscosity [GASP, WASP & GASPAK Property Programs]
  Thermal Conductivity
  Flow Resistance Factor Empirical Relations
  Heat Transfer Coefficient
Mathematical Formulation (2/2)

## Slide 10
Program Structure

## Slide 11
Resistance Options (1/3)
1. Pipe Flow
2. Flow Through a Restriction
3. Non-Circular Duct
4. Pipe Flow with Entrance
& Exit Losses
5. Thin, Sharp Orifice
6. Thick Orifice
7. Square Reduction
8. Square Expansion
9. Rotating Annular Duct

## Slide 12
Resistance Options (2/3)
10. Rotating Radial Duct
11. Labyrinth Seal
12. Face Seal
13. Common Fittings
& Valves
14. Pump Characteristics
15. Pump Power
16. Valve with Given Cv
17. Viscojet
P
18. Control Valve

## Slide 13
Resistance Options (3/3)
U
19. User Defined
20. Heat Exchanger Core
21. Parallel Tube
22. Compressible Orifice
23. Labyrinth Seal (Egli Correlation
24. Fixed Flowrate
25. Cartesian Grid

## Slide 14
GFSSP requires the following thermodynamic and thermophysical properties of fluids for the solution of the governing equations
      Density [r (T, p)]
      Absolute Viscosity [m (T, p)]
      Thermal Conductivity [k (T, p)]
      Specific Heat at Constant Pressure [Cp (T, p)]
      Specific Heat Ratio [g (T, p)]
GFSSP requires these properties at every node, at each iteration
Properties are supplied by thermodynamic property programs integrated into GFSSP
  GASP/WASP
  GASPAK
User can also supply these properties with:
  Interpolation tables
  Calls to user-supplied Fortran code
  Ideal gas properties
Fluid Options (1/2)

## Slide 15
Fluid Options (2/2)
ID Number | SOURCE / FLUID | ID Number | SOURCE / FLUID | ID Number | SOURCE / FLUID
1 | GASP He | 51 | GASPAK He | 69 | GASPAK Kr
2 | GASP CH4 | 52 | GASPAK CH4 | 70 | GASPAK Propane
3 | GASP Ne | 53 | GASPAK Ne | 71 | GASPAK Xe
4 | GASP N2 | 54 | GASPAK N2 | 72 | GASPAK R-11
5 | GASP CO | 55 | GASPAK CO | 73 | GASPAK R-12
6 | GASP O2 | 56 | GASPAK O2 | 74 | GASPAK R-22
7 | GASP Ar | 57 | GASPAK Ar | 75 | GASPAK R-32
8 | GASP CO2 | 58 | GASPAK CO2 | 76 | GASPAK R-123
9 | GASP F2 | 59 | GASPAK H2 (para) | 77 | GASPAK R-124
10 | GASP H2 (para) | 60 | GASPAK H2 (normal) | 78 | GASPAK R-125
11 | WASP H2O | 61 | GASPAK H2O | 79 | GASPAK R-134A
12 | RP-1 Tables | 62 | GASPAK RP-1 (liq) | 80 | GASPAK R-152A
 |  | 63 | GASPAK Isobutane | 81 | GASPAK N2F3
33 | Ideal Gas | 64 | GASPAK Butane | 82 | GASPAK NH3
 |  | 65 | GASPAK Deuterium | 84 | GASPAK H2O2
37 | User Fluid 1 | 66 | GASPAK Ethane | 86 | GASPAK Air
38 | User Fluid 2 | 67 | GASPAK Ethylene |  | 
39 | User Fluid 3 | 68 | GASPAK H2S |  | 

## Slide 16
Additional Options
Variable Geometry
Variable Rotation
Variable Heat Addition
Turbopump
Heat Exchanger
Tank Pressurization
Control Valve
Valve Open/Close
Conjugate Heat Transfer
Pressure Regulator
Flow Regulator
Relief Valve
Multi-dimensional flow
Fluid Mixture
Psychrometric Calculation
Multi-Layer Insulation

## Slide 17
FASTRAC Turbopump (1/4)

## Slide 18
GFSSP Model of the Fastrac Turbopump
FASTRAC Turbopump (2/4)

## Slide 19
Turbopump Test to 20000 RPM with Gas Generator
FASTRAC Turbopump (3/4)

## Slide 20
Pressure History Comparison at RP-1 Impeller Back Face
[Labyrinth Seal Inlet (211) and Outlet (212)]
FASTRAC Turbopump Model Results
FASTRAC Turbopump (4/4)

## Slide 21
LOX Tank
RP-1 Tank
Engine
Interface
Tank Pressurization (1/3)

## Slide 22
Tank Pressurization (2/3)
Example 12 – MIG Canvas
LOX Tank
Engine
Interface
RP-1 Tank

## Slide 23
Engine Cut
Comparison of GFSSP Predicted LOX Ullage Pressure with Test Data
Tank Pressurization (3/3)

## Slide 24
Ball Valve Opening History Parameters
a = Lg/LT
PR = pR/p0
Rapid Valve Opening (priming)
Schematic of Pipeline System with Ball Valve location

## Slide 25
Results (priming)
Ball Valve
Opening History
Parameters
a = Lg/LT = 0.45
PR = pR/p0 = 7
Pressure at Dead End (entrapped air pressure)

## Slide 26
Ex14: GFSSP Model of Cryogenic Transfer Line

## Slide 27
Ex14: Comparison with Analytical Solution

## Slide 28
p = 86.7 psia
p = 36.74 psia
p = 61.72 psia
p = 161 psia
Subcooled LH2 for various driving pressures
Station #1 (violet)
—20 ft from tank inlet
Station #2 (red)
—80 ft from tank inlet
Station #3 (green)
—141 ft from tank inlet
Station #4 (blue)
—198 ft from tank inlet
Ex14: Comparison with Test Data

## Slide 29
Inflatable Re-Entry Vehicle (IRVE3) (1/2)
N2 Tank
Control Valve
Ballutes (x7)
Pressure
Regulator

## Slide 30
Orange: Flight Data
Green: GFSSP Prediction
IRVE3 (2/2)
Pressure in Ballute 3

## Slide 31
Ex28: Charge-Hold-Vent Chill & Fill
K-site LH2 tank test data
GH2 vented:
  32 lb (test)
  32.5 lb (GFSSP prediction)

## Slide 32
GFSSP Demonstration Problem 1

## Slide 33
Build Model on MIG Canvas

## Slide 34
Q (GPM) | (lbm/s) | Head (ft) | P (psf) | (lbm/s)2
0 | 0 | 495 | 30888 | 0
4000 | 556.13 | 485 | 30264 | 3.093x105
8000 | 1112.3 | 470 | 29328 | 1.2372x106
12000 | 1668.4 | 450 | 28080 | 2.784x106
16000 | 2224.5 | 425 | 26520 | 4.948x106
20000 | 2781 | 385 | 24024 | 7.734x106
Q (GPM) |  | Head (ft) | P (psf) | 
0 | 0 | 495 | 30888 | 0
4000 | 556.13 | 485 | 30264 | 3.093x105
8000 | 1112.3 | 470 | 29328 | 1.2372x106
12000 | 1668.4 | 450 | 28080 | 2.784x106
16000 | 2224.5 | 425 | 26520 | 4.948x106
20000 | 2781 | 385 | 24024 | 7.734x106
Manufacturer’s Pump Curve
(Head vs. Flowrate)
2) Convert to lb/s and psf
3) Plot DP vs.
Determination of Pump Characteristics
4) Curve fit

## Slide 35
Tank
V = 10 ft3
Initial Conditions
Pi = 100 psia
Ti = 80°F
d = 0.1 in
Patm = 14.7 psia
Tank
Atmosphere
GFFSP Demonstration Problem 2

## Slide 36
Tank Volume
Initial P, T
Internal Node Initial Conditions

## Slide 37
Specify History Filename
GFSSP will interpolate transient boundary conditions from the history file
Even if boundary conditions are constant, at least two lines must be given
Transient Boundary Conditions

## Slide 38
Start Winplot
Select Parameters
Plotting Transient Results

## Slide 39
Add Conjugate Heat Transfer (1/2)
    Enable Conjugate Heat Transfer with User-Specified Solid-to-Fluid heat transfer coefficient
    Add Solid Node 3, and Fluid-to-Solid Conductor 31
Demo 3: Tank Blowdown with Heat Transfer (1/2)

## Slide 40
Add Conjugate Heat Transfer (2/2)
    Tank material, mass: SS304, 471 lbm ; initially at 80 °F
    Tank surface area: 3250 in2
    Heat transfer coefficient value of 6×10-4 BTU/ft2-s-F (= 2.2 BTU/ft2-hr-F) will be entered as a placeholder
        Value can be overwritten by the value calculated by the user subroutine
Demo 3: Tank Blowdown with Heat Transfer (2/2)

## Slide 41
Problem of a Steady State Flow Network
Given: Boundary Node Pressures and Temperatures
Find: Internal Node Pressures and Temperatures; Flowrates in Branches
Mathematical Closure (1/2)
Primary Variables
Secondary Variables

## Slide 42
Mathematical Closure (2/2)
Problem of an Unsteady Flow Network
Given: Boundary Node Pressures and Temperatures; Initial Values at Internal Nodes
Find: Internal Node Pressures and Temperatures; Flowrates in Branches with Time
Tank
V = 10 ft3
Initial Conditions
Pi = 100 psia
Ti = 80°F
d = 0.1 in
Patm = 14.7 psia
Secondary Variables
Primary Variables

## Slide 43
Mass Conservation Equation
Note: Pressure does not appear explicitly in Mass Conservation Equation although it is earmarked for calculating pressures
Governing Equations (1/4)

## Slide 44
Governing Equations (2/4)
Energy Conservation Equation
    Can be written in terms of Enthalpy (h) or Entropy (s)
    Based on Upwind Scheme
Enthalpy Equation
Note: J = 778.17 ft-lbf/Btu
Rate of Increase of Internal Energy = Enthalpy Inflow - Enthalpy Outflow + Heat Source

## Slide 45
Conservation Equation
Successive Substitution Form
Solid Node
Ambient Node
Fluid Node
Governing Equations (3/4)

## Slide 46
Governing Equations (4/4)
mass * acceleration = forces
Unsteady
Longitudinal Inertia
Transverse Inertia
Pressure
Gravity
Friction
Centrifugal
Shear Stress
Moving Boundary
Normal Stress
External Force
i
j
g
q
w
Axis of Rotation
Branch
Node
Node
ri
rj
Momentum Conservation Equation
    Represents Newton’s Second Law of Motion

## Slide 47
Mass x Acceleration Terms in GFSSP
    Unsteady
    Longitudinal Inertia
    Transverse Inertia
Momentum Conservation Equation (1/2)
i
j

## Slide 48
Momentum Conservation Equation (2/2)
Force Terms in GFSSP
    Pressure
    Gravity
    Friction
    Centrifugal
i
j
g
q
w
Axis of Rotation
Branch
Node
Node
ri
rj

## Slide 49
In classical fluid mechanics, pressure drop can be related to dynamic head by a dimensionless constant K
GFSSP’s momentum equation expresses friction losses in terms of flow rate
The relationship between K and Kf
Note that Kf is not dimensionless
    Units:
Friction Term in GFSSP’s Momentum Equation

## Slide 50
Resistance Option 1
Pipe Flow
For Re < 2300, Friction Factor (f )
For Re > 2300, Friction Factor
(using Colebrook Equation)
Flow Resistance Factor

## Slide 51
Flow Through a Restriction (1/2)
Loss Coefficient: CL
      Sometimes called “Flow Coefficient” or “Discharge Coefficient”
      Smaller values of CL indicate greater resistance
      K and CL are related by:
      If User sets CL = 0
            GFSSP will set Kf to 0 (inviscid flow through the branch)
Resistance Option 2

## Slide 52
Common Fittings and Valves
Types of Fittings and Valves
45°, 90°, and 180° Elbows
Standard
Long
Mitered
Tees
Valves
Screwed
Flanged/Welded
Stub-in-Type
Gate/Ball/Plug
Globe [Std., Angle/Y-Type]
Diaphragm [Dam Type]
Butterfly
Check [Lift, Swing, Tilt]
Two-K Method
Resistance Option 13
Flow Resistance Factor
where:
K1 = K for the fitting at Re = 1
K∞ = K for the fitting at Re = ∞ (K2 in GFSSP)
D = Internal diameter of attached pipe (in)

## Slide 53
Pump Characteristics
        Option 14 considers the branch as a pump with given characteristics
        Pump Characteristics are expressed in the pressure rise
        Momentum Source (S) used to induce the desired flow
Resistance Option 14
where:
Dp = Pressure Rise (lbf/ft2)
= Flow Rate (lbm/sec)
Dp

## Slide 54
Resistance Option 15
Pump Power
      Considers the branch as a pump with a given horsepower (P) and efficiency (h )
      Momentum Source (S ) used to induce the desired flow

## Slide 55
Resistance Option 16
Valve with Given Cv
    Branch considered as a valve with a given Cv
Flow Resistance Factor

## Slide 56
Compressible Orifice (1/2)
  Option 22 considers branch as an orifice for compressible flow
  Flowrate is calculated from a simplified momentum equation
  Input is identical to Option 2 (Restriction)
  Flow will choke at the critical pressure ratio (Pdown/Pup)
Resistance Option 22 (1/2)

## Slide 57
Compressible Orifice (2/2)
  If (choked flow)
  If
Resistance Option 22 (2/2)
=
=

## Slide 58
Thank You!
For more information:
  https://www.nasa.gov/gfssp
Contact:
  alok.k.majumdar@nasa.gov
  andre.c.leclair@nasa.gov
Videos of GFSSP 3-day training class:
  https://nescacademy.nasa.gov