## Slide 1: Outer Planets Exploration: Considerations for International Cooperation
Kunio M. Sayanagi (NASA Langley Research Center)
ISAS Planetary Exploration Workshop 2023（August 28-30, 2023）
https://www.isas.jaxa.jp/en/researchers/info/003437.html
Background: Voyager 2 Image of Uranus (NASA Image Release PIA00143)

## Slide 2: Goals of this talk
From the Meeting Announcement:
https://www.isas.jaxa.jp/en/researchers/info/003437.html
“One of the other purposes of this workshop is to build a cross-sectoral team across universities, international organizations, and JAXA that will lead to mission proposals to help create our own exploration roadmap for the next few years or even future decades.”
Perspective: Ideas presented in this presentation are what I want to see as an individual scientist.

## Slide 3: Japan-US Space Collaboration Agreement
On January 13, 2023, Japan and US signed: “Framework Agreement between the Government of Japan and the Government of The United States of America for Cooperation in the Exploration and Use of Outer Space, Including the Moon and Other Celestial Bodies, for Peaceful Purposes”
Signed by US Secretary of State Anthony Blinken and Japanese Foreign Minister Yoshimasa Hayashi at NASA HQ
NASA Press Release: https://www.nasa.gov/press-release/us-japan-sign-space-collaboration-agreement-at-nasa-headquarters
Full Text available at Japanese Ministry of Foreign Affairs website: https://www.mofa.go.jp/mofaj/ila/st/page24_002128.html

## Slide 4: Scopes of Japan-US Framework Agreement
Activities Areas:
Space science, including lunar science;
Earth science;
Space operations and exploration, including lunar operations and exploration;
Aeronautical science and technology;
Space technology;
Space transportation;
Safety and mission assurance; and
Other relevant areas as mutually determined.
Forms of Cooperation:
Use of spacecraft and space research platforms;
Use of scientific instruments onboard spacecraft and space research platforms;
Crewed spaceflight operations;
Use of sounding rockets and scientific balloons;
Use of aircraft;
Use of ground-based antennas for tracking and data acquisition;
Use of ground-based space research facilities;
Exchanges of scientists, engineers, or other experts on general or specific subjects;
Exchanges of scientific data;
Space education;
Public outreach activities; and
Other forms of cooperation as mutually determined.

## Slide 5: Action Item
Find out what is needed to leverage this Framework Agreement to do more Science!

## Slide 6: Considerations for Instruments
Example: Uranus Orbiter and Probe (UOP) Imaging Instrument
  UOP Report: https://tinyurl.com/2p88fx4f
  Originally presented at Uranus Flagship 2023 Meeting: https://www.hou.usra.edu/meetings/uranusflagship2023/pdf/8145.pdf

## Slide 7: Measurement Requirement Summary (From UOP Decadal Study)
Science Measurement Requirements
Uranus:
  Imaging: 50 km/pix
  VIS/NIR Spectrometer: 500 km/pix
  Rings/Small Moons:
  Imaging: 0.1 km/pix
  VIS/NIR Spectrometer: 1 km/pix
Major Satellites:
  Imaging: 0.5 km/pix
  VIS/NIR Spectrometer: 3 km/pix
Instrument Performance
Field of View (FOV; degree)
Resolution (degree/pix)
Wavelength Range
How many / Which filters?
Spectral Resolution
How many imaging instruments?
Must Translate to Instrument Performance

## Slide 8: Uranus and Rings Imaging (Based on Decadal UOP orbits)
Sunlight
Uranus Obs. Opportunities
Obs. Range: 5e5 – 2e6 km
Imag. Res. (50 km/pix): 100 µrad/pix – 25 µrad/pix
VIS/NIR Res (500 km/pix): 1000 µrad/pix – 250 µrad/pix
FOV: Uranus Size varies: 5.8 deg – 1.5 deg
Sunlight
Ring Obs. Opportunities
Initial Orbit: 30 deg Inclination
S/C Distance above ring plane: 50,000 km (30 deg orb) 17,000 km (10 deg orb) 3,500 km (2 deg orb)
Imaging Req: 0.1 km/pix  can be met at 3,500 km range with 28 µrad/pix
VIS/NIR Req: 1 km/pix  can be met at 3,500 km range with 280 µrad/pix
Uranus
Rings

## Slide 9: Major Satellites – Flyby Ranges in UOP Decadal Orbits
Ariel: Range: ~2500 km Imaging 0.5 km/pix = 260 µrad/pix VIS/NIR 3 km/pix = 1500 µrad/pix
Ang. Size = 26 degree
Umbriel: Range: ~6000 km Imaging 0.5 km/pix = 92 µrad/pix VIS/NIR 3 km/pix = 550 µrad/pix
Ang. Size = 11.1 degree
Titania: Range: ~2500 km Imaging 0.5 km/pix = 290 µrad/pix VIS/NIR 3 km/pix = 1700 µrad/pix
Ang. Size = 35 degree
Oberon: Range: ~3500 km Imaging 0.5 km/pix = 180 µrad/pix VIS/NIR 3 km/pix = 1100 µrad/pix
Ang. Size = 25 degree
Steepest Req.

## Slide 10: Instrument Considerations Summary
Synthesized Imaging Instrument Requirements based on 2020 UOP Study Orbits:
Above “requirements” are dependent on the assumed orbits
During early mission panning, the process to tune the instrument performance is more important than any intermediate parameters
Early coordination between instrument + orbit design is important, especially in international cooperation mission
NAC | WAC | VIS/NIR
Resolution <25 µrad/pix FOV: >3 degree | Resolution <92 µrad/pix FOV: >10 degree | Resolution: 250 µrad/pix FOV: >10 degree Spec. Res: 7 nm

## Slide 11: Considerations for SmallSats + Probes
Challenges for Outer Planets SmallSats + Probes:
  Power
    Juno’s solar panel: 350 kg for 400 W
  Thermal
    Juno’s electric heaters need 250W
    SNAP probe needs 3W heating for 30 days after separation from orbiter
  Large delta-V needs
    UOP’s total delta-V = ~ 2 km/s
   SmallSats + Probes benefit from large carrier spacecraft
Examples:
  Small Next-generation Atmospheric Probe (SNAP) https://link.springer.com/article/10.1007/s11214-020-00686-7
  Outer Planet Rideshare Concept: https://www.hou.usra.edu/meetings/opag2020/pdf/6003.pdf

## Slide 12: SNAP as a Second Probe
Mass in orbit: 1913 kg
Payload Mass: 50 kg
UOI rp: 1.05 RU
Orbital Period: ~142 days
Mass: 321 kg
Diameter: 1.2 m, 45° sphere-cone
10-bar* pressure altitude
Probe release: ~60 days
EPFA: -20° to -50°
Mass: 30 kg
Diameter: 0.5 m, 45° sphere-cone
10-bar* pressure altitude
Probe release: 30–60 days
EPFA: -20° to -50°
Orbiter
Primary Atm. Probe (PP)
SNAP
Not to scale with Orbiter
*10-bar is requirement for hardware operation for margin, science objective is to reach 5-bar.
From 2017 Ice Giant SDT Study
SNAP
Baseline Orbiter and Probe: Ice Giant SDT Architecture #5
120 cm
91 cm
50 cm
37 cm

## Slide 13
SNAP: Concept of Operations

## Slide 14: SNAP: Concept of Operations
Not to Scale
Probe Separation
UOI: T = 0 day

## Slide 15: Rideshare to Outer Solar System
Case Study: Use Dragonfly launch to send small missions to Saturn Study conducted at NASA Langley Research Center
Dragonfly’s preliminary interplanetary trajectory: Total ΔV = 217.7 m/s Launch C3 = 16 km2/s2 (Scott et al. 2018, Advances in the Astronautical Sciences 18-416).
Carrier-Relay Spacecraft (CRSC) based on a Propulsive ESPA Bus (Stender et al. 2015, 31st Space Symposium).
CRSC Subsystem | Mass
Structure (Estimate) | 391 kg
Solar Panels | 202 kg
TCS+ACS+CDH+Comm | 105 kg
RCS | 46 kg
SmallSats / Probe | 130 kg x2 = 260 kg
Dry Mass | 1,005 kg
Propellant (ΔV = 246.6 m/s) | 128 kg
Total CRSC Launch Mass | 1,132 kg

## Slide 16: Potential Small Missions to Saturn Case Study: Mission Concepts for the Saturn System Enabled by the Dragonfly Launch 1Kunio M. Sayanagi, 2Cindy L. Young, 3Robert W. Ebert, 4Morgan L. Cable, 5Matthew S. Tiscareno, 6Matthew M. Hedman, 4David H. Atkinson, and 7Olivier Mousis 1Hampton University, 2NASA Langley Research Center, 3SwRI, 4NASA-JPL/Caltech, 5SETI Institute, 6University of Idaho, 7Aix-Marseille Université https://www.hou.usra.edu/meetings/opag2020/pdf/6003.pdf

## Slide 17: Considerations for SmallSats + Probes
Small missions and probes can be carried on a larger mission, or a dedicated carrier spacecraft
Potential model for international cooperation

## Slide 18: Considerations for Earth-orbiting Missions
Valuable planetary observations are possible from Earth orbit
Examples:
  Shadow Chaser: Earth-orbiting Stellar Occultation Mission: https://agu.confex.com/agu/fm22/meetingapp.cgi/Paper/1104976

## Slide 19: Shadow Chaser: a Stellar Occultation Mission
Measure the middle and upper atmospheric temperature and density of Uranus and Neptune through stellar occultation (SO) technique from Earth orbit.
Animation by William Saunders (Boston University)
Ingress
Egress

## Slide 20: Stellar Occultation Predictions
  Predicted 56 Uranus and 14 Neptune Occultations between 2025-2035
  20 Uranus and 6 Neptune occultations are observable from the ground
    Demonstrated the value of future orbital mission
  Instrument Requirement: Threshold aperture size of 20 cm to measure vertical structure
  2031-2033 period has multiple viable SO events
  Published as Saunders et al (2022, Planetary and Space Science)
Magnitudes of occulted stars for Predicted SO events in 2025-2035
(Saunders et al. 2022, Planetary and Space Science)
50 cm (S/N=100)
20 cm (S/N=100)
50 cm (S/N=30)
20 cm (S/N=30)
50 cm (S/N=100)
20 cm (S/N=100)
50 cm (S/N=30)
20 cm (S/N=30)

## Slide 21: Shadow Chaser: Potential for International Cooperation
Shadow Chaser has significant potential for international collaboration:
Launch RideShare?
  Shadow Chaser could be launched on RideShare on a Launch by an International Partner
Hosted Payload?
  Shadow Chaser could be an instrument on a host satellite in appropriate orbit
Satellite Constellation?
  Multiple Satellites launched by international partners can measure different locations on Uranus and Neptune

## Slide 22: Summary: Enabling International Outer Planets Missions
Japan-US Space Collaboration Agreement:
  Find out how we leverage the agreement to enable more science
Instrument Collaboration:
  Early cooperation is crucial to design instruments and orbits
SmallSats and Probes to Outer Planets:
  Carrier Spacecraft may enable small missions to outer planets
Earth Orbiting Missions
  Unique opportunities (e.g. stellar occultations) enable high-value outer planet science from Earth orbits with international cooperation potential