## Slide 1: Probing the Sun with Imaging Spectrographs
Amy Winebarger1, P. S. Athiray2, Amir Caspi3, Patrick Champey1, Ken Kobayashi1, Charles Kankelborg4, Katharine Reeves5
1NASA MSFC, 2University of Alabama Huntsville, 3Southwest Research Institute, 4Montana State University, 5Smithsonian Astrophysical Observatory
Predicted MOXSI data
CubeSat to be launch 2025

## Slide 2: The problem
The solar atmosphere is
multi-dimensional
complicated
unpredictable
Solar observations are inherently limited.
Notes: The solar atmosphere is multi-dimensional, complicated and unpredictable.
Three spatial dimensions structured by the magnetic field (not axisymmetric)
Structures in the corona can have strong temperature and density gradients and unique elemental abundances
The structures themselves as well as the density and temperature along the structure can vary at many time scales (sub-second to years)
Variation in elemental abundances from structure-to-structure as a function of time
Solar observations are inherently limited.
Two-dimensional detectors with limited number of pixels
Choose between spatial resolution and field of view
Time scales limited by detector readout time and SNR requirements on short side and instrument lifetime on the long side
Though we can make images with different temperature sensitivity, like arrowband EUV images or X-ray filtergrams. But these images can confuse the density and abundances. If you see something brighten in the image, it is because the plasma cooled or was heated into that passband? Or did the density of the structure increase? Or the abundances of iron increase in that structure?

## Slide 3: Slit Spectrographs

## Slide 4: What is an Imaging Spectrograph?
An Imaging Spectrograph is instrument
with a grating
with spatial resolution
The Imaging Spectrographs in this talk are also slitless:
with large field of view
Spectroheliograms or “Overlappograms” - spatial and spectral data are overlapped.

## Slide 5: History
First spectroheliogram in Lyman alpha observed on March 13, 1959.
Subsequent rocket flights explored the solar spectrum and revealed the atmospheric structure.
Tousey, 1967, ApJ, 149
Notes: On a rocket launch in 1959 was the first spectraheliogram in Lyman alpha. It was made with a slitless, objective type single grating spectrograph with an aluminum filter in the front.

## Slide 6: History
1963
1965
1966
“Therefore this image is not easy to interpret.” - R. Tousey
Tousey, 1967, ApJ, 149
Notes: More spectroheliograms followed. In this paper, Tousey notes “At 256 Ang there is another good image. This is formed by a blend of three strong lines, one is the second line of the He+ Lyman series another is Si X and third is partly S X. Therefore this image is not easy to interpret

## Slide 7: History
Skylab S082A – long wavelength range
O V 63 nm
He II 30.4 nm
Ne VII 46.5 nm
He I 58.4 nm
O IV 55.5 nm
Si XII 50 nm
Mg VII 36.7 nm
Skylab data have been digitized and are available: https://lasco-www.nrl.navy.mil/skylab/index.php?p=content/so82a
Spectroheliograms were obtained by astronauts from May 14, 1973 – February 8, 1974.
Skylab was the only time spectroheliograms were obtained by NASA on an orbiting satellite.
Notes: Despite the difficulty in interpreting these images, an imaging spectrograph was flown in Skylab operational in the year of my birth, 1973. The instrument’s name was S082-A and it had two different wavelength ranges, I am showing the long wavelength range only. As far as I know this is the only time NASA regularly obtained this type of data, though there have been missions from other countries, but the data from those instruments aren’t readily available.

## Slide 8: Unfolding Spectroheliograms
Write a set of linear equations:
Observations = Response Matrix # Solar Parameters(space, [T, ion, velocity])
y = Mx

## Slide 9: Unfolding Spectroheliograms
Write a set of linear equations:
Observations = Response Matrix # Solar Parameters(space, [T, ion, velocity])
y = Mx
Solar Parameters (space, Log T)
“Multi-Ion Model”
Solar Parameters (space, ion)
“Single-Ion Model”

## Slide 10: Unfolding Spectroheliograms
Write a set of linear equations:
Observations = Response Matrix # Solar Parameters(space, [T, ion, velocity])
y = Mx
To find velocity, we find a sparse and smooth solution was best:
Standard least squares term
Penalty on total EM set by 𝛂𝛒
Penalty on square EM set by 0.5𝛂(1- 𝛒)
𝛒 = 1 -> sparse
solution
𝛒 = 0 -> smooth
solution

## Slide 11: Current and Upcoming Imaging Specrographs
Observed ESIS Sounding Rocket data
Observed MaGIXS Sounding Rocket data
Predicted ECCCO data
Proposed SMEX to be launched 2028
Predicted MOXSI data
In Implementation for 2025 launch
Notes: Today I am going to break the cardinal rule of giving a talk – I am not going to give you a highly focused talk on a single specific topic. I am going to cover a lot of different topics, a lot of different instruments and even talk about poorly constrained inversion problems. My main goal of today’s talk is to convince you that this type of data, data taken from a slitless spectrograph, is extremely useful and should be pursued in the next decade of solar observations.

## Slide 12: MaGIXS Instrument Design
Telescope section
Spectrometer section
Camera section
Avionics
Grating
Beam footprint subtends 34o
First mission to use replicated deterministic polished X-ray mandrels

## Slide 13: MaGIXS Instrument Alignment and Calibration
Telescope Mirror Assembly (TMA)
Slit interface Plate: Telescope focal plane, Slit-Jaw system, and interface to rocket skin
Telescope Mirror Assembly (TMA)
Slit interface Plate: Telescope focal plane, Slit-Jaw system, and interface to rocket skin
Science Camera
SOA interface (embedded inside bench)
~1.5 m between TMA and SOA
Calibration activities at 500 m X-Ray beamline at MSFC.

## Slide 14: MaGIXS Flight Summary
30 July 2021, ~18:20 UT
~296 s science data
Notes: Connect vignetting to strw

## Slide 15: Unfolding Spectroheliograms – MaGIXS Outputs
Outputs include :
Fit Data
Spectra at each spatial pixel
Spectrally Pure Maps

## Slide 16: MaGIXS-2 instrument changes
MaGIXS–2 will have
Easier alignment process
Better spatial resolution (x4)
Better spectral resolution (x4)
Larger FOV (4’ –> 12’)
Higher throughput
MaGIXS 2 will launch Summer 2024
MaGIXS-1 Recovery Team

## Slide 17: EUV Snapshot Imaging Spectrograph (ESIS)
N - 1
N - 2
N - 3
N - 4
Sounding rocket instrument
Flew September 30, 2019
300 s of data
Quiet Sun
O V 63 and He I 58.4 nm
Ch 1
Ch 2
Ch 3
Ch 4
dispersion
solar north
Jake Parker, Roy Smart, ESIS, and Charles Kankelborg (ESIS PI)
O V
He I

## Slide 18
4
N
S
E
W
ESIS has 4 Imaging Spectrographs
N
S
E
W
N
S
E
W
3
2
N
S
E
W
1
Combining the four channels allows for the measurement of velocity
𝝺
𝝺
𝝺
𝝺
Exploding Monochromatic Point Source on Sun

## Slide 19: ESIS Data Processing
Level 1 data
Level 2 data
O V spectral line
Level 2 data processing:
Remove optical distortions & vignetting
Extract single spectral line
Rotate solar north is up
2
3
N
N
2
3
𝝺2
𝝺3
N

## Slide 20: ESIS Difference Images – IS 3 – IS 2
Images courtesy of Jake Parker, MSU
N
𝝺2
𝝺3

## Slide 21: Preliminary results from MART
ESIS - 10 s
Slit spectrographs - ~ 1hr
Images courtesy of Jake Parker, Roy Smart, Charles Kankelborg (MSU)

## Slide 22: Multi-Order X-ray Spectral Imager (MOXSI) – PI: A. Caspi (SwRI)
MOXSI uses a spare transmission grating from Chandra High Energy Transmission Grating (HETG).
Chandra HETG
MOXSI is an instrument on CubIXSS
To be launch ___-
Soft X-ray wavelength range
Images courtesy of Amir Caspi (SwRI)

## Slide 23: Multi-Order X-ray Spectral Imager (MOXSI) – PI: A. Caspi (SwRI)
Expected data
0 order
+1, 2, 3 orders
-1, 2, 3 orders
Science goals:
Measure abundance and temperature distribution

## Slide 24: EUV CME and Coronal Connectivity Observatory (ECCCO) – PI: K. Reeves (SAO)
ECCCO proposed to SMEX 2022
Instrument complement includes:
Wide field EUV 2-channel imager
EUV Imaging spectrographs (2)
Short channel
13.1 nm
Long channel
19.3 nm
RAL CCD
Camera
Prime Focus Reflective Grating Spectrometer
Entrance
Filter
Front
Hatch
Focus Mirror
Fold Mirror
Filter Wheel
Shutter Assy

## Slide 25: EUV CME and Coronal Connectivity Observatory (ECCCO) – PI: K. Reeves (SAO)
Fe VIII
Fe XIII
Spectrally pure images
South
Fe VIII
Fe XIII
Simulated data

## Slide 26: Summary
“Therefore this image is not easy to interpret.” - R. Tousey
Expected MOXSI data

## Slide 27: Summary
“Therefore this image is not easy to interpret.” - R. Tousey
Expected MOXSI data

## Slide 28: What’s next?
Imaging spectrometer data allows for rapid measurement of temperature, density, abundances, and velocities over large FOV.
Inversion techniques can be applied to similar observations of extended astrophysical objects.
These diagnostics can be used to solve many open solar physics questions, develop space weather models and forecasting capabilities, and probe fundamental physics in the universe. These key capabilities are currently missing from the Heliophysics System Observatory.