## Slide 1: Intelligent Long Endurance Observing System (ILEOS)
Bryan Duncan (co-I, NASA GSFC)
Meghan Saephan (PI, NASA Ames)
NASA Ames: Jeremy Frank (co-I), Richard Levinson (co-I), Eugene Turkov (co-I), Douglas Caldwell (co-I), Vinay Ravindra (co-I)
Sarah Strode (co-I, NASA GSFC)
William Swartz (co-I, JHU APL)
Kristen Manies (co-I, USGS)
IMPACT: ILEOS will provide a science activity planning system to enable new observing strategies

## Slide 2
Concept of Operations
Example vehicle: High-Altitude-Long-Endurance (HALE) Unmanned Aerial Systems (UAS), but ILEOS could be applied to an airplane platform
  Advantage over airplanes: operate for months and able to loiter over targets at reduced costs
Example instruments: HALE UAS fitted with nitrogen dioxide (NO2) or methane (CH4) sensors
  See Bill Swartz’s talk next on a lightweight NO2 sensor
Example applications: validating satellite data, quantifying emissions, monitoring pollution, environmental justice (neighborhood scale), etc., including in challenging environments (e.g., Arctic, urban).

## Slide 3
ILEOS Architecture
Targeter – leverages scientists’ expertise to fuse data (e.g., emissions, land cover, satellite data, meteorological forecasts) into pixel value maps
Planner – generates flight plan to observe best identified target scenes while enforcing HALE UAS operating constraints (e.g., winds, FAA restrictions)
Reporter – allow users to configure Targeter and Planner, visualize all data and flight plan, and request explanations

## Slide 4
Full ILEOS Pipeline
Example: HALE UAS with a methane sensor to target wetland emissions in Alaska

## Slide 5
Day 1
Day 2
Day 30
.
.
.
.
.
.
30-Day
Average
Gulf of Mexico
Wind direction
.
.
.
Potential Utility of ILEOS: Considering Clouds
Example: Use a HALE UAS fitted with a NO2 sensor to characterize NOx emissions in the Gulf of Mexico from
Oil & natural gas extraction activities (e.g., rigs, support ships, flaring)
International shipping
Intuitively, a raster flight pattern (i.e., “lawn mower” pattern) makes sense, but clouds* complicate this strategy.
*Information on cloud forecasts is just one data input that ILEOS will consider for flight planning.

## Slide 6
Reporter: Flight Plan
Darker red = higher target value

## Slide 7
Reporter: Input Data Sources
Shipping lanes and platform sources
Tropospheric column density of NO2
Users may also view input data to help understand the rationale for the ILEOS flight plan:
Meteorological forecasts (clouds, winds)
Land cover types
Emissions
Point sources (latitude, longitude)
Satellite data

## Slide 8
Future Work
ILEOS’ first 2 years will culminate with a capstone demo featuring simulated observing campaigns overseen by scientists
  Evaluated on at least 2, ideally 4 climate-relevant gas sensing science use cases
Assess users’ ability to generate desired plans and understand relationship between scenes, priority, constraints, and their impact on plan
  Human-in-the-loop evaluation
Sensing Domain | Use Case Type | 
 | Nominal | Stressing
Methane | Urban emissions | Arctic permafrost thaw
Nitrogen Dioxide | Emissions Validation | Upper atmospheric lightning

## Slide 9
Thank You
Byran Duncan, ILEOS co-I
bryan.n.duncan@nasa.gov
Meghan Saephan, ILEOS PI
meghan.saephan@nasa.gov

## Slide 10
BACKUP

## Slide 11
Objectives
Optimize fine-grained spatio-temporal resolution data collection of Earth observations, such as GHG-relevant gases
Novel automated target generation technology
Incorporates coarse-grained satellite data and near real-time environmental (e.g., wind, weather, airspace constraints) data to generate high-value fine-grained resolution data collection plans.
  State-of-the-art automated planning and scheduling algorithms
Designed for human operators; plan explanation and data provenance features will ensure science mission planners understand all key choices made while generating targets and plans.
Innovative techniques for user control and review of decision making
IMPACT: Reduced cost for Earth observations in environments ranging from arctic to urban to offshore (some previously inaccessible), continuous observations not possible for current field/in-situ campaigns, improved science outcomes

## Slide 12
Reporter: Targets and Plans
Targets
Plan

## Slide 13: Targeter Pipeline
Build the ‘features’ of a ‘pixel’
Pixel resolution ~1km
Cluster regions with similar feature spaces
Choose Clusters based on their mean values of the features
Segment Clusters of interest
Assign Segment Value based on formulation by SMEs
Data sources selected based on science case

## Slide 14: Features(1/3)
Cloud feature
(9:30 ET)
(12:30 ET)
(15:30 ET)
Less clouds => good observation possible
If clouds are above a threshold, then the area is completely deprioritized.

## Slide 15: Features (2/3)
NO2 feature
(9:30 ET)
(12:30 ET)
(15:30 ET)
The weights ‘a’, ‘b’, ‘c’ depend upon the GEOS-CF TROPCOL-NO2 which is a measure of continental influence. If the GEOS-CF TROPCOL-NO2 is above a threshold, the Tropomi NO2 reading is deemphasized.
(Land-water mask has been applied prior to normalization of the Tropomi NO2 data)

## Slide 16
Targeter
The Targeter leverages a pixel value module to assign pixel values from varying inputs (left). It then groups similar pixels (middle), and then breaks these groups into scenes with values aggregated from the pixels within them (right).

## Slide 17
Planner
The Planner determines which scenes should be visited and in which order (left),
detailed behaviors within each scene (middle), and refines routes for traveling between and within scenes with wind speed and velocity and HALE UAS operating constraints (right).

## Slide 18
Reporter
The Reporter provides explanations for Targeter and Planner outputs to the user. For example, explanations include icon and popout descriptions of why scenes were not included in a flight.

## Slide 19
Targeter
Interest values:
Unique for each use case
Based on available coarse-grained data (satellite measurements, meteorological, etc.)
Leverage Science SME domain knowledge to provide priority
  NO2 Use Case Coarse Grained Data:
  Land cover (target water)
  Measured satellite NO2
  Cloud cover
  Aerosol optical thickness
  Methane Use Case Coarse Grained Data:
  Land cover (target wetlands)
  Cloud cover
  Inundation
  Measured Methane
Interest Values
Cloud Feature
Sample Value Map for NO2 BOEM Inventory Use Case

## Slide 20
Relevance to Earth Science
ILEOS will focus on use cases related to NO2 and CH4, which both high relevance to the science and application priorities presented in the 2019 Decadal Survey:
  NO2, here a proxy for combustion emissions (e.g., CO2), over oil and natural gas extraction areas of the Gulf of Mexico.
    Estimation of these emission sources(e.g., point - large rigs, line - shipping lanes, and area - small wells and support ships).
  NO2 down to the city block level in urban environments
    Human health (unhealthy to breathe) and environmental justice
  NO2 generated from lightning (collected from above storm clouds)
    Important ingredient in formation of upper tropospheric ozone, expensive to collect with crewed aircraft
  CH4 over Artic-Boreal zone
    Characterize how the water table and air temperature affect the rate of emission
  CH4 from various anthropogenic sources such as industrial processes and leaky natural gas distribution pipelines, in complex urban environments
    Pinpoint sources needing migration for safety reasons or to reduce the GHG footprint of urban areas