## Slide 1: Characterization of In-Space Propulsion Trade Space to Support Initial Human Mars Segment
Patrick R. Chai
Mars Architecture Team
Strategy & Architecture Office
Exploration Systems Development Mission Directorate
NASA Langley Research Center

## Slide 2: Historical Mars Architecture Approach
Design Reference Architecture 5 (2009) Optimized around a long-duration stay with minimal Mars landed mass
Von Braun Mars (1969)
Optimized around Apollo extensibility
Evolvable Mars Campaign (2016)
Optimized around minimal Earth- launched mass and Solar Electric propulsion extensibility
Mars Base Study (1987) Optimized around ISS module extensibility

## Slide 3: Current Mars Architecture Team Approach
The answer to each question requires one or more decisions—but all of these decisions are interrelated, and order matters
WHY We Go
WHO We Send
WHERE We Go
HOW We Get There & Back
WHEN We Go
WHAT We Do There
To define the Mars Architecture, we must answer 6 key questions

## Slide 4: Architecting from the Right
The answers to “Why?” have been defined in the Agency’s Moon-to-Mars Objectives
go.nasa.gov/3zzSNhp
WHY We Go
WHO We Send
WHAT We Do There
WHERE We Go
WHEN We Go
HOW We Get There & Back

## Slide 5
In-Space Transportation Considerations

## Slide 7: How - Transportation Options
NEP Hybrid Nuclear Electric Propulsion
1
NTP Nuclear Thermal Propulsion
2
  ALL-CHEM Chemical Propulsion
4
SEP Hybrid Solar Electric Propulsion
3
Artistic Conceptual Elements Shown
Not to Scale

## Slide 8: Mars Distance Considerations
Mars is much farther from Earth than the Moon is
 | Closest Approach to Earth | Farthest Distance from Earth | Typical Round-Trip “Odometer” Reading | Round-trip Duration
Moon | 360,000 km | 405,000 km | 1,900,000 km | Weeks
Mars | 54,600,000 km | 400,000,000 km | 1,800,000,000 km | Years
Round-trip Mars missions may be twice as long as our longest duration experience base
There will be no way to abort quickly to Earth
On-demand resupply will not be possible

## Slide 9: Roundtrip Mission Duration Drives Energy Need
Energy Needs Exponential for Short Durations
Optimal Roundtrip

## Slide 10: Energy Needs Drives Transportation Concept
NTP
NEP

## Slide 11: Energy Needs Drives Transportation Concept
SEP
Chemical

## Slide 12: Architecture Concept Review Products
www.nasa.gov/MoonToMarsArchitecture
Architecture Definition Document
Detailed documentation of a snapshot of NASA’s human spaceflight architecture and exploration strategy
Moon to Mars Architecture Summary
High-level overview of NASA’s Moon to Mars architecture and exploration strategy
White Papers
Six papers on architecture study details for frequently discussed topics
Notes: Jim briefs charts 17-22

## Slide 13: Summary
Mars missions will require significantly more energy and much longer system service life, with more constrained departure windows, than lunar missions
Shorter total roundtrip duration missions could reduce crew health and performance concerns but pushes the challenge to the in-space transportation system
Four In-Space Transportation propulsion technologies are currently under consideration
Access Mars Transportation White Paper with this QR code or at www.nasa.gov/MoonToMarsArchitecture
13

## Slide 14
BACK UP

## Slide 15: Optimum Departure Windows ~Every 2 Years But must also consider optimum return window
Long-Stay
Short-Stay
Minimum Energy Long-Stay Class, ~ 3 Years Roundtrip
High Energy Short-Stay Class, ~ 2 Years Roundtrip
Increasing Energy = Exponential Increase in Vehicle Mass
Higher energy Mars missions require vehicles that are multiple ISS mass equivalents
“When” is a very complicated decision to address.
What is an acceptable roundtrip duration for humans? What are the Surface Cargo pre-deployment needs? How many rockets do we have and how often can we launch them? What transportation system performance can we afford?
For human mission, we need to wait for alignment for BOTH legs of the trajectory to minimize energy
Higher energy missions can reduce total trip time at the expense of shorter Mars vicinity stay time
Energy needs also vary more, making these missions more challenging to plan