## Slide 1
NASA Atmosphere Observing System (AOS)
Daniel J. Cecil1, NASA MSFC
AOS Deputy Project Scientist – Suborbital
Daniel.J.Cecil@nasa.gov
Scott Braun2, John Yorks2, Tyler Thorsen3
1 NASA Marshall Space Flight Center
2 NASA Goddard Space Flight Center
3 NASA Langley Research Center
ESA-JAXA Pre-Launch EarthCARE Science and Validation Workshop
November 2023
Notes: NASA’s Earth System Observatory is a constellation of satellite observing systems that addresses the five major designated observables from the 2017 NASA Earth Science Decadal Survey. The Atmosphere Observing System, or AOS, addresses two of these designated observables, aerosols and clouds, convection, and precipitation, or CCP. In this talk, I will provide a brief background on the decadal survey recommendations, the AOS science objectives, and the observing system.

## Slide 2: AOS Addresses Aerosol, Cloud, Convection, and Precipitation Processes
AOS-Storm (Inclined orbit, 2029)
  JAXA PMM Radar (Ku-band, Doppler)
  CNES C2OMODO tandem radiometers (89-325 GHZ)
  ALICAT backscatter lidar (532, 1064 nm)
AOS-Sky (Sun-synchronous orbit, 2031)
  Backscatter lidar (details TBD – Italian partnership?)
  Doppler radar (details TBD)
  Passive microwave radiometer (89-700 GHz)
  Polarimeter (350-1570 nm)
  CSA Thin Ice Cloud Imaging Radiometer (4-73 mm)
  CSA aerosol and moisture limb imagers
AOS Suborbital
  Post-launch field programs
  Surface-based networks, supersites
  Leverage existing capabilities, more international partners
International partnerships are very important to AOS, both in the satellite constellation and in suborbital activities.
AOS-Storm [US led)
AOS-Sky [US led)
Pre-decisional
Doppler Radar

## Slide 3: AOS Suborbital
Low Clouds: Microphysics, precipitation initiation
Convection/High Clouds: Microphysics and dynamics, anvil cirrus lifecycle.
Aerosol-Cloud-Radiation Interactions: Vertically resolved aerosol-cloud-radiation interaction processes and lifecycle.
Large airborne campaigns addressing all science themes
Link airborne campaigns with well-instrumented surface sites
Partner with other programs / nations where practical
Campaigns after launch to enable cal-val
Aircraft and payloads depicted are notional… instruments to be prioritized / deconflicted for each campaign.
Need a high altitude (over-storm) remote sensor…
…mid/high altitude aircraft to provide both remote sensing and in situ (aerosol, cloud, precip)
…low/mid altitude aircraft to provide both remote sensing and in situ (aerosol, cloud, precip)
Aircraft, surface sites, and networks from partners will be especially helpful.

## Slide 4: AOS and EarthCARE
AOS and EarthCARE approach cloud and aerosol profiling using similar instrument types, but different frequencies and other details
  Many people / institutions aligned with both missions
Some commonality in the cal-val needs
Surface-based measurements, field campaigns, validation approaches used by each will be of interest to the other
  Validation best-practices talk Wednesday afternoon
  I’m here to discuss collaborations, match names to faces, etc.
Graphic reflects initial architecture concept directed at KDP-A. Additional direction was provided to study architecture changes, which are still on-going.
AOS-Storm [US led)
AOS-Sky [US led)
Pre-decisional
Doppler Radar

## Slide 5: JAXA PMM Radar Capabilities
JAXA Wide Swath Ku Doppler Radar
Height (km)
Simulated Ku Doppler Velocity
Model “Truth”
Courtesy of Pavlos Kollias
Normal scan obs.
Dense sampling obs.
Doppler obs.
x3
・・・
x49
Nadir direction of flight
Vertical sampling, resolution:
250, 500 m for Doppler, dense
125, 250 m for normal scan
Horizontal Resolution: 5 km
Observation range (altitude):
Doppler 17 km
Dense 20 km
Normal 18-20 km
Swath: 250 km
Sensitivity (min dBZ):
Doppler 7.3 dBZ
Dense 7.3 dBZ
Normal 15 dBZ
Doppler uncertainty: 2 m/s @ 16 dBZ
Unambiguous Doppler range: ±30 m/s
Baseline Requirements
  NLT March 2029 launch
  430 km orbit, 55° inclination
Notes: As mentioned, the inclined project is comprised of contributions from NASA, JAXA, and CNES. JAXA will contribute a Ku-band wide-swath precipitation radar with nadir Doppler capability for measuring convective vertical air motions. Dense over-sampling at nadir combined with the use of the displaced phase center antenna, or DPCA, approach for better removal of spacecraft motion and non-uniform beam filling effects allows us to obtain good measurements of the structure of convective vertical motions for many convective systems. Takuji Kubota will provide details of the radar in his presentation. CNES will provide two identical passive microwave radiometers with channels ranging from 89-325 GHz for characterization of ice cloud properties. The tandem radiometers provide the time rate of change of brightness temperatures over a 2-minute period to allow inference of evolving microphysics and convective vertical ice mass flux. NASA will provide a two-wavelength backscatter lidar with performance similar to or better than CALIPSO, but in a more compact, lower-cost package. The lidar will provide profiles of aerosols and clouds as well as boundary layer height. The expected launch is no earlier than mid 2028.

## Slide 6: C2OMODO Radiometer Capabilities
CNES Microwave Radiometers (89, 183, 325 GHz)
89 GHz 10 km FOV 1 channel Nyquist sampling
183.31 GHz 5 km FOV 6 channels Nyquist sampling
325.15 GHz 3 km FOV 3 channels Continuous sampling
CNES Radiometer Scan Pattern Near Nadir
89 GHz
183 GHz
325 GHz
  NLT March 2029 launch
  430 km orbit, 55° inclination
C2OMODO: Convective Core Observations through MicrOwave Derivatives in the trOpics (Brogniez et al. 2022)
Time-differenced radiometer measurements (~1-2-minutes) contain information on convective vertical motions
Notes: As mentioned, the inclined project is comprised of contributions from NASA, JAXA, and CNES. JAXA will contribute a Ku-band wide-swath precipitation radar with nadir Doppler capability for measuring convective vertical air motions. Dense over-sampling at nadir combined with the use of the displaced phase center antenna, or DPCA, approach for better removal of spacecraft motion and non-uniform beam filling effects allows us to obtain good measurements of the structure of convective vertical motions for many convective systems. Takuji Kubota will provide details of the radar in his presentation. CNES will provide two identical passive microwave radiometers with channels ranging from 89-325 GHz for characterization of ice cloud properties. The tandem radiometers provide the time rate of change of brightness temperatures over a 2-minute period to allow inference of evolving microphysics and convective vertical ice mass flux. NASA will provide a two-wavelength backscatter lidar with performance similar to or better than CALIPSO, but in a more compact, lower-cost package. The lidar will provide profiles of aerosols and clouds as well as boundary layer height. The expected launch is no earlier than mid 2028.

## Slide 7: ALICAT Lidar Capabilities
CATS Backscatter Lidar Example
ALICAT: Atmospheric Lidar for Cloud and Aerosol Transport
Low pulse energy, high pulse repetition frequency
Frequencies: 532, 1064 nm
Provides total attenuated backscatter and depolarization at both frequencies
Heritage: Cloud Physics Lidar, Cloud-Aerosol Transport System (CATS)
  NLT March 2029 launch
  430 km orbit, 55° inclination
Notes: As mentioned, the inclined project is comprised of contributions from NASA, JAXA, and CNES. JAXA will contribute a Ku-band wide-swath precipitation radar with nadir Doppler capability for measuring convective vertical air motions. Dense over-sampling at nadir combined with the use of the displaced phase center antenna, or DPCA, approach for better removal of spacecraft motion and non-uniform beam filling effects allows us to obtain good measurements of the structure of convective vertical motions for many convective systems. Takuji Kubota will provide details of the radar in his presentation. CNES will provide two identical passive microwave radiometers with channels ranging from 89-325 GHz for characterization of ice cloud properties. The tandem radiometers provide the time rate of change of brightness temperatures over a 2-minute period to allow inference of evolving microphysics and convective vertical ice mass flux. NASA will provide a two-wavelength backscatter lidar with performance similar to or better than CALIPSO, but in a more compact, lower-cost package. The lidar will provide profiles of aerosols and clouds as well as boundary layer height. The expected launch is no earlier than mid 2028.

## Slide 8: AOS-Sky Lidar
532 nm, 1064 Backscatter Lidar*
Clouds
Smoke
Dust
Clouds
• Target requirement of daytime SNR equivalent to CALIPSO night SNR
• NASA HQ has initiated study of partnership with Italian Space Agency (ASI)
ASI lidar:
  355 nm Raman (extinction)
  532, 1064 nm backscatter
• Requires formation flying of AOS-Sky and ASI lidar
  NET December 2031 launch
  450 km orbit, sun-sync-13:30 LTAN
Notes: The polar mission builds on the heritage of the A Train and is designed to optimize instrument synergies to obtain accurate information on processes relevant to climate sensitivity and feedback and aerosol forcing of climate, which requires globally distributed observations. It includes several advanced sensors provided by NASA and industry and contributed instruments from CSA. The next several slides will focus on the key capabilities within each orbit.

## Slide 9: AOS-Sky Radar
Quantity | Resolution @ altitude | Accuracy | Sensitivity @ altitude
Radar reflectivity, cloud-profiling | Horiz.: 2.0 km Vert.: 300 m @ 0.5 – 1.0 km 300 m @ 1.0 - 2.5 km 500 m @ 2.5 – 6 km 500 m @ 6 – 20 km | 1.5 dB * | ≤–5 dBZ @ 0.5 km – 1 km ≤–15 dBZ @ 1 km – 2.5 km ≤–20 dBZ @ 2.5 km – 6 km ≤–24 dBZ @ 6 km – 20 km
Baseline Requirements
Figures at left courtesy of Matt McLinden
• Requirements are frequency agnostic
• Enhancements to be studied: Second frequency, narrow swath, passive measurements if Ka band, LDR
  NET December 2031 launch
  450 km orbit, sun-sync-13:30 LTAN
Notes: Third party images:
Lower center image provided by Vanderlei Martins, permission obtained June 8, 2022. Email text below:
“Hi Scott, Yes, this is a multi-angle sequence from HARP showing 10 viewing angles. Since all other examples in your slide are for level 2, I am also attaching an example of level 2 retrieval from HARP and, another case with 60 viewing angles. Feel free to use any combination you prefer. Vanderlei
Lower right figure provided by Landon Rieger, permission obtained July 13, 2022. Permission email text is below:
Lidar image from https://www.researchgate.net/figure/The-CATS-1064-nm-attenuated-total-backscatter-ATB-a-volume-depolarization-ratio-b_fig1_351400300, with CC 4.0 license.
Hi Sheri and Scott,
Feel free to use that graphic wherever it's helpful, including posting it online. If you ever need a higher resolution or vector format just let me know too.
Best regards,
Landon

## Slide 10: AOS-Sky Radiometer Requirements
Microwave Radiometer: 89-700 GHz
Bands (# Channels) | Accuracy (K) | Polarization
89-113 GHz (1) 118 GHz (3) | ≤ 0.5 K ≤ 0.75 K | Target: Dual Minimum: Single
183.3 GHz (3) 165/205 GHz (1) | ≤0.75 K ≤0.75 K | Target: Dual Minimum: Single
310 GHz (3) 325.2 or 380.2 GHz (2) | ≤ 1.5 K ≤ 1.5 K | Target: Dual Minimum: Single
640-700 GHz (1) | ≤ 1.5 K | Dual
Cross-track scanning, ≥750 km swath
FOV ≤10 km at nadir, ≤20 km at edge of swath
Baseline Requirements
Courtesy of Matt McLinden
Courtesy of Yuli Liu, UMBC
Sub-mm wavelengths bring a cloud sensitivity that is new for NASA missions
Notes: Third party images:
Lower center image provided by Vanderlei Martins, permission obtained June 8, 2022. Email text below:
“Hi Scott, Yes, this is a multi-angle sequence from HARP showing 10 viewing angles. Since all other examples in your slide are for level 2, I am also attaching an example of level 2 retrieval from HARP and, another case with 60 viewing angles. Feel free to use any combination you prefer. Vanderlei
Lower right figure provided by Landon Rieger, permission obtained July 13, 2022. Permission email text is below:
Lidar image from https://www.researchgate.net/figure/The-CATS-1064-nm-attenuated-total-backscatter-ATB-a-volume-depolarization-ratio-b_fig1_351400300, with CC 4.0 license.
Hi Sheri and Scott,
Feel free to use that graphic wherever it's helpful, including posting it online. If you ever need a higher resolution or vector format just let me know too.
Best regards,
Landon

## Slide 11: AOS Polarimeter Requirements
Example AOD from HARP
Cloud-top properties available also
UV-VIS-NIR-SWIR Multi-angle Polarimeter
Type and/or Wavelength range (nm) | Number of spectral channels | Number of viewing angles per pixel
UV: 350 – 390 nm1 | 1 | 10
VIS: 410 – 750 nm | 2 | 10
Hyperangle: 660 – 870 nm | 1 | 60
Water Vapor: ~940nm | 1 | 10
SWIR Cirrus: ~1380 | 1 | 10
VNIR-SWIR: 870 – 1570 nm | 3 | 10
Baseline Requirements
300 km swath width
0.5 km IFOV (at nadir)
Notes: Third party images:
Left image provided by Vanderlei Martins, permission obtained June 8, 2022. Email text below:
“Hi Scott, Yes, this is a multi-angle sequence from HARP showing 10 viewing angles. Since all other examples in your slide are for level 2, I am also attaching an example of level 2 retrieval from HARP and, another case with 60 viewing angles. Feel free to use any combination you prefer. Vanderlei

## Slide 12: CSA Contributions
Canadian Space Agency Longwave-Far Infrared Imaging Radiometer (4-73 mm),
Aerosol/Moisture Limb Sounding
AOS-Storm [US led)
AOS-Sky [US led)
Notes: Lower right figure provided by Landon Rieger, permission obtained July 13, 2022. Permission email text is below:
Hi Sheri and Scott,
Feel free to use that graphic wherever it's helpful, including posting it online. If you ever need a higher resolution or vector format just let me know too.
Best regards,
Landon

## Slide 13: Summary of AOS Measurements & Timeline
AOS-Storm, JAXA PMM, and CNES C2OMODO:
Ku-Doppler radar
dTB/dt (~mm-wavelength)
Backscatter lidar
AOS-Sky, CSA HAWCsat:
Cloud-profiling Doppler radar
Backscatter lidar
sub-mm radiometer
Polarimeter
Longwave radiometer
Limb sounder (aerosol+moisture)
Inclined orbit (diurnal variations)
55° inclination
NLT March 2029
Polar orbit
Sun-synch
1330 LTAN
NET Dec 2031
2019
2031
2027
2023
CloudSat/CALIPSO
GPM
PMM
AOS-Sky + HAWCsat
INCUS
Polar
Inclined
CSA
JAXA
CNES
Possible extended mission
Possible extended mission
Possible extended mission
End of GPM station keeping fuel
AOS-Storm
Possible extended mission
Suborbital campaigns
after launches
Notes: Radiative forcing license info: https://creativecommons.org/licenses/by-sa/4.0/. No change made to figure. Source: https://archive.ipcc.ch/report/graphics/index.php?t=Assessment%20Reports&r=AR5%20-%20WG1&f=Chapter%2008