## Slide 1: Spatial Mode-Diversity Optical Receivers for Free-Space Optical and Quantum Communications
Brian Vyhnalek
NASA Glenn Research Center
November 13, 2023

## Slide 2: Overview
NASA communications and navigation systems in the Lunar and deep space environment envisioned for the future will need to accommodate human exploration, science experiments, human and robotic mobility operations, basecamp operations, and other missions in general requiring high data-volume transmissions
Optical communications can provide orders of magnitude system improvements vs. current RF systems
Need operational optical ground stations
  Low-cost, 1-meter class (20 – 70 cm) telescopes
  Efficient multi-spatial mode receivers
  Low-cost adaptive optics
NASA Laser Communications Relay Demonstration (LCRD)
NASA GSFC Low-cost optical terminal (LOCT)

## Slide 3: Efficient Multi-Spatial Mode Receivers - Photonic Lanterns
The laser transmitted from a spacecraft originates as a Gaussian shape (LP01)
Atmosphere distorts the beam profile and scatters energy into higher-order spatial modes
The number of fiber spatial modes coupled by a photonic lantern matches the sum of the modes supported by the output fibers

## Slide 4: Direct-Detection Photon-Counting Optical Receiver
NASA is using the CCSDS Optical Communications High Photon Efficiency (HPE) waveform on future missions: Optical Artemis-2 Orion (O2O), Psyche
  PPM: 4, 8, 16, 32, 64, 128, 256
  Slot widths: 512 ns - 125 ps
  Maximum data rate: ~2 Gbps
NASA Glenn is building a photon-counting ground receiver compliant with the CCSDS Optical Communications HPE standard
  PPM: 16, 32
  Slot widths: 2 ns, 1 ns, 0.5 ns
  Maximum data rate: 267 Mbps
Goals:
  Utilize commercial off the shelf (COTS) components where possible
  Demonstrate with O2O at the NASA Goddard Low-Cost Optical Terminal (LCOT) ground station

## Slide 5: Receiver Subsystems Under Development at NASA GRC
Fiber Interconnects:
Photonic lantern (one multimode fiber input to 7-FMF outputs) or FMF
Input fiber core size, number of outputs, and output fiber core size scalable to application
In house prototyping capability; development partnership with University of Sydney
Single Photon Detectors:
Superconducting nanowire single-photon detectors (SNSPDs)
Individual FMF-coupled detectors, or single 16-channel array
Continuous < 3 K operation, 60-80% detection efficiency, < 100 ps timing resolution
FPGA-based Receiver:
1 ADC per detector channel; digital detector channel combining
Real time processing; COTS development platform
Compatible with CCSDS downlink optical waveform (high photon efficiency)
FPGA VHDL/Verilog receiver code will be released

## Slide 6: Fiber-Detector Receiver Subsystem
Photonic Lantern:
FMFs:
  20 um graded-index core
  4LP, 6-mode
MMF input:
  55 um
  42 total modes
Fully packaged photonic lantern
Rack-mounted SNSPD cryogenic system
55 um
System Diagram

## Slide 7: FMF Coupling to Single-Element SNSPDs
 | LP01 | LP11 | LP21 | LP02
MFD (μm) | 10.30 | 14.67 | 18.43 | 18.86
Aeff (μm2) | 83.12 | 168.08 | 235.77 | 185.13
14 µm detector
Position (um)
Position (um)
Detector area ~ 14 x 14 um^2 (196 um^2)
Graded-index 20- μm FMF can couple to ≈ 14x14 μm2 SNSPDs with minimal fiber/chip coupling loss. Compared with SMF the additional modes represent a gain of ≈ 4 dB

## Slide 8: FMF + 16-Channel SNSPD Array
*Rambo, T. M., Conover, A. R., and Miller, A. J., “16-element superconducting nanowire single-photon detector for gigahertz counting at 1550-nm," (2021). https://arxiv.org/abs/2103.14086
Detector array layout*
FMF on alignment stage
Rack-mounted SNSPD cryogenic system
FMF #2 (20 m system input):
25 um graded-index core
6 LP, 10-modes
FMF #1 (coupled to SNSPD array):
20 um graded-index core
4 LP, 6-modes
System Diagram

## Slide 9: Test Setup With Arbitrary Light Field Generator (ALF-G)
Simulated 2D beam profiles (phase and intensity) are recreated in the lab by modulating the beam via a complex amplitude phase hologram written to the SLM.
Vary numerical aperture with L3 to measure light distribution on detectors
42 modes/7 detectors
10 modes/16 detectors

## Slide 10: Fiber-Detector Subsystem Loss Comparison
Combined coupling loss, blocking loss, and input distribution effects over a range of input power
FMF/SNSPD array system has more loss at lower received power and higher D/r0 due to coupling
Photonic lantern/single SNSPDs system has more loss at higher input powers due to detector count rate limitations/blocking loss
There is a cross-over input power where relative coupling loss balances detector blocking losses

## Slide 11: CWER Results – PPM-16, Code Rate 1/2, 200 Mbps
Detector Jitter & FPGA Implementation Loss (dB) |  | Fiber & Detector Loss (dB) |  | Measured Kb at 10-5 CWER (dB photons/slot) |  | Required Input Power at 10-5 CWER (dBm) | 
PL | A | PL | A | PL | A | PL | A
0.3 | 1.2 | 9.6 | 3.5 | -24.7 | -20.8 | -68.7 | -73.5
Receiver
Test transmitter
SNSPDs

## Slide 12: Receiver will be demonstrated at the NASA GSFC Low Cost Optical Terminal*

## Slide 13: Multi-Gbps Spatial Mode-Diversity Coherent Optical Receivers
Photonic lantern can provide spatial diversity similar to a multi-aperture array, but with considerable savings in SWaP and cost
A silicon photonic integrated circuit (PIC), can couple to the photonic lantern and incorporate on-chip demodulators and high bandwidth photodetectors (10s of GHz)
  Serves as the optical front-end outputting electrical signals for further processing.
  Accommodate many 10s of channels
  Wide variety of other functions such as narrowband filtering, and wavelength multiplexing.
  Can support coherent optical modulations – DPSK, QPSK, dual-polarization, QAM, etc.
Possible to do active signal combining on-chip to reduce output channels to one SMF for processing – currently under investigation
Optical front end can be realized on a single PIC chip –
or in combination with optical pre-amp stage
Multi-aperture array
Single-aperture with photonic lantern

## Slide 14: Photonic Lantern Coherent Combining at NASA GSFC*
10 Gbps DP-QPSK transmit signal from CFP2 module
Variable optical attenuator and atmospheric distortion emulator
Four separate integrated coherent receivers (ICR)
DFB local oscillator shared between integrated receivers
High sample rate digitizing oscilloscopes collect X/Y-pol I and Q signals for post processing
Experiments repeated at powers between -3 and -33 dBm
COTS Integrated coherent receiver (ICR) module stack
Photonic lantern
Distortion element
Coherent combining test setup
Multiple sampling oscilloscopes for data collection
*Yevick, A., Lafon, R., Bayne, R., Garcia, R., Grigoryan, V.S., and J. Veselka,
“Experimental demonstration of coherent receiver with photonic lantern and digital signal processing”

## Slide 15: GSFC - Recent Coherent Combining Results*
Digital-domain coherent combining
  Optical carrier frequency recovery and equalization
  Optical carrier phase recovery and equalization
  Signal clock recovery
  Signal polarization tracking and polarization demultiplexing
  Time misalignment equalization between PL output legs
  Optimal digital coherent combining of signals from PL output legs to maximize signal SNR
SNR improvement due to optimum coherent combining increases as SNR for best individual leg decreases: SNR improvement reaches ≈ 4dB at Pch = -34dBm
Theoretical maximum ≈ 4.77 dB
Power monitoring each signal will maximize SNR improvement
*Yevick, A., Lafon, R., Bayne, R., Garcia, R., Grigoryan, V.S., and J. Veselka,
“Experimental demonstration of coherent receiver with photonic lantern and digital signal processing”

## Slide 16: Photonic Lantern Wavefront Sensing
Photonic lanterns can efficiently couple to single mode fiber (needed for coupling to coherent comm. detectors)
Intensities and phases of the SM outputs have a direct relationship to both phase and amplitude information of the incident wavefront
Replace the wavefront sensor (WFS) – expensive part of adaptive optics (AO) systems
If combined with a photonic integrated circuit, could serve as both light delivery and adaptive optics system through optical coherent combining to greatly reduce size, weight, power, and complexity
Increase optical ground station scalability
Intensity
Phase
1
2
3
4
5
6
7
1x7 SMF photonic lantern input/output measured with wavefront sensor
Light from space

## Slide 17: Towards Satellite-Based Quantum Networks
Quantum entanglement distribution over long distances
  Quantum key distribution (QKD)
  Teleportation / entanglement swapping
  Distributed quantum computing
NASA GRC has established the NASA Quantum Metrology Laboratory (NQML):
  Compactified metrology builds: Reduction in system footprints, complexities, and photon losses
  Environmental emulation: Measurement of space-based environmental impacts on quantum processes.
  Verification and validation: Entanglement swapping link analysis (among many other link assessment capabilities)
  Standards for space-based assets: Establishment of definitions consistent with the overall research community
Analysis and testing of quantum communications protocols
Currently investigating use of photonic lanterns, multi-plane light conversion (MPLC) for transmit and receive systems

## Slide 18: Integrated Quantum Technologies Under Development
Micro-ring resonator SFWM entanglement source
Integrated photonic chips on probe station
Waveguide SPDC source
Sources
MgO-doped LiNbO3 spontaneous parametric down-conversion (SPDC) waveguide sources
Silicon photonic spontaneous four-wave mixing (SFWM) bi-photon sources nominally in the 1530-1570 nm wavelength range; also 775 nm, 794 nm, etc.
Thin-film lithium niobate (TFLN) SPDC sources (SBIR/STTR)
Analysis
Bell state analyzer (BSA) with Franson-type interferometry capability for highly-nondegenerate sources, i.e. 1588/794 nm, 1550/775 nm, etc.
Two-photon interference for BSA and entanglement swapping, or thermal source interference
Integrated tunable, high-Q resonant filters
Tunable phase shifters
Detectors
Waveguide integrated SNSPDs
Waveguide integrated SNSPDs

## Slide 19: Summary
We have developed 1x7 MMF – FMF photonic lantern coupled to superconducting nanowire single photon detectors (SNSPDs) for a spatial-mode diversity photon-counting optical receiver – will demonstrate with the GSFC 70-cm low-cost optical receiver (LCOT)
With optimal coupling, the receiver concept based on a FMF photonic lantern with 7 single-element SNSPDs has lower total losses - data rate and input power dependent, due to detector blocking
Currently investigating applications to coherent optical communications – multiple parallel channels digitally combined
Photonic lanterns can be used for wavefront sensing – can potentially reduce cost and requirements for adaptive optics
Currently investigating use of photonic lanterns, multi-plane light conversion (MPLC) for quantum communications transmit and receive systems
Developing photonic circuit packages for integrated receiver systems

## Slide 20: Acknowledgements:
NASA GRC: Sarah Tedder, Jennifer Downey, Bertram Floyd, and Yousef Chahine
NASA GSFC: Aaron Yevick, Robert Lafon, Vladimir Grigoryan, and John Veselka
NASA GRC Communications and Intelligent Systems Division
NASA Space Communications and Navigation (SCaN) Program