## Slide 1: Inside the Fire: Simulating Combustion of Oxygen-Methane Fuel for Spacecraft Applications
Brian R. Richardson
2023 Supercomputing Conference
Denver, CO
Nov. 13-17, 2023

## Slide 2: Introduction to the Fluid Analysis Branch / ER42
Approximately 50 NASA Civil Servants and Support Contractors at MSFC
  Computational Fluid Dynamics (CFD) Team
  Unsteady Fluid Environments (UFE) Team
Our Work is Propulsion-Focused Direct Program Support
  Liquid Rocket Engines: SLS, RS-25, RL-10, Human Lander System, Commercial Crew Program
  Solid Motors: SLS Solid Rocket Motors, Peregrine, Mars Ascent Vehicle
  Space Nuclear Propulsion Program: DRACO
  Team Products: Propulsion hardware design support, pre-test predictions, fluid-induced loads and environments
CFD Team Uses Multiple Loci-based CFD Tools
  Loci/CHEM, Loci-STREAM, Loci/Boltzmann (Rarified Gas Dynamics), Loci/GGFS (Gas-Granular Flow)
  Loci framework allows for streamlined development of specialized modules in the CFD codes
MSFC CFD Team Utilizes NASA Supercomputing Resources at NASA Ames
  Pleiades, Aitken and Electra Supercomputers
  CFD Team utilizes >200 Million CPU hours per year

## Slide 3: Propulsion Elements and ER42 CFD Analysis Capabilities
SLS Exploration Upper Stage
Propellant Settling in Microgravity
Credit: Jacob Brodnick/ER42
Propellant Slug Through Feedline
Credit: Jeff West/ER42
Oxygen/Methane Linear Combustor
Supersonic Turbine Flow
Credit: Matthew Fischels/ER42
Focus of this presentation is combustion modeling using CFD tools.

## Slide 4: Propelling the New Generation of Manned Spaceflight
Why use CFD to model Oxygen-Methane combustion applications at NASA?
Liquid Oxygen (LOX) and Methane (CH4) propellant fueled engines have been considered for In-Space Propulsion and a number of developing programs
  Mars Lander concepts, Potential RL-10 replacement, SpaceX Raptor
Methane offers several advantages over fuels traditionally used by NASA and others in the space flight industry
  Denser than Hydrogen, More energy per volume than H2; Less corrosive than Hydrazine
Methane Ignition presents unique and difficult challenges and is a significant risk for In-Space Ignition
  Ignition of Hydrocarbon fuels is complex and stable combustion has been historically difficult for engine design
    RL-10 was a H2/O2 Engine and presented significant ignition challenges at altitude, Methane would present additional challenges
  Methane stored as a cryogenic liquid like H2, experiences phase changes at ambient temperatures and pressures unlike some other hydrocarbons, and requires a separate oxidizer unlike monopropellants
Shallow base of design experience in Space Flight propulsion applications
  Empirical test-based experience focused on hydrogen, RP and hypergolic fuels
NASA Morpheus Lander Test

## Slide 5: It’s Only Rocket Science
Multiple choices for in-space propulsion system design
Cryogenic liquid propulsion systems basic elements
  Turbine drives pumps
  Pumps move propellants from tanks into feedlines at high pressure
  Injectors direct propellants into combustion chamber
  Combustion provides additional energy
  Nozzle expands and accelerates gases, propelling spacecraft
  Heat from the combustion chamber and nozzle drives the turbines
Our focus here is using CFD to model the combustion inside the Main Combustion Chamber to provide critical engineering metrics
  Reliable Ignition – Difficult for In-Space environments
  Stable Combustion – Injector design is critical
  Sufficient Heat Transfer – Required to drive the turbine
Example Engine Diagram

## Slide 6: Computational Challenges of Combustion Modeling
Why use CFD to model combustion?
  CFD-guided design can be cheaper and safer than an empirically-guided test development program
Why is combustion modeling considered to be computationally expensive?
  Non-reacting CFD simulations have a significant set of base equations
    Numerical methods used to solve 5 base PDEs that comprise the Navier-Stokes equations, plus turbulence closure equations and a species balance equation for multi-species
  Finite-rate chemistry modeling of combustion adds additional equations
    1 additional scalar equation for each additional species is added to the computation, practical chemistry models have 10-100+ species
  Finite-rate models march slowly in physical time
    Simulations typically require small time step sizes to be numerically stable
Flamelet Models provide an efficiency gain for combustion CFD simulations
  Chemical reactions are computed for a fuel and oxidizer combination and tabulated prior to the CFD simulation
  Combustion modeling in the CFD simulation achieved using just 2 new PDEs
  Modest efficiency gain in time-step size
Ultimately, complexity, resolution and completion time of the CFD simulations is limited by computational resource availability
  ER42 uses the NAS HPC resources at NASA Ames: Pleiades, Electra and Aitken Supercomputing Clusters

## Slide 7: Progression of CPU Resources and Combustion Modeling in ER42 Through the Years
2008 - Columbia Supercomputer ~0.062 Pflops/s:
2D, steady-state CFD simulations using a finite-rate chemistry model
2013 - Pleiades Supercomputer Online +7.09 Pflops/s:
3D, Time-accurate CFD simulations of a single injector element using a flamelet-based combustion model, ~60 Million volume cells in CFD mesh
2017 - Electra Supercomputer Online +8.32 Pflops/s:
3D, Time-accurate CFD simulations of O(10) injector elements using a flamelet-based combustion model ~140 Million cells in CFD mesh
Temperature Contours through Chamber Centerline Plane

## Slide 8: Engineering Utilization of CFD Results on HPC Resources
Impact of Growing Computational Resources on CFD Simulation Fidelity
  Effectively Utilize Complex Chemistry Mechanisms – Increases the accuracy of CFD simulations
  Allows CFD Models to Include Complex Geometry and Finer Meshes – Improved spatial representation of the application in the CFD simulation
  Improves Simulation Turn-around Time – Easier to engage with customers and provide actionable results
Introduction to three modern combustion CFD simulations conducted to support In-Space propulsion development projects
Ignition modeling of gaseous oxygen and methane flow inside a linear array chamber using LOCI\Chem
  Project goal was to study to onset of transverse combustion instabilities
  Finite-rate chemistry model with 12 species and 20 chemical reactions used to provide accurate flame speed propagation through the chamber
Mainstage combustion modeling of liquid oxygen and methane flow in an engine design concept using shear flow injector elements
  Project goal was to extract heat flux distribution to chamber walls for a range of conditions to ensure that enough heat was extracted from the chamber walls to drive the turbine
  Flamelet model utilized to enable efficient use of a large mesh and complex geometry
Mainstage combustion modeling of liquid oxygen and methane flow in an engine design concept using impinging flow injector elements
  Project goal here was to quantify the heat release distribution in the primary combustion zone to quantify potential combustion instability modes
  Flamelet model utilized to enable efficient use of a large mesh and complex geometry: Largest combustion CFD simulation completed by ER42 to date, >100 Injector Elements and 600+ Million Volume Cells

## Slide 9: Animation of Ignition and Flame Spreading in Linear Array Chamber
CFD Temperature Contours
Test Video Schlieren - Density Contours
Comparison between CFD simulation and video recorded through optical window is test show similar physical behavior
Reacting Flow Simulation produced physically realistic results, required ~3 weeks of run time on 3000 CPUs
Visible in CFD and Test Results
1) Pressure wave leads high temperature and perturbs GOX jets
2) Flame front contains eddys and is clearly subsonic
3) Transverse oscillation occurs in chamber during ignition transient
Animation of Temperature Contours from LOCI\Chem CFD

## Slide 10: Liquid Oxygen and Methane Combustion Inside Concept Engine Chamber
Blue Iso-surface shows where flame rapidly transitions from majority unburned O2 and CH4 propellant to majority combustion products such as CO2, CO and H2O
The green-yellow wall surface plot shows contours of heat flux into the chamber wall. The hardware designed to have higher heat flux at the aft end (right side) of the chamber which is uncommon in most chamber design concepts. Traditional, empirically derived design tools are not capable of accurately predicting this type of axial heat flux distribution down the chamber wall. The CFD-predicted wall heat flux was used to develop the turbine power cycle. Note: The sudden wall heat flux change halfway through the animation was part of a parametric study to help thermal analysts understand model changes due to fluctuating temperate at the solid walls.

## Slide 11: Liquid Oxygen and Methane Combustion Inside Chamber with Impinging Injectors
Blue Iso-surface shows where flame rapidly transitions from majority unburned O2 and CH4 propellant to majority combustion products such as CO2, CO and H2O
Cross-section shows temperature contours. Combustion gas temperature rapidly increases just downstream of blue iso-surface, vigorous combustion zone.
The green-yellow wall surface plot shows contours of heat flux into the chamber wall.
The impinging injector elements force rapid combustion of the propellants as indicated by the relatively short persistence of the blue iso-surface down the chamber. Peak combustion heat release occurs at a location just downstream of the iso-surface. Since the gases in the chamber are moving, this location has a time associated which is called sensible time lag. Sensible time lag is used in combustion stability calculations to predict frequencies and mode shapes of combustion instability events. CFD was able to provide this time lag parameter which is not well quantified in traditional combustion stability analysis methods for this injector type.

## Slide 12: Next Steps in ER42 CFD Combustion Modeling
CFD Model Fidelity Improvements
  Equation of State robustness improvements – Enable robust simulations of two liquid propellants at sub-critical conditions such as engine start
  Hypergolic Flamelet Model – Enable modeling combustion of two liquid hypergolic propellants which spontaneously ignite on contact
Harnessing Additional Computational Resources
  Enable finer mesh CFD models to improve model spatial accuracy and better simulation temporal resolution while maintain impactful analysis completion times
  Include additional engine geometry such as propellant manifolds – Critical for a CFD-only prediction of combustion instability events