## Slide 1: High Reliability at Minimum Cost
Harry W. Jones, Ph.D., MBA
Nasa Ames Research Center

## Slide 2: Overview
This paper investigates the minimum cost of improving the reliability of complex technical systems.
The two major methods to improve reliability are
  designing the system for high reliability and
  providing redundant components to replace failed elements.
The costs of design for reliability and adding redundancy are estimated.
The most cost-effective combination for high reliability is identified.

## Slide 3: The cost of improving reliability
Designing a system for higher reliability is usually considered very difficult.
  The first steps are sometimes surprisingly easy.
If reliability was not considered in the initial design,
  simply selecting more reliable components,
  derating to reduce stresses, and
  limiting the operational envelope can greatly improve reliability.
On the other hand, common systems such as automobiles and computers, have had their reliability greatly improved by intense continued effort.
  Further improvements are very difficult.
Improving reliability has increasing costs and diminishing returns.

## Slide 4: We need a mathematical formula for the cost of higher reliability
The formula should reflect several basic constraints.
  The cost of more reliability should always be greater than zero.
  The cost for higher reliability increases with higher reliability.
  The cost of reliability equal to one should be infinite.
The engineering facts are;
  no free lunch,
  diminishing returns, and
  sooner or later, everything fails.

## Slide 5: Several different mathematical rules have been proposed for the cost of improving reliability
If the original cost is C0, for the original failure rate, F0, the cost for failure rate F is:
  Log cost C(F) = C0 [1 + log2 (F0/F)]
  Proportional cost C(F) = C0 (F0/F)a, for a = 0.25 or 1
  Exponential cost C(F) = C(0) exp [(F0 - F)/F]
The log2 (1/F) and exp (1/F) can be approximated by (1/F)a for different “a” exponents.
  Cost of failure rate F is C(F) = C0 (F0/F)a

## Slide 6: The proportional function cost of reliability covers all the expected cases by varying “a”
Cost of failure rate F is C0 (F0/F)a
The slowest cost increase is for (1/F)0.25
The next slowest for 1 + log2 (1/F), which can be approximated by 1.59 (1/F)0.35
The third slowest increase is for (1/F)1
The fastest is for exp [(F0-F)/F], which can be approximated by 0.68 (1/F) 2.35
Chart: Different cost curves for reduced failure rate
| 1 | 0.9 | 0.8 | 0.70000000000000007 | 0.60000000000000009 | 0.55000000000000004 | 0.5 | 0.45 | 0.4 | 0.35000000000000003 | 0.30000000000000004 | 0.25000000000000006 | 0.20000000000000007 | 0.15000000000000008 | 0.10000000000000007 | 9.000000000000008E-2 | 8.0000000000000085E-2 | 7.000000000000009E-2 | 6.0000000000000088E-2 | 5.0000000000000086E-2 | 4.0000000000000084E-2 | 3.0000000000000082E-2 | 2.000000000000008E-2 | 1.000000000000008E-2 | 5.0000000000000001E-3 | 1E-3
(F0/F)^0.25 | 1 | 1.0267 | 1.0574 | 1.0933 | 1.1362 | 1.1612 | 1.1892 | 1.2209 | 1.2574 | 1.3001 | 1.3512 | 1.4142 | 1.4953 | 1.6069 | 1.7783 | 1.8257 | 1.8803 | 1.9441 | 2.0205 | 2.1147 | 2.2361 | 2.4028 | 2.6591 | 3.1623 | 3.7606 | 5.6234
1+log2 (F0/F) | 1 | 1.152 | 1.3219 | 1.5146 | 1.737 | 1.8625 | 2 | 2.152 | 2.3219 | 2.5146 | 2.737 | 3 | 3.3219 | 3.737 | 4.3219 | 4.4739 | 4.6439 | 4.8365 | 5.0589 | 5.3219 | 5.6439 | 6.0589 | 6.6439 | 7.6439 | 8.6439 | 10.9658
(F0/F)^1 | 1 | 1.1111 | 1.25 | 1.4286 | 1.6667 | 1.8182 | 2 | 2.2222 | 2.5 | 2.8571 | 3.3333 | 4 | 5 | 6.6667 | 10 | 11.1111 | 12.5 | 14.2857 | 16.6667 | 20 | 25 | 33.3333 | 50 | 100 | 200
exp [(F0-F)/F] | 1 | 1.1175 | 1.284 | 1.5351 | 1.9477 | 2.2664 | 2.7183 | 3.3947 | 4.4817 | 6.4054 | 10.3123 | 20.0855 | 54.5982

## Slide 7: The cost of redundancy
The failure rate for N parallel redundant units is (system failure rate)N
The cost of redundancy is N times the system cost.
  The total redundant system cost is proportional to N/(system failure rate)a
  [Since each redundant system has cost proportional to 1/(system failure rate)a ]
The cost of redundancy increases as N gets larger, but a larger N allows a higher system failure rate, which reduces system design cost.
  There is a certain N, a certain level of redundancy, that has the minimum cost to achieve the required overall redundant system failure rate.

## Slide 8: The minimum cost for the redundant system is achieved at the optimum level of redundancy
The N for minimum cost is equal to -a ln (redundant system failure rate).
The minimum cost of the N redundant systems is proportional to N * (original system failure rate)a.
  The higher the original system failure rate, the higher the minimum cost for the desired redundant reliability.
The optimum redesigned individual system failure rate is proportional to exp (-1/a).
  The greater the difficulty, the higher the optimum individual system failure rate.

## Slide 9: Summary – high reliability at minimum cost
The cost to reduce a system failure rate from F0 to F is (F0/F)a, where
  F0 is the original system failure rate, and
  “a” from 0.25 to 2.50 reflects the degree of difficulty.
The number N of redundant systems is needed to achieve the required overall failure rate, FN.
  The minimum cost of the N redundant systems is proportional to N * (original system failure rate)a.
Increasing the intrinsic reliability of a system has diminishing returns.
  Ultimately it becomes more cost-effective to add redundancy.