## Slide 1: Redundancy: How Many Unreliable Spares are Needed for High Reliability and Confidence?
Harry W. Jones, Ph.D., MBA,
NASA Ames Research Center

## Slide 2: How many redundant units are needed to achieve high reliability with high confidence?
Suppose the failure probability is too high for a single unit to provide the required reliability.
To achieve the required higher reliability, N redundant units are used.
  The needed redundancy, N, can be computed using the failure probability .
  The failure rate has measurement uncertainty.
  If the failure rate is higher than measured, the computed number N of spares is too few for the expected reliability.
The confidence that a certain reliability is achieved can be computed using the cumulative Poisson distribution or the chi-square distribution.
  The reliability and confidence can be traded off.
  Lower reliability goals are met with higher confidence.
Both the desired reliability and the confidence can be set as requirements.
  This determines N, the needed number of redundant units.

## Slide 3: Optimum test time for minimum total cost
System integration and test produces a record of the failure times.
  This record determines the measured failure rate and its distribution.
  The failure rate confidence intervals can be estimated.
Further testing will more accurately determine the failure rate.
  This reduces the variance of the failure rate and the width of the confidence intervals.
Narrowing the confidence interval reduces the number of redundant units needed for the required confidence.
  This reduces the system implementation cost.
  However, the additional test time increases cost.
The total cost is the sum of the costs of the redundant units and of the extended test program.
  There is an optimum test time for the minimum total cost.

## Slide 4: Approach to determine N for the required reliability and confidence.
Determine the required reliability, say reliability = 0.9.
  The failure probability can be estimated from the measured failure rate and operational time.
This failure probability determines the number N of redundant units needed to achieve the required reliability.
  But this required reliability is achieved with only about 50% confidence.
The confidence that reliability = 0.9 can be increased by increasing N, the number of redundant units.
  This is done by increasing the failure rate used to determine N so that confidence reaches its requirement, say confidence = 0.9.

## Slide 5: Failure data, number of redundant units N, and costs for the 41-failure data set.
n - the failure count
t - the failure times
l(t) - the decreasing failure rate
l0.9(t) - the increased failure rate for confidence = 0.9
N - the required number of units for reliability = 0.9 and confidence = 0.9
Test cost - 1 unit cost + test time
Total cost = N + 1 + 0.015 * test time
Minimum cost = 6.4 at t = 27.4.
n | Time t | l(t) | l0.9(t) | Units N | Test cost | Total cost
7 | 1.9 | 3.7 | 6.2 |  |  | 
8 | 3.1 | 2.6 | 4.2 | 13.0 | 1.0 | 14.0
9 | 4.3 | 2.1 | 3.3 | 11.0 | 1.1 | 12.1
10 | 5.5 | 1.8 | 2.8 | 10.0 | 1.1 | 11.1
11 | 6.8 | 1.6 | 2.5 | 9.0 | 1.1 | 10.1
12 | 8.0 | 1.5 | 2.2 | 8.0 | 1.1 | 9.1
14 | 10.4 | 1.3 | 1.9 | 7.0 | 1.2 | 8.2
19 | 16.5 | 1.2 | 1.6 | 6.0 | 1.2 | 7.2
23 | 21.4 | 1.1 | 1.4 | 6.0 | 1.3 | 7.3
27 | 26.2 | 1.0 | 1.3 | 6.0 | 1.4 | 7.4
28 | 27.4 | 1.0 | 1.3 | 5.0 | 1.4 | 6.4
31 | 31.1 | 1.0 | 1.3 | 5.0 | 1.5 | 6.5
35 | 35.9 | 1.0 | 1.2 | 5.0 | 1.5 | 6.5
40 | 42.0 | 1.0 | 1.2 | 5.0 | 1.6 | 6.6
41 | 49.2 | 0.8 | 1.0 | 5.0 | 1.7 | 6.7

## Slide 6: Upper confidence bounds
If the measured failure rate is used to determine the number of spares, there is only a 50% confidence that the number of spares is not too low.
  If a higher, say a 90%, confidence is needed that there are sufficient spares, this can be achieved by using an increased failure rate l(t) that would produce fewer than the measured number of failures only 10% of the time.
Instead of using the measured failure rate to determine the number of spares, the 90% upper confidence bound on l(t), l0.9(t), is used.
  If this is done, there is a 90% confidence that l0.9(t) is not lower than the actual failure rate and the number of spares is not too low for 90% confidence in the predicted reliability.
l0.9(t) is the 90% upper confidence bound on l(t).
  The upper confidence bounds on l(t) can be determined using either the Poisson distribution or the chi-square distribution, which are included in available spreadsheets.

## Slide 7: The increased number of redundant units N
For high reliability, the number of spares provided must be greater than the expected number of failures.
The needed number of redundant units, N, can be determined from tables of the cumulative Poisson distribution.
  The upper 0.9 probability confidence bound, l0.9(t), is set as the expected failure rate.
  The corresponding number of failures for a single unit over the mission length L is lx(t) * L.
  This is the expected number of failures for the required confidence bound.
The required number of redundant units was computed for confidence = 0.9 and reliability = 0.9.

## Slide 8: Minimizing the total system development cost
The cost is equal to the cost of developing N redundant operational units and M test units plus the estimated cost of testing the M test units.
  The cost metric is the cost of producing a single unit.
  The cost of N units is N.
  Suppose the cost of testing is 0.015 of the unit development cost per hour.
  Total cost = N + M + 0.015 M t
The increasing test time reduces the upper confidence bound on the system failure probability, l0.9(t), so the the number of redundant units N decreases with longer test time.
  The minimum total cost is 6.4 units first reached at = 27.4 hours.
  However, a cost of 7.2 is reached at 16.5 hours.
  The test time can be cut 40% with only a 13% increase in cost.

## Slide 9: The trade-off between confidence and reliability
For any redundancy, N,
  a higher reliability will be met with lower confidence, and
  a higher confidence can be achieved only at lower reliability.
At the design point both reliability and confidence are equal to 0.90.
  Increasing the reliability requirement above 0.90 to causes the confidence that the requirement will be met to drop rapidly toward zero.
  Reducing the reliability requirement increases the confidence it will be met from one 9 to two, three, and even four 9’s.
Chart: Confidence versus Reliability
| 0.94 | 0.93 | 0.92 | 0.91 | 0.9 | 0.85 | 0.8 | 0.7 | 0.6
 | 0.08 | 0.51 | 0.73 | 0.84 | 0.9 | 0.9855 | 0.9966 | 0.9996 | 0.9999

## Slide 10: The increase in required N as reliability and confidence requirements increase
Suppose that reliability and confidence have equal requirements, but the requirement is other than 0.90.
As the requirement for the reliability = confidence increases from 0.50 to 0.995, the required number of redundant systems N increases from 5 to 12.
Chart: N versus Reliability = Confidence
| 0.995 | 0.99 | 0.98 | 0.95 | 0.93 | 0.91 | 0.9 | 0.85 | 0.8 | 0.7 | 0.6 | 0.5
 | 11.84 | 10.7 | 9.57 | 8.1 | 7.57 | 7.36 | 7.01 | 6.37 | 5.93 | 5.31 | 4.87 | 4.53

## Slide 11: Conclusion
A procedure was developed to compute N, the number of redundant units needed to achieve any required reliability at any confidence level.
  N depends on the measured system failure rate, l(t), the mission length, L, the required reliability, and the required confidence in that reliability.
It is possible to set the requirements for both the redundant reliability and the confidence level and then test until the time needed to minimize the total cost required to achieve these requirements.
  The total mission cost is the sum of the redundant units cost and the test time cost.
Initial testing produces reliability growth, which often has a major impact in reducing the unit failure rate.
Testing to better determine the long-term failure rate reduces the confidence interval of the failure rate, which seems to have a smaller effect in reducing cost.
  Longer testing is justified as long as total cost is decreasing.
If the testing is terminated before the minimum cost time, a greater number of redundant units must be provided to achieve the required reliability and confidence.