## Slide 1: The abcd Reliability Growth Model
Harry W. Jones, Ph.D., MBA,
NASA Ames Research Center

## Slide 2: Overview - the Duane and abcd Models
The Duane reliability growth model is failure rate = n(t)/t = k t-a.
  k is a constant. The reliability growth rate is a.
  The model implies the failure rate can decrease forever but instead it usually reaches a constant low value.
The abcd model adds a second time period with a constant failure rate.
  n(t)/t = a t-b + c from t = 0 to td
  = c + d after td, where d = a td-b
Notes: The term a t-b describes the initial reliability growth period that continues out to time td and c is the constant long term failure rate. The parameter d represents an additional constant failure rate due to remaining correctable but accepted failure modes. After the reliability growth process is terminated, the failure rate n(t)/t = c + d.

## Slide 3: The Crow data set in two plots
Crow used a 56-failure data set to study reliability growth.
  The fitted straight line in the log-log plot corresponds to n(t)/t = 0.640 t-0.283.
The linear plot shows reliability growth followed by a constant failure rate, c = 0.14.
Chart: Cumulative failure rate, log-log plot
| 0.7 | 3.7 | 13.2 | 15 | 17.600000000000001 | 25.3 | 47.5 | 54 | 54.5 | 56.4 | 63.6 | 72.2 | 99.2 | 99.6 | 100.3 | 102.5 | 112 | 112.2 | 120.9 | 121.9 | 125.5 | 133.4 | 151 | 163 | 164.7 | 174.5 | 177.4 | 191.6 | 192.7 | 213 | 244.8 | 249 | 250.8 | 260.10000000000002 | 263.5 | 273.10000000000002 | 274.7 | 282.8 | 285 | 304 | 315.39999999999998 | 317.10000000000002 | 320.60000000000002 | 324.5 | 324.89999999999998 | 342 | 350.2 | 355.2 | 364.6 | 364.9 | 366.3 | 373 | 379.4 | 389 | 394.9 | 395.2
Data | 1.4286 | 0.54054 | 0.22727 | 0.26667 | 0.28409 | 0.23715 | 0.14737 | 0.14815 | 0.16514 | 0.1773 | 0.17296 | 0.1662 | 0.13105 | 0.14056 | 0.14955 | 0.1561 | 0.15179 | 0.16043 | 0.15715 | 0.16407 | 0.16733 | 0.16492 | 0.15232 | 0.14724 | 0.15179 | 0.149 | 0.1522 | 0.14614 | 0.15049 | 0.14085 | 0.12663 | 0.12851 | 0.13158 | 0.13072 | 0.13283 | 0.13182 | 0.13469 | 0.13437 | 0.13684 | 0.13158 | 0.12999 | 0.13245 | 0.13412 | 0.13559 | 0.1385 | 0.1345 | 0.13421 | 0.13514 | 0.13439 | 0.13702 | 0.13923 | 0.13941 | 0.13969 | 0.13882 | 0.13928 | 0.1417
Duane line fit | 1.2274 | 0.70806 | 0.11808 | 0.090827
Chart: Cumulative failure rate
| 0.7 | 3.7 | 13.2 | 15 | 17.600000000000001 | 25.3 | 47.5 | 54 | 54.5 | 56.4 | 63.6 | 72.2 | 99.2 | 99.6 | 100.3 | 102.5 | 112 | 112.2 | 120.9 | 121.9 | 125.5 | 133.4 | 151 | 163 | 164.7 | 174.5 | 177.4 | 191.6 | 192.7 | 213 | 244.8 | 249 | 250.8 | 260.10000000000002 | 263.5 | 273.10000000000002 | 274.7 | 282.8 | 285 | 304 | 315.39999999999998 | 317.10000000000002 | 320.60000000000002 | 324.5 | 324.89999999999998 | 342 | 350.2 | 355.2 | 364.6 | 364.9 | 366.3 | 373 | 379.4 | 389 | 394.9 | 395.2
Cumulative failure rate | 1.4286 | 0.54054 | 0.22727 | 0.26667 | 0.28409 | 0.23715 | 0.14737 | 0.14815 | 0.16514 | 0.1773 | 0.17296 | 0.1662 | 0.13105 | 0.14056 | 0.14955 | 0.1561 | 0.15179 | 0.16043 | 0.15715 | 0.16407 | 0.16733 | 0.16492 | 0.15232 | 0.14724 | 0.15179 | 0.149 | 0.1522 | 0.14614 | 0.15049 | 0.14085 | 0.12663 | 0.12851 | 0.13158 | 0.13072 | 0.13283 | 0.13182 | 0.13469 | 0.13437 | 0.13684 | 0.13158 | 0.12999 | 0.13245 | 0.13412 | 0.13559 | 0.1385 | 0.1345 | 0.13421 | 0.13514 | 0.13439 | 0.13702 | 0.13923 | 0.13941 | 0.13969 | 0.13882 | 0.13928 | 0.1417

## Slide 4: The Crow Failure Rate Data and the abcd Model
The constant c = 0.14 was subtracted from the Crow data and an exponential curve fit for t = 0 to t d =100.
The abcd model is
  n(t)/t = 1.37 t-0.99 + 0.14 from t = 0 to td = 100
  n(t)/t = 0.14 + 0.01 = 0.15 after td = 100
Chart: Crow failure rate data and partial abcd model
| 0.7 | 3.7 | 13.2 | 15 | 17.600000000000001 | 25.3 | 47.5 | 54 | 54.5 | 56.4 | 63.6 | 72.2 | 99.2 | 99.6 | 100.3 | 102.5 | 112 | 112.2 | 120.9 | 121.9 | 125.5 | 133.4 | 151 | 163 | 164.7 | 174.5 | 177.4 | 191.6 | 192.7 | 213 | 244.8 | 249 | 250.8 | 260.10000000000002 | 263.5 | 273.10000000000002 | 274.7 | 282.8 | 285 | 304 | 315.39999999999998 | 317.10000000000002 | 320.60000000000002 | 324.5 | 324.89999999999998 | 342 | 350.2 | 355.2 | 364.6 | 364.9 | 366.3 | 373 | 379.4 | 389 | 394.9 | 395.2
n(t)/t - 0.14 | 1.2936 | 0.40554 | 0.092273 | 0.13167 | 0.14909 | 0.10215 | 0.012368 | 0.013148 | 0.030138 | 0.042305 | 0.037956 | 0.031205 | 0.0055622 | 0.014551 | 0.021098 | 0.016786 | 0.025428 | 0.022155 | 0.029069 | 0.032331 | 0.029918 | 0.017318 | 0.012239 | 0.016791 | 0.013997 | 0.017198 | 0.011138 | 0.015493 | 0.0058451 | -0.008366 | -0.0064859 | -0.0034211 | -0.004281 | -0.0021727 | -0.0031802 | -0.00030761 | -0.00062942 | 0.0018421 | -0.0034211 | -0.0050063 | -0.0025497 | -0.00087648 | 0.00059322 | 0.0035042 | -0.00049708 | -0.00079098 | 0.00013514 | -0.00060614 | 0.0020238 | 0.0042301 | 0.0044102 | 0.0046943 | 0.0038175 | 0.0042758 | 0.0067004
1.37 t^-0.99 (fit 0 to 100) | 1.945 | 0.37728 | 0.10779 | 0.095036 | 0.081191 | 0.056789 | 0.030535 | 0.026911 | 0.026668 | 0.025783 | 0.022905 | 0.020215 | 0.014783 | 0.014725 | 0.014624 | 0.014315 | 0.013118 | 0.013095 | 0.012166 | 0.012068 | 0.011727 | 0.011042 | 0.0097734 | 0.0090643 | 0.0089722 | 0.0084756 | 0.0083391 | 0.00773 | 0.0076866 | 0.0069644 | 0.0060724 | 0.0059715 | 0.0059293 | 0.0057204 | 0.0056477 | 0.0054521 | 0.0054208 | 0.0052678 | 0.0052278 | 0.0049058 | 0.0047311 | 0.0047061 | 0.0046555 | 0.0046004 | 0.0045948 | 0.0043684 | 0.0042676 | 0.0042085 | 0.0041016 | 0.0040983 | 0.0040828 | 0.0040106 | 0.0039439 | 0.003848 | 0.0037914 | 0.0037886
a = 1.37, b = 0.99, c = 0.14, d = 0.01
Notes: B = 0.99 ~ 1
Due to 1/t effect. Originally X failures no more n(t)/t =X/t declines as 1/t, t ^ 1

## Slide 5: Additional Reliability Growth Data Sets
The top data set has a declining failure rate to the end, so c =0.
  The end of the test has d = 0.83, due to possibly correctable failures.
The lower data set reaches a constant failure rate, d = 0.0
  Note b = 1.00, the maximum 1/t decline.
Chart: Failure rate, n(t)/t, and the abcd model fit versus time
| 0.68 | 1.89 | 3.11 | 4.32 | 5.54 | 6.75 | 7.97 | 9.18 | 10.4 | 11.61 | 12.83 | 14.06 | 15.27 | 16.489999999999998 | 17.7 | 18.920000000000002 | 20.13 | 21.35 | 22.56 | 23.78 | 24.99 | 26.21 | 27.44 | 28.65 | 29.85 | 31.08 | 32.299999999999997 | 33.51 | 34.729999999999997 | 35.94 | 37.159999999999997 | 38.369999999999997 | 39.590000000000003 | 40.82 | 42.03 | 43.1 | 44.31 | 45.53 | 46.74 | 47.96 | 49.17 | 49.5
n(t)/t = 5.49 t^-1.0 + 0.00 + 0.83 | 8.8888 | 3.7295 | 2.5921 | 2.0985 | 1.8192 | 1.6419 | 1.5176 | 1.4269 | 1.3569 | 1.302 | 1.2571 | 1.2198 | 1.1889 | 1.1623 | 1.1396 | 1.1196 | 1.1022 | 1.0867 | 1.0729 | 1.0604 | 1.0493 | 1.0391 | 1.0297 | 1.0213 | 1.0136 | 1.0063 | 0.99966 | 0.99353 | 0.98779 | 0.98248 | 0.97747 | 0.97282 | 0.96842 | 0.96425 | 0.96038 | 0.95715 | 0.95367 | 0.95036 | 0.94724 | 0.94426 | 0.94145 | 0.94071
n(t)/t | 8.8235 | 3.7037 | 2.5723 | 2.0833 | 1.8051 | 1.6296 | 1.5056 | 1.4161 | 1.3462 | 1.292 | 1.2471 | 1.2091 | 1.1788 | 1.1522 | 1.1299 | 1.1099 | 1.0929 | 1.0773 | 1.0638 | 1.0513 | 1.0404 | 1.0301 | 1.0204 | 1.0122 | 1.005 | 0.99743 | 0.99071 | 0.98478 | 0.97898 | 0.97385 | 0.96878 | 0.9643 | 0.95984 | 0.95541 | 0.9517 | 0.95128 | 0.9253 | 0.90051 | 0.87719 | 0.85488 | 0.83384 | 0.82828
Chart: Failure rate, n(t)/t, and the abcd model fit versus time
| 0.24 | 1.46 | 2.67 | 3.9 | 5.12 | 6.33 | 7.55 | 8.76 | 9.98 | 11.19 | 12.41 | 13.62 | 14.84 | 16.05 | 17.28 | 18.5 | 18.78 | 19.989999999999998
2.7 t^-1 +1.0+0.0 | 12.25 | 2.8493 | 2.0112 | 1.6923 | 1.5273 | 1.4265 | 1.3576 | 1.3082 | 1.2705 | 1.2413 | 1.2176 | 1.1982 | 1.1819 | 1.1682 | 1.1562 | 1.1459 | 1.1438 | 1.1351
n(t)/t | 12.25 | 2.8493 | 2.0112 | 1.6923 | 1.5273 | 1.4265 | 1.3576 | 1.3082 | 1.2705 | 1.2413 | 1.2176 | 1.1982 | 1.1819 | 1.1682 | 1.1562 | 1.1459 | 1.1438 | 1.1351
a = 5.49, b = 1.0, c = 0.00, d = 0.83
a = 2.77, b = 1.0, c = 1.0 , d = 0.0

## Slide 6: Discussion - 1
The familiar bathtub curve shows the failure rate initial declining with time, remaining constant for a long period, and finally increasing.
  It is surprising that reliability growth goes on forever in the Duane-Crow model.
  In fact, since the model is n(t)/t = a t-b, the failure rate declines to 0 as t grows large.
The abcd parameters of the model are determined by the failure test data.
  The failure rate usually reaches a constant value of c.
  After a constant c is reached, reliability growth has ended, so d = 0.
  The values of a and b are determined by fitting a t-b to n(t)/t - c.
  Usually b =0.99 or 1.0, reflecting the 1/t time averaging factor in n(t)/t.

## Slide 7: Discussion - 2
A new system often has unexpected failure causes.
  Each failure cause will have some intrinsic failure rate.
  The inverse of the failure rate is the MTBF, the mean time before failure.
  The first failure will tend to occur at a time of the order of its MTBF.
  Early failures have shorter MTBFs and do not recur if the system has been redesigned to remove them.
  A reliability growth exponent b = 1.0 reflects the fastest possible reliability growth
    Each failure mode contributes only once to the failure count.
    Its effect on the average failure rate declines linearly with time.

## Slide 8: Applications
The abcd reliability growth model has applications in analyzing completed tests, tracking ongoing tests, and planning future tests.
Four completed tests were analyzed here.
If a similar test is tracked from the beginning, the time td when a constant failure rate begins, and the constant failure rate c, can be identified and the abcd model applied.
  The expected result would be b = 1.
  If the time td is set too late, the result is usually b < 1, if too early the result may be an impossible b > 1.
The abcd reliability improvement model can be useful in planning and guiding the failure rate reduction process.
  The model can help determine how much reliability growth and failure rate testing is cost effective by comparting the cost of testing to the cost of using systems having higher or more uncertain failure rates than necessary.