## Slide 1
Brett Hiller, Richard Campbell, and Michelle Banchy
NASA Langley Research Center
Transonic Cruise Slotted Wing Design for Commercial Transport Aircraft using CDISC
Copyright 2024 United States Government as represented by the Administrator of the National Aeronautics and Space Administration. No copyright is claimed in the United States under Title 17, U.S. Code. All Other Rights Reserved. Published by the American Institute of Aeronautics and Astronautics, Inc. with permission.
AIAA SciTech Forum, January 2024
Notes: 0

## Slide 2: Outline
Introduction
Geometry and Design Conditions
Computational Tools and Design Constraints
Design Approach
Design Results
Concluding Remarks

## Slide 3: Cruise Slotted Wing Technology
Concept The Cruise Slotted Wing (CSW) is a transonic multielement wing concept with a forward main element and an aft flap element, separated to form an intermediate slot.
Design Advantage Flow-through slot permits stronger pressure recovery without separation, enables greater aft loading to help reduce shock strength and pressure drag

## Slide 4: Cruise Slotted Wing Design Trades
Increased Mach Number ()
    Reduced travel time, more daily city pairs
Decreased Wing Sweep ()
    Lighter wing, potential laminar flow benefit
Decreased Cruise Drag
    Less fuel consumption, lower emissions
Increased Lift Coefficient ()
    Greater payload capacity or lower wing area
Design Benefits
Korn Equation
Competing design trades analytically described using 3D Korn Equation for transonic wing performance
Airfoil Technology Factor
Improvement in aerodynamic efficiency (ML/D) considered an increase in technology factor
Enables one or a combination of vehicle-level benefits
Increased Wing Thickness()
    Lighter wing, greater fuel volume + range

## Slide 5: Research Plan
Objective Quantify the potential vehicle performance benefits of CSW technology in application to next-generation, single-aisle transonic commercial transports with cruise speeds near Mach 0.8
Goal: To develop design tool AIAA Paper 2021-2525
Goal: To confirm drag benefit Current Paper
Goal: To quantify drag benefit AIAA Paper 2021-2525
CDISC Development
2D Airfoil Design
3D Wing Design
Aft Laminar Multielement Airfoil (ALMA) 2.7% profile drag reduction relative to supercritical airfoil

## Slide 6: Geometry and Design Conditions
Baseline Conventional Wing
Mach-0.8 variant of the Common Research Model (CRM-M8) created for a representative single-aisle, transonic transport aircraft model
Baseline Cruise Slotted Wing
MAKESLOT code creates partial-span, slotted wing geometry from conventional wing
Features common fuselage and inboard wing, outboard slotted wing with main element and flap
CRM-M8 Conventional Wing
CRM-M8 Cruise Slotted Wing

## Slide 7: Computational Tools

## Slide 8: CDISC Multielement Design Constraints
Flow Constraints
Target Pressure Generation
End of Initial Acceleration
   Main: multipoint best practice  Flap: 5% of flap chord, limited crossflow (CF)
  concern due to low Rec and sweep
Midchord Pressure Gradient
   Main: multipoint best practice  Flap: control Tollmien-Schlichting (TS)
Start of Pressure Recovery
   Main: stable shock at 70% total chord  Flap: attached recovery at 95% total chord
Multielement Load Balancing
Alters sectional lift required for both elements
   loading ratio = cl,flap / cl,main
CDISC Slotted Airfoil Target Pressures
End of Initial Acceleration (x1)
Midchord Pressure Gradient ()
Start of Pressure Recovery (x2)
CP*
Subsonic Flap Load Balancing

## Slide 9: CDISC Multielement Design Constraints
Geometry Constraints
Flap Overhang (oF) Horizontal distance between the flap leading edge (LE) and the main element trailing edge (TE)  slot length
Flap Deflection (𝛅F) Flap incidence angle relative to the 𝛂 = 0° reference line  flap loading
Slot Exit Gap (ge) Vertical distance between the main element TE and the flap upper surface  min. wake interference
Slot Inlet Gap (gi) Shortest distance between flap LE and the max. surface slope point on the main element lower surface
 increase main element camber and aft loading
CDISC Slotted Airfoil Parameterization

## Slide 10: Design Approach
Design Stations (13 Total)
Design Strategy
Conventional Wing
CDISC best practices for turbulent supercritical wing design, used target pressure constraint
Cruise Slotted Wing
Matched design 𝛂 of conventional wing
 Limit change in fuselage/fairing drag
Matched spanwise lift distribution  Limit change in induced drag
Identical inboard wing design constraints  Isolate drag change to outboard wing
Outboard wing design using new constraints  Min. shock strength with subsonic flap

## Slide 11: Design Results: Pressures and Geometry
Conventional Wing
Slotted Wing
M = 0.8, Recref = 21.1 million, CL = 0.543
8
8

## Slide 12: Design Results: NLF Predictions
NLF Predictions for Flap Design
Transition predictions estimate NLF for 71% of upper surface and 77% of lower surface using critical N-factor (NF) of 9

## Slide 13: Design Results: Cruise Forces and Moments
Cruise Assessment (M = 0.8, Recref = 21.1 million) The CSW shows comparable cruise drag (~1 ct.) to the conventional wing. NLF flap significantly reduces skin-friction penalty, but no pressure drag savings at design condition
+3.9 ct
+0.5 ct
+2.5 ct
+0.6 ct
92 ct
125 ct
21 ct

## Slide 14: Design Results: Off-design Performance
Flap Upper Surface
Flap Lower Surface
M = 0.8, Recref = 21.1 million

## Slide 15: Design Results: Off-design Performance
Flap Upper Surface
Flap Lower Surface
CL = 0.543, Recref = 21.1 million

## Slide 16: Concluding Remarks
Series of CDISC multielement flow and geometry constraints created to enable the computational design of transonic cruise slotted wings
Partial-span, Cruise Slotted Wing (CSW) designed for a Mach-0.8 variant of the CRM
  Subsonic flap loading was maximized to reduce main element shock strength and shift terminating shock location aft by 10% chord relative to supercritical wing
  Leverages Aft Laminar Multielement Airfoil (ALMA) concept to achieve NLF on approximately 75% of flap surface area (upper/lower surfaces)
  Cruise drag estimates from USM3D-ME showed comparable performance relative to supercritical wing at flight conditions representative of single-aisle, transonic transports
  Off-design assessments showed limited NLF sensitivity to 𝛂 and more gradual drag rise
Future work planned to explore other trades and CSW design with full-chord NLF
  Explore alternative design trades, including Mach number, thickness, etc.
  Crossflow Attenuated Natural Laminar Flow (CATNLF) methods used to design main element
    Achieves skin-friction drag reductions and improved drag rise behavior

## Slide 17
Contact: Brett Hiller <brett.hiller@nasa.gov>