## Slide 1: VERIFICATION OF THE GENERALIZED AEROSPACE SIMULATION IN SIMULINK® AAS-24-081 Nicholas Olson (Jacobs), Justin Ganiban (Jacobs), Juan Orphee, Matt Hawkins NASA Marshall Space Flight Center – Huntsville Alabama
2/3-7/2024
46th AAS Guidance and Control Conference 2024
Breckenridge, CO

## Slide 2: Overview
Introduction
NESC Check Case Introduction
GLASS Framework
Verification Plan
Orbital Check Case Verification
Conclusions

## Slide 3: The big question is, “What is the best way to verify the dynamics of a 6-DoF aerospace vehicle simulation?"
6-DoF Aerospace Vehicle Verification
Use Real World Data
Compare to other in-house simulations
NASA NESC 6-DoF Check Cases
Complex dynamics interactions
Data rates
Data availability
Simulation complexity
Is the other sim verified?
Multiple cases incrementally building complexity
Multiple simulations to compare against
Is there another in-house simulation to compare to?

## Slide 4: NESC Check Case Introduction
Atmospheric and Exo-atmospheric check-cases to verify 6-DoF flight simulation tools
  Multiple simulation tools incorporated the check cases to provide a family of solutions to each scenario
  Results were anonymized
Orbital check-cases compared 4 different simulation tools
Atmospheric check-cases compared 6 different simulation tools
GLASS verification done by ensuring that differences between GLASS simulation results and average of NESC simulation results are bounded by worst case NESC simulation differences
  Some leeway given when GLASS models differed, although difference is expected to be of the same magnitude as the NESC simulations
  Note that the NESC report calls the difference ‘error’ and this terminology is used here as well

## Slide 5: GLASS Framework
GLASS is designed to be modern, modular, user-friendly, and efficient simulation framework
Built in Simulink utilizing Simscape Multibody® as the dynamics engine
Basic simulations can be constructed with as little as 6 GLASS blocks
GLASS’s primary role is within the HLS Guidance Navigation and Control (GNC) Insight Team
  Simulate and test HLS Commercial Partners GNC algorithms

## Slide 6: Verification Plan Against NESC Check Cases
Focused on orbital check-cases
  Main area of insight work with GLASS in the HLS program
  Atmospheric check-cases will be completed in the future
All orbital cases were simulated using GLASS
  Cases shown below are discussed in report
  Highlighted cases presented here for brevity:
Case Number | Case Name | Verifies
2 | Keplerian Propagation | Integration, RNP, orientation
3B | 8x8 gravitation model | 8x8 harmonic gravitation model
4 | Planetary Ephemeris | Third body gravitational forces
6B | Aero Drag with Dynamic Atmosphere | Response to dynamic drag
9D | Non-Zero Initial Rate w/ T + F | Rotational response
10D | Non-Zero Initial Rate; Elliptical Orbit | Gravity gradient modeling
FULL | Integrated 6-DOF Orbital Motion | Combined effects response

## Slide 7: NESC Orbital Check Case Verification

## Slide 8: Orbital Check Case 2 – Keplerian Propagation
Case Conditions
  Inverse-square gravitational model
Checks
  Integration methods
  Earth rotation models (rotation, nutation, precession)
Analytical solution exists to compare to!
If you don’t have this one right, you’re not going anywhere!
GLASS modeling differences/assumptions
  No nutation/precession for Earth-Centered Earth-Fixed (ECEF) frame
    This holds true for all cases
    SPICE rotation, nutation, precession matrices did not agree with the orientation of the frame in the study to desired accuracy
All GLASS simulation results fell within error bounds

## Slide 9: Orbital Check Case 2 – Keplerian Propagation
Earth Inertial (EI) Position
Accurate to within 10-3 m
EI Velocity
<10-6 m/s of error

## Slide 10: Orbital Check Case 2 – Keplerian Propagation
EI Acceleration
10-7 m/s2 of error
ECEF Position
< 0.3 m of error

## Slide 11: Orbital Check Case 2 – Keplerian Propagation
LVLH Euler Angles
<10-6 rad of error
Body Angular Rates
<10-8 rad/s of error

## Slide 12: Orbital Check Case 3B – 8x8 Gravitation Model
Case Conditions
  8x8 spherical harmonic gravity model
Checks
  Spherical harmonic gravitation model
GLASS modeling differences/assumptions
  Utilized Mathworks Aerospace Blockset spherical harmonic gravity model with EGM2008 parameters
  No nutation/precession for Earth-Centered Earth-Fixed (ECEF) frame
All GLASS simulation results fell on the same order of magnitude of difference scale of the NESC simulation errors

## Slide 13: Orbital Check Case 3B
Gravitational Acceleration
<10-5 m of error

## Slide 14: Orbital Check Case 3B
ECEF Position Comparison
<10 m of error
EI Position Comparison
<10 m of error

## Slide 15: Orbital Check Case 4 – Planetary Ephemeris
Case Conditions:
  3rd body gravitational effects from Sun and Moon
Checks
  Ephemeris data accuracy
  3rd order gravitational effect models
GLASS modeling differences/assumptions
  No nutation/precession for Earth-Centered Earth-Fixed (ECEF) frame
All GLASS simulation results fell within error bounds

## Slide 16: Orbital Check Case 4
EI Position Comparison
<0.02 m of error

## Slide 17: Orbital Check Case 6B – Aero Drag with Dynamic Atmosphere
Case Conditions:
  Thermosphere Atmospheric model
  Drag
Checks
  Atmospheric model
  Drag modeling effects
GLASS modeling differences/assumptions
  No nutation/precession for Earth-Centered Earth-Fixed (ECEF) frame
  US Naval Research Laboratory Mass Spectrometer and Incoherent Scatter Radar 00 (NRLMSISE-00) atmospheric model from Mathworks Aerospace Blockset used instead of Marshall Engineering Thermosphere (MET) model
Most GLASS simulation results fell within error bounds except for atmospheric properties due to model differences
  These differences were expected and accepted

## Slide 18: Orbital Check Case 6B
Atmospheric Properties Comparison

## Slide 19: Orbital Check Case 6B
EI Position Comparison
<20m of error

## Slide 20: Orbital Check Case FULL – Integrated 6-DOF Orbital Motion
Case Conditions:
  Non-zero initial rates
  Elliptical Orbit
  8x8 Spherical Harmonic Gravity Model
  Gravitational Gradient Model
Checks
  All previous effects except manual force and torque application
GLASS modeling differences/assumptions
  No nutation/precession for Earth-Centered Earth-Fixed (ECEF) frame
  Utilized Aerospace Blockset spherical harmonic gravity model with EGM2008 parameters
  NRLMSISE-00 atmospheric model from Aerospace Blockset used instead of MET model
Most GLASS simulation results fell within error bounds except for those associated with previously mentioned modeling differences
  These differences were expected and accepted

## Slide 21: Orbital Check Case FULL
EI Acceleration Comparison
<10-5 m of error
EI Position Comparison
< 10m of error

## Slide 22: Orbital Check Case FULL
Body Angular Rates
Similar trends and magnitudes for half of flight
2nd half stays bounded
LVLH Euler Angles
Similar trends and magnitudes throughout flight

## Slide 23: Conclusions
The GLASS framework was successfully verified against the NESC 6-DOF simulation study
This verified:
  Simscape Multibody solver
  Gravitational models
  Atmospheric models
  GLASS framework and related code
Small differences seen are attributable to modeling choices:
  Gravitational model differences
  Gravitational gradient model differences
  Atmospheric model differences

## Slide 24: Thank you Thanks to... Co-Authors: Nicholas Olson (Jacobs), Justin Ganiban (Jacobs), Juan Orphee, Matt Hawkins Also, we would like to thank the Human Landing System project and NASA NESC, both supporting this verification activity
Any questions?

## Slide 25: Backup

## Slide 26: Orbital Check Case 9D – Non-Zero Initial Rate w/ T + F
Case Conditions:
  Non-zero initial rates
  Torque and force application
Checks
  Translational response
  Rotational response
GLASS modeling differences/assumptions
  No nutation/precession for Earth-Centered Earth-Fixed (ECEF) frame

## Slide 27: Orbital Check Case 9D
EI Acceleration Comparison
<10-8 m of error
EI Position Comparison
<10-3 m of error

## Slide 28: Orbital Check Case 9D
LVLH Euler Angles
<10-5 rad of error
Body Angular Rates
<10-8 rad/s of error

## Slide 29: Orbital Check Case 10D – Non-Zero Initial Rate; Elliptical Orbit
Case Conditions:
  Non-zero initial rates
  Elliptical Orbit
  8x8 Spherical Harmonic Gravity Model
  Gravitational Gradient Model
Checks
  Gravitational gradient model effects
GLASS modeling differences/assumptions
  No nutation/precession for Earth-Centered Earth-Fixed (ECEF) frame

## Slide 30: Orbital Check Case 10D
LVLH Euler Angles
Similar trends and magnitudes throughout flight
Body Angular Rates
Roll: <10-17 rad/s of error
Pitch/Yaw: <10-5 m of error

## Slide 31: Orbital Check Case 10D
EI Position Comparison
<10-5 m of error