## Slide 1: The next generation Marshall Grazing Incidence X-ray Spectrometer (MaGIXS) sounding rocket experiments P.S. Athiray1,2, Amy Winebarger2, Patrick Champey2, Ken Kobayashi2, Sabrina Savage2, Adam Kobelski2, Genevieve Vigil2, Brent Beabout2, Dyana Beabout2, Peter Cheimets3, Leon Golub3, Anthony Guillory2, Harlan Haight2, Edward Hertz3, Paola Testa3, William Hogue2, Jagan Ranganathan2, Robert Walsh4 and the Science Team 1 The University of Alabama in Huntsville, 2 NASA Marshall Space Flight Center, 3 Smithsonian Astrophysical Observatory, 4 The University of Central Lancashire
MaGIXS-1
Science Goal : To constrain the frequency of heating events in solar active region structures
Wavelength range : 8 to 30 Å
Field of view : 9.5’ x 25’
Spot size ~ 27” HPD
Launch : 30 July 2021
Observation Highlights
First demonstration of unfolding spectroheliograms
X-ray bright points observed are consistent with high frequency heating scenario[5] (see Poster )
Discovered ‘missing’ emission lines of Fe XVI, Fe XV in CHIANTI atomic database  MaGIXS-3
Missed to observe high temperature diagnostic emission lines due to internal vignetting  MaGIXS-2
Telescope Mirror
Spectrometer Mirrors + Reflective Grating
Cross-Dispersion (spatial)
Dispersion (increasing λ)
Fig. 2: MaGIXS-1 flight observations
Fig. 3:
MaGIXS-1 FOV
Introduction
References:
[1] Athiray, P. S., et al. 2019, ApJ; [2] Champey, P. R. et al. 2022, JAI ; [3] Cheung, M. C. M., et al. 2019, ApJ ; [4] Winebarger, A. R et al. 2019, ApJ ; [5] Savage, S et al. 2023, ApJ;
          The Marshall Grazing Incidence X-ray Spectrometer (MaGIXS) is a slitless soft X-ray (SXR) imaging spectrometer designed to constrain frequency of heating events in solar active regions[1,2]. The instrument produces spatially resolved SXR spectra, known as “spectroheliogram”, where spectral information from different spatial locations overlap on the detector. The first sounding rocket flight of MaGIXS occurred on July 30, 2021, from the White Sands Missile Range, New Mexico. Spectrally pure images of X-ray bright points are obtained through novel customized inversion techniques[3,4,5]. Here we present the design of next generation MaGIXS instrument, objectives and status updates.
Slot
Fig. 1: MaGIXS-1 Optical Layout
Telescope Mirror
Reflective Grating
MaGIXS-2
Goal : Measure high temperature diagnostic emission lines from hot active region
Wavelength range : 8 to 30 Å
Field of view : 16’ x 33’
Spot size ~ 17” HPD
Instrument Upgrades : MaGIXS-2 is a simplified design from MaGIXS-1
Spectrometer mirrors are eliminated, and grating is placed behind telescope
MaGIXS-1 telescope assembly and grating will be reused.
Increases effective area, spatial resolution and field-of-view
Fig. 4: MaGIXS-2 Optical Layout
Telescope Mirror
Reflective Grating
MaGIXS 2 will be calibrated in the 100m beamline at the Stray Light Test Facility and fly in July 2024
N
MaGIXS 1
MaGIXS 2
Smaller PSF reduces spatial spectral overlap.
Greater effective area over a larger FOV than MaGIXS-1.
Fig. 5: MaGIXS-2 Forward Model (Right) using the solar FOV (left)
Instrument Upgrades
A new instrument The Resolving Inversion Context X-ray Bragg crystal spectrometer (TRICXS) is added
MaGIXS will carry a new high resolution X-ray telescope mirror
Wavelength range : 8 to 30 Å (MaGIXS), 14 to 16 Å (TRICXS)
Field of view : 16’ x 33’ (MaGIXS), 3’ diameter (TRICXS)
MaGIXS-3
MaGIXS
TRICXS
Fig. 6: MaGIXS-3 Optical Layout
New High resolution Telescope Mirror
Reflective grating
Science Upgrades
Goal: Determine if the plasma is in equilibrium or not
Measure high temperature diagnostic emission lines  Determine DEM, abundances
Measure satellite lines of Fe XVII, XVI and resonance lines of Fe XVII near 15 Å
Acknowledgments:
We acknowledge the MaGIXS instrument team for making the data available through the 2014 NASA Heliophysics Technology and Instrument Development for Science (HTIDS) Low Cost Access to Space (LCAS) program, funded via grant NNM15AA15C. MSFC/NASA led the mission with partners including the Smithsonian Astrophysical Observatory, the University of Central Lancashire, and the Massachusetts Institute of Technology.