## Slide 1
Demonstration of frequency-scanning burst-mode filtered Rayleigh scattering for multi-parameter
gas-phase measurements
| 1
Copyright © by Purdue University and the U.S.A., as represented by the Administrator of the
National Aeronautics and Space Administration. All rights reserved. Published by the American Institute of Aeronautics and Astronautics, Inc., with permission.
Amanda M. Braun1 Neil S. Rodrigues2, Paul M. Danehy2 Alexander R. Suppiah1, James Braun3 Mikhail N. Slipchenko1, Terrence R. Meyer1
2024 AIAA SciTech Forum
AMT-08, Laser Absorption and Scattering Techniques
January 9, 2024
1 Purdue University
2NASA Langley Research Center
3North Carolina State University

## Slide 2: Acknowledgements
NASA Space Technology Graduate Research Opportunity (NSTGRO20), Dr. Paul Danehy as Mentor
N. Rodrigues and P. Danehy acknowledge the support of the NASA STMD/ESDMD Plume Surface Interaction project and the ARMD Transformative Tools and Technologies project
William Holt Ripley, Dr. Ross Burns, Dr. Timothy Fahringer
Steve Jones, Scott Bartram
Chris Crabtree from Spectral Energies, LLC
Dr. Jerome Braun

## Slide 3: Why do we need optical diagnostics?
Surface Pressure
Surface Temperature
Mach Number
Hyper-X[2]
HIFiRE Flight 2 Vehicle [1]
- Laser electronic excitation tagging (FLEET, PLEET)
- Schlieren/shadowgraphy
- Fluorescence-based (PLIF)
- Laser scattering (CARS, Raman, Rayleigh, DGV, PIV)

## Slide 4: Why use Rayleigh scattering?
Particle Image Velocimetry
Technique
Velocity
Temperature
Pressure
Density
Doppler Global Velocimetry
Raman Scattering
Rayleigh Scattering
Unseeded
* Background interferences, weak signal levels, and difficulty making multi-parameter measurements
Notes: Unseeded technique

## Slide 5: What is Rayleigh scattering?
Incident Laser
Flow Molecules
Scattering Vector
Wave Vector
Laser Vector
Velocity Vector
Doppler Shift
Rayleigh Scattering
Notes: Explanation

## Slide 6: Why use filtered Rayleigh scattering?
Incident Laser
Flow Molecules
Rayleigh Scattering
Rayleigh Scattering
Mie/Stray Scattering
Notes: Explanation

## Slide 7: Why use filtered Rayleigh scattering?
532 nm
Flow Molecules
Rayleigh Scattering
Filter
Molecular
Filter
Gaseous Iodine
Up to 6 unknowns:
Notes: Explanation

## Slide 8: Frequency-scanning FRS for a single pixel
Function of the flow conditions and
Author | Meas. | # Steps | # Avg. | Total time
[3]Forkey et al. (1996) |  | 30 | 30 | 50 min.
[4]Boguszko et al. (2005) |  | 120 | 50 | 10 min.
[5]Doll et al. (2014) |  | 13 | 60 s | 12 min.
Author | Meas. | # Steps | # Avg. | Total time
[3]Forkey et al. (1996) |  | 30 | 30 | 50 min.
[4]Boguszko et al. (2005) |  | 120 | 50 | 10 min.
[5]Doll et al. (2014) |  | 13 | 60 s | 12 min.
Can we reduce this measurement time?

## Slide 9: Frequency-scanning burst-mode laser
Doppler global velocimetry
Planar
laser-induced fluorescence
[6] Fahringer et al. (2020)
[7] Burns et al. (2018)
[8] Rodrigues et al. (2023)
Potential to decrease measurement time to 10 ms or less

## Slide 10: Frequency-scanning burst-mode laser
532 nm
SHG
1064 nm
Power Amplifier
cw Laser
Pulse Slicing
Function Generator
Master Oscillator
Function Generator Signal

## Slide 11: Frequency-scanning burst-mode laser
Relative Frequency (GHz)
Function Generator Signal
532 nm
SHG
1064 nm
Power Amplifier
cw Laser
Pulse Slicing
Function Generator
Master Oscillator
Wavemeter
Wavemeter Measurement

## Slide 12: Frequency-scanning burst-mode laser
Relative Frequency (GHz)
Function Generator Signal
532 nm
SHG
1064 nm
Power Amplifier
cw Laser
Pulse Slicing
Function Generator
Master Oscillator
Wavemeter
Wavemeter Measurement
Unfiltered
Unfiltered Burst Profile

## Slide 13: Frequency-scanning burst-mode laser
Relative Frequency (GHz)
Function Generator Signal
532 nm
SHG
1064 nm
Power Amplifier
cw Laser
Pulse Slicing
Function Generator
Master Oscillator
Wavemeter
Wavemeter Measurement
Unfiltered
Unfiltered Burst Profile
Iodine Cell
Iodine Cell
Filtered
Filtered Burst Profile

## Slide 14: Underexpanded jet flow
532 nm
SHG
1064 nm
Power Amplifier
cw Laser
Pulse Slicing
Function Generator
Master Oscillator
Wavemeter
Unfiltered
Iodine Cell
Iodine Cell
Filtered
Orifice-style sonic nozzle coupled with coflow
Plenum pressure,
Back pressure,
Schlieren

## Slide 15: Computational fluid dynamics
532 nm
SHG
1064 nm
Power Amplifier
cw Laser
Pulse Slicing
Function Generator
Master Oscillator
Wavemeter
Unfiltered
Iodine Cell
Iodine Cell
Filtered
Reynolds Averaged Navier Stokes (RANS)
2D axisymmetric mesh with ~60,000 hexahedral cells
Computational Fluid Dynamics

## Slide 16: Filtered/unfiltered Rayleigh scattering images
532 nm
SHG
1064 nm
Power Amplifier
cw Laser
Pulse Slicing
Function Generator
Master Oscillator
Wavemeter
Unfiltered
Iodine Cell
Iodine Cell
Filtered
Iodine Cell
Unfiltered Camera
Filtered Camera
Filtered Camera
Time-averaged
Calculated density
Unfiltered Camera
Instantaneous
Mean density
Laser Sheet
Schlieren
Flow
+ Velocity

## Slide 17: Effects of conditions on pixel intensities
Reference
Experiment
Filtered Rayleigh
Filtered Background

## Slide 18: Effects of conditions on pixel intensities
Reference
Experiment
Filtered Rayleigh
Filtered Background

## Slide 19: Summary of frequency-scanning parameters
Configuration | Rate | Burst | mJ/Pulse | Pulses/Scan | Scans/Burst | Total Time
1 | 20 kHz | 5 ms | 860 | 100 | 1 | 5 ms
2 | 20 kHz | 5 ms | 860 | 20 | 5 | 1 ms
3 | 200 kHz | 1 ms | 280 | 200 | 1 | 1 ms

## Slide 20: Configuration 1: Single 5-ms measurement for NPR 7
Calculated density from ideal gas law
Density
Radial Velocity
Pressure
Temperature
Mean density from unfiltered RS
CFD
Experimental
| 20

## Slide 21: Centerline pressure, temperature, and density
Temperature
Pressure
Density
Centerline Mach number: Ashkenas et al.
Mach disc location: Gibbings et al.
Isentropic and normal shock relations

## Slide 22: Radial velocity at varying axial locations
Radial Velocity
z = 5 mm
z = 4 mm
z = 3 mm
z = 2 mm

## Slide 23: Summary of frequency-scanning parameters
Configuration | Rate | Burst | mJ/Pulse | Pulses/Scan | Scans/Burst | Total Time
1 | 20 kHz | 5 ms | 860 | 100 | 1 | 5 ms
2 | 20 kHz | 5 ms | 860 | 20 | 5 | 1 ms
3 | 200 kHz | 1 ms | 280 | 200 | 1 | 1 ms

## Slide 24: Configuration 2: Five 1-ms measurements
Pressure
Temperature
Rad. K Velocity
Calc. Density
Mean Density
1 ms
2 ms
3 ms

## Slide 25: Configuration 2: Five 1-ms measurements
Pressure
Temperature
Rad. K Velocity
Calc. Density
Mean Density
1 ms

## Slide 26: Configuration 2: Five 1-ms measurements
Pressure
Temperature
Rad. K Velocity
Calc. Density
Mean Density
z = 5 mm
z = 4 mm
z = 3 mm
z = 2 mm
1 ms

## Slide 27: Summary of frequency-scanning parameters
Configuration | Rate | Burst | mJ/Pulse | Pulses/Scan | Scans/Burst | Total Time
1 | 20 kHz | 5 ms | 860 | 100 | 1 | 5 ms
2 | 20 kHz | 5 ms | 860 | 20 | 5 | 1 ms
3 | 200 kHz | 1 ms | 280 | 200 | 1 | 1 ms

## Slide 28: Configuration 3: Single 1-ms measurements
Pressure
Temperature
Rad. Velocity
Calc. Density
Mean Density
Single 1-ms Meas.

## Slide 29: Configuration 3: Single 1-ms measurements
Pressure
Temperature
Rad. Velocity
Calc. Density
Mean Density
Single 1-ms Meas.
Increasing measurement rate requires higher signal levels

## Slide 30: Conclusions
Simultaneous in up to 1 ms
Comparison with CFD and empirical correlations
Increased measurement rate by 600,000x
5 ms
5 x 1 ms
1 ms
CFD
Potential for 100s of kHz
  Increase signal levels
  High repetition rate wavelength measurement

## Slide 31: References
[1] Baurle, R. A. (n.d.). VULCAN-CFD applications. https://vulcan-cfd.larc.nasa.gov/WebPage/vulcan_apps.html
[2] “Hyper-X ED97-43968-1: Computational Fluid Dynamics (CFD) Image of Hyper-X Research Vehicle at Mach 7 with Engine Operating.” https://www.dfrc.nasa.gov/Gallery/Photo/X-43A/HTML/ED97-43968-1.html (accessed Oct. 02, 2022).
[3] J. N. Forkey, N. D. Finkelstein, W. R. Lempert, and R. B. Miles, “Demonstration and characterization of filtered Rayleigh scattering for planar velocity measurements,” AIAA Journal, vol. 34, no. 3, pp. 442–448, Mar. 1996, doi: 10.2514/3.13087.
[4] M. Boguszko and G. S. Elliott, “Property measurement utilizing atomic/molecular filter-based diagnostics,” Progress in Aerospace Sciences, vol. 41, no. 2, pp. 93–142, Feb. 2005, doi: 10.1016/j.paerosci.2005.03.001.
[5] U. Doll, G. Stockhausen, and C. Willert, “Endoscopic filtered Rayleigh scattering for the analysis of ducted gas flows,” Exp Fluids, vol. 55, no. 3, p. 1690, Mar. 2014, doi: 10.1007/s00348-014-1690-z.
[6] T. W. Fahringer, R. A. Burns, P. M. Danehy, P. M. Bardet, and J. Felver, “Pulse-Burst Cross-Correlation Doppler Global Velocimetry,” AIAA Journal, vol. 58, no. 6, pp. 2364–2369, Jun. 2020, doi: 10.2514/1.J059172.
[7] R. A. Burns, T. W. Fahringer, and P. M. Danehy, “Velocity measurements across an oblique shock using pulse-burst cross-correlation DGV,” in AIAA Scitech 2021 Forum, American Institute of Aeronautics and Astronautics. doi: 10.2514/6.2021-0120.
[8] N. S. Rodrigues, P. M. Danehy, N. Jiang, P. Hsu, J. Leicht, and S. Roy, “100 kHz High-Spectral-Resolution NO-PLIF Measurements for Compressible Flows,” in AIAA SCITECH 2023 Forum, National Harbor, MD & Online: American Institute of Aeronautics and Astronautics, Jan. 2023. doi: 10.2514/6.2023-0405.
[9] H. Ashkenas and Sherman, Frederick, “Structure and utilization of supersonic free jets in low density wind tunnels,” vol. No. NASA-CR-60423, 1965.
[10] C. Gibbings, J, Ingham, and D. Johnson, “Flow in a Supersonic Jet expanding from a Convergent Nozzle,” 2002. Accessed: Nov. 15, 2023

## Slide 32: Backup Slides

## Slide 33: Filtered/unfiltered camera video
Configuration 1
Configuration 2
Configuration 3
Counts
0
1200
Counts
0
300
Counts
0
1200

## Slide 34: Demonstration image sequence

## Slide 35: Image processing steps

## Slide 36: Sensitivity to pressure, temperature, velocity

## Slide 37: Empirical Correlations
(4.8)
Centerline Mach number before Mach disc [9]
Centerline pressure, temperature, and density before Mach disc (isentropic relations)
Mach disc location [10]
Mach number, pressure, temperature, and density after the Mach disc (normal shock equations)

## Slide 38: Wavemeter Correction

## Slide 39: Uncertainty in background constant estimates

## Slide 40: Background correction for density measurements
b.
Before Correction
Background Fit
After Correction

## Slide 41: Background correction for density measurements
b.
Before Correction
Background Fit
After Correction

## Slide 42: Unfiltered Rayleigh scattering processing
b.
0
50
0
50
Before Correction
Background Fit
After Correction

## Slide 43: Flow property fitting process
Calibration
Fit
Intensity at known
Experiment
Fit
Intensity at known

## Slide 44: Additional CFD Details
The Reynolds Averaged Navier Stokes (RANS) equations were solved with the k-ω Shear Stress Transport (SST) turbulence model
ANSYS FLUENT was used, and the mesh generated with ANSYS ICEM CFD.
A series of total pressures of varying magnitudes was applied at the inlet to mimic the different pressure ratios.
A static pressure of 1 atm was applied to the outlet.
Walls were treated as viscous with a first layer thickness (y+) of less than 1 at the nozzle walls, to capture the viscous sublayer.
A small portion of the chamber, as well as a small air volume for the jet, was modeled to capture the exhaust in the experimental setup.
Within the Fluent solver, a convergence criterion of 1e-3 was used, and cases were run until residuals plateaued.
A mesh sensitivity on a 3D domain was performed and compared to the two-dimensional simulations to verify the two-dimensionality of the domain.

## Slide 45: Achieving MHz rate
Laser Settings |  | Scan Settings |  | Total Time
Rep. Rate | Burst | Pulses/Scan | Scans/Burst | 
10 MHz | 1 ms | 10 | 1000 | 1 us
100 ns
1 us
Frequency-scanning
Energy
Time