## Slide 1
An Experimental System for Strategic Flight Path Management in Advanced Air Mobility
This material is a work of the U.S. Government and is not subject to copyright protection in the United States. Published by the American Institute of Aeronautics and Astronautics, Inc., with permission.
David A. Karr and James L. Sturdy Bryan A. Barrows and Mark G. Ballin
Analytical Mechanics Associates, Hampton, VA NASA Langley Research Center, Hampton, VA
AIAA SCITECH 2024, January 9, 2024

## Slide 2: Overview
The Autonomous Operations Planner (AOP) is a reference Flight Path Management (FPM) automation system for research.
We adapted AOP from en route commercial transport operations to Urban Air Mobility (UAM) operations with dense traffic.
First application of certain key AOP functions in live flight test.
AOP met expectations.
Lessons learned.
Notes: Will define these terms (AOP, FPM, UAM) during the presentation.

## Slide 3: Companion Presentations
Designing a Flight Test of a Flight Path Management System for Advanced Air Mobility Research
Stewart L. Nelson*, Mark G Ballin, Bryan A. Barrows, Matthew C. Underwood, David J. Wing
NASA Langley Research Center, Hampton, VA, USA
James L. Sturdy Ethan R. Williams
Analytical Mechanics Associates, Hampton, VA, USA American Systems Corporation, Edwards, CA, USA
Tue, Jan 9, 1:00pm‒1:20pm (Eastern) TF-01, Blue Spring I
Sim to Flight: Evaluating Flight Path Management Automation in High Density Urban Environments
Bryan A. Barrows*, Mark G Ballin, Terique L. Barney, Stewart L. Nelson, Matthew C. Underwood, David J. Wing
NASA Langley Research Center, Hampton, VA, USA
Tue, Jan 9, 1:20pm‒1:40pm (Eastern) TF-01, Blue Spring I
*presenter

## Slide 4: Flight Path Management (FPM) Automation Concept
Goal:
  A safe and operationally acceptable flight path is available to airspace users and aircraft systems throughout the flight
FPM: In-flight autonomy in shared airspace
  Continuous replanning to safely achieve mission objectives in the presence of traffic, flow restrictions, and weather
Feasible – Conforms to aircraft performance and range; Complies with airspace structure, rules, and constraints
Deconflicted – Avoids unsafe proximity to known traffic, terrain, obstacles, weather, and airspace hazards
Harmonized – Follows cooperative rules and procedures to be compatible with other airspace users & systems
Flexible – Provides adequate degrees of freedom to enable future flight path changes
Optimal – Achieves business objectives and preferences of the pilot and fleet operator
FPM Objectives: Create | Monitor | Evaluate | Revise | Coordinate the flight path to have:
Five Qualities:
Assumed for this research: An FPM system is located onboard each aircraft

## Slide 5: Urban Air Mobility at Scale
Urban Air Mobility (UAM) – a vision for a future transportation system that provides economical high-access air travel within urban environments.
UAM Maturity Level 4 (UML-4)
  Comparable to FAA’s UAM Mature Operational Stage
  Hundreds of aircraft serving a metropolitan area
  Dozens of vertiports, restricted airspace volumes, and corridors
The need for FPM automation:
  Human-centric flight path management may not be feasible at UML-4 traffic complexity
  Increasingly dense and complex operations with closer separation
  Safe and assured operations
Our Assumptions for UML-4
  Future eVTOL vehicles with low margin for contingencies
  Short flight durations (0.5 hr or less); continuous 4D trajectory conformance
  1500 ft (~0.25 NM) lateral and 450 ft vertical assumed separation
  Short time constraints and strategic look-ahead (3 minutes)

## Slide 6: Autonomous Operations Planner (AOP)
Reference implementation role:
Platform for assessing FPM system requirements
Advanced algorithms for complex FPM operations
Supporting NASA autonomy R&D for 20+ years
AOP core functionality:
Generates the flight path
Monitors the flight path and the factors which may impact it
Evaluates ongoing acceptability of the flight path and proposed changes
Revises the flight path, as needed, to sustain the desired qualities
Coordinates the flight path with other airspace users and service providers

## Slide 7: Autonomous Operations Planner (AOP)
Pilot’s FPM Engineering
User Interface
Data Sources:
Traffic state
Traffic intent
Wind
Temperature
Weather
Airspace
Terrain
Schedule
AOP Conflict Detector
with Trajectory Prediction Uncertainty Bounds (TPUBs)
AOP Strategic Resolver
with Pattern-Based Genetic Algorithm (PBGA)
  eVTOL Model
  Interpolation
  tables
AOP/UAM Trajectory Generator
Behavior-Based Trajectory Generator (BBTG)
monitor,
evaluate
coordinate,
revise
generate
Implementation for UAM R&D

## Slide 8: Research Activities
Initial prototype of UAM systems
Two large-scale simulation studies using Dallas-Fort Worth (DFW) demand model
Integration with actual aircraft (ground tests and flight trials)
Flight test
FPM-1 simulation study (2021)
FPM-2 simulation study (2022)
Flight test (2023)
Notes: Compare with Bryan’s slide with the sequence of images; his captions are more specific.

## Slide 9: Flight Test
Sikorsky Autonomy Research Aircraft (SARA) ownship
Sikorsky S-70TM
Optionally Piloted Vehicle (OPV) live intruder
Sikorsky Memorial Airport Stratford, Connecticut, USA
October 2023
Airspace restrictions from UAM concept for DFW metro region
250 to 330 virtual “background” traffic aircraft from UAM / DFW simulation
Photo by NASA
Used with permission of Sikorsky,
a Lockheed Martin company.
AOP
+
NASA Middleware
+
SARA guidance
NASA Middleware + OPV guidance

## Slide 10: Strategic Planning
Prediction all the way to the destination
Respect aircraft performance limits and operator preferences
Account for wind, air temperature, density, etc.
Track fuel/energy usage
Adjust airspeed to meet a required time of arrival (RTA)
Climb
Climb / accel
Perf climb
Const speed
Climb / turn
Level turn
Perf descent
Transition
Descent / flare
Const speed
Level / decel
Descent / decel
Level / accel
Departure
Arrival

## Slide 11: Behavior-Based Trajectory Generator (BBTG)
Specialized modules (“behaviors”) for each part of each phase of flight
  Constraints on nominal flight path
  Compute only what is needed
  VTOL behaviors, accelerations, battery usage data, turn rate limits, speed constraint types, rules for sequencing behaviors for UAM
Aircraft performance model in interpolation tables
  Models for UAM quadcopter and a UAM lift-cruise aircraft
2nd-order explicit Runge-Kutta methods (midpoint, trapezoid)
  where is whichever variable has a target value
    Distance
    Altitude
    Groundspeed
  Support interrupted timesteps
Karr, Vivona, Woods and Wing, "Point-Mass Aircraft Trajectory Prediction Using a Hierarchical, Highly-Adaptable Software Design," AIAA Paper 2017-3336, in AIAA Modeling and Simulation Technologies Conference, Denver, 2017.

## Slide 12: Conflict Detection (CD)
Required traffic separation 1500 ft horizontal, 450 ft vertical (“hockey puck”)
4D “envelope” around the nominal trajectory: Trajectory Prediction Uncertainty Bounds (TPUBs)
Estimation of “4D actual navigational precision” (along-path and altitude deviations, as well as lateral deviations) is essential to the CD algorithm
For flight test, ±150 ft cross-track, ±25 ft vertical, ±3 sec along-path
  Based on observations during integration testing in flight
Cross-track
Altitude
Time
Separation requirements apply to every point in volume A vs. every point in volume B
Notes: 3 seconds is equivalent to about 450 ft at the typical speeds of the aircraft during test

## Slide 13: Strategic Replanning: Pattern-Based Genetic Algorithm (PBGA)
Invoke to resolve a conflict or unmet RTA
Change trajectory by applying a maneuver pattern
Four choices of degrees of freedom (DOF):
  Lateral
  Vertical
  Hybrid lateral/vertical
  Speed (new for UAM)
Mutation, mating, survival of fittest (approx. 200 to 400 trajectories per DOF)
Search for optimized trajectory
Result must have no conflicts
Ownship
Intruder
Ownship
Intruder
Ownship
Intruder
Vertical maneuver
Lateral maneuver
Speed maneuver
Slow down
Speed up
Change altitude
Turn

## Slide 14: Computational Requirements of Strategic Replanning
  ~300 × 4 iterations of BBTG, CD, fitness
  250 – 330 traffic aircraft
  15 second time limit
AOP Conflict Detector
AOP Strategic Resolver
AOP/UAM Trajectory Generator
54 cm
(2.1 in)
Available computing hardware:
Intel NUC11TNHi7 Next Unit of Computing 64 GB memory, 4 cores, 8 hardware threads
Maximum clock rate 4.7 GHz
Windows operating system
⟹ Run on 4 parallel threads

## Slide 15: Adapting to Equipage
Simulated commercial transports:
  Flight Management System (FMS) determines the trajectory flown
  AOP mimics the prediction of the FMS
    Same aircraft performance tables
    Same assumptions about guidance
    (Sometimes) same trajectory generator (TG) source code
No compatible FMS in simulated UAM or on test aircraft
  No specification for eVTOL FMS
  Forced to provide some FMS functions in research code (i.e., AOP)
  All active trajectories were BBTG trajectories
  Scenario generation used BBTG to obtain nominal RTAs

## Slide 16: Why Use One Trajectory Generator for All Trajectories
Other TG predicts ownship trajectory
RTA
TOD
t = t1
t = t1
t = t2
t = t2
Ownship
Intruder
Predicted loss of separation
(conflict)

## Slide 17: Why Use One Trajectory Generator for All Trajectories
BBTG predicts ownship trajectory
RTA
TOD
t = t1
t = t2
t = t2
Ownship
Intruder
t = t1
Higher airspeed
Lower airspeed
Separation maintained

## Slide 18: 4D Guidance on SARA in Flight Test
AOP
Efficient Universal Trajectory Language (EUTL) Flight Plan
NASA Middleware
SARA or OPV Guidance
breadcrumbs
Sensors
actual flight path
sensed state

## Slide 19: Preliminary results
34 Flight Test Management test points executed
First AOP alert for conflict detected between live aircraft
First AOP resolution of conflict between live aircraft
  Continued flight verified no loss of separation
First AOP response to RTA change aboard live aircraft
Conflict alert, conflict resolution, and/or RTA change replicated in real time over multiple test points
PBGA mean elapsed time 8.8 seconds, maximum time 12.1 seconds
“Stressor” scenarios with 330 aircraft did not stress AOP
No violations of UAM airspace restrictions, even in “corridor” scenarios
Actual flight visually replicated simulation results
  Including “future AOP features” previously observed in simulation (2 test points affected)
Notes: I would like to say what the range of wind speeds was, but I don’t know where to find a consistent source of data for that.

## Slide 20: 4D Conformance
Typical maximum 4D deviations during flight: < 25 ft vertical < 10 feet cross track < 1 second along path
10 runs with conformance violations
  4 altitude violations
  1 cross-track violation
  2 along-path violations in completed runs
  3 along-path violations in incomplete runs of one test point
  Identified mitigations for violations and unusual deviations

## Slide 21: Conclusions and Questions
Good preliminary results
More complete analysis planned for publication July 2024
Can use airspeed to plan a trajectory, ground speed to communicate the trajectory
Tight 4D conformance is achievable
AOP performance — good and bad — was well represented in simulation
There are clear paths to address observed defects
AOP is a flexible and general tool for research in advanced flight deck automation for future civil aviation operations
What degree of 4D conformance do we really want?
How will future flight decks and ground systems be configured?
What is the desired functional architecture of an FPM system?

## Slide 22: Further Information
Email: david.a.karr@nasa.gov
Designing a Flight Test of a Flight Path Management System for Advanced Air Mobility Research
Stewart L. Nelson*, Mark G Ballin, Bryan A. Barrows, Matthew C. Underwood, David J. Wing
NASA Langley Research Center, Hampton, VA, USA
James L. Sturdy Ethan R. Williams
Analytical Mechanics Associates, Hampton, VA, USA American Systems Corporation, Edwards, CA, USA
Tue, Jan 9, 1:00pm‒1:20pm (Eastern) TF-01, Blue Spring I
Sim to Flight: Evaluating Flight Path Management Automation in High Density Urban Environments
Bryan A. Barrows*, Mark G Ballin, Terique L. Barney, Stewart L. Nelson, Matthew C. Underwood, David J. Wing
NASA Langley Research Center, Hampton, VA, USA
Tue, Jan 9, 1:20pm‒1:40pm (Eastern) TF-01, Blue Spring I
*presenter

## Slide 23
Email: david.a.karr@nasa.gov

## Slide 24: UAM Flight Path Differs from Commercial Transport
Climb
Climb / accel
Perf climb
Const speed
Climb / turn
Level turn
Perf descent
Transition
Descent / flare
Const speed
Level / decel
Descent / decel
Level / accel
Departure
Arrival
Accelerating or decelerating during a large fraction of flight time
Vertical takeoff and landing
Steep flight path angles
Low cruise speeds (60 to 129 knots)
No fuel usage
Must track battery usage

## Slide 25: Sharing Intended Trajectories
Efficient Universal Trajectory Language (EUTL) developed by NASA
groundspeed changes
in second turn
ID,lat,lon,alt,time,type,tcp_trk,tcp_gs,tcp_vs,radius,accel_gs,accel_vs,center_lat,center_lon,center_alt,info,name
unitless,deg,deg,ft,s,unitless,unitless,unitless,unitless,NM,m/s^2,m/s^2,deg,deg,ft,unitless,unitless
AOP110L,41.08814885,-73.00212920,2000.00000000,1600169062.90000010,Orig,NONE,NONE,NONE,0.00000000,0.00000000,0.00000000,-,-,-,-,-
AOP110L,41.07825540,-73.03501905,2000.00000000,1600169114.03785062,Orig,BOT,BGS,NONE,-0.63791351,-0.74495200,0.00000000,41.06839911,-73.02979903,609.60000000,-,-
AOP110L,41.07599900,-73.03962510,2000.00000000,1600169122.51021338,Orig,MOT,EGSBGS,NONE,0.00000000,-0.88216260,0.00000000,-,-,-,-,-
AOP110L,41.07258551,-73.04273473,2000.00000000,1600169132.37732053,Orig,EOT,EGS,NONE,0.00000000,0.00000000,0.00000000,-,-,-,-,-
AOP110L,41.02257153,-73.07118438,2000.00000000,1600169273.08290076,Orig,BOT,BGS,NONE,0.63783975,0.88204201,0.00000000,41.02675282,-73.08411222,609.60000000,-,-
AOP110L,41.01915759,-73.07428948,2000.00000000,1600169282.95052576,Orig,MOT,EGSBGS,NONE,0.00000000,0.74524741,0.00000000,-,-,-,-,-
AOP110L,41.01689988,-73.07888952,2000.00000000,1600169291.42301226,Orig,EOT,EGS,NONE,0.00000000,0.00000000,0.00000000,-,-,-,-,-
AOP110L,40.98033378,-73.19980732,2000.00000000,1600169479.82579756,Orig,BOT,BGS,NONE,0.72022116,0.25106029,0.00000000,40.99145309,-73.20572181,609.60000000,-,-
AOP110L,40.97947162,-73.20589393,2000.00000000,1600169488.67776299,Orig,MOT,EGSBGS,NONE,0.00000000,-0.27908704,0.00000000,-,-,-,-,-
AOP110L,40.98043321,-73.21195435,2000.00000000,1600169497.54954100,Orig,EOT,EGS,NONE,0.00000000,0.00000000,0.00000000,-,-,-,-,-
AOP110L,40.99897618,-73.26955271,2000.00000000,1600169588.53214574,Orig,NONE,NONE,BVS,0.00000000,0.00000000,-0.98000000,-,-,-,-,-
AOP110L,40.99950399,-73.27119400,1989.20068064,1600169591.12398243,Orig,NONE,BGS,NONE,0.00000000,0.12842323,0.00000000,-,-,-,-,-
AOP110L,41.00003682,-73.27285096,1956.80271725,1600169593.71581936,Orig,NONE,NONE,EVS,0.00000000,0.00000000,0.00000000,-,-,-,-,-
AOP110L,41.00198588,-73.27891297,1800.82463150,1600169603.07450438,Orig,BOT,EGSBGS,NONE,-0.47967828,0.12842323,0.00000000,40.99464389,-73.28305669,518.84597604,-,-
AOP110L,41.00262381,-73.28295138,1702.25057756,1600169608.98894763,Orig,MOT,EGS,NONE,0.00000000,0.00000000,0.00000000,-,-,-,-,-
AOP110L,41.00262113,-73.28334991,1692.96887645,1600169609.54584980,Orig,NONE,BGS,NONE,0.00000000,-1.01149620,0.00000000,-,-,-,-,-
AOP110L,41.00204672,-73.28700582,1601.72863607,1600169615.08028579,Orig,EOT,EGSBGS,NONE,0.00000000,-0.98032533,0.00000000,-,-,-,-,-
AOP110L,41.00030807,-73.29272688,1427.31321310,1600169625.55015039,Orig,NONE,NONE,BVS,0.00000000,0.00000000,0.98000000,-,-,-,-,-
AOP110L,41.00023421,-73.29296988,1419.40034214,1600169626.04917860,Orig,NONE,EGSBGS,NONE,0.00000000,-0.97715360,0.00000000,-,-,-,-,-
AOP110L,41.00016142,-73.29320936,1412.28815528,1600169626.54820681,Orig,NONE,NONE,EVS,0.00000000,0.00000000,0.00000000,-,-,-,-,-
AOP110L,40.99695935,-73.30374240,823.72237610,1600169670.30829620,Orig,NONE,NONE,BVS,0.00000000,0.00000000,-0.98000000,-,-,-,-,-
AOP110L,40.99695910,-73.30374322,818.80181597,1600169670.65940666,Orig,NONE,EGS,NONE,0.00000000,0.00000000,0.00000000,-,-,-,-,-
AOP110L,40.99695910,-73.30374322,813.48488784,1600169671.01051712,Orig,NONE,NONE,EVS,0.00000000,0.00000000,0.00000000,-,-,-,-,-
AOP110L,40.99695910,-73.30374322,807.36896317,1600169671.39987731,Orig,NONE,NONE,BVS,0.00000000,0.00000000,0.98000000,-,-,-,-,-
AOP110L,40.99695910,-73.30374322,769.00000000,1600169676.28526998,Orig,NONE,NONE,EVS,0.00000000,0.00000000,0.00000000,-,-,-,-,-
4D point coordinates
first turn geometry
top of descent
reduce speed
to hover
touchdown

## Slide 26: Conflict Detection
Predict future losses of separation with traffic aircraft and other hazards
“Hockey puck” protected zone for aircraft-aircraft encounters
Protected zone for flight test: R = 1500 ft radius, H = 450 ft
Any penetration of one aircraft’s protected zone by another aircraft is a conflict
Any penetration of an “area hazard” is a conflict
R
H
H

## Slide 27: Using PBGA for UAM
Time scales are shorter than in previous research
  Conflict alert 3 minutes before loss of separation
  Less than 20 seconds to produce resolution (less than 15 seconds in some scenarios)
Traffic density higher than in previous research
  150 aircraft in first batch simulation, observed long elapsed times for PBGA
  250 to 330 aircraft “seen” by AOP in flight test
  Elapsed time of CD for N traffic aircraft has at least linear growth
New development: run four parallel threads

## Slide 28: Installation of AOP on SARA
Intel NUC11TNHi7 Next Unit of Computing (NUC)
64 GB of memory
4 cores
8 hardware threads
Maximum clock rate 4.7 GHz
Windows operating system
54 cm
(2.1 in)

## Slide 29: AOP Defect #1
Replanning for an RTA without checking for conflicts
Example: speed reduction to meet RTA allows trailing aircraft to overtake
Workaround for flight test:
  BBTG produces new flight plan in response to new RTA
  Pilot executes flight plan
  PBGA resolves the resulting conflict
  Pilot selects and executes resolution flight plan
Proposed design:
  BBTG produces new flight plan in response to new RTA
  AOP checks flight plan for conflicts
  If conflict, PBGA generates new flight plan
  Pilot executes flight plan

## Slide 30: AOP Defect #2
Instability of conflict detection (CD) results
Cause: assumption that trajectories for CD must always be recomputed with latest data
  Inherited from operating environment where definitive trajectories were not available
  Some conflict geometries are highly sensitive to input data
  Recomputation with new data leads to new predicted trajectories
Proposed design:
  Use only the broadcast 4D trajectories (4DTs) for ownship and traffic in CD
Implications for operating environment
  Broadcast of 4DT is a conditional guarantee to follow it
  When should the guarantee expire?
  Contingencies: what conditions for early cancellation of 4DT?

## Slide 31: Why Use One Trajectory Generator for All Trajectories
RTA
TOD
t = t1
t = t1
t = t2
t = t2
Ownship
Intruder
RTA
TOD
t = t1
t = t2
t = t2
Ownship
Intruder
t = t1
Other TG predicts ownship trajectory
BBTG predicts ownship trajectory
Loss of separation
Higher airspeed
Lower airspeed