## Slide 1
Presenter Jonathan Jackson | DTNME Team Ivica Ristovski Joshua Deaton Jonathan Jackson Patricia Shatz Robert Neutze
DTN Marshall Enterprise (DTNME) Overview SCaN DTN F2F January 22 – 26, 2023 | 

## Slide 2
Agenda
Introduction | Current ISS DTN | DTNME In-Work | Strategic Planning

## Slide 3
International Space Station (ISS) Delay Tolerant Networking (DTN) supports a multipath routing architecture between the ISS and the ground.
  This service supports numerous payloads and reliable payload data transfers.
Support teams are strategically planning and implementing improvements to the ISS DTN framework to satisfy technical standards, improve the user experience and meet the anticipated increase of various DTN clients onboard the ISS.
  The ISS DTN team is implementing a strategy and migration of the current ISS DTN architecture to a more robust and sustainable subsystem. This effort will provide the framework to support additional DTN clients onboard the ISS and address current operational limitations for the next level of support for standards.
This presentation describes our Strategic Planning and progress towards implementing these improvements.
Introduction

## Slide 4
Current ISS DTN
NOTE:
JSL DTNME v1.0.1 is ready for operations.
Payload A
TREK/ION
Payload B
TREK/ION
Payload C
Payload D
Payload E
TREK/ION
TREK/ION
(VM)
ION
G/W
1
DTNME
G/W
2
DTNME
G/W
HOSC
DTNME
G/W
HOSC
Payload Investigator A
TREK/ION
Payload Investigator B
EPC/ION
Payload Investigator C
TREK/ION
Payload Investigator D
TREK/ION
BP over STCP/TCP
TCP over Wireless
UDP
BP over STCP/TCP
BPv6 Stream
BP over LTP
over UDP
Space Link Encapsulation
BPv6 Stream
UDP
BP over TCP
BP over TCP
ONBOARD | GROUND

## Slide 5
MSFC and JSC are currently working on upgrading their DTNME ground and onboard nodes to include the latest DTNME features.
  Currently available on Github DTNME v1.2_BETA Features
    BPv7 and BPv6 support
    RHEL 8 compatibility
    Bundle Architectural Restaging Daemon (BARD)
Bundle Architectural Restaging Daemon (BARD) is a new DTNME technology feature that allows operations to have better control over different bundle flows within a DTN system.
  BARD is planned for incorporation into ISS operations during FY24.
Updated Console Interface. Previously DTNME provided a raw socket interface that a user could connect locally to perform certain status and control commands. This interface has been updated to use web sockets with TLS.
  Web sockets are planned for incorporation into ISS operations during FY24
DTN Management Architecture (DTNMA) integration planned ISS work to be completed in FY25.
  MSFC DTN Development efforts will include collaboration with other centers to develop the operations user interface
DTNME In-Work

## Slide 6
IMC Orange Book draft was submitted for review to the CCSDS DTN Working Group Fall 23.
  In February 2022, the MSFC DTN team proposed an integration for IMC.
  This version provided DTNME interoperability with the ION 4.1.1 Bundle Multicast implementation and provided an enhanced capability using IMC Router Nodes.
  There is currently no standard for IMC, thus the DTNME implementation required examination of the ION source code to determine the potential for compatibility.
  IMC Orange book draft includes:
    Definition of the IMC URI
    Basic Requirements on its usage
    Discussion of basic routing concepts
  IMC White Paper/Yellow Book Draft is in work
    The Orange Book originally included a discussion on how ION and DTNME implemented IMC and discussed routing concepts between the two; however, it was suggested that this information would be better suited for a Yellow Book or White Paper, so it was removed and is being planned for release as such.
Interplanetary Multipoint Communication (IMC)

## Slide 7
During the Fall Space Communications and Navigation (SCaN) DTN Working Group face-to-face, the consensus was reached to develop a unified DTN API.
  Scope
    Develop an Application Programming Interface (API) prototype to demonstrate the potential for merging communications and operations among different Delay Tolerant Network (DTN) software implementations.
  Benefits
    Will reduce the cost of maintaining multiple distinct DTN implementations throughout NASA.
    Sits between the Bundle Protocol Agent and End User Applications, will allow NASA implementations to share technological advancements instead of having to redevelop code for each implementation.
    This effort is a potential steppingstone to incorporating additional end-user applications for the ISS.
Unified DTN API

## Slide 8
Backup

## Slide 9
AMP | Asynchronous Management Protocol |  |  | JSC | Johnson Space Center
BARD | Bundle Architectural Restaging Daemon |  |  | JSL | Joint Station LAN
BP | Bundle Protocol |  |  | LCRD | Laser Communication Relay Demonstration
BPsec | Bundle Protocol Security |  |  | LTP | Licklider Transmission Protocol
DMC | Data Management Controller |  |  | MSFC | Marshall Space Flight Center
DOCR | Data Operations Control Room |  |  | NORM | NACK-Oriented Reliable Multicast
DTN | Delay Tolerant Networking |  |  | RHEL | Red Hat Enterprise Linux
DTNME | DTN Marshall Enterprise |  |  | RTPoverDTN | Real Time Protocol over DTN
EHS | Enhanced HOSC System |  |  | SABR | Schedule Aware Bundle Routing
EID | Endpoint ID |  |  | SCaN | Space Communications and Navigation
ENCODE | Enabling Network Communication with Optical and DTN for Exploration |  |  | STCP | Simple TCP
EPC | EHS Personal Computer |  |  | TCP | Transmission Control Protocol
GRC | Glen Research Center |  |  | TReK | Telescience Resource Kit
G/W | Gateway |  |  | UDP | User Datagram Protocol
HDTN | High-rate Delay Tolerant Networking |  |  | VM | Virtual Machine
HOSC | Huntsville Operations Support Center |  |  |  | 
IMC-BMD | Interplanetary Multicast Bundle Multi-destination |  |  |  | 
ION | Interplanetary Overlay Network |  |  |  | 
ISS | International Space Station |  |  |  | 
Acronyms

## Slide 10
DTNME
G/W 1
HOSC
Future ISS DTN
ONBOARD | GROUND
KEY: |  | Web Service | 
New |  | AMP Agent | 
Current |  | AMP Manager | 
Local or Remote Client
BP over STCP/TCP
TCP over Wireless
UDP
BP over STCP/TCP
UDP
BP over TCP
BP over TCP
Payload A
TREK/ION
Payload B
TREK/ION
Payload C
Payload D
Payload E
TREK/ION
TREK/ION
(VM)
ION
G/W
1
DTNME
G/W
2
Payload Investigator A
TREK/ION
Payload Investigator B
EPC/ION
Payload Investigator C
TREK/ION
Payload Investigator D
TREK/ION
User Interface
DMC from EPC
DOCR Console
DTNME
G/W 2
HOSC