## Slide 1: Mars Sample Return: Capture, Containment and Return System

## Slide 2: My background
Bachelors in Math, Physics at University of Oregon
  Worked in an ant lab, PI also worked with LIGO
  Winter and Summer holidays spent at Hanford LIGO
PhD at LSU (2014 - 2019), commissioner for LIGO Louisiana
  Sept 14 2015: First gravitational wave detection
  2017: LIGO founders awarded the Nobel Prize in Physics
  Thesis under Gaby Gonzalez: High power and optomechanics in Advanced LIGO detectors
Postdoctoral Fellow at NASA GSFC with LISA Telescope
  Laser Interferometer Space Antenna (i.e. LIGO in space and really big)
  Planned launch date: 2037
NASA Aerospace Technology Optical Engineer at GSFC
  Mars Sample Return Capture, Containment and Return System
  DAVINCI (planned Venus probe mission)
  Artemis optical communication systems
Atta Cephalotes leafcutter
gardening ants

## Slide 3: Mars Sample Return

## Slide 4: Why bring samples back?

## Slide 5: Mars 2020 Perseverance landing in Jezero Crater: ancient biosignatures and sample diversity
NASA/JPL-Caltech
M2020 Perseverance Rover
Long-lived and habitable ancient crater lake system
Clay-rich delta with mineralogical diversity
Crater floor igneous rocks for age dating

## Slide 6: Perseverance Sample collection and storage
Image of drilled rock
Images of top of sample tubes
Sample of Mars rock inside sample tube
rock
drill bit
sample tube opening
Carbon and Sulfur detected (organic/inorganic origins unknown)
Sample Tube

## Slide 7: Mars Sample Return Campaign
Mars
Mars Launch
System
Orbiting
Sample
Mars 2020 Perseverance
Retrieve OS
Earth Entry System
Break-the-Chain
Avoid Earth
ERO
SRL
Tube Collection and Depot
Tube Delivery
Tube Retrieval
Relay Support
SFH
with CCRS
Mars 2020 (JPL)
Sample Receiving Project (SRP) (NASA/ESA)
Earth
2027
2028
2033
2020
3 June 2022
Sample Retrieval Lander (SRL) (JPL),
with
Sample Fetch Helicopter(s) (SFH) (JPL)
and Mars Ascent Vehicle (MAV) (MSFC)
Earth Return Orbiter (ERO) (ESA), with
Capture, Containment, and Return System (CCRS) (GSFC)
CCRS is a GSFC payload on ESA’s Earth Return Orbiter (ERO) that:
Captures the Orbiting Sample (OS) in Mars Orbit
Contains and prepares the OS for Earth delivery
Returns Mars samples to Earth
Changes to the Campaign
Architecture and Dates may
change due to the September
2023 Independent Review
Board (IRB) Report

## Slide 8: Summary of CCRS Architecture and Key Functions
CCRS
OS Concept (2020)
Subsystems I work on
This is the Main Character

## Slide 10: Vision System

## Slide 11: Vision System: verify OS orientation prior to UV sterilization
Capture Lid opened and OS rendezvous
Capture Lid closed and OS funneling
Vision System confirms OS orientation
OS has ‘base’ and ‘lid’ ends
LID
BASE
Lid needs to be oriented towards Earth impact
(no parachutes for return!)
CCRS uses cameras with human in the loop to verify orientation
Cameras
Illumination
System
At this point, the OS can be flipped 180˚
50/50 chance of correct orientation

## Slide 12: Was Orbiting Sample (OS) captured in correct orientation?
OS lid  CORRECT
OS base  INCORRECT
Physics/Optics concepts we care about:
Radiometry
MTF
Signal to Noise
BRDF (bidirectional reflectance distribution function)
Base (incorrect orientation)
Lid (correct orientation)
Base (incorrect orientation)
Lid (correct orientation)
OS Lid
OS Base
Testbed
Simulation
OS Lid
OS Base
Worst-case OS Base
Worst-case OS Lid
OS Base
OS Lid

## Slide 13: System performance predicted using lab and software tools
Test bed acquired image
FRED simulated image
MTF over OS surface
Python pipelines (significant effort to develop & fast, flexible results):
  Calculate spatial sampling on OS surface, MTF, and other key metrics via Zemax OpticStudio (ZOS) API
  Transform and interpolate test bed images to simulate flight system
  Degrade images to simulate worst case scenarios (e.g., contamination)
  Automate determination of OS orientation within images (solely for analysis purposes)
COTS test bed (limited, approximate setups & rapid results):
  Predict system performance under a wide range of scenarios
  Provide worst-case images of OS for Python pipeline analysis
  Inform and cross-check computational models
FRED models (computationally intensive & flexible, precise setups):
  Predict system performance with all relevant surfaces and measured BRDFs
  Provide worst-case images of OS for Python pipeline analysis
  Inform and cross-check lab measurements
Lid endcap coverage

## Slide 14: Laboratory mock-up of VS to produce high-fidelity images
Imaging System
Off-the-shelf Color 20 Mpx 1” sensor cameras + lenses
Testbed imaging system is higher resolution (SNR>80) and better performing than assumed flight system, allowing us to degrade images in post processing to match specific flight system candidates
Comparing Modulation Transfer Function (spatial frequency response) validates performance similarity between lab lens system and assumed flight lens system
Cameras radiometrically calibrated to lumens/m2/sr
Illumination System
Genesis EDU1 board + 3D printed baffle providing EDU2 illumination footprint
Integrated System Level Testing
Surrounding architecture 3D printed; similar optical properties to flight hardware
3D printed OS endcaps; baseline and worst-case (most specular) proxies
Chart: MTF for lab testbed and TAGCAMS lens systems (on-axis)
Requirement | 100 | 60 | 60 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
TAGCAMS | 100 | 87 | 78 | 62 | 50 | 40 | 32 | 26 | 20
Requirement
TAGCAMS,
Example flight system
Lab testbed
system
Al 7075,
Teflon anodized
3D printed
material

## Slide 15: Vision System Components Heritage
Vision System illumination system is built around white light LEDs that have been operating for more than 4 years on the Mars Perseverance CacheCam
Vision System cameras are the Bayer filter versions of build-to-print MSSS ECAMs that have been operating in the inner Solar System for more than 7 years as OSIRIS-REx TAGCAMS (Touch And Go Camera System)
TAGCAMS StowCam image
September 23, 2023
TAGCAMS NavCam 1 image
September 24, 2023
September 22, 2016
September 23, 2023
September 24, 2023

## Slide 16: Machine learning code tests if endcaps are distinguishable
This is only for analysis – ground will be in the loop in flight
Machine learning (ML) code identifies endcaps in images taken in the lab or simulated using FRED
ML code identifies endcaps even when images are degraded to fail requirements
MTFs compared to requirement
Gaussian PSFs (log x-axis)
(expected MTF)
Notes: These are the PSFs and MTFs that I used, which are also color coded
So again, blue means that the model is confident while pink means that it failed
The black curve is the expected MTF of the camera, which is also shown on the left
The red curve is the minimum MTF requirement
And you can see with this color coding that compared to the requirement, your MTF would have be ridiculously bad before the model fails (you can barely see the pink lines)
To first order, this tells us that as long as the Vision System meets this requirement, if we just consider the MTF, we can be confident that it will be able to do its job and distinguish between the two endcaps (orientations) of the OS

## Slide 17: UV Sterilization

## Slide 18: Planetary protection is a key priority of MSR
“Planetary Protection is the discipline of protecting solar system bodies such as planets and moons from possible contamination by Earth life, and protecting Earth’s biosphere from any potential adverse effects that could result from bringing material collected from these bodies back to our planet.” - Mars Sample Return Safety Factsheet (nasa.gov)
MSR follows a ‘container within a container’ approach
Sample tube container – OS – is first externally sterilized
OS then returns to Earth inside of another sterile container
The nested containers are only opened in a specialized clean room upon Earth return
https://planetaryprotection.jpl.nasa.gov/missions

## Slide 19: UV sterilization system inside CCRS irradiates outside of OS

## Slide 20: Outer surface of OS is sterilized in discreet steps
Step 1
Step 11
Step 2
Step 3
Step 4
…
…
…

## Slide 21: Optical Design – Optical Error Budget
Accounts for radiant flux losses from LED output to OS illumination.
Losses are due to UVIA to OS pointing plus factors reducing radiant output. Tracked in these categories:
Post-Launch Systematic Loss:
Molecular Contamination
Particle Contamination
Radiation (Diode Irradiation)
Diode aging
Post-Launch Random Loss:
OS Position Uncertainty
  Thermal impact on Pointing Angle
  Vibration
    Thermal impact on LED output
    Current uncertainty impact on LED strings
Base
illumination
Side
illumination
Lid
illumination
Manufacturing/Alignment errors account for irradiance loss from LED mount in die to the UVIA (UV Optical bench) relative to the OS
  LED Die
  LED
  Submount
  Submount Assembly
  Lens Array
  Light Engine
  Module Mount (1 & 2)
  Module (1 & 2) Assembly
  Base Ring & Lid Ring
  UV Optical Bench
  UV Optical Bench Flexures
Test Uncertainties
  Telemetry Uncertainty (Fresnel loss, angle uncertainty)
  Other
UVIA pointing to OS
OS relative to UVIA
Losses to radiance
Legend:

## Slide 22: Setup of MC Simulation – Ray Tracing and OS Irradiance Evaluation
  Python codes and ZOS-API establish the software infrastructure for MC modeling/simulations
@Step 11 (Base + Step 1 thru 11)
Reference
MC1
MC Simulation allows for Manufacturing, Alignment/Assembly errors and OS uncertainty to evaluate OS Irradiance
  Target Design Value (480 W/m2) above the requirement (375 W/m2) is set to compensate for irradiance reduction arising from other errors
  Base and Lid reference + Manufacturing + Alignment/Assembly + OS Uncertainty
  Base illumination plus 11 Lid Ring translations, 25 mm each step, >480 W/m2

## Slide 23: Verifying performance of LED with no space heritage
Hours
Optical power doesn’t drop too much over long periods
Spectral emission is what the datasheet claims it is
Spectral emission doesn’t change too much with temperature changes
Chart: Nichia SU bare LED irradiance (WD = 140 mm)
| -300 | -250 | -200 | -150 | -100 | -50 | 0 | 50 | 100 | 150 | 200
Measured | 0.05 | 0.11 | 0.25 | 0.61 | 1.3 | 2.01 | 2.17 | 2.02 | 1.33
Modelled | 0.03 | 0.092 | 0.172 | 0.42 | 0.89 | 1.39 | 1.49 | 1.43 | 0.93 | 0.45 | 0.182
Chart: Nichia SU + custom asphere irradiance
| 0 | 5 | 10 | 15 | 20 | -5 | -10 | -15 | -20
Measured, Horizontal Axis | 745.4667 | 376.6 | 63.3 | 6.7667 | 2.6667 | 408.6333 | 51.3333 | 6.4667 | 1.9667
Measured, Vertical Axis | 743.4333 | 337.7333 | 41.2333 | 6.3 | 2.5333 | 330.8 | 44.9333 | 5.9333 | 2.4667
Measured, small steps | 745.1333 | 678.5 | 606.7667 | 464.1667 | 399.8667 | 337.7 | 254.5667 | 166.8333 | 130.9 | 72.7667 | 50.9667 | 34.6667 | 11.3667 | 9.1 | 7.2667 | 5.5 | 3.8667 | 2.9667 | 2.5333 | 2.4 | 2.1333
Modelled, one axis | 3.041 | 5.2403 | 9.0916 | 15.3631 | 24.0968 | 35.5665 | 52.4028 | 79.8668 | 118.9058 | 180.9894 | 257.8047 | 339.8813 | 417.7488 | 490.3551 | 549.2819 | 588.2156 | 600.8428 | 590.3202 | 555.5954 | 500.8777 | 423.0102 | 341.9858 | 259.9092 | 185.1985 | 121.0104 | 73.9742 | 46.0892 | 27.9902 | 17.2571 | 10.5226 | 6.1242 | 3.6619 | 2.5465
Modelled, other axis | 2.6412 | 3.9355 | 6.9555 | 11.9958 | 20.4139 | 33.5672 | 54.6125 | 86.6013 | 137.8466 | 203.087 | 275.6932 | 352.5085 | 425.1147 | 497.7209 | 553.4909 | 589.2679 | 600.8428 | 588.2156 | 549.2819 | 491.4073 | 419.8534 | 348.2994 | 271.4841 | 198.8779 | 132.5853 | 83.655 | 52.7184 | 33.0411 | 20.0982 | 12.3115 | 6.7134 | 3.725 | 2.3781
Chart: Percent loss relative to aligned
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
Measured, translation | 0 | 3.6635 | 11.5599 | 22.0913 | 35.3725 | 47.696 | 60.527 | 73.027 | 83.1965 | 91.3577 | 95.9834
Modelled, translation | 0 | 1.6667 | 6.6667 | 13.3333 | 24.8333 | 36.5 | 48.6667 | 60.1667 | 70.8333 | 80.8333 | 88.6667
Measured, piston | 0 | 0.72308 | 3.4267 | 6.9748 | 10.8821 | 14.9331 | 19.1682 | 24.113 | 28.932 | 33.6792 | 37.7077
Modelled, piston | 0 | 1.6667 | 5 | 8.3333 | 11.6667 | 16.6667 | 21.5 | 26.1667 | 31 | 36.1667 | 41
Absolute irradiance out of LED is what we expect (it was more!)
Model and measurement match with

## Slide 24
Optical Design – UV LED Irradiance Measurements
Nichia SU LEDs exceed spec’d output power in testbed measurements
Chart: Nichia SU bare LED irradiance (WD = 140 mm)
| -300 | -250 | -200 | -150 | -100 | -50 | 0 | 50 | 100 | 150 | 200
Measured | 0.05 | 0.11 | 0.25 | 0.61 | 1.3 | 2.01 | 2.17 | 2.02 | 1.33
Modelled | 0.03 | 0.092 | 0.172 | 0.42 | 0.89 | 1.39 | 1.49 | 1.43 | 0.93 | 0.45 | 0.182
Modelled in Zemax using total power over 11 mm aperture detector circle, LED source file from Nichia
3 Nichia SU LEDs giving 45% more power than expected
Chart: Nichia SU + custom asphere irradiance at 62.35 mm from LED
| 0 | 5 | 10 | 15 | 20 | -5 | -10 | -15 | -20
Measured, Horizontal Axis | 745.4667 | 376.6 | 63.3 | 6.7667 | 2.6667 | 408.6333 | 51.3333 | 6.4667 | 1.9667
Measured, Vertical Axis | 743.4333 | 337.7333 | 41.2333 | 6.3 | 2.5333 | 330.8 | 44.9333 | 5.9333 | 2.4667
Measured, small steps | 745.1333 | 678.5 | 606.7667 | 464.1667 | 399.8667 | 337.7 | 254.5667 | 166.8333 | 130.9 | 72.7667 | 50.9667 | 34.6667 | 11.3667 | 9.1 | 7.2667 | 5.5 | 3.8667 | 2.9667 | 2.5333 | 2.4 | 2.1333
Modelled, one axis | 3.041 | 5.2403 | 9.0916 | 15.3631 | 24.0968 | 35.5665 | 52.4028 | 79.8668 | 118.9058 | 180.9894 | 257.8047 | 339.8813 | 417.7488 | 490.3551 | 549.2819 | 588.2156 | 600.8428 | 590.3202 | 555.5954 | 500.8777 | 423.0102 | 341.9858 | 259.9092 | 185.1985 | 121.0104 | 73.9742 | 46.0892 | 27.9902 | 17.2571 | 10.5226 | 6.1242 | 3.6619 | 2.5465
Modelled, other axis | 2.6412 | 3.9355 | 6.9555 | 11.9958 | 20.4139 | 33.5672 | 54.6125 | 86.6013 | 137.8466 | 203.087 | 275.6932 | 352.5085 | 425.1147 | 497.7209 | 553.4909 | 589.2679 | 600.8428 | 588.2156 | 549.2819 | 491.4073 | 419.8534 | 348.2994 | 271.4841 | 198.8779 | 132.5853 | 83.655 | 52.7184 | 33.0411 | 20.0982 | 12.3115 | 6.7134 | 3.725 | 2.3781
Measurements within error bars of model, except higher at peak

## Slide 25: Measured sensitivity not giving any red flags for error budget expectations
asphere
Nichia SU LED
Chart: Percent loss relative to aligned
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
Measured, translation | 0 | 3.6635 | 11.5599 | 22.0913 | 35.3725 | 47.696 | 60.527 | 73.027 | 83.1965 | 91.3577 | 95.9834
Modelled, translation | 0 | 1.6667 | 6.6667 | 13.3333 | 24.8333 | 36.5 | 48.6667 | 60.1667 | 70.8333 | 80.8333 | 88.6667
Measured, piston | 0 | 0.72308 | 3.4267 | 6.9748 | 10.8821 | 14.9331 | 19.1682 | 24.113 | 28.932 | 33.6792 | 37.7077
Modelled, piston | 0 | 1.6667 | 5 | 8.3333 | 11.6667 | 16.6667 | 21.5 | 26.1667 | 31 | 36.1667 | 41
Chart: Irradiance sensitivity to asphere translation
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
Measured | 755.2 | 727.5333 | 667.9 | 588.3667 | 488.0667 | 395 | 298.1 | 203.7 | 126.9 | 65.2667 | 30.3333
Modelled | 600 | 590 | 560 | 520 | 451 | 381 | 308 | 239 | 175 | 115 | 68
Chart: Irradiance sensitivity to asphere piston
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
Measured | 742.2 | 736.8333 | 716.7667 | 690.4333 | 661.4333 | 631.3667 | 599.9333 | 563.2333 | 527.4667 | 492.2333 | 462.3333
Modelled | 600 | 590 | 570 | 550 | 530 | 500 | 471 | 443 | 414 | 383 | 354
Modelled using total power over 11 mm circle detector, assuming 45% higher power from LED than datasheet
@ 0.1 mm translation, 3.7% loss
@ 0.1 mm piston, 0.7% loss
Initial measurements matching alignment sensitivity expectations

## Slide 26: Work at NASA

## Slide 27: How to work for/with NASA
NASA OSTEM internships
  https://stemgateway.nasa.gov/public/s/explore-opportunities
  Traditional summer ~3-month internship
  Paid ($10-12k), housing and transport not included
  Note that JPL has their own special thing going on: https://www.jpl.nasa.gov/edu/intern/apply/
NASA Pathways
  Government part time job
  Work >10 hrs/wk during undergrad/grad school
  Direct pipeline to full time employment upon graduation
  Must be a US citizen
  Apply: USAjobs.gov, search NASA Pathways
    Applications have just opened in Feb
Future Investigators in NASA Earth and Space Science and Technology (FINESST)
  https://go.nasa.gov/FINESST23
  Graduate student research grant
  $50K per year, up to 3 years, discipline specific proposal categories
  Proposals due Feb each year
NASA Postdoctoral Program (NPP)
  https://npp.orau.org/applicants/opportunities.html
  2 years with extension possible, gateway to permanent position
  $70k-80k + $10k travel grant
NASA permanent position
  NASA engineer or scientist
  Openings are rare and govt funding dependent
  >$100k (location dependent) with PhD
  Apply: USAjobs.gov; you do not need a PhD to work at NASA
NASA contractor position (KBR, Peraton)
  Opportunities for foreign nationals
  Historically, similar to NASA position, bit less job security

## Slide 28: How to get involved with NASA: undergrad and grad internships
NASA OSTEM internships
  https://stemgateway.nasa.gov/public/s/explore-opportunities
  Traditional summer ~3-month internship
  Paid ($10-12k), housing and transport not included
  Note that JPL has their own special thing going on: https://www.jpl.nasa.gov/edu/intern/apply/
NASA Pathways
  Government part time job
  Work >10 hrs/wk during undergrad/grad school
  Direct pipeline to full time employment upon graduation
  Must be a US citizen
  Apply: USAjobs.gov, search NASA Pathways
    Applications have just opened in Feb
Future Investigators in NASA Earth and Space Science and Technology (FINESST)
  https://go.nasa.gov/FINESST23
  Graduate student research grant
  $50K per year, up to 3 years, discipline specific proposal categories
  Proposals due Feb each year
NASA Postdoctoral Program (NPP)
  https://npp.orau.org/applicants/opportunities.html
  2 years with extension possible, gateway to permanent position
  $70k-80k + $10k travel grant
NASA permanent position
  NASA engineer or scientist
  Openings are rare and govt funding dependent
  >$100k (location dependent) with PhD
  Apply: USAjobs.gov; you do not need a PhD to work at NASA
NASA contractor position (KBR, Peraton)
  Opportunities for foreign nationals
  Historically, similar to NASA position, bit less job security

## Slide 29: How to get involved with NASA
NASA OSTEM internships
  https://stemgateway.nasa.gov/public/s/explore-opportunities
  Traditional summer ~3-month internship
  Paid ($10-12k), housing and transport not included
  Note that JPL has their own special thing going on: https://www.jpl.nasa.gov/edu/intern/apply/
NASA Pathways
  Government part time job
  Work >10 hrs/wk during undergrad/grad school
  Direct pipeline to full time employment upon graduation
  Must be a US citizen
  Apply: USAjobs.gov, search NASA Pathways
    Applications have just opened in Feb
Future Investigators in NASA Earth and Space Science and Technology (FINESST)
  https://go.nasa.gov/FINESST23
  Graduate student research grant
  $50K per year, up to 3 years, discipline specific proposal categories
  Proposals due Feb each year
NASA Postdoctoral Program (NPP)
  https://npp.orau.org/applicants/opportunities.html
  2 years with extension possible, gateway to permanent position
  $70k-80k + $10k travel grant
NASA permanent position
  NASA engineer or scientist
  Openings are rare and govt funding dependent
  >$100k (location dependent) with PhD
  Apply: USAjobs.gov; you do not need a PhD to work at NASA
NASA contractor position (KBR, Peraton)
  Opportunities for foreign nationals
  Historically, similar to NASA position, bit less job security

## Slide 30: Backup

## Slide 31: Modulation Transfer Function [MTF]
Click to edit Master text styles
  Second level
    Third level
      Fourth level
        Fifth level
Analyzing the MTF of an imaging system is a way to understand how the contrast within an image varies with spatial frequency
Previously:
  Measuring MTF by placing a series of sinusoidal patterns at the object plane and measuring the contrast in the image plane, resulting in a set of data points for a given location on the OS